## Slide 1
Calling Conventions
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee and Sirer]

## Slide 2: Big Picture: Where are we going?
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
Forward
unit
Detect
hazard

## Slide 3: Big Picture: Where are we going?
addi x5, x0, 10
muli x5, x5, 2
addi x5, x5, 15
int x = 10;
x = 2 * x + 15;
C
compiler
RISC-V
assembly
machine
code
assembler
CPU
Circuits
Gates
Transistors
Silicon
x0 = 0
x5 = x0 + 10
x5 = x5<<1 #x5 = x5 * 2
x5 = x15 + 15
op = r-type x5 shamt=1 x5 func=sll
00000000101000000000001010010011
00000000001000101000001010000000
00000000111100101000001010010011
10 r0 r5 op = addi
15 r5 r5 op = addi
Notes: 32 bits, 4 bytes
Add a line to represent the instruction set architecture
Another line for assembly
Another line, high level language

## Slide 4: Big Picture: Where are we going?
SandyBridge Motherboard, 2011
http://news.softpedia.com
CPU
Main Memory
(DRAM)

## Slide 5: Goals for this week
Calling Convention for Procedure Calls
Enable code to be reused by allowing code snippets to be invoked
Will need a way to
  call the routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register
Notes: Ninja example from book

## Slide 6: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data
What is a Convention?
Warning: There is no one true RISC-V calling convention.
lecture != book != gcc != spim != web

## Slide 7: Cheat Sheet and Mental Model for Today
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
Forward
unit
Detect
hazard
How do we share registers and use memory when making procedure calls?

## Slide 8: Cheat Sheet and Mental Model for Today
  first eight arg words passed in a0, a1, … , a7
  remaining arg words passed in parent’s stack frame
  return value (if any) in a0, a1
  stack frame at sp
    contains ra (clobbered on JAL
    to sub-functions)
    contains local vars (possibly
    clobbered by sub-functions)
    contains space for incoming args
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs (s1 ... s11)
locals
incoming args
fp 
sp 

## Slide 9: RISC-V Register
Return address: x1 (ra)
Stack pointer: x2 (sp)
Frame pointer: x8 (fp/s0)
First eight arguments: x10-x17 (a0-a7)
Return result: x10-x11 (a0-a1)
Callee-save free regs: x18-x27 (s2-s11)
Caller-save free regs: x5-x7,x28-x31 (t0-t6)
Global pointer: x3 (gp)
Thread pointer: x4 (tp)

## Slide 10: RISC-V Register Conventions
x0 | zero | zero
x1 | ra | return address
x2 | sp | stack pointer
x3 | gp | global data pointer
x4 | tp | thread pointer
x5 | t0 | temps (caller save)
x6 | t1 | 
x7 | t2 | 
x8 | s0/fp | frame pointer
x9 | s1 | saved (callee save)
x10 | a0 | function args or return values
x11 | a1 | 
x12 | a2 | function arguments
x13 | a3 | 
x14 | a4 | 
x15 | a5 | function arguments
x16 | a6 | 
x17 | a7 | 
x18 | s2 | saved (callee save)
x19 | s3 | 
x20 | s4 | 
x21 | s5 | 
x22 | s6 | 
x23 | s7 | 
x24 | s7 | 
x25 | s9 | 
x26 | s10 | 
x27 | s11 | 
x28 | t3 | temps (caller save)
x29 | t4 | 
x30 | t5 | 
x31 | t6 | 

## Slide 11: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data
What is a Convention?
Warning: There is no one true RISC-V calling convention.
lecture != book != gcc != spim != web

## Slide 12: How does a function call work?
int main (int argc, char* argv[ ]) {
int n = 9;
int result = myfn(n);
}
int myfn(int n) {
int f = 1;
int i = 1;
int j = n – 1;
while(j >= 0) {
f *= i;
i++;
j = n - i;
}
return f;
}

## Slide 13: Jumps are not enough
main:
j myfn
after1:
add x1,x2,x3
myfn:
…
…
j after1
Jumps to the callee
Jumps back
1
2
Notes: Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back

## Slide 14: Jumps are not enough
main:
j myfn
after1:
add x1,x2,x3
j myfn
after2:
sub x3,x4,x5
myfn:
…
…
j after1
Jumps to the callee
Jumps back
What about multiple sites?
1
2
??? Change target
on the fly ???
j after2
3
4
Notes: Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back

## Slide 15: Takeaway1: Need Jump And Link
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register x1 (aka $ra or return address)
Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register x1

## Slide 16: Jump-and-Link / Jump Register
main:
jal myfn
after1:
add x1,x2,x3
jal myfn
after2:
sub x3,x4,x5
myfn:
…
…
jr x1
JAL saves the PC in register $31
Subroutine returns by jumping to $31
1
2
x1
after1
First call

## Slide 17: Jump-and-Link / Jump Register
after1
main:
jal myfn
after1:
add x1,x2,x3
jal myfn
after2:
sub x3,x4,x5
myfn:
…
…
jr x1
JAL saves the PC in register x1
Subroutine returns by jumping to x1
What happens for recursive invocations?
1
2
x1
after2
Second call
4
3

## Slide 18: JAL / JR for Recursion?
int main (int argc, char* argv[ ]) {
int n = 9;
int result = myfn(n);
}
int myfn(int n) {
int f = 1;
int i = 1;
int j = n – 1;
while(j >= 0) {
f *= i;
i++;
j = n - i;
}
return f;
}

## Slide 19: JAL / JR for Recursion?
int main (int argc, char* argv[ ]) {
int n = 9;
int result = myfn(n);
}
int myfn(int n) {
if(n > 0) {
return n * myfn(n - 1);
} else {
return 1;
}
}

## Slide 20: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
1
x1
after1
First call

## Slide 21: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
1
x1
Recursive Call
2
after1
after2

## Slide 22: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
1
x1
after2
Return from Recursive Call
2
3

## Slide 23: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
1
x1
after2
Return from Original Call???
2
3
4
Stuck!

## Slide 24: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
Need a way to save and restore register contents
1
x1
after2
Return from Original Call???
2
3
4
Stuck!

## Slide 25: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register (x2) on the RISC-V
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
after1
high mem
low mem
x1 =
sp

## Slide 26: Cheat Sheet and Mental Model for Today
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
Forward
unit
Detect
hazard

## Slide 27: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register (x2) on the RISC-V
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
after1
high mem
low mem
x1 =
sp
sp
after2
Push: ADDI sp, sp, -4
SW x1, 0 (sp)
x1 =

## Slide 28: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register (x2) on the RISC-V
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
after1
high mem
low mem
x1 =
sp
sp
after2
Push: ADDI sp, sp, -4
SW x1, 0 (sp)
x1 =
Pop: LW x1, 0 (sp)
ADDI sp, sp, 4
JR x1

## Slide 29: Need a “Call Stack”
after1
high mem
low mem
after2
sp
after2
after2
sp
sp
Stack used to save and restore contents of x1
main:
jal myfn
after1:
add x1,x2,x3
myfn:
addi sp,sp,-4
sw x1, 0(sp)
if (test)
jal myfn
after2:
lw x1, 0(sp)
addi sp,sp,4
jr x1
2

## Slide 30: Need a “Call Stack”
after1
high mem
low mem
after2
sp
after2
after2
sp
sp
Stack used to save and restore contents of x1
main:
jal myfn
after1:
add x1,x2,x3
myfn:
addi sp,sp,-4
sw x1, 0(sp)
if (test)
jal myfn
after2:
lw x1, 0(sp)
addi sp,sp,4
jr x1
2
sp

## Slide 31: Stack Growth
(Call) Stacks start at a high address in memory
Stacks grow down as frames are pushed on
  Note: data region starts at a low address and grows up
  The growth potential of stacks and data region are not artificially limited

## Slide 32: An executing program in memory
top
bottom
system reserved
stack
system reserved
.data
.text
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)

## Slide 33: An executing program in memory
top
bottom
system reserved
stack
system reserved
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)
“Data Memory”
“Program Memory”

## Slide 34: Anatomy of an executing program
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
Forward
unit
Detect
hazard
Stack, Data, Code
Stored in Memory
x2 ($sp)
x1 ($ra)
Stack, Data, Code
Stored in Memory

## Slide 35: An executing program in memory
top
bottom
system reserved
stack
system reserved
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)
“Data Memory”
“Program Memory”

## Slide 36: Return Address lives in Stack Frame
x2000
x1FD0
Stack Manipulated by push/pop operations
Context: after 2nd JAL to myfn (from myfn)
PUSH: ADDI sp, sp, -20 // move sp down
SW x1, 16(sp) // store retn PC 1st
Context: 2nd myfn is done (x1 == ???)
POP: LW x1, 16(sp) // restore retn PC r31
ADDI sp, sp, 20 // move sp up
JR x1 // return
myfn stack frame
main stack frame
myfn stack frame
after2
r31
r29
x2000
For now: Assume each frame = x20 bytes
(just to make this example concrete)
x1FD0
after2
XXXX

## Slide 37: The Stack
Stack contains stack frames (aka “activation records”)
  1 stack frame per dynamic function
  Exists only for the duration of function
Grows down, “top” of stack is sp, x2
Example: lw x5, 0(sp) puts word at top of stack into x5
Each stack frame contains:
  Local variables, return address (later), register
  backups (later)
int main(…) {
...
myfn(x);
}
int myfn(int n) {
...
myfn();
}
system reserved
stack
code
heap
system reserved
static data
myfn stack frame
myfn stack frame
main stack frame
$sp

## Slide 38: The Heap
Heap holds dynamically allocated memory
Program must maintain pointers to anything allocated
  Example: if x5 holds x
  lw x6, 0(x5) gets first word x points to
Data exists from malloc() to free()
void some_function() {
int *x = malloc(1000);
int *y = malloc(2000);
free(y);
int *z = malloc(3000);
}
system reserved
stack
X
Y
z
code
heap
system reserved
static data
1000 bytes
2000 bytes
3000 bytes

## Slide 39: Data Segment
Data segment contains global variables
  Exist for all time, accessible to all routines
Accessed w/global pointer
  gp, x3, points to middle of segment
  Example: lw x5, 0(gp) gets middle-most word
  (here, max_players)
int max_players = 4;
int main(...) {
...
}
gp
4
system reserved
stack
code
heap
system reserved
static data

## Slide 40: Globals and Locals
int n = 100;
int main (int argc, char* argv[ ]) {
int i, m = n, sum = 0;
int* A = malloc(4*m + 4);
for (i = 1; i <= m; i++) {
sum += i; A[i] = sum; }
printf ("Sum 1 to %d is %d\n", n, sum);
}
Variables Visibility Lifetime Location
Function-Local
Global
Dynamic
Where is i ?
Stack
Heap
Global Data
Text
Where is n ?
Stack
Heap
Global Data
Text
Where is main ?
Stack
Heap
Global Data
Text
Notes: function / func invocation / stack
file or prog / prog execution / data segment
undef / malloc to free / heap
bug in this code

## Slide 41: An executing program in memory
top
bottom
system reserved
stack
system reserved
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)
“Data Memory”
“Program Memory”

## Slide 42: Globals and Locals
int n = 100;
int main (int argc, char* argv[ ]) {
int i, m = n, sum = 0;
int* A = malloc(4*m + 4);
for (i = 1; i <= m; i++) {
sum += i; A[i] = sum; }
printf ("Sum 1 to %d is %d\n", n, sum);
}
Variables Visibility Lifetime Location
Function-Local
Global
Dynamic
i, m, sum, A
n, str
w/in function
function
invocation
stack
whole program
program
execution
.data
b/w malloc
and free
heap
Anywhere that
has a pointer
*A
Notes: function / func invocation / stack
file or prog / prog execution / data segment
undef / malloc to free / heap
bug in this code

## Slide 43: Takeaway2: Need a Call Stack
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register x1 (aka ra or return address) Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register x1
Need a Call Stack to return to correct calling procedure. To maintain a stack, need to store an activation record (aka a “stack frame”) in memory. Stacks keep track of the correct return address by storing the contents of x1 in memory (the stack).

## Slide 44: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data

## Slide 45: Next Goal
Need consistent way of passing arguments and getting the result of a subroutine invocation

## Slide 46: Arguments & Return Values
Need consistent way of passing arguments and getting the result of a subroutine invocation
Given a procedure signature, need to know where arguments should be placed
  int min(int a, int b);
  int subf(int a, int b, int c, int d, int e, int f, int g, int h, int i);
  int isalpha(char c);
  int treesort(struct Tree *root);
  struct Node *createNode();
  struct Node mynode();
Too many combinations of char, short, int, void *, struct, etc.
  RISC-V treats char, short, int and void * identically
$a0, $a1
stack?
$a0
$a0, $a1
$a0

## Slide 47: Simple Argument Passing (1-8 args)
First eight arguments:
passed in registers x10-x17
  aka $a0, $a1, …, $a7
Returned result:
passed back in a register
  Specifically, x10, aka a0
  And x11, aka a1
main:
li x10, 6
li x11, 7
jal myfn
addi x5, x10, 2
main() {
int x = myfn(6, 7);
x = x + 2;
}
Note: This is not the entire story for 1-8 arguments.
Please see the Full Story slides.

## Slide 48: Conventions so far:
  args passed in $a0, $a1, …, $a7
  return value (if any) in $a0, $a1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
Q: What about argument lists?

## Slide 49: Many Arguments (8+ args)
First eight arguments:
passed in registers x10-x17
  aka a0, a1, …, a7
Subsequent arguments:
”spill” onto the stack
Args passed in child’s stack frame
main:
li x10, 0
li x11, 1
…
li x17, 7
li x5, 8
sw x5, -8(x2)
li x5, 9
sw x5, -4(x2)
jal myfn
main() {
myfn(0,1,2,..,7,8,9);
…
}
Note: This is not the entire story for 9+ args.
Please see the Full Story slides.
9
8
sp
space for x17
space for x16
space for x15
space for x14
space for x13
space for x12
space for x11
space for x10

## Slide 50: Many Arguments (8+ args)
First eight arguments:
passed in registers x10-x17
  aka a0, a1, …, a7
Subsequent arguments:
”spill” onto the stack
Args passed in child’s stack frame
main:
li a0, 0
li a1, 1
…
li a7, 7
li t0, 8
sw t0, -8(sp)
li t0, 9
sw t0, -4(sp)
jal myfn
main() {
myfn(0,1,2,..,7,8,9);
…
}
Note: This is not the entire story for 9+ args.
Please see the Full Story slides.
9
8
sp
space for x17
space for x16
space for x15
space for x14
space for x13
space for x12
space for x11
space for x10

## Slide 51: Argument Passing: the Full Story
main() {
myfn(0,1,2,..,7,8,9);
…
}
Arguments 1-8:
passed in x10-x17 room on stack
Arguments 9+:
placed on stack
Args passed in child’s stack frame
-40($sp)
-36($sp)
-32($sp)
-28($sp)
-24($sp)
-20($sp)
9
8
sp
space for x17
space for x16
space for x15
space for x14
space for x13
space for x12
space for x11
space for x10
-16($sp)
-12($sp)
-8($sp)
-4($sp)
main:
li a0, 0
li a1, 1
…
li a7, 7
li t0, 8
sw t0, -8(x2)
li t0, 9
sw t0, -4(x2)
jal myfn

## Slide 52: Pros of Argument Passing Convention
Consistent way of passing arguments to and from subroutines
Creates single location for all arguments
  Caller makes room for a0-a7 on stack
  Callee must copy values from a0-a7 to stack
   callee may treat all args as an array in memory
  Particularly helpful for functions w/ variable length inputs: printf(“Scores: %d %d %d\n”, 1, 2, 3);
Aside: not a bad place to store inputs if callee needs to call a function (your input cannot stay in $a0 if you need to call another function!)

## Slide 53: iClicker Question
  Which is a true statement about the arguments to the function
  void sub(int a, int b, int c, int d, int e, int f, int g, int h, int i);
Arguments a-i are all passed in registers.
Arguments a-i are all stored on the stack.
Only i is stored on the stack, but space is allocated for all 9 arguments.
Only a-h are stored on the stack, but space is allocated for all 9 arguments.

## Slide 54: iClicker Question
  Which is a true statement about the arguments to the function
  void sub(int a, int b, int c, int d, int e, int f, int g, int h, int i);
Arguments a-i are all passed in registers.
Arguments a-i are all stored on the stack.
Only i is stored on the stack, but space is allocated for all 9 arguments.
Only a-h are stored on the stack, but space is allocated for all 9 arguments.

## Slide 55: Frame Layout & the Frame Pointer
blue() {
pink(0,1,2,3,4,5);
}
blue’s Ret Addr
sp
blue’s stack frame
sp

## Slide 56: Frame Layout & the Frame Pointer
space for a4
space for a3
space for a2
space for a1
space for a0
space for a5
blue’s Ret Addr
pink’s Ret Addr
sp
fp
pink’s stack frame
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
…
}
Notice
Pink’s arguments are on pink’s stack
sp changes as functions call other functions, complicates accesses
 Convenient to keep pointer to bottom of stack == frame pointer
x8, aka fp (also known as s0)
can be used to restore sp on exit
sp
blue’s stack frame

## Slide 57: Conventions so far
  first eight arg words passed in $a0, $a1, …, $a7
  Space for args in child’s stack frame
  return value (if any) in $a0, $a1
  stack frame ($fp/$s0 to $sp) contains:
    $ra (clobbered on JAL to sub-functions)
    space for 8 arguments to Callees
    arguments 9+ to Callees

## Slide 58: RISCV Register Conventions so far:
x0 | zero | zero
x1 | ra | Return address
x2 |  | 
x3 |  | 
x4 |  | 
x5 |  | 
x6 |  | 
x7 |  | 
x8 | s0/fp | Saved register or framepointer
x9 | s1 | Saved register
x10 | a0 | Function args or return values
x11 | a1 | 
x12 | a2 | Function args
x13 | a3 | 
x14 | a4 | 
x15 | a5 | 
x16 |  | 
x17 |  | 
x18 | s2 | Saved registers
x19 |  | 
x20 |  | 
x21 |  | 
x22 |  | 
x23 |  | 
x24 |  | 
x25 |  | 
x26 |  | 
x27 |  | 
x28 | t3 | Temporary registers
x29 |  | 
x30 |  | 
x31 |  | 
 | sp | Stack pointer
 |  | Temporary registers
 | t0 | 
 | t1 | 
 | t2 | 

## Slide 59: C & RISCV: the fine print
C allows passing whole structs
  int dist(struct Point p1, struct Point p2);
  Treated as collection of consecutive 32-bit arguments
    Registers for first 4 words, stack for rest
  Better: int dist(struct Point *p1, struct Point *p2);
Where are the arguments to:
  void sub(int a, int b, int c, int d, int e, int f, int g, int h, int i);
  void isalpha(char c);
  void treesort(struct Tree *root);
Where are the return values from:
  struct Node *createNode();
  struct Node mynode();
Many combinations of char, short, int, void *, struct, etc.
  RISCV treats char, short, int and void * identically
a0, a1
a2, a3
a0
a1
a0, a1
stack
a0
a0, a1
a0

## Slide 60: Globals and Locals
Global variables are allocated in the “data” region of the program
  Exist for all time, accessible to all routines
Local variables are allocated within the stack frame
  Exist solely for the duration of the stack frame
Dangling pointers are pointers into a destroyed stack frame
  C lets you create these, Java does not
  int *foo() { int a; return &a; }
Return the address of a,
But a is stored on stack, so will be removed
when call returns and point will be invalid

## Slide 61: Global and Locals
How does a function load global data?
  global variables are just above 0x10000000
Convention: global pointer
  x3 is gp (pointer into middle of global data section) gp = 0x10000800
  Access most global data using LW at gp +/- offset LW t0, 0x800(gp) LW t1, 0x7FF(gp)
Notes: # data at 0x10000000
# data at 0x10000FFF
(4KB range)

## Slide 62: Anatomy of an executing program
top
bottom
system reserved
stack
system reserved
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)
$gp

## Slide 63: Frame Pointer
It is often cumbersome to keep track of location of data on the stack
  The offsets change as new values are pushed onto and popped off of the stack
Keep a pointer to the bottom of the top stack frame
  Simplifies the task of referring to items on the stack
A frame pointer, x8, aka fp/s0
  Value of sp upon procedure entry
  Can be used to restore sp on exit

## Slide 64: Conventions so far
first eight arg words passed in a0-a7
Space for args in child’s stack frame
return value (if any) in a0, a1
stack frame (fp/s0 to sp) contains:
  ra (clobbered on JALs)
  space for 8 arguments
  arguments 9+
global data accessed via gp

## Slide 65: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data

## Slide 66: Next Goal
What convention should we use to share use of registers across procedure calls?

## Slide 67: Register Management
Functions:
Are compiled in isolation
Make use of general purpose registers
Call other functions in the middle of their execution
  These functions also use general purpose registers!
  No way to coordinate between caller & callee
 Need a convention for register management
Notes: Also, $gp is a callee save register

## Slide 68: Register Usage
Suppose a routine would like to store a value in a register
Two options: callee-save and caller-save
Callee-save:
  Assume that one of the callers is already using that register to hold a value of interest
  Save the previous contents of the register on procedure entry, restore just before procedure return
  E.g. $ra, $fp/$s0, $s1-$s11, $gp, $tp
  Also, $sp
Caller-save:
  Assume that a caller can clobber any one of the registers
  Save the previous contents of the register before proc call
  Restore after the call
  E.g. $a0-a7, $t0-$t6
RISCV calling convention supports both

## Slide 69: Caller-saved
Registers that the caller cares about: t0… t9
About to call a function?
Need value in a t-register after function returns?
 save it to the stack before fn call
 restore it from the stack after fn returns
Don’t need value?  do nothing
Functions
  Can freely use these registers
  Must assume that their contents
  are destroyed by other functions
void myfn(int a) {
int x = 10;
int y = max(x, a);
int z = some_fn(y);
return (z + y);
}
Suppose:
t0 holds x
t1 holds y
t2 holds z
Where do we save and restore?

## Slide 70: Callee-saved
Registers a function intends to use: s0… s9
About to use an s-register? You MUST:
Save the current value on the stack before using
Restore the old value from the stack before fn returns
Functions
  Must save these registers before
  using them
  May assume that their contents
  are preserved even across fn calls
void myfn(int a) {
int x = 10;
int y = max(x, a);
int z = some_fn(y);
return (z + y);
}
Suppose:
s1 holds x
s2 holds y
s3 holds z
Where do we save and restore?

## Slide 71: Caller-Saved Registers in Practice
Assume the registers are free for the taking, use with no overhead
Since subroutines will do the same, must protect values needed later:
  Save before fn call
  Restore after fn call
Notice: Good registers to use if you don’t call too many functions or if the values don’t matter later on anyway.
main:
…
[use x5 & x6]
…
addi x2, x2, -8
sw x6, 4(x2)
sw x5, 0(x2)
jal myfn
lw x6, 4(x2)
lw x5, 0(x2)
addi x2, x2, 8
…
[use x5 & x6]

## Slide 72: Caller-Saved Registers in Practice
Assume the registers are free for the taking, use with no overhead
Since subroutines will do the same, must protect values needed later:
  Save before fn call
  Restore after fn call
Notice: Good registers to use if you don’t call too many functions or if the values don’t matter later on anyway.
main:
…
[use $t0 & $t1]
…
addi $sp, $sp,-8
sw $t1, 4($sp)
sw $t0, 0($sp)
jal myfn
lw $t1, 4($sp)
lw $t0, 0($sp)
addi $sp, $sp, 8
…
[use $t0 & $t1]

## Slide 73: Callee-Saved Registers in Practice
Assume caller is using the registers
Save on entry
Restore on exit
Notice: Good registers to use if you make a lot of function calls and need values that are preserved across all of them.
Also, good if caller is actually using the registers, otherwise the save and restores are wasted. But hard to know this.
main:
addi x2, x2, -16
sw x1, 12(x2)
sw x8, 8(x2)
sw x18, 4(x2)
sw x9, 0(x2)
addi x8, x2, 12
…
[use x9 and x18]
…
lw x1, 12(x2)
lw x8, 8(x2)($sp)
lw x18, 4(x2)
lw x9, 0(x2)
addi x2, x2, 16
jr x1

## Slide 74: Callee-Saved Registers in Practice
Assume caller is using the registers
Save on entry
Restore on exit
Notice: Good registers to use if you make a lot of function calls and need values that are preserved across all of them.
Also, good if caller is actually using the registers, otherwise the save and restores are wasted. But hard to know this.
main:
addi $sp, $sp, -16
sw $ra, 12($sp)
sw $fp, 8($sp)
sw $s2, 4($sp)
sw $s1, 0($sp)
addi $fp, $sp, 12
…
[use $s1 and $s2]
…
lw $ra, 12($sp)
lw $fp, 8($sp)($sp)
lw $s2, 4($sp)
lw $s1, 0($sp)
addi $sp, $sp, 16
jr $ra

## Slide 75: Clicker Question
You are a compiler. Do you choose to put a in a:
Caller-saved register (t)
Callee-saved register (s)
Depends on where we put the other variables in this fn
Both are equally valid

## Slide 76: Clicker Question
You are a compiler. Do you choose to put a in a:
Caller-saved register (t)
Callee-saved register (s)
Depends on where we put the other variables in this fn
Both are equally valid
Repeat but assume that foo is recursive (bar/baz  foo)

## Slide 77: Clicker Question
You are a compiler. Do you choose to put b in a:
Caller-saved register (t)
Callee-saved register (s)
Depends on where we put the other variables in this fn
Both are equally valid

## Slide 78: Frame Layout on Stack
Assume a function uses two callee-save registers.
How do we allocate a stack frame? How large is the stack frame?
What should be stored in the stack frame?
Where should everything be stored?
saved ra
saved fp
saved regs ($s1 ... $s11)
locals
incoming args
fp 
sp 
outgoing args

## Slide 79: Frame Layout on Stack
ADDI sp, sp, -16 # allocate frame
SW ra, 12(sp) # save ra
SW fp, 8(sp) # save old fp
SW s2, 4(sp) # save ...
SW s1, 0(sp) # save ...
ADDI fp, sp, 12 # set new frame ptr
… ...
BODY
… ...
LW s1, 0(sp) # restore …
LW s2, 4(sp) # restore …
LW fp, 8(sp) # restore old fp
LW ra, 12(sp) # restore ra
ADDI sp, sp, 16 # dealloc frame
JR ra
saved ra
saved fp
saved regs ($s1 ... $s11)
locals
incoming args
fp 
sp 
outgoing args

## Slide 80: Frame Layout on Stack
blue() {
pink(0,1,2,3,4,5);
}
saved regs
args for pink
saved fp
blue’s ra
fp
blue’s stack frame
sp

## Slide 81: Frame Layout on Stack
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
int x;
orange(10,11,12,13,14);
}
saved regs
args for pink
saved fp
blue’s ra
pink’s ra
blue’s fp
saved regs
pink’s stack frame
fp
x
args for orange
sp
blue’s stack frame

## Slide 82: Frame Layout on Stack
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
int x;
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // no bounds check!
}
saved regs
args for pink
saved fp
blue’s ra
pink’s ra
blue’s fp
saved regs
pink’s stack frame
x
args for orange
What happens if more than 100 bytes
is written to buf?
fp
sp
orange’s ra
pink’s fp
saved regs
orange
stack frame
buf[100]
blue’s stack frame

## Slide 83: Buffer Overflow
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
int x;
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // no bounds check!
}
saved regs
args for pink
saved fp
blue’s ra
pink’s ra
blue’s fp
saved regs
pink’s stack frame
x
args for orange
What happens if more than 100 bytes
is written to buf?
fp
sp
orange’s ra
pink’s fp
saved regs
orange
stack frame
buf[100]
blue’s stack frame

## Slide 84: RISCV Register Recap
Return address: x1 (ra)
Stack pointer: x2 (sp)
Frame pointer: x8 (fp/s0)
First four arguments: x10-x17 (a0-a7)
Return result: x10-x11 (a0-a1)
Callee-save free regs: x9,x18-x27 (s1-s11)
Caller-save (temp) free regs: x5-x7, x28-x31 (t0-t6)
Global pointer: x3 (gp)

## Slide 85: Convention Summary
first eight arg words passed in $a0-$a7
Space for args in child’s stack frame
return value (if any) in $a0, $a1
stack frame ($fp to $sp) contains:
  $ra (clobbered on JALs)
  local variables
  space for 8 arguments to Callees
  arguments 9+ to Callees
callee save regs: preserved
caller save regs: not preserved
global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
incoming args
$fp 
$sp 

## Slide 86: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5,6,7,8);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
Correct Order:
Body First
Determine stack frame size
Complete Prologue/Epilogue

## Slide 87: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s =sum(tmp,1,2,3,4,5,6,7,8);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
test:
MOVE s1, a0
MOVE s2, a1
AND t0, a0, a1
OR t1, a0, a1
ADD t0, t0, t1
MOVE a0, t0
LI a1, 1
LI a2, 2
…
LI a7, 7
LI t1, 8
SW t1, -4(sp)
SW t0, 0(sp)
JAL sum
LW t0, 0(sp)
MOVE a0, a0 # s
MOVE a1, t0 # tmp
MOVE a2, s2 # b
MOVE a3, s1 # a
MOVE a4, s2 # b
MOVE a5, s1 # a
JAL sum
# add u (a0) and a (s1)
ADD a0, a0, s1
ADD a0, a0, s2
# a0 = u + a + b
Prologue
Epilogue

## Slide 88: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s =sum(tmp,1,2,3,4,5,6,7,8);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
Prologue
Epilogue
How many bytes do we
need to allocate for the
stack frame?
24
28
36
40
48
test:
MOVE s1, a0
MOVE s2, a1
AND t0, a0, a1
OR t1, a0, a1
ADD t0, t0, t1
MOVE a0, t0
LI a1, 1
LI a2, 2
…
LI a7, 7
LI t1, 8
SW t1, -4(sp)
SW t0, 0(sp)
JAL sum
LW t0, 0(sp)
MOVE a0, a0 # s
MOVE a1, t0 # tmp
MOVE a2, s2 # b
MOVE a3, s1 # a
MOVE a4, s2 # b
MOVE a5, s1 # a
JAL sum
# add u (v0) and a (s1)
ADD a0, a0, s1
ADD a0, a0, s2
# a0 = u + a + b

## Slide 89: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s =sum(tmp,1,2,3,4,5,6,7,8);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
Prologue
Epilogue
saved ra
saved fp
saved regs (s1 ... s11)
locals
(t0)
outgoing args
space for a0 – a7
and 9th arg
$fp 
$sp 
space for a1
space for a0
test:
MOVE s1, a0
MOVE s2, a1
AND t0, a0, a1
OR t1, a0, a1
ADD t0, t0, t1
MOVE a0, t0
LI a1, 1
LI a2, 2
…
LI a7, 7
LI t1, 8
SW t1, -4(sp)
SW t0, 0(sp)
JAL sum
LW t0, 0(sp)
MOVE a0, v0 # s
MOVE a1, t0 # tmp
MOVE a2, s2 # b
MOVE a3, s1 # a
MOVE a4, s2 # b
MOVE a5, s1 # a
JAL sum
# add u (a0) and a (s1)
ADD a0, a0, s1
ADD a0, a0, s2
# a0 = u + a + b

## Slide 90: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s =sum(tmp,1,2,3,4,5,6,7,8);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
Prologue
Epilogue
saved ra
saved fp
$fp 
$sp 
saved reg s2
saved reg s1
local t0
outgoing 9th arg
space for a7
space for a6
…
space for a1
space for a0
-28
…
-12
-8
-36
-4
0
4
8
12
16
space incoming for a1
space incoming for a0
20
24
test:
MOVE s1, a0
MOVE s2, a1
AND t0, a0, a1
OR t1, a0, a1
ADD t0, t0, t1
MOVE a0, t0
LI a1, 1
LI a2, 2
…
LI a7, 7
LI t1, 8
SW t1, -4(sp)
SW t0, 0(sp)
JAL sum
LW t0, 0(sp)
MOVE a0, a0 # s
MOVE a1, t0 # tmp
MOVE a2, s2 # b
MOVE a3, s1 # a
MOVE a4, s2 # b
MOVE a5, s1 # a
JAL sum
# add u (a0) and a (s1)
ADD a0, a0, s1
ADD a0, a0, s2
# a0 = u + a + b
Notes: -4 9th outgoing arg
-8 a7
-12 a6
-16 a5
-20 a4
-24 a3
-28 a2
-32 a1
-36 a0

## Slide 91: Activity #2: Calling Convention Example: Prologue, Epilogue
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
test:
saved ra
saved fp
$fp 
$sp 
saved reg s2
saved reg s1
local t0
outgoing 9th arg
space for a7
space for a6
…
space for a1
space for a0
-28
…
-12
-8
-36
-4
0
4
8
12
16
space incoming for a1
Space incoming for a0
20
24

## Slide 92: Activity #2: Calling Convention Example: Prologue, Epilogue
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
test:
ADDI sp, sp, -28
SW ra, sp, 16
SW fp, sp, 12
SW s2, sp, 8
SW s1, sp, 4
ADDI fp, sp, 24
LW s1, sp, 4
LW s2, sp, 8
LW fp, sp, 12
LW ra, sp, 16
ADDI sp, sp, 28
JR ra
Body
(previous slide, Activity #1)
Space for t0
saved ra
saved fp
$fp 
$sp 
saved reg s2
saved reg s1
local t0
outgoing 9th arg
space for a7
space for a6
…
space for a1
space for a0
-28
…
-12
-8
-36
-4
0
4
8
12
16
space incoming for a1
Space incoming for a0
20
24
Space for a0 and a1

## Slide 93: Next Goal
Can we optimize the assembly code at all?

## Slide 94: Minimum stack size for a standard function?

## Slide 95: Minimum stack size for a standard function?
saved ra
saved fp
saved regs ($s1 ... $s11)
locals
incoming args
$fp 
$sp 

## Slide 96: Minimum stack size for a standard function?
Leaf function does not invoke any other functions
int f(int x, int y) { return (x+y); }
Optimizations?
No saved regs (or locals)
No incoming args
Don’t push $ra
No frame at all?
Maybe.
saved ra
saved fp
saved regs ($s1 ... $s11)
locals
incoming args
$fp 
$sp 

## Slide 97: Next Goal
Given a running program (a process), how do we know what is going on (what function is executing, what arguments were passed to where, where is the stack and current stack frame, where is the code and data, etc)?

## Slide 98: Anatomy of an executing program
top
bottom
system reserved
stack
system reserved
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)
.data
.text
PC

## Slide 99: Activity #4: Debugging
init(): 0x400000
printf(s, …): 0x4002B4
vnorm(a,b): 0x40107C
main(a,b): 0x4010A0
pi: 0x10000000
str1: 0x10000004
0x00000000
0x004010c4
0x00000000
0x00000000
0x7FFFFFF4
0x00000000
0x00000000
0x0040010c
0x00000015
0x10000004
0x00401090
0x00000000
0x00000000
CPU:
$pc=0x004003C0
$sp=0x7FFFFFAC
$ra=0x00401090
0x7FFFFFB0
What func is running?
Who called it?
Has it called anything?
Will it?
Args?
Stack depth?
Call trace?
0x7FFFFFDC

## Slide 100: Activity #4: Debugging
init(): 0x400000
printf(s, …): 0x4002B4
vnorm(a,b): 0x40107C
main(a,b): 0x4010A0
pi: 0x10000000
str1: 0x10000004
0x00000000
0x004010c4
0x00000000
0x00000000
0x7FFFFFF4
0x00000000
0x00000000
0x0040010c
0x00000015
0x10000004
0x00401090
0x00000000
0x00000000
CPU:
$pc=0x004003C0
$sp=0x7FFFFFAC
$ra=0x00401090
0x7FFFFFB0
What func is running?
Who called it?
Has it called anything?
Will it?
Args?
Stack depth?
Call trace?
0x7FFFFFDC
printf
vnorm
no
no
printf, vnorm, main, init
Str1 and 0x15
4
0x7FFFFFAC
0x7FFFFFB4
0x7FFFFFB8
0x7FFFFFBC
0x7FFFFFC0
0x7FFFFFC4
0x7FFFFFC8
0x7FFFFFCA
0x7FFFFFD0
0x7FFFFFD4
0x7 …D8
DC
E0
Memory
ra
fp
a3
a2
a1
a0
ra
fp
a3
a2
a1
a0
a0
ra
E4
E8
EA
…F0
…F4
a1
a2
a3
fp
ra
b/c no space for
outgoing args
0x7FFFFFA8
main
vnorm
0x7FFFFFC4
printf
Notes: pc  in printf
ra  called from vnorm? or called vnorm?
0(sp)  looks like in printf, called by vnorm, and not going to call anything else
4,8(sp)  looks like args are str1 and 0x15
20(sp)  looks like a return address, probably main called vnorm with less than 4 args
44(sp)  looks like a return address, probably init called main
how large is init’s stack frame?

## Slide 101: Recap
  How to write and Debug a RISCV program using calling convention
  First eight arg words passed in a0, a1, …, a7
  Space for args passed in child’s stack frame
  return value (if any) in a0, a1
  stack frame (fp/s0 to sp) contains:
    ra (clobbered on JAL to sub-functions)
    fp
    local vars (possibly clobbered by sub-functions)
    Contains space for incoming args
  callee save regs are preserved
  caller save regs are not
  Global data accessed via gp
saved ra
saved fp
saved regs (s0 ... s7)
locals
incoming args
fp 
sp 