## Slide 1: Caches & Memory
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee, and Sirer]

## Slide 2: Programs 101
Load/Store Architectures:
Read data from memory (put in registers)
Manipulate it
Store it back to memory
int main (int argc, char* argv[ ]) {
int i;
int m = n;
int sum = 0;
for (i = 1; i <= m; i++) {
sum += i;
}
printf (“...”, n, sum);
}
C Code
main: addi sp,sp,-48
sw x1,44(sp)
sw fp,40(sp)
move fp,sp
sw x10,-36(fp)
sw x11,-40(fp)
la x15,n
lw x15,0(x15)
sw x15,-28(fp)
sw x0,-24(fp)
li x15,1
sw x15,-20(fp)
L2: lw x14,-20(fp)
lw x15,-28(fp)
blt x15,x14,L3
. . .
RISC-V Assembly
Instructions that read from
or write to memory…

## Slide 3: Programs 101
Load/Store Architectures:
Read data from memory (put in registers)
Manipulate it
Store it back to memory
int main (int argc, char* argv[ ]) {
int i;
int m = n;
int sum = 0;
for (i = 1; i <= m; i++) {
sum += i;
}
printf (“...”, n, sum);
}
C Code
main: addi sp,sp,-48
sw ra,44(sp)
sw fp,40(sp)
move fp,sp
sw a0,-36(fp)
sw a1,-40(fp)
la a5,n
lw a5,0(x15)
sw a5,-28(fp)
sw x0,-24(fp)
li a5,1
sw a5,-20(fp)
L2: lw a4,-20(fp)
lw a5,-28(fp)
blt a5,a4,L3
. . .
RISC-V Assembly
Instructions that read from
or write to memory…

## Slide 4: 1 Cycle Per Stage: the Biggest Lie (So Far)
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
ALU
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
Code Stored in Memory
(also, data and stack)

## Slide 5: What’s the problem?
+ big
– slow
– far away
SandyBridge Motherboard, 2011
http://news.softpedia.com
CPU
Main Memory

## Slide 6: The Need for Speed
CPU Pipeline

## Slide 7: The Need for Speed
Instruction speeds:
add,sub,shift: 1 cycle
mult: 3 cycles
load/store: 100 cycles
  off-chip 50(-70)ns
  2(-3) GHz processor  0.5 ns clock
CPU Pipeline

## Slide 8: The Need for Speed
CPU Pipeline

## Slide 9: What’s the solution?
Level 2 $
Level 1
Data $
Level 1
Insn $
Intel Pentium 3, 1999
Caches !

## Slide 10: Aside
Go back to 04-state and 05-memory and look at how registers, SRAM and DRAM are built.

## Slide 11: What’s the solution?
Level 2 $
Level 1
Data $
Level 1
Insn $
Intel Pentium 3, 1999
Caches !
What lucky data gets to go here?

## Slide 12: Locality Locality Locality
If you ask for something, you’re likely to ask for:
the same thing again soon
 Temporal Locality
something near that thing, soon
 Spatial Locality
total = 0;
for (i = 0; i < n; i++)
total += a[i];
return total;

## Slide 13: Your life is full of Locality
Last Called
Speed Dial
Favorites
Contacts
Google/Facebook/email

## Slide 14: Your life is full of Locality

## Slide 15: The Memory Hierarchy
1 cycle,
128 bytes
4 cycles,
64 KB
Intel Haswell Processor, 2013
12 cycles,
256 KB
36 cycles,
2-20 MB
50-70 ns,
512 MB – 4 GB
5-20 ms
16GB – 4 TB,
Small, Fast
Big, Slow
Registers
L1 Caches
L2 Cache
L3 Cache
Main Memory
Disk

## Slide 16: Some Terminology
Cache hit
data is in the Cache
thit : time it takes to access the cache
Hit rate (%hit): # cache hits / # cache accesses
Cache miss
data is not in the Cache
tmiss : time it takes to get the data from below the $
Miss rate (%miss): # cache misses / # cache accesses
Cacheline or cacheblock or simply line or block
Minimum unit of info that is present/or not in the cache

## Slide 17: The Memory Hierarchy
1 cycle,
128 bytes
4 cycles,
64 KB
Intel Haswell Processor, 2013
12 cycles,
256 KB
36 cycles,
2-20 MB
50-70 ns,
512 MB – 4 GB
5-20 ms
16GB – 4 TB,
  average access time
  tavg = thit + %miss* tmiss
  = 4 + 5% x 100
  = 9 cycles
Registers
L1 Caches
L2 Cache
L3 Cache
Main Memory
Disk

## Slide 18: Single Core Memory Hierarchy
ON CHIP
Disk
Processor
Regs
I$
D$
L2
Main Memory
Registers
L1 Caches
L2 Cache
L3 Cache
Main Memory
Disk

## Slide 19
Multi-Core Memory Hierarchy
ON CHIP
Main Memory
Processor
Regs
I$
D$
L2
L3
Processor
Regs
I$
D$
L2
Processor
Regs
I$
D$
L2
Processor
Regs
I$
D$
L2
Disk

## Slide 20
Memory Hierarchy by the Numbers
CPU clock rates ~0.33ns – 2ns (3GHz-500MHz)
*Registers,D-Flip Flops: 10-100’s of registers
Memory technology | Transistor count* | Access time | Access time in cycles | $ per GIB in 2012 | Capacity
SRAM (on chip) | 6-8 transistors | 0.5-2.5 ns | 1-3 cycles | $4k | 256 KB
SRAM (off chip) |  | 1.5-30 ns | 5-15 cycles | $4k | 32 MB
DRAM | 1 transistor (needs refresh) | 50-70 ns | 150-200 cycles | $10-$20 | 8 GB
SSD (Flash) |  | 5k-50k ns | Tens of thousands | $0.75-$1 | 512 GB
Disk |  | 5M-20M ns | Millions | $0.05-$0.1 | 4 TB

## Slide 21
Basic Cache Design
Direct Mapped Caches

## Slide 22
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
16 Byte Memory
MEMORY
Byte-addressable memory
4 address bits  16 bytes total
b addr bits  2b bytes in memory
load 1100  r1

## Slide 23
4-Byte, Direct Mapped Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
data
A
B
C
D
Direct mapped:
Each address maps to 1 cache block
4 entries  2 index bits (2n  n bits)
Index with LSB:
Supports spatial locality
index
XXXX
index
00
01
10
11
Cache entry
= row
= (cache) line
= (cache) block
Block Size: 1 byte

## Slide 24: Analogy to a Spice Rack
Compared to your spice wall
  Smaller
  Faster
  More costly (per oz.)
A
B
C
D
E
F
…
Z
http://www.bedbathandbeyond.com
Spice Wall
(Memory)
Spice Rack
(Cache)
index spice

## Slide 25: Analogy to a Spice Rack
Cinnamon
How do you know what’s in the jar?
Need labels
  Tag = Ultra-minimalist label
innamon
Spice Wall
(Memory)
A
B
C
D
E
F
…
Z
Spice Rack
(Cache)
index spice
tag

## Slide 26
tag|index
XXXX
 | data
 | A
 | B
 | C
 | D
tag
00
00
00
00
4-Byte, Direct Mapped Cache
MEMORY
CACHE
Tag: minimalist label/address
address = tag + index
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 27
4-Byte, Direct Mapped Cache
MEMORY
CACHE
One last tweak: valid bit
V | tag | data
0 | 00 | X
0 | 00 | X
0 | 00 | X
0 | 00 | X
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 28: Simulation #1 of a 4-byte, DM Cache
MEMORY
CACHE
V | tag | data
0 | 11 | X
0 | 11 | X
0 | 11 | X
0 | 11 | X
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
Lookup:
Index into $
Check tag
Check valid bit
load 1100
tag|index
XXXX

## Slide 29
Block Diagram 4-entry, direct mapped Cache
CACHE
V | tag | data
1 | 00 | 1111 0000
1 | 11 | 1010 0101
0 | 01 | 1010 1010
1 | 11 | 0000 0000
tag|index
1101
2
2
2
=
Hit!
data
8
1010 0101
Great!
Are we done?

## Slide 30: Simulation #2: 4-byte, DM Cache
MEMORY
CACHE
V | tag | data
1 | 11 | N
0 | 11 | X
0 | 11 | X
0 | 11 | X
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
Miss
Lookup:
Index into $
Check tag
Check valid bit
load 1100
load 1101
load 0100
load 1100

## Slide 31
Reducing Cold Misses by Increasing Block Size
Leveraging Spatial Locality

## Slide 32
Increasing Block Size
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
CACHE
V | tag | data
0 | x | A ¦ B
0 | x | C ¦ D
0 | x | E ¦ F
0 | x | G ¦ H
MEMORY
Block Size: 2 bytes
Block Offset: least significant bits indicate where you live in the block
Which bits are the index? tag?
offset
XXXX
index
00
01
10
11

## Slide 33
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
Simulation #3: 8-byte, DM Cache
MEMORY
CACHE
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
0 | x | X ¦ X
0 | x | X ¦ X
load 1100
load 1101
load 0100
load 1100
tag| |offset
XXXX
index
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 34
Removing Conflict Misses with Fully-Associative Caches

## Slide 35
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
Simulation #4: 8-byte, FA Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
load 1100
load 1101
load 0100
load 1100
Miss
XXXX
tag|offset
Lookup:
Index into $
Check tags
Check valid bits
CACHE
LRU Pointer

## Slide 36: Pros and Cons of Full Associativity
+ No more conflicts!
+ Excellent utilization!
But either:
Parallel Reads
– lots of reading!
Serial Reads
– lots of waiting
  tavg = thit + %miss* tmiss
  = 4 + 5% x 100
  = 9 cycles
  = 6 + 3% x 100
  = 9 cycles

## Slide 37
Pros & Cons
 | Direct Mapped | Fully Associative
Tag Size | Smaller | Larger
SRAM Overhead | Less | More
Controller Logic | Less | More
Speed | Faster | Slower
Price | Less | More
Scalability | Very | Not Very
# of conflict misses | Lots | Zero
Hit Rate | Low | High
Pathological Cases | Common | ?

## Slide 38
Reducing Conflict Misses with Set-Associative Caches
Not too conflict-y. Not too slow.
… Just Right!

## Slide 39
8 byte, 2-way set associative Cache
CACHE
MEMORY
What should the offset be?
What should the index be?
What should the tag be?
XXXX
tag||offset
index
XXXX
offset
V | tag | data
0 | xx | E ¦ F
0 | xx | C ¦ D
V | tag | data
0 | xx | N ¦ O
0 | xx | P ¦ Q
XXXX
index
0
1
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 40
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
8 byte, 2-way set associative Cache
CACHE
index
0
1
MEMORY
XXXX
tag||offset
index
V | tag | data
0 | xx | X ¦ X
0 | xx | X ¦ X
V | tag | data
0 | xx | X ¦ X
0 | xx | X ¦ X
load 1100
load 1101
load 0100
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
LRU Pointer

## Slide 41: Eviction Policies
Which cache line should be evicted from the cache to make room for a new line?
Direct-mapped: no choice, must evict line selected by index
Associative caches
  Random: select one of the lines at random
  Round-Robin: similar to random
  FIFO: replace oldest line
  LRU: replace line that has not been used in the longest time

## Slide 42: Misses: the Three C’s
Cold (compulsory) Miss:
never seen this address before
Conflict Miss:
cache associativity is too low
Capacity Miss:
cache is too small

## Slide 43: Miss Rate vs. Block Size

## Slide 44: Block Size Tradeoffs
For a given total cache size,
Larger block sizes mean….
  fewer lines
  so fewer tags, less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  can decrease performance if working set can’t fit in $
  and larger miss penalty (time to fetch block)

## Slide 45: Miss Rate vs. Associativity

## Slide 46: ABCs of Caches
+ Associativity:
⬇conflict misses 
⬆hit time 
+ Block Size:
⬇cold misses 
⬆conflict misses 
+ Capacity:
⬇capacity misses 
⬆hit time 
  tavg = thit + %miss* tmiss

## Slide 47: Which caches get what properties?
L1 Caches
L2 Cache
L3 Cache
Fast
Big
More Associative
Bigger Block Sizes
Larger Capacity
  tavg = thit + %miss* tmiss
Design with miss rate in mind
Design with speed in mind

## Slide 48: Roadmap
Things we have covered:
  The Need for Speed
  Locality to the Rescue!
  Calculating average memory access time
  $ Misses: Cold, Conflict, Capacity
  $ Characteristics: Associativity, Block Size, Capacity
Things we will now cover:
  Cache Figures
  Cache Performance Examples
  Writes

## Slide 49
2-Way Set Associative Cache (Reading)
hit?
line select
64bytes
Tag Index Offset
data
word select
32bits
=
=
Tag
Tag
V
V
Data
Data

## Slide 50
data
3-Way Set Associative Cache (Reading)
word select
hit?
line select
=
=
=
32bits
64bytes
Tag Index Offset

## Slide 51
How Big is the Cache?
n bit index, m bit offset, N-way Set Associative
Question: How big is cache?
Data only?
(what we usually mean when we ask “how big” is the cache)
Data + overhead?
Tag Index Offset

## Slide 52: Performance Calculation with $ Hierarchy
Parameters
  Reference stream: all loads
  D$: thit = 1ns, %miss = 5%
  L2: thit = 10ns, %miss = 20% (local miss rate)
  Main memory: thit = 50ns
What is tavgD$ without an L2?
  tmissD$ =
  tavgD$ =
What is tavgD$ with an L2?
  tmissD$ =
  tavgL2 =
  tavgD$ =
  tavg = thit + %miss* tmiss

## Slide 53: Performance Summary
Average memory access time (AMAT) depends on:
cache architecture and size
Hit and miss rates
Access times and miss penalty
Cache design a very complex problem:
Cache size, block size (aka line size)
Number of ways of set-associativity (1, N, )
Eviction policy
Number of levels of caching, parameters for each
Separate I-cache from D-cache, or Unified cache
Prefetching policies / instructions
Write policy

## Slide 54: Takeaway
Direct Mapped  fast, but low hit rate
Fully Associative  higher hit cost, higher hit rate
Set Associative  middleground
Line size matters. Larger cache lines can increase performance due to prefetching. BUT, can also decrease performance is working set size cannot fit in cache.
Cache performance is measured by the average memory access time (AMAT), which depends cache architecture and size, but also the access time for hit, miss penalty, hit rate.

## Slide 55: What about Stores?
We want to write to the cache.
If the data is not in the cache?
  Bring it in. (Write allocate policy)
Should we also update memory?
Yes: write-through policy
No: write-back policy

## Slide 56
Write-Through Cache
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Instructions:
LB x1  M[ 1 ]
LB x2  M[ 7 ]
SB x2  M[ 0 ]
SB x1  M[ 5 ]
LB x2  M[ 10 ]
SB x1  M[ 5 ]
SB x1  M[ 10 ]
Cache
Register File
x0
x1
x2
x3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
16 byte, byte-addressed memory
4 btye, fully-associative cache:
2-byte blocks, write-allocate
4 bit addresses:
3 bit tag, 1 bit offset
lru V tag data
1
0

## Slide 57
Cache
Register File
Write-Through (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
x0
x1
x2
x3
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
Memory
Instructions:
LB x1  M[ 1 ]
LB x2  M[ 7 ]
SB x2  M[ 0 ]
SB x1  M[ 5 ]
LB x2  M[ 10 ]
SB x1  M[ 5 ]
SB x1  M[ 10 ]
lru V tag data
1
0

## Slide 58: Summary: Write Through
Write-through policy with write allocate
Cache miss: read entire block from memory
Write: write only updated item to memory
Eviction: no need to write to memory

## Slide 59: Next Goal: Write-Through vs. Write-Back
What if we DON’T to write stores immediately to memory?
  Keep the current copy in cache, and update memory when data is evicted (write-back policy)
  Write-back all evicted lines?
    No, only written-to blocks

## Slide 60: Write-Back Meta-Data (Valid, Dirty Bits)
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 61: Write-back Example
Example: How does a write-back cache work?
Assume write-allocate

## Slide 62: Handling Stores (Write-Back)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Instructions:
LB x1  M[ 1 ]
LB x2  M[ 7 ]
SB x2  M[ 0 ]
SB x1  M[ 5 ]
LB x2  M[ 10 ]
SB x1  M[ 5 ]
SB x1  M[ 10 ]
Cache
Register File
x0
x1
x2
x3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
16 byte, byte-addressed memory
4 btye, fully-associative cache:
2-byte blocks, write-allocate
4 bit addresses:
3 bit tag, 1 bit offset
0
0
lru V d tag data
1
0

## Slide 63: Write-Back (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Instructions:
LB x1  M[ 1 ]
LB x2  M[ 7 ]
SB x2  M[ 0 ]
SB x1  M[ 5 ]
LB x2  M[ 10 ]
SB x1  M[ 5 ]
SB x1  M[ 10 ]
Cache
Register File
x0
x1
x2
x3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
lru V d tag data
1
0

## Slide 64: How Many Memory References?
Write-back performance
How many reads?
How many writes?

## Slide 65: Write-back vs. Write-through Example
Assume: large associative cache, 16-byte lines
N 4-byte words
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]

## Slide 66: So is write back just better?
Short Answer: Yes (fewer writes is a good thing)
Long Answer: It’s complicated.
Evictions require entire line be written back to memory (vs. just the data that was written)
Write-back can lead to incoherent caches on multi-core processors (later lecture)

## Slide 67: Optimization: Write Buffering

## Slide 68: Write-through vs. Write-back
Write-through is slower
  But simpler (memory always consistent)
Write-back is almost always faster
  write-back buffer hides large eviction cost
  But what about multiple cores with separate caches but sharing memory?
Write-back requires a cache coherency protocol
  Inconsistent views of memory
  Need to “snoop” in each other’s caches
  Extremely complex protocols, very hard to get right

## Slide 69
Cache-coherency
Q: Multiple readers and writers?
  A: Potentially inconsistent views of memory
Mem
L2
L1
L1
Cache coherency protocol
  May need to snoop on other CPU’s cache activity
  Invalidate cache line when other CPU writes
  Flush write-back caches before other CPU reads
  Or the reverse: Before writing/reading…
  Extremely complex protocols, very hard to get right
CPU
L1
L1
CPU
L2
L1
L1
CPU
L1
L1
CPU
disk
net
A
A
A
A
A’
A

## Slide 70
Write-through policy with write allocate
  Cache miss: read entire block from memory
  Write: write only updated item to memory
  Eviction: no need to write to memory
  Slower, but cleaner
Write-back policy with write allocate
  Cache miss: read entire block from memory
    **But may need to write dirty cacheline first**
  Write: nothing to memory
  Eviction: have to write to memory entire cacheline because don’t know what is dirty (only 1 dirty bit)
  Faster, but more complicated, especially with multicore
Takeaway

## Slide 71
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  | 
// H = 6, W = 10
int A[H][W];
for(x=0; x < W; x++)
for(y=0; y < H; y++)
sum += A[y][x];
Cache Conscious Programming
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
MEMORY
CACHE
YOUR MIND
H
W

## Slide 72: By the end of the cache lectures…

## Slide 73: A Real Example
> dmidecode -t cache
Cache Information
Socket Designation: L1 Cache
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Location: Internal
Installed Size: 128 kB
Maximum Size: 128 kB
Supported SRAM Types:
Synchronous
Installed SRAM Type: Synchronous
Speed: Unknown
Error Correction Type: Parity
System Type: Unified
Associativity: 8-way Set-associative
Cache Information
Socket Designation: L2 Cache
Configuration: Enabled, Not Socketed,
Level 2
Operational Mode: Write Back
Location: Internal
Installed Size: 512 kB
Maximum Size: 512 kB
Supported SRAM Types:
Synchronous
Installed SRAM Type: Synchronous
Speed: Unknown
Error Correction Type: Single-bit ECC
System Type: Unified
Associativity: 4-way Set-associative
Microsoft Surfacebook
Dual core
Intel i7-6600 CPU @ 2.6 GHz (purchased in 2016)
Cache Information
Socket Designation: L3 Cache
Configuration: Enabled, Not Socketed,
Level 3
Operational Mode: Write Back
Location: Internal
Installed Size: 4096 kB
Maximum Size: 4096 kB
Supported SRAM Types:
Synchronous
Installed SRAM Type: Synchronous
Speed: Unknown
Error Correction Type: Multi-bit ECC
System Type: Unified
Associativity: 16-way Set-associative

## Slide 74: A Real Example
> sudo dmidecode -t cache
Cache Information
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Installed Size: 128 KB
Error Correction Type: None
Cache Information
Configuration: Enabled, Not Socketed, Level 2
Operational Mode: Varies With Memory Address
Installed Size: 6144 KB
Error Correction Type: Single-bit ECC
> cd /sys/devices/system/cpu/cpu0; grep cache/*/*
cache/index0/level:1
cache/index0/type:Data
cache/index0/ways_of_associativity:8
cache/index0/number_of_sets:64
cache/index0/coherency_line_size:64
cache/index0/size:32K
cache/index1/level:1
cache/index1/type:Instruction
cache/index1/ways_of_associativity:8
cache/index1/number_of_sets:64
cache/index1/coherency_line_size:64
cache/index1/size:32K
cache/index2/level:2
cache/index2/type:Unified
cache/index2/shared_cpu_list:0-1
cache/index2/ways_of_associativity:24
cache/index2/number_of_sets:4096
cache/index2/coherency_line_size:64
cache/index2/size:6144K
Dual-core 3.16GHz Intel (purchased in 2011)

## Slide 75: A Real Example
Dual 32K L1 Instruction caches
  8-way set associative
  64 sets
  64 byte line size
Dual 32K L1 Data caches
  Same as above
Single 6M L2 Unified cache
  24-way set associative (!!!)
  4096 sets
  64 byte line size
4GB Main memory
1TB Disk
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 77: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
NEXT: Multi-core processors are complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right