## Slide 1: Virtual Memory
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee, and Sirer]

## Slide 2: Where are we now and where are we going?
How many programs do you run at once?
a) 1
b) 2
c) 3-5
d) 6-10
e) 11+
Notes: Take a class poll
People often have many programs/application running at the same time such as a browser, Skype, Facetime, etc

## Slide 3: Big Picture: Multiple Processes
Can we execute more than one program at a time with our current RISC-V processor?
a) Yes, no problem at all
b) No, because memory addresses will conflict
c) Yes, caches can avoid memory address conflicts
d) Yes, our modified Harvard architecture avoids memory address conflicts
e) Yes, because we have multiple processors (multiple cores)

## Slide 4: Big Picture: Multiple Processes
How to run multiple processes?
Time-multiplex a single CPU core (multi-tasking)
  Web browser, skype, office, … all must co-exist
Many cores per processor (multi-core) or many processors (multi-processor)
  Multiple programs run simultaneously

## Slide 5
Processor & Memory
CPU address/data bus...
… routed through caches
… to main memory
  Simple, fast, but…
CPU
Text
Data
Stack
Heap
Memory
0x000…0
0x7ff…f
0xfff…f
$$
Notes: Q: What happens for LW/SW to an invalid location?
  0x000000000 (NULL)
  uninitialized pointer
A: Need a memory management unit (MMU)
  Throw (and/or handle) an exception

## Slide 6
Multiple Processes
Q: What happens when another program is executed concurrently on another processor?
A: The addresses will conflict
  Even though, CPUs may take
  turns using memory bus
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f
$$
$$

## Slide 7
Multiple Processes
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f
$$
$$
Q: Can we relocate second program?

## Slide 8
Solution? Multiple processes/processors
Q: Can we relocate second program?
A: Yes, but…
  What if they don’t fit?
  What if not contiguous?
  Need to recompile/relink?
  …
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap

## Slide 9
Big Picture: (Virtual) Memory
Process 1
A
B
C
D
3
2
1
0
Process 2
E
F
G
H
3
2
1
0
Give each process an illusion that it has exclusive access to entire main memory

## Slide 10
But In Reality…
Process 1
Process 2
C
B
A
D
E
F
G
H
Physical Memory
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14

## Slide 11
How do we create the illusion?
Process 1
A
B
C
D
3
2
1
0
Process 2
E
F
G
H
3
2
1
0
C
B
A
D
E
F
G
H
Physical Memory
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14

## Slide 12
How do we create the illusion?
Process 1
A
B
C
D
3
2
1
0
Process 2
E
F
G
H
3
2
1
0
C
B
A
D
E
F
G
H
Physical Memory
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
All problems in computer science can be solved by another level of indirection.
– David Wheeler

## Slide 13
How do we create the illusion?
Process 1
A
B
C
D
3
2
1
0
Process 2
E
F
G
H
3
2
1
0
C
B
A
D
E
F
G
H
Physical Memory
Virtual Memory
(just a concept; does not exist physically)
Virtual address
Memory management unit (MMU) takes care of the mapping
Map virtual address to physical address
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Physical address

## Slide 14
How do we create the illusion?
Process 1
A
B
C
D
3
2
1
0
Process 2
E
F
G
H
3
2
1
0
C
B
A
D
E
F
G
H
Physical Memory
Virtual Memory
(just a concept; does not exist physically)
Virtual address
Process 1 wants to access data C
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Physical address
Process 1 thinks it is stored at addr 1
So CPU generates addr 1
This addr is intercepted by MMU
MMU knows this is a virtual addr
MMU looks at the mapping
Virtual addr 1 -> Physical addr 9
Data at Physical addr 9 is sent to CPU
And that data is indeed C!!!

## Slide 15
How do we create the illusion?
Process 1
A
B
C
D
3
2
1
0
Process 2
E
F
G
H
3
2
1
0
C
B
D
E
G
H
Physical Memory
Virtual Memory
A
F
Disk
Memory management unit (MMU) takes care of the mapping
Map virtual address to physical address
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14

## Slide 16
Big Picture: (Virtual) Memory
From a process’s perspective –
  Process only sees the virtual memory
    Contiguous memory
Process 1
A
B
C
D
3
2
1
0
Virtual Memory
C
Physical Memory
Hidden from Process

## Slide 17
Big Picture: (Virtual) Memory
Process 1
A
B
C
D
3
2
1
0
Virtual Memory
C
Physical Memory
Hidden from Process
From a process’s perspective –
  Process only sees the virtual memory
    Contiguous memory
    No need to recompile - only mappings need to be updated

## Slide 18
Big Picture: (Virtual) Memory
From a process’s perspective –
  Process only sees the virtual memory
    Contiguous memory
    No need to recompile - only mappings need to be updated
Process 1
A
B
C
D
3
2
1
0
Virtual Memory
C
Physical Memory
Hidden from Process

## Slide 19
Big Picture: (Virtual) Memory
From a process’s perspective –
  Process only sees the virtual memory
    Contiguous memory
    No need to recompile - only mappings need to be updated
    When run out of memory, MMU maps data on disk in a transparent manner
Process 1
A
B
C
D
3
2
1
0
Virtual Memory
C
Physical Memory
Disk
Hidden from Process

## Slide 20: Next Goal
How does Virtual Memory work?
i.e. How do we create the “map” that maps a virtual address generated by the CPU to a physical address used by main memory?

## Slide 21: Next Goal (after spring break!)
How does Virtual Memory work?
i.e. How do we create the “map” that maps a virtual address generated by the CPU to a physical address used by main memory?

## Slide 22: Have a great Spring Break!!!

## Slide 23: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance

## Slide 24
Virtual Memory: Recap
Process 1
3
2
1
0
Process 2
3
2
1
0
Physical Memory
Virtual Memory
{just a set of numbers (addresses);
does not exist physically}
Virtual address
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
Physical address
Store B at 2
Store H at 2
Load data at 2
B
B
H
Hidden from the process

## Slide 25
Picture Memory as… ?
addr | data
0xffffffff | xaa
 | …
 | …
 | x00
 | x00
 | xef
 | xcd
 | xab
 | xff
0x00000000 | x00
Byte Array:
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
system
reserved
stack
system
reserved
text
data
heap
Segments:
0x00000000
0xffffe000
0xfffff000
0x00003000
0x00001000
page 0
Page Array:
page 1
page 2
. . .
. . .
page n
0x00002000
0x00004000
0xffffd000
each segment uses some # of pages
New!

## Slide 26
A Little More About Pages
Memory size = depends on system
say 4GB
Page size = 4KB (by default)
Then, # of pages = 2^20
Any data in a page # 2 has address of the form: 0x00002xxx
Lower 12 bits specify which byte you are in the page:
0x00002200 = 0010 0000 0000
= byte 512
upper bits = page number (PPN)
lower bits = page offset
0x00000000
0xffffe000
0xfffff000
0x00003000
0x00001000
Page Array:
…
4KB
0x00002000
0x00004000
0xffffd000

## Slide 27
Page Table:Datastructure to store mapping
1 Page Table per process
Lives in Memory, i.e. in a page (or more…)
Location stored in Page Table Base Register
Part of program state (like PC)
C
B
A
Physical
Address
Space
9
8
7
6
5
4
3
2
1
0
PTBR
0x00008000
Assuming each page = 4KB
. . .
00000001
00000004
00000005
00000000
0x00008000
0x00008004
0x00008008
0x0000800c
0x00008FFF

## Slide 28
Address Translator: MMU
Programs use virtual addresses
Actual memory uses physical addresses
Memory Management Unit (MMU)
HW structure
Translates virtual  physical address on the fly
A
B
C
Program #1
D
A
B
C
D
Program #2
C
B
A
Physical Address Space
Memory (DRAM)
MMU
B
C
D
3
2
1
0
9
8
7
6
5
4
3
2
1
0
3
2
1
0
Notes: each mmu has own mappings
Easy relocation
Higher memory utilization
Easy sharing

## Slide 29
Simple Page Table Translation
Memory
PTBR
0x90000000
Assuming each page = 4KB
0x10045
. . .
0xC20A3
0x4123B
0x10044
0x00000
0x90000000
0x90000004
0x90000008
0x9000000c
0x00008FFF
0x00000000
0x90000000
0x10045000
0xC20A3000
0x10044000
0x4123B000
0x00002 | 0xABC
vaddr
0
11
12
31
0x4123B | 0xABC
paddr
0x4123BABC
index into the page table
page offset

## Slide 30: General Address Translation
What if the page size is not 4KB?
 Page offset is no longer 12 bits
Clicker Question:
Page size is 16KB  how many bits is page offset?
(a) 12 (b) 13 (c) 14 (d) 15 (e) 16
What if Main Memory is not 4GB?
 Physical page number is no longer 20 bits
Clicker Question:
Page size 4KB, Main Memory 512 MB
 how many bits is PPN?
(a) 15 (b) 16 (c) 17 (d) 18 (e) 19

## Slide 31: Virtual Memory: Summary
Virtual Memory: a Solution for All Problems
Each process has its own virtual address space
  Program/CPU can access any address from 0…2N-1
  (N=number of bits in address register)
  A process is a program being executed
  Programmer can code as if they own all of memory
On-the-fly at runtime, for each memory access
  all accesses are indirect through a virtual address
  translate fake virtual address to a real physical address
  redirect load/store to the physical address
map

## Slide 32: Advantages of Virtual Memory
Easy relocation
Loader puts code anywhere in physical memory
Virtual mappings to give illusion of correct layout
Higher memory utilization
Provide illusion of contiguous memory
Use all physical memory, even physical address 0x0
Easy sharing
Different mappings for different programs / cores
And more to come…

## Slide 33: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]

## Slide 34: Feedback
How much did you love today’s lecture?
  A: As much as Melania loves Trump
  B: As much as Kanye loves Kanye
  C: Somewhere in between, but closer to A
  D: Somewhere in between, but closer to B
  E: I am incapable of loving anything 

## Slide 35: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance

## Slide 36: Page Table Overhead
How large is PageTable?
Virtual address space (for each process):
  Given: total virtual memory: 232 bytes = 4GB
  Given: page size: 212 bytes = 4KB
  # entries in PageTable?
  size of PageTable?
Physical address space:
  total physical memory: 229 bytes = 512MB
  overhead for 10 processes?
220 = 1 million entries
PTE size = 4 bytes
PageTable size = 4 x 220 = 4MB
10 x 4MB = 40 MB of overhead!
40 MB /512 MB = 7.8% overhead,
space due to PageTable
Notes: 220 entries in pagetable, so 222 bytes = 4MB (w/ 4byte entries), so 40MB (25% of total!)
Q: Can we possibly have a “full” pagetable?
A: Not enough physical memory pages – some pagetable entries will be duplicates!

## Slide 37: But Wait... There’s more!
Page Table Entry won’t be just an integer
Meta-Data
  Valid Bits
    What PPN means “not mapped”? No such number…
    At first: not all virtual pages will be in physical memory
    Later: might not have enough physical memory to map all virtual pages
  Page Permissions
    R/W/X permission bits for each PTE
    Code: read-only, executable
    Data: writeable, not executable

## Slide 38
Less Simple Page Table
V | R | W | X | Physical Page Number
0 |  |  |  | 
1 | 1 | 1 | 0 | 0xC20A3
0 |  |  |  | 
0 |  |  |  | 
1 | 1 | 0 | 0 | 0xC20A3
1 |  |  |  | 0x4123B
1 |  |  |  | 0x10044
0 |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000
Aliasing: mapping several virtual addresses  same physical page
Process tries to access a page without proper permissions
Segmentation Fault
Example:
Write to read-only?  process killed

## Slide 39: Now how big is this Page Table?
struct pte_t page_table[220]
Each PTE = 8 bytes
How many pages in memory will the page table take up?
Clicker Question: (a) 4 million (222) pages
(b) 2048 (211) pages
(c) 1024 (210) pages
(d) 4 billion (232) pages
(e) 4K (212) pages
Assuming each page = 4KB

## Slide 40: Now how big is this Page Table?
struct pte_t page_table[220]
Each PTE = 8 bytes
How many pages in memory will the page table take up?
Clicker Question: (a) 4 million (222) pages
(b) 2048 (211) pages
(c) 1024 (210) pages
(d) 4 billion (232) pages
(e) 4K (212) pages
Assuming each page = 4KB

## Slide 41: Wait, how big is this Page Table?
page_table[220] = 8x220 =223 bytes
(Page Table = 8 MB in size)
How many pages in memory will the page table take up? 223 /212 =211 2K pages!
Clicker Question: (a) 4 million (222) pages
(b) 2048 (211) pages
(c) 1024 (210) pages
(d) 4 billion (232) pages
(e) 4K (212) pages
Assuming each page = 4KB

## Slide 42: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]
A page is constant size block of virtual memory. Often, the page size will be around 4kB to reduce the number of entries in a PageTable.
We can use the PageTable to set Read/Write/Execute permission on a per page basis. Can allocate memory on a per page basis. Need a valid bit, as well as Read/Write/Execute and other bits.
But, overhead due to PageTable is significant.

## Slide 43: Next Goal
How do we reduce the size (overhead) of the PageTable?

## Slide 44: Next Goal
How do we reduce the size (overhead) of the PageTable?
A: Another level of indirection!!

## Slide 45
Single-Level Page Table
20 bits
PTBR
12 bits
vaddr
Page Table
PTEntry
31 12 11 0
PPN
Where is my physical page?
Total size = 220 * 4 bytes
= 4MB

## Slide 46: Multi-Level Page Table
10 bits
PTBR
10 bits
12 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
* Indirection to the Rescue, AGAIN!
31 22 21 12 11 0
PPN
Where is my translation?
Where is my physical page?
Also referred to as Level 1 and Level 2 Page Tables

## Slide 47: Multi-Level Page Table
10 bits
PTBR
10 bits
12 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
* Indirection to the Rescue, AGAIN!
31 22 21 12 11 0
PPN
Where is my translation?
Where is my physical page?
Also referred to as Level 1 and Level 2 Page Tables
Assuming each entry is
4bytes,What is the size of
Page Directory?
A: 2KB B: 2MB
C: 4KB D: 4MB

## Slide 48: Multi-Level Page Table
10 bits
PTBR
10 bits
12 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
* Indirection to the Rescue, AGAIN!
31 22 21 12 11 0
PPN
Where is my translation?
Where is my physical page?
Also referred to as Level 1 and Level 2 Page Tables
Assuming each entry is
4bytes,What is the total
size of ALL Page tables?
A: 2KB B: 2MB
C: 4KB D: 4MB

## Slide 49: Multi-Level Page Table
10 bits
PTBR
10 bits
12 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
31 22 21 12 11 0
PPN
Where is my translation?
Where is my physical page?
Size = 210 * 4 bytes = 4KB
Size = 210 * 210 *4 bytes = 4MB
# page tables
# entries per page table

## Slide 50: Multi-Level Page Table
Doesn’t this take up more memory than before?
- YES, but..
Benefits
Don’t need 4MB contiguous physical memory
Don’t need to allocate every PageTable, only those containing valid PTEs
Drawbacks
Performance: Longer lookups
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 51: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance

## Slide 52: Paging
What if process requirements > physical memory?
Virtual starts earning its name
Memory acts as a cache for secondary storage (disk)
  Swap memory pages out to disk when not in use
  Page them back in when needed
Courtesy of Temporal & Spatial Locality (again!)
  Pages used recently mostly likely to be used again
More Meta-Data:
Dirty Bit, Recently Used, etc.
OS may access this meta-data to choose a victim

## Slide 53
Paging
Example: accessing address beginning with 0x00003 (PageTable[3]) results in a Page Fault which will page the data in from disk sector 200
V | R | W | X | D | Physical Page Number
0 |  |  |  |  | --
1 | 1 | 0 | 1 | 0 | 0x10045
0 |  |  |  |  | --
0 |  |  |  |  | --
0 |  |  |  | 0 | disk sector 200
0 |  |  |  | 0 | disk sector 25
1 | 1 | 1 | 0 | 1 | 0x00000
0 |  |  |  |  | --
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
25
200
Notes: A: can make code read-only, executable; make data read-write but not executable; etc.

## Slide 54: Page Fault
Valid bit in Page Table = 0
 means page is not in memory
OS takes over:
Choose a physical page to replace
  “Working set”: refined LRU, tracks page usage
If dirty, write to disk
Read missing page from disk
  Takes so long (~10ms), OS schedules another task
Performance-wise page faults are really bad!

## Slide 55: RISC-V Processor Milestone
Notes: Need to finish project1!

## Slide 56: RISC-V Processor Milestone Celebration!
Notes: Need to finish project1!

## Slide 57: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance

## Slide 58: Watch Your Performance Tank!
For every instruction:
MMU translates address (virtual  physical)
  Uses PTBR to find Page Table in memory
  Looks up entry for that virtual page
Fetch the instruction using physical address
  Access Memory Hierarchy (I$  L2  Memory)
Repeat at Memory stage for load/store insns
  Translate address
  Now you perform the load/store

## Slide 59: Performance
Virtual Memory Summary
PageTable for each process:
  Page
    Single-level (e.g. 4MB contiguous in physical memory)
    or multi-level (e.g. less mem overhead due to page table),
    …
  every load/store translated to physical addresses
  page table miss: load a swapped-out page and retry instruction, or kill program
Performance?
  terrible: memory is already slow translation makes it slower
Solution?
  A cache, of course
Notes: 4x slower!
Pipelining? No. Parallelization? No.

## Slide 60: Next Goal
How do we speedup address translation?

## Slide 61
Translation Lookaside Buffer (TLB)
Small, fast cache
Holds VPNPPN translations
Exploits temporal locality in pagetable
TLB Hit: huge performance savings
TLB Miss: invoke TLB miss handler
    Put translation in TLB for later
VPN
PPN
VPN
PPN
VPN
PPN
“tag”
“data”
CPU
VA
PA
VA
PA
MMU
TLB
VA

## Slide 62: TLB Parameters
Typical
very small (64 – 256 entries)  very fast
fully associative, or at least set associative
Example: Intel Nehalem TLB
128-entry L1 Instruction TLB, 4-way LRU
64-entry L1 Data TLB, 4-way LRU
512-entry L2 Unified TLB, 4-way LRU

## Slide 63: TLB to the Rescue!
For every instruction:
Translate the address (virtual  physical)
  CPU checks TLB
  That failing, walk the Page Table
    Use PTBR to find Page Table in memory
    Look up entry for that virtual page
    Cache the result in the TLB
Fetch the instruction using physical address
  Access Memory Hierarchy (I$  L2  Memory)
Repeat at Memory stage for load/store insns
  CPU checks TLB, translate if necessary
  Now perform load/store

## Slide 64: Translation in Action
yes
Next Topic:
Exceptional Control Flow
Virtual Address
TLB Access
TLB Hit?
no
Physical Address
$ Access
$
Hit?
yes
no
deliver Data back to CPU
DRAM
Access
TLB miss handler
(HW or OS)
DRAM
Hit?
yes

## Slide 65: Takeaways
Need a map to translate a “fake” virtual address (from process) to a “real” physical Address (in memory).
The map is a Page Table: ppn = PageTable[vpn]
A page is constant size block of virtual memory. Often ~4KB to reduce the number of entries in a PageTable.
Page Table can enforce Read/Write/Execute permissions on a per page basis. Can allocate memory on a per page basis. Also need a valid bit, and a few others.
Space overhead due to Page Table is significant.
Solution: another level of indirection!
Two-level of Page Table significantly reduces overhead.
Time overhead due to Address Translations also significant.
Solution: caching! Translation Lookaside Buffer (TLB) acts as a cache for the Page Table and significantly improves performance.