## Slide 1: Syscalls, exceptions, and interrupts, …oh my!
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Altinbuken, Weatherspoon, Bala, Bracy, McKee, and Sirer]

## Slide 2: Announcements
P4-Buffer Overflow is due tomorrow
  Due Tuesday, April 16th
C practice assignment
  Due Friday, April 19th
  Due Friday, April 27th

## Slide 3: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.

## Slide 4: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 5: Operating System

## Slide 6: Operating System
Manages all of the software and hardware on the computer.
Many processes running at the same time, requiring resources
  CPU, Memory, Storage, etc.
The Operating System multiplexes these resources amongst different processes, and isolates and protects processes from one another!

## Slide 7: Operating System
Operating System (OS) is a trusted mediator:
  Safe control transfer between processes
  Isolation (memory, registers) of processes
P1
P2
P3
P4
VM
filesystem
net
driver
driver
untrusted
disk
netw
card
MMU
CPU
trusted
software
hardware
OS

## Slide 8: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 9: Privileged (Kernel) Mode

## Slide 10: One Brain, Many Personalities
You are what you execute.
Personalities:
hailstone_recursive
Microsoft Word
Minecraft
Linux  yes, this is just software like
every other program
that runs on the CPU
Are they all equal?
Brain

## Slide 11: Trusted vs. Untrusted
Only trusted processes should access & change important things
  Editing TLB, Page Tables, OS code, OS sp, OS fp…
If an untrusted process could change the OS’ sp/fp/gp/etc., OS would crash!

## Slide 12: Privileged Mode
CPU Mode Bit in Process Status Register
Many bits about the current process
Mode bit is just one of them
Mode bit:
  0 = user mode = untrusted:
  “Privileged” instructions and registers are
  disabled by CPU
  1 = kernel mode = trusted
  All instructions and registers are enabled

## Slide 13: Privileged Mode at Startup
Boot sequence
  load first sector of disk (containing OS code) to predetermined address in memory
  Mode  1; PC  predetermined address
2. OS takes over
  initializes devices, MMU, timers, etc.
  loads programs from disk, sets up page tables, etc.
  Mode  0; PC  program entry point
    User programs regularly yield control back to OS

## Slide 14: Users need access to resources
If an untrusted process does not have privileges to use system resources, how can it
  Use the screen to print?
  Send message on the network?
  Allocate pages?
  Schedule processes?

## Slide 15: System Call Examples
putc(): Print character to screen
  Need to multiplex screen between competing processes
send(): Send a packet on the network
  Need to manipulate the internals of a device
sbrk(): Allocate a page
  Needs to update page tables & MMU
sleep(): put current prog to sleep, wake other
  Need to update page table base register

## Slide 16: System Calls
System calls called executive calls (ecall) in RISC-V
System call: Not just a function call
  Don’t let process jump just anywhere in OS code
  OS can’t trust process’ registers (sp, fp, gp, etc.)
ECALL instruction: safe transfer of control to OS
RISC-V system call convention:
  Exception handler saves temp regs, saves ra, …
  but: a7 = system call number, which specifies the operation the application is requesting

## Slide 17
User Application
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text
User Mode
Privileged (Kernel) Mode
System Call Interface
printf()
printf.c
Implementation
of printf() syscall!
SYSCALL!

## Slide 18: Libraries and Wrappers
Compilers do not emit SYSCALL instructions
  Compiler doesn’t know OS interface
Libraries implement standard API from system API
libc (standard C library):
  getc()  ecall
  sbrk()  ecall
  write()  ecall
  gets()  getc()
  printf()  write()
  malloc()  sbrk()
  …

## Slide 19: Invoking System Calls
char *gets(char *buf) {
while (...) {
buf[i] = getc();
}
}
int getc() {
asm("addi a7, 0, 4");
asm(“ecall");
}
4 is number for getc syscall
Notes: ecall (executive call) is the system call for RISC-V

## Slide 20: Anatomy of a Process, v1
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code
(text)
static data
dynamic data (heap)
(user) gets
(library) getc
??

## Slide 21: Where does the OS live?
In its own address space?
  Syscall has to switch to a different address space
  Hard to support syscall arguments passed as pointers
  . . . So, NOPE
In the same address space as the user process?
  Protection bits prevent user code from writing kernel
  Higher part of virtual memory
  Lower part of physical memory
  . . . Yes, this is how we do it.

## Slide 22: Anatomy of a Process
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 23: Full System Layout
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
stack
system reserved
code (text)
static data
dynamic data (heap)
OS Heap
OS Data
OS Stack
OS Text
All kernel text & most data:
At same virtual address in every address space
OS is omnipresent, available to help user-level applications
  Typically in high memory

## Slide 24: Full System Layout
Virtual Memory
OS Text
OS Data
OS Heap
OS Stack
Physical Memory
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
stack
system reserved
code (text)
static data
dynamic data (heap)
OS Heap
OS Data
OS Stack
OS Text
0x00...00

## Slide 25: Anatomy of a Process, v2
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
gets
getc
implementation of getc() syscall

## Slide 26: Inside the ECALL instruction
ECALL is s SYSCALL in RISC-V
ECALL instruction does an atomic jump to a controlled location (i.e. RISC-V 0x8000 0180)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value (= return address)
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel syscall handler

## Slide 27: Inside the ECALL implementation
Kernel system call handler carries out the desired system call
  Saves callee-save registers
  Examines the syscall ecall number
  Checks arguments for sanity
  Performs operation
  Stores result in a0
  Restores callee-save registers
  Performs a “supervisor exception return” (SRET) instruction, which restores the privilege mode, SP and PC

## Slide 28: Takeaway
It is necessary to have a privileged (kernel) mode to enable the Operating System (OS):
  provides isolation between processes
  protects shared resources
  provides safe control transfer

## Slide 29: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 30: Exceptional Control Flow
Anything that isn’t a user program executing its own user-level instructions.
System Calls:
just one type of exceptional control flow
Process requesting a service from the OS
Intentional – it’s in the executable!

## Slide 31: Software Exceptions
Trap
Intentional
  Examples:
  System call
  (OS performs service)
Breakpoint traps
Privileged instructions
Abort
Unintentional
Not recoverable
  Examples:
Parity error
Fault
Unintentional but
Possibly recoverable
  Examples:
Division by zero
Page fault
One of many ontology / terminology trees.

## Slide 32: Terminology
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous and planned, process-to-kernel transfer
  ECALL instruction in RISC-V (various on x86)
Exception: Synchronous but unplanned, process-to-kernel transfer
  exceptional events: div by zero, page fault, page protection err, …
Interrupt: Asynchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks

## Slide 33: Hardware support for exceptions
SEPC register
  Supervisor Exception Program Counter or SEPC
  32-bit register, holds addr of affected instruction
  Syscall case: Address of ECALL
SCAUSE register
  Supervisor Exception Cause Register or SCAUSE
  Register to hold the cause of the exception
  Syscall case: 8, Sys
Special instructions to load TLB
  Only do-able by kernel
Notes: Precise and imprecise exceptions
  In pipelined architecture
    Have to correctly identify PC of exception
    RISC-V and modern processors support this
For the operating system to handle the exception, it must know the reason for the exception, in addition to the instruction that caused it. There are two main methods used to communicate the reason for an exception. The method used in the RISC-V architecture is to include a register (called the Supervisor Exception Cause Register or SCAUSE), which holds a field that indicates the reason for the exception.

## Slide 34: Hardware support for exceptions
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
x0
x1
x30
x31
Code Stored in Memory
(also, data and stack)
SEPC
SCAUSE
Notes: Precise and imprecise exceptions
  In pipelined architecture
    Have to correctly identify PC of exception
    RISC-V and modern processors support this

## Slide 35: Hardware support for exceptions
Precise exceptions: Hardware guarantees
  (similar to a branch)
  Previous instructions complete
  Later instructions are flushed
  SEPC and SCAUSE register are set
  Jump to prearranged address in OS
  When you come back, restart instruction
  Disable exceptions while responding to one
    Otherwise can overwrite SEPC and SCAUSE

## Slide 36: Exceptional Control Flow
Hardware interrupts
Asynchronous
= caused by events external to CPU
Software exceptions
Synchronous
= caused by CPU executing an instruction
Maskable
Can be turned off by CPU
Example: alert from network device that a packet just arrived, clock notifying CPU of clock tick
Unmaskable
Cannot be ignored
Example: alert from the power supply that electricity is about to go out
AKA Exceptions

## Slide 37: Interrupts & Unanticipated Exceptions
No ECALL instruction. Hardware steps in:
  Saves PC of supervisor exception instruction (SEPC)
  Saves cause of the interrupt/privilege (Cause register)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel syscall hander interrupt/exception handler
SYSCALL

## Slide 38: Inside Interrupts & Unanticipated Exceptions
Kernel system call handler carries out system call
  all
  Saves callee-save registers
  Examines the syscall number cause
  Checks arguments for sanity
  Performs operation
  Stores result in a0
  Restores callee-save registers
  Performs a SRET instruction (restores the privilege mode, SP and PC)
interrupt/exception handler handles event
all

## Slide 39: Address Translation: HW/SW Division of Labor
Virtual  physical address translation!
Hardware
has a concept of operating in physical or virtual mode
helps manage the TLB
raises page faults
keeps Page Table Base Register (PTBR) and ProcessID
Software/OS
manages Page Table storage
handles Page Faults
updates Dirty and Reference bits in the Page Tables
keeps TLB valid on context switch:
  Flush TLB when new process runs (x86)
  Store process id (MIPS)
Notes: RISC-V offers ASID (address space ID) to reduce TLB flushes on context switches. The process identifier is concatenated to the tag portion of the TLB, so that a TLB hit occurs only if both the page number and the process identifier match. This combination eliminates the need to clear the TLB, except on rare occasions.

## Slide 40: Demand Paging on RISC-V
TLB miss
Trap to kernel
Walk Page Table
Find page is invalid
Convert virtual address to file + offset
Allocate page frame
  Evict page if needed
Initiate disk block read into page frame
Disk interrupt when DMA complete
Mark page as valid
Load TLB entry
Resume process at faulting instruction
Execute instruction