## Slide 1: Parallelism, Multicore, and Synchronization
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee, and Sirer, Roth, Martin]

## Slide 2: Announcements
P4-Buffer Overflow is due today
  Due Tuesday, April 16th
C practice assignment
  Due Friday, April 19th
P5-Cache project
  Due Friday, April 26th
Prelim2
  Thursday, May 2nd, 7:30pm

## Slide 3: xkcd/619

## Slide 4: Pitfall: Amdahl’s Law
affected execution time
amount of improvement
+ execution time unaffected
Execution time after improvement =
Timproved = + Tunaffected

## Slide 5: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
Example: multiply accounts for 80s out of 100s
Multiply can be parallelized
Timproved = + Tunaffected

## Slide 6: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors?
Single processor: Time = (10 + 100) × tadd
10 processors
100 processors
Assumes load can be balanced across processors

## Slide 7: Scaling Example
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
100 processors
Assuming load balanced

## Slide 8: Takeaway
Unfortunately, we cannot not obtain unlimited scaling (speedup) by adding unlimited parallel resources, eventual performance is dominated by a component needing to be executed sequentially.
Amdahl's Law is a caution about this diminishing return

## Slide 9: Performance Improvement 101
seconds instructions cycles seconds
program program instruction cycle
2 Classic Goals of Architects:
⬇ Clock period (⬆ Clock frequency)
⬇ Cycles per Instruction (⬆ IPC)
=
x
x

## Slide 10: Clock frequencies have stalled
Darling of performance improvement for decades
Why is this no longer the strategy?
Hitting Limits:
Pipeline depth
Clock frequency
Moore’s Law & Technology Scaling
Power

## Slide 11: Improving IPC via ILP
Exploiting Intra-instruction parallelism:
Pipelining (decode A while fetching B)
Exploiting Instruction Level Parallelism (ILP):
Multiple issue pipeline (2-wide, 4-wide, etc.)
Statically detected by compiler (VLIW)
Dynamically detected by HW
Dynamically Scheduled (OoO)

## Slide 12: Instruction-Level Parallelism (ILP)
Pipelining: execute multiple instructions in parallel
Q: How to get more instruction level parallelism?
Notes: Draw pictures: 250MHz 1-stage; 500Mhz 2-stage; 1GHz 4-stage; 4GHz 16-stage

## Slide 13: Multiple issue pipeline
Static multiple issue
aka Very Long Instruction Word
Decisions made by compiler
Dynamic multiple issue
Decisions made on the fly
Cost: More execute hardware
Reading/writing register files: more ports

## Slide 14: Static Multiple Issue
a.k.a. Very Long Instruction Word (VLIW)
Compiler groups instructions to be issued together
  Packages them into “issue slots”
How does HW detect and resolve hazards?
It doesn’t.  Compiler must avoid hazards
Example: Static Dual-Issue 32-bit RISC-V
  Instructions come in pairs (64-bit aligned)
    One ALU/branch instruction (or nop)
    One load/store instruction (or nop)
Notes: show program, decode stage
Ideal CPI = 0.5

## Slide 15: RISC-V with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 16: Scheduling Example
Loop: lw t0, s1, 0 # $t0=array element add t0, t0, s2 # add scalar in $s2 sw t0, s1, 0 # store result addi s1, s1,–4 # decrement pointer bne s1, zero, Loop # branch $s1!=0
Schedule this for dual-issue MIPS
 | ALU/branch | Load/store | cycle
Loop: |  |  | 1
 |  |  | 2
 |  |  | 3
 |  |  | 4

## Slide 17: Techniques and Limits of Static Scheduling
Goal: larger instruction windows (to play with)
Predication
Loop unrolling
Function in-lining
Basic block modifications (superblocks, etc.)
Roadblocks
Memory dependences (aliasing)
Control dependences

## Slide 18: Speculation
Reorder instructions
To fill the issue slot with useful work
Complicated: exceptions may occur

## Slide 19: Optimizations to make it work
Move instructions to fill in nops
Need to track hazards and dependencies
Loop unrolling

## Slide 20: Scheduling Example
Loop: lw t0, s1, 0 # t0 = A[i]
lw t1, s1, 4 # t1 = A[i+1] add t0, t0, s2 # add s2 add t1, t1, s2 # add s2 sw t0, s1, 0 # store A[i] sw t1, s1, 4 # store A[i+1] addi s1, s1, +8 # increment pointer bne s1, s3, Loop # continue if s1!=end
ALU/branch slot Load/store slot cycle
Loop: nop lw t0, s1, 0 1
nop lw t1, s1, 4 2
add t0, t0, s2 nop 3
add t1, t1, s2 sw t0, s1, 0 4
addi s1, s1, +8 sw t1, s1, 4 5
bne s1, s3, Loop nop 6
Compiler scheduling for dual-issue RISC-V…
Notes:   assume 1 delay slot for loads
  can move addi earlier
  CPI = 6 cycles / 8 instructions = 0.75
  CPI = 5 cycles / 8 instructions = 0.625

## Slide 21: Limits of Static Scheduling
lw t0, s1, 0 # load A
addi t0, t0, +1 # increment A
sw t0, s1, 0 # store A
lw t0, s2, 0 # load B
addi t0, t0, +1 # increment B
sw t0, s2, 0 # store B
ALU/branch slot Load/store slot cycle
nop lw t0, s1, 0 1
nop nop 2
addi t0, t0, +1 nop 3
nop sw t0, s1, 0 4
nop lw t0, s2, 0 5
nop nop 6
addi t0, t0, +1 nop 7
nop sw t0, s2, 0 8
Compiler scheduling for dual-issue RISC-V…
Notes: Rename registers, move load B up, eliminate delay slot
But! s1 and s2 might be equal => Aliasing!

## Slide 22: Improving IPC via ILP
Exploiting Intra-instruction parallelism:
Pipelining (decode A while fetching B)
Exploiting Instruction Level Parallelism (ILP):
Multiple issue pipeline (2-wide, 4-wide, etc.)
Statically detected by compiler (VLIW)
Dynamically detected by HW
Dynamically Scheduled (OoO)

## Slide 23: Dynamic Multiple Issue
aka SuperScalar Processor (c.f. Intel)
  CPU chooses multiple instructions to issue each cycle
  Compiler can help, by reordering instructions….
  … but CPU resolves hazards
Even better: Speculation/Out-of-order Execution
  Execute instructions as early as possible
  Aggressive register renaming (indirection to the rescue!)
  Guess results of branches, loads, etc.
  Roll back if guesses were wrong
  Don’t commit results until all previous insns committed

## Slide 24: Dynamic Multiple Issue

## Slide 25: Effectiveness of OoO Superscalar
It was awesome, but then it stopped improving
Limiting factors?
  Programs dependencies
  Memory dependence detection  be conservative
    e.g. Pointer Aliasing: A[0] += 1; B[0] *= 2;
  Hard to expose parallelism
    Still limited by the fetch stream of the static program
  Structural limits
    Memory delays and limited bandwidth
  Hard to keep pipelines full, especially with branches

## Slide 26: Power Efficiency
Q: Does multiple issue / ILP cost much?
A: Yes.
 Dynamic issue and speculation requires power
CPU | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Those simpler cores did something very right.

## Slide 27: Moore’s Law
486
286
8088
8080
8008
4004
386
Pentium
Atom
P4
Itanium 2
K8
K10
Dual-core Itanium 2

## Slide 28: Why Multicore?
Moore’s law
  A law about transistors
  Smaller means more transistors per die
  And smaller means faster too
But: Power consumption growing too…

## Slide 29: Power Limits
Hot Plate
Rocket Nozzle
Nuclear Reactor
Surface of Sun
Xeon
180nm
32nm

## Slide 30: Power Wall
Power = capacitance * voltage2 * frequency
In practice: Power ~ voltage3
Reducing voltage helps (a lot)
... so does reducing clock speed
Better cooling helps
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
Lower Frequency

## Slide 31: Why Multicore?
Power
1.0x
1.0x
Performance
Single-Core
Power
1.2x
1.7x
Performance
Single-Core Overclocked +20%
Power
0.8x
0.51x
Performance
Single-Core
Underclocked -20%
1.6x
1.02x
Dual-Core
Underclocked -20%

## Slide 32: Power Efficiency
Q: Does multiple issue / ILP cost much?
A: Yes.
 Dynamic issue and speculation requires power
CPU | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Those simpler cores did something very right.
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
Core i5 Nehal | 2010 | 3300MHz | 14 | 4 | Yes | 1 | 87W
Core i5 Ivy Br | 2012 | 3400MHz | 14 | 4 | Yes | 8 | 77W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 33: Inside the Processor
AMD Barcelona Quad-Core: 4 processor cores

## Slide 34: Inside the Processor
Intel Nehalem Hex-Core
4-wide pipeline

## Slide 35: Improving IPC via ILP TLP
Exploiting Thread-Level parallelism
Hardware multithreading to improve utilization:
  Multiplexing multiple threads on single CPU
  Sacrifices latency for throughput
  Single thread cannot fully utilize CPU? Try more!
  Three types:
    Course-grain (has preferred thread)
    Fine-grain (round robin between threads)
    Simultaneous (hyperthreading)

## Slide 36: What is a thread?
Process: multiple threads, code, data and OS state
Threads: share code, data, files, not regs or stack

## Slide 37: Standard Multithreading Picture
Time evolution of issue slots
  Color = thread, white = no instruction
CGMT
FGMT
SMT
4-wide
Superscalar
time
  Switch to thread B on thread A L2 miss
  Switch threads every cycle
  Insns from multiple threads coexist

## Slide 38: Hyperthreading
Multi-Core vs. Multi-Issue
Programs:
Num. Pipelines:
Pipeline Width:
Hyperthreads
  HT = MultiIssue + extra PCs and registers – dependency logic
  HT = MultiCore – redundant functional units + hazard avoidance
Hyperthreads (Intel)
  Illusion of multiple cores on a single core
  Easy to keep HT pipelines full + share functional units
vs. HT

## Slide 39: Example: All of the above
8 die (aka 8 sockets)
4 core per socket
2 HT per core
Note: a socket is a processor,
where each processor may
have multiple processing
cores, so this is an example
of a multiprocessor multicore
hyperthreaded system

## Slide 40: Parallel Programming
Q: So lets just all use multicore from now on!
A: Software must be written as parallel program
Multicore difficulties
  Partitioning work
  Coordination & synchronization
  Communications overhead
  How do you write parallel programs?
    ... without knowing exact underlying architecture?

## Slide 41: Work Partitioning
Partition work so all cores have something to do

## Slide 42: Load Balancing
Load Balancing
Need to partition so all cores are actually working

## Slide 43: Amdahl’s Law
If tasks have a serial part and a parallel part…
Example:
step 1: divide input data into n pieces
step 2: do work on each piece
step 3: combine all results
Recall: Amdahl’s Law
As number of cores increases …
  time to execute parallel part?
  time to execute serial part?
  Serial part eventually dominates
goes to zero
Remains the same

## Slide 44: Amdahl’s Law

## Slide 45: Parallelism is a necessity
Necessity, not luxury
Power wall
Not easy to get performance out of
Many solutions
Pipelining
Multi-issue
Hyperthreading
Multicore

## Slide 46: Parallel Programming
Q: So lets just all use multicore from now on!
A: Software must be written as parallel program
Multicore difficulties
  Partitioning work
  Coordination & synchronization
  Communications overhead
  How do you write parallel programs?
    ... without knowing exact underlying architecture?
HW
SW
Your
career…

## Slide 47: Big Picture: Parallelism and Synchronization
How do I take advantage of parallelism?
How do I write (correct) parallel programs?
What primitives do I need to implement correct parallel programs?

## Slide 48: Parallelism & Synchronization
Cache Coherency
  Processors cache shared data  they see different (incoherent) values for the same memory location
Synchronizing parallel programs
  Atomic Instructions
  HW support for synchronization
How to write parallel programs
  Threads and processes
  Critical sections, race conditions, and mutexes

## Slide 49: Parallelism and Synchronization
Cache Coherency Problem: What happens when to two or more processors cache shared data?

## Slide 50: Parallelism and Synchronization
Cache Coherency Problem: What happens when to two or more processors cache shared data?
i.e. the view of memory held by two different processors is through their individual caches.
As a result, processors can see different (incoherent) values to the same memory location.

## Slide 51: Parallelism and Synchronization

## Slide 52: Parallelism and Synchronization
Each processor core has its own L1 cache

## Slide 53: Parallelism and Synchronization
Each processor core has its own L1 cache

## Slide 54: Parallelism and Synchronization
Each processor core has its own L1 cache
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
Core3
Cache
Core2
Cache

## Slide 55: Shared Memory Multiprocessors
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 4 processor dies, 2 – 8 cores each
  HW provides single physical address space for all processors
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
Core3
Cache
Core2
Cache

## Slide 56: Shared Memory Multiprocessors
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 4 processor dies, 2 – 8 cores each
  HW provides single physical address space for all processors
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
...
CoreN
Cache
...
...

## Slide 57: Cache Coherency Problem
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { x = x + 1; x = x + 1; } }
What will the value of x be after both loops finish?
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
...
CoreN
Cache
...
...

## Slide 58: Not just a problem for Write-Back Caches
Executing on a write-thru cache
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
...
CoreN
Cache
...
...

## Slide 59: Two issues
Coherence
What values can be returned by a read
Need a globally uniform (consistent) view of a single memory location
Solution: Cache Coherence Protocols
Consistency
When a written value will be returned by a read
Need a globally uniform (consistent) view of all memory locations relative to each other
Solution: Memory Consistency Models

## Slide 60: Coherence Defined
Informal: Reads return most recently written value
Formal: For concurrent processes P1 and P2
  P writes X before P reads X (with no intervening writes)  read returns written value
    (preserve program order)
  P1 writes X before P2 reads X  read returns written value
    (coherent memory view, can’t read old value forever)
  P1 writes X and P2 writes X  all processors see writes in the same order
    all see the same final value for X
    Aka write serialization
    (else PA can see P2’s write before P1’s and PB can see the opposite; their final understanding of state is wrong)

## Slide 61: Cache Coherence Protocols
Operations performed by caches in multiprocessors to ensure coherence
  Migration of data to local caches
    Reduces bandwidth for shared memory
  Replication of read-shared data
    Reduces contention for access
Snooping protocols
  Each cache monitors bus reads/writes

## Slide 62: Snooping
Snooping for Hardware Cache Coherence
  All caches monitor bus and all other caches
  Bus read: respond if you have dirty data
  Bus write: update/invalidate your copy of data
...
Core0
Cache
Memory
I/O
Interconnect
...
...
Snoop
Core1
Cache
Snoop
CoreN
Cache
Snoop

## Slide 63: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read in another cache misses
    Owning cache supplies updated value
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X |  |  |  | 
2 | CPU B reads X |  |  |  | 
3 | CPU A writes 1 to X |  |  |  | 
4 | CPU B read X |  |  |  | 

## Slide 64: Writing
Write-back policies for bandwidth
Write-invalidate coherence policy
  First invalidate all other copies of data
  Then write it in cache line
  Anybody else can read it
Permits one writer, multiple readers
In reality: many coherence protocols
  Snooping doesn’t scale
  Directory-based protocols
    Caches and memory record sharing status of blocks in a directory

## Slide 65: Hardware Cache Coherence
Coherence
  all copies have same data at all times
Coherence controller:
  Examines bus traffic (addresses and data)
  Executes coherence protocol
    What to do with local copy when you see different things happening on bus
Three processor-initiated events
  Ld: load
  St: store
  WB: write-back
Two remote-initiated events
  LdMiss: read miss from another processor
  StMiss: write miss from another processor
CPU
D$ data
D$ tags
CC
bus

## Slide 66: VI Coherence Protocol
VI (valid-invalid) protocol:
  Two states (per block in cache)
    V (valid): have block
    I (invalid): don’t have block
    Can implement with valid bit
Protocol diagram (left)
  If you load/store a block: transition to V
  If anyone else wants to read/write block:
    Give it up: transition to I state
    Write-back if your own copy is dirty
I
V
Load, Store
LdMiss, StMiss, WB
Load, Store
LdMiss/
StMiss

## Slide 67: VI Protocol (Write-Back Cache)
lw by Thread B generates an “other load miss” event (LdMiss)
  Thread A responds by sending its dirty copy, transitioning to I
0
V:0
0
V:1
0
I:
1
V:1
1
V:2
CPU0
Mem
CPU1
Thread A
lw t0, r3, 0
ADDIU t0, t0, 1
sw t0, r3, 0
Thread B
lw t0, r3, 0
ADDIU t0, t0, 1
sw t0, r3, 0

## Slide 68: VI  MSI
LdMiss
I
M
Store
StMiss, WB
Load, Store
S
Store
Load, LdMiss
StMiss
Load
LdMiss/
StMiss
VI protocol is inefficient
  Only one cached copy allowed in entire system
  Multiple copies can’t exist even if read-only
    Not a problem in example
    Big problem in reality
MSI (modified-shared-invalid)
  Fixes problem: splits “V” state into two states
    M (modified): local dirty copy
    S (shared): local clean copy
  Allows either
    Multiple read-only copies (S-state) --OR--
    Single read/write copy (M-state)

## Slide 69: MSI Protocol (Write-Back Cache)
lw by Thread B generates a “other load miss” event (LdMiss)
  Thread A responds by sending its dirty copy, transitioning to S
sw by Thread B generates a “other store miss” event (StMiss)
  Thread A responds by transitioning to I
Thread A
lw t0, r3, 0
ADDIU t0, t0, 1
sw t0, r3, 0
Thread B
lw t0, r3, 0
ADDIU t0, t0, 1
sw t0, r3, 0
0
S:0
0
M:1
0
S:1
1
S:1
I:
1
M:2
CPU0
Mem
CPU1

## Slide 70: Cache Coherence and Cache Misses
Coherence introduces two new kinds of cache misses
  Upgrade miss
    On stores to read-only blocks
    Delay to acquire write permission to read-only block
  Coherence miss
    Miss to a block evicted by another processor’s requests
Making the cache larger…
  Doesn’t reduce these type of misses
  As cache grows large, these sorts of misses dominate
False sharing
  Two or more processors sharing parts of the same block
  But not the same bytes within that block (no actual sharing)
  Creates pathological “ping-pong” behavior
  Careful data placement may help, but is difficult

## Slide 71: More Cache Coherence
In reality: many coherence protocols
  Snooping: VI, MSI, MESI, MOESI, …
    But Snooping doesn’t scale
  Directory-based protocols
    Caches & memory record blocks’ sharing status in directory
    Nothing is free  directory protocols are slower!
Cache Coherency:
requires that reads return most recently written value
Is a hard problem!

## Slide 72: Takeaway: Summary of cache coherence
Informally, Cache Coherency requires that reads return most recently written value
Cache coherence hard problem
Snooping protocols are one approach

## Slide 73: Next Goal: Synchronization
Is cache coherency sufficient?
i.e. Is cache coherency (what values are read) sufficient to maintain consistency (when a written value will be returned to a read). Both coherency and consistency are required to maintain consistency in shared memory programs.

## Slide 74: Are We Done Yet?
What just happened???
Is Cache Coherency Protocol Broken??
Thread A
lw t0, r3, 0
ADDIU t0, t0, 1
sw t0, x, 0
Thread B
lw t0, r3, 0
ADDIU t0, t0, 1
sw t0, x, 0
0
S:0
0
S:0
0
S:0
M:1
1
I:
CPU0
Mem
CPU1
I:
0
M:1

## Slide 75: Is Cache Coherency Sufficient?
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { LW t0, addr(x) LW t0, addr(x)
ADDIU t0, t0, 1 ADDIU t0, t0, 1
SW t0, addr(x) SW t0, addr(x) } }
Very expensive and difficult to maintain consistency
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
...
CoreN
Cache
...
...

## Slide 76: Programming with Threads
Need it to exploit multiple processing units
…to parallelize for multicore
…to write servers that handle many clients
Problem: hard even for experienced programmers
  Behavior can depend on subtle timing differences
  Bugs may be impossible to reproduce
Needed: synchronization of threads

## Slide 77: Programming with Threads
Within a thread: execution is sequential
Between threads?
  No ordering or timing guarantees
  Might even run on different cores at the same time
Problem: hard to program, hard to reason about
  Behavior can depend on subtle timing differences
  Bugs may be impossible to reproduce
Cache coherency is not sufficient…
Need explicit synchronization to make sense of concurrency!

## Slide 78: Programming with Threads
Concurrency poses challenges for:
Correctness
  Threads accessing shared memory should not interfere with each other
Liveness
  Threads should not get stuck, should make forward progress
Efficiency
  Program should make good use of available computing resources (e.g., processors).
Fairness
  Resources apportioned fairly between threads

## Slide 79: Example: Multi-Threaded Program
Apache web server
void main() { setup();
while (c = accept_connection()) {
req = read_request(c);
hits[req]++; send_response(c, req);
}
cleanup();
}

## Slide 80: Example: web server
Each client request handled by a separate thread (in parallel)
  Some shared state: hit counter, ...
(look familiar?)
Timing-dependent failure  race condition
  hard to reproduce  hard to debug
Thread 52
read hits
addiu
write hits
Thread 205
read hits
addiu
write hits

## Slide 81: Two threads, one counter
Possible result: lost update!
Timing-dependent failure  race condition
  Very hard to reproduce  Difficult to debug
ADDIU/SW: hits = 0 + 1
LW (0)
ADDIU/SW: hits = 0 + 1
LW (0)
T1
T2
hits = 1
hits = 0
time

## Slide 82: Race conditions
Timing-dependent error involving access to shared state
Race conditions depend on how threads are scheduled
  i.e. who wins “races” to update state
Challenges of Race Conditions
  Races are intermittent, may occur rarely
  Timing dependent = small changes can hide bug
Program is correct only if all possible schedules are safe
Number of possible schedules is huge
Imagine adversary who switches contexts at worst possible time

## Slide 83: Critical Sections
What if we can designate parts of the execution as critical sections
  Rule: only one thread can be “inside” a critical section
Thread 52
CSEnter()
read hits
addi
write hits
CSExit()
Thread 205
CSEnter()
read hits
addi
write hits
CSExit()

## Slide 84: Critical Sections
To eliminate races: use critical sections that only one thread can be in
  Contending threads must wait to enter
CSEnter();
  Critical section
CSExit();
T1
T2
time
CSEnter();
  # wait
  # wait
  Critical section
CSExit();
T1
T2

## Slide 85: Mutual Exclusion Lock (Mutex)
Implement CSEnter and CSExit; ie. a critical section
Only one thread can hold the lock at a time
“I have the lock”
Mutual Exclusion Lock (mutex)
lock(m): wait till it becomes free, then lock it
unlock(m): unlock it
safe_increment() {
pthread_mutex_lock(&m);
hits = hits + 1;
pthread_mutex_unlock(&m);
}

## Slide 86: Mutexes
Only one thread can hold a given mutex at a time
Acquire (lock) mutex on entry to critical section
  Or block if another thread already holds it
Release (unlock) mutex on exit
  Allow one waiting thread (if any) to acquire & proceed
pthread_mutex_lock(&m);
  hits = hits+1;
pthread_mutex_unlock(&m);
T1
T2
pthread_mutex_lock(&m);
# wait
# wait
  hits = hits+1;
pthread_mutex_unlock(&m);
pthread_mutex_init(&m);

## Slide 87: Next Goal
How to implement mutex locks?
What are the hardware primitives?
Then, use these mutex locks to implement critical sections, and use critical sections to write parallel safe programs

## Slide 88: Hardware Support for Synchronization
Atomic read & write memory operation
  Between read & write: no writes to that address
Many atomic hardware primitives
test and set (x86)
atomic increment (x86)
bus lock prefix (x86)
compare and exchange (x86, ARM deprecated)
linked load / store conditional (pair of insns) (RISC-V, ARM, PowerPC, DEC Alpha, …)

## Slide 89: Synchronization in RISC-V
Load Reserved: LR.W rd, rs1
“I want the value at address X. Also, start monitoring any writes to this address.”
Store Conditional: SC.W rd, rs1, rs2
“If no one has changed the value at address X since the LL, perform this store and tell me it worked.”
  Data at location has not changed since the LR?
    SUCCESS:
      Performs the store
      Returns 1 in rd
  Data at location has changed since the LR?
    FAILURE:
      Does not perform the store
      Returns 0 in rd

## Slide 90: Synchronization in RISC-V
Load Reserved: LR.W rd, rs1
Store Conditional: SC.W rd, rs1, rs2
  Succeeds if location not changed since the LR
    Returns 1 in rd
  Fails if location is changed
    Returns 0 in rd
Any time a processor intervenes and modifies the value in memory between the LR and SC instruction, the SC returns 0 in t0, causing the code to try again.
i.e. use this value 0 in t0 to try again.

## Slide 91: Synchronization in RISC-V
Load Reserved: LR.W rd, rs1
Store Conditional: SC.W rd, rs1, rs2
  Succeeds if location not changed since the LR
    Returns 1 in rd
  Fails if location is changed
    Returns 0 in rd
Example: atomic incrementor
i++
↓
LW t0, s0, 0
ADDIU t0, t0, 1
SW t0, s0, 0
LR.W t0, s0
ADDIU t0, t0, 1
SC.W t0, s0, 0
BEQZ t0, try
atomic(i++)
↓
Value in memory changed between LR and SC ?
 SC returns 0 in t0  retry
try:

## Slide 92: Atomic Increment in Action
Load Reserved: LR.W rd, rs1
Store Conditional: SC.W rd, rs1, rs2
Time | Thread A | Thread B | Thread A $t0 | Thread B $t0 | Mem [$s0]
0 |  |  |  |  | 0
1 | try: LR.W t0, s0 |  |  |  | 
2 |  | try: LR.W t0, s0 |  |  | 
3 | ADDIU t0, t0, 1 |  |  |  | 
4 |  | ADDIU t0, t0, 1 |  |  | 
5 | SC.W t0, s0, 0 |  |  |  | 
6 | BEQZ t0, try |  |  |  | 
7 |  | SC.W t0, s0, 0 |  |  | 
8 |  | BEQZ t0, try |  |  | 

## Slide 93: Mutex from LR and SC
Load Reserved / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
old = *m;
*m = 1;
return old;
}
LR.W Atomic
SC.W
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 94: Mutex from LR and SC
Load Reserved / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
LI t0, 1
LR.W t1, a0
SC.W t0, a0, 0
MOVE v0, t1
}
BEQZ t0, try
try:

## Slide 95: Mutex from LR and SC
Load Reserved / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
try:
LI t0, 1
LR.W t1, a0,
SC.W t0, a0, 0
BEQZ t0, try
MOVE a0, t1
}

## Slide 96: Mutex from LR and SC
Load Reserved / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
test_and_set:
LI t0, 1
LR.W t1, a0
BNEZ t1, test_and_set
SC.W t0, a0, 0
BEQZ t0, test_and_set
}
mutex_unlock(int *m) {
*m = 0;
}

## Slide 97: Mutex from LR and SC
Load Reserved / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
test_and_set:
LI t0, 1
LR.W t1, a0
BNEZ t1, test_and_set
SC.W t0, a0, 0
BEQZ t0, test_and_set
}
mutex_unlock(int *m) {
SW zero, a0, 0
}
This is called a
Spin lock
Aka spin waiting

## Slide 98: Mutex from LR and SC
Load Reserved / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
Time Step | Thread A | Thread B | ThreadA t0 | ThreadA t1 | ThreadB t0 | ThreadB t1 | Mem M[a0]
0 |  |  |  |  |  |  | 0
1 | try: LI t0, 1 | try: LI t0, 1 |  |  |  |  | 
2 | LR.W t1, a0 | LR.W t1, a0 |  |  |  |  | 
3 | BNEZ t1, try | BNEZ t1, try |  |  |  |  | 
4 |  | SC.W t0, a0, 0 |  |  |  |  | 
5 | SC.W t0, a0, 0 |  |  |  |  |  | 
6 | BEQZ t0, try | BEQZ t0, try |  |  |  |  | 
7 |  |  |  |  |  |  | 

## Slide 99: Mutex from LR and SC
Load Reserved / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
test_and_set:
LI t0, 1
LR.W t1, a0
BNEZ t1, test_and_set
SC.W t0, a0, 0
BEQZ t0, test_and_set
}
mutex_unlock(int *m) {
SW zero, a0, 0
}
This is called a
Spin lock
Aka spin waiting

## Slide 100: Mutex from LR and SC
Load Reserved / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
Time Step | Thread A | Thread B | ThreadA t0 | ThreadA t1 | ThreadB t0 | ThreadB t1 | Mem M[a0]
0 |  |  |  |  |  |  | 1
1 | try: LI t0, 1 | try: LI t0, 1 |  |  |  |  | 
2 |  |  |  |  |  |  | 
3 |  |  |  |  |  |  | 
4 |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 
6 |  |  |  |  |  |  | 
7 |  |  |  |  |  |  | 
8 |  |  |  |  |  |  | 
9 |  |  |  |  |  |  | 

## Slide 101: Now we can write parallel and correct programs
Thread A Thread B for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) {
x = x + 1; x = x + 1;
} }
mutex_lock(m); mutex_lock(m);
mutex_unlock(m); mutex_unlock(m);

## Slide 102: Alternative Atomic Instructions
Other atomic hardware primitives
- test and set (x86)
- atomic increment (x86)
- bus lock prefix (x86)
- compare and exchange (x86, ARM deprecated)
- load reserved / store conditional (RISC-V, ARM, PowerPC, DEC Alpha, …)

## Slide 103: Synchronization
Synchronization techniques
clever code
  must work despite adversarial scheduler/interrupts
  used by: hackers
  also: noobs
disable interrupts
  used by: exception handler, scheduler, device drivers, …
disable preemption
  dangerous for user code, but okay for some kernel code
mutual exclusion locks (mutex)
  general purpose, except for some interrupt-related cases

## Slide 104: Summary
Need parallel abstractions, especially for multicore
Writing correct programs is hard
Need to prevent data races
Need critical sections to prevent data races
Mutex, mutual exclusion, implements critical section
Mutex often implemented using a lock abstraction
Hardware provides synchronization primitives such as LR and SC (load reserved and store conditional) instructions to efficiently implement locks

## Slide 105: Next Goal
How do we use synchronization primitives to build concurrency-safe data structure?

## Slide 106: Producer/Consumer Example (1)
Access to shared data must be synchronized
  Goal: enforce datastructure invariants
// invariant: // data is in A[h … t-1]
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
A[t] = c;
t = (t+1)%n;
}
1
2
3
head
tail

## Slide 107: Producer/Consumer Example (1)
Access to shared data must be synchronized
  Goal: enforce datastructure invariants
// invariant: // data is in A[h … t-1]
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
A[t] = c;
t = (t+1)%n;
}
// consumer: take from list head
char get() {
while (h == t) { };
char c = A[h];
h = (h+1)%n;
return c;
}
1
2
3
4
head
tail

## Slide 108: Protecting an invariant Example (2)
// invariant: (protected by mutex m) // data is in A[h … t-1]
pthread_mutex_t *m = pthread_mutex_create();
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
pthread_mutex_lock(m);
A[t] = c;
t = (t+1)%n;
pthread_mutex_unlock(m);
}
// consumer: take from list head
char get() {
pthread_mutex_lock(m);
while(h == t) {}
char c = A[h];
h = (h+1)%n;
pthread_mutex_unlock(m);
return c;
}

## Slide 109: Guidelines for successful mutexing
Insufficient locking can cause races
  Skimping on mutexes? Just say no!
Poorly designed locking can cause deadlock
  know why you are using mutexes!
  acquire locks in a consistent order to avoid cycles
  use lock/unlock like braces (match them lexically)
    lock(&m); …; unlock(&m)
    watch out for return, goto, and function calls!
    watch out for exception/error conditions!
  P1: lock(m1); lock(m2);
  P2: lock(m2); lock(m1);
Circular
Wait

## Slide 110: Beyond mutexes Example (3)
Writers must check for full buffer & Readers must check for empty buffer
  ideal: don’t busy wait… go to sleep instead
char get() {
acquire(L);
char c = A[h];
h = (h+1)%n;
release(L);
return c;
}
head
last==head
empty

## Slide 111: Language-level Synchronization

## Slide 112: Condition variables
Use [Hoare] a condition variable to wait for a condition to become true (without holding lock!)
wait(m, c) :
  atomically release m and sleep, waiting for condition c
  wake up holding m sometime after c was signaled
signal(c) : wake up one thread waiting on c
broadcast(c) : wake up all threads waiting on c
POSIX (e.g., Linux): pthread_cond_wait, pthread_cond_signal, pthread_cond_broadcast

## Slide 113: Using a condition variable Example (5)
wait(m, c) : release m, sleep until c, wake up holding m
signal(c) : wake up one thread waiting on c
char get() {
lock(m);
while (t == h)
wait(m, not_empty);
char c = A[h];
h = (h+1) % n;
unlock(m);
signal(not_full);
return c;
}
cond_t *not_full = ...;
cond_t *not_empty = ...;
mutex_t *m = ...;
void put(char c) {
lock(m);
while ((t-h) % n == 1)
wait(m, not_full);
A[t] = c;
t = (t+1) % n;
unlock(m);
signal(not_empty);
}

## Slide 114: Monitors
A Monitor is a concurrency-safe datastructure, with…
  one mutex
  some condition variables
  some operations
All operations on monitor acquire/release mutex
  one thread in the monitor at a time
Ring buffer was a monitor
Java, C#, etc., have built-in support for monitors

## Slide 115: Java concurrency
Java objects can be monitors
  “synchronized” keyword locks/releases the mutex
  Has one (!) builtin condition variable
    o.wait() = wait(o, o)
    o.notify() = signal(o)
    o.notifyAll() = broadcast(o)
  Java wait() can be called even when mutex is not held. Mutex not held when awoken by signal(). Useful?

## Slide 116: Language-level Synchronization
Lots of synchronization variations… Reader/writer locks
  Any number of threads can hold a read lock
  Only one thread can hold the writer lock
Semaphores
  N threads can hold lock at the same time
Monitors
  Concurrency-safe data structure with 1 mutex
  All operations on monitor acquire/release mutex
  One thread in the monitor at a time
Message-passing, sockets, queues, ring buffers, …
  transfer data and synchronize

## Slide 117: Summary
Hardware Primitives: test-and-set, LR.W/SC.W, barrier, ...
… used to build …
Synchronization primitives: mutex, semaphore, ...
… used to build …
Language Constructs: monitors, signals, ...