## Slide 1: I/O
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee, and Sirer]

## Slide 2: Big Picture: Input/Output (I/O)
How does a processor interact with its environment?

## Slide 3: Big Picture: Input/Output (I/O)
How does a processor interact with its environment?
Computer System =
Memory + Datapath + Control
Display
Keyboard
Network
Disk
+ Input + Output

## Slide 4: I/O Devices Enables Interacting with Environment
Device | Behavior | Partner | Data Rate (b/sec)
Keyboard | Input | Human | 100
Mouse | Input | Human | 3.8k
Sound Input | Input | Machine | 3M
Voice Output | Output | Human | 264k
Sound Output | Output | Human | 8M
Laser Printer | Output | Human | 3.2M
Graphics Display | Output | Human | 800M – 8G
Network/LAN | Input/Output | Machine | 100M – 10G
Network/Wireless LAN | Input/Output | Machine | 11 – 54M
Optical Disk | Storage | Machine | 5 – 120M
Flash memory | Storage | Machine | 32 – 200M
Magnetic Disk | Storage | Machine | 800M – 3G

## Slide 5: Round 1: All devices on one interconnect
Replace all devices as the interconnect changes
e.g. keyboard speed == main memory speed ?!
Unified Memory and I/O Interconnect
Memory
Display
Disk
Keyboard
Network

## Slide 6: Round 2: I/O Controllers
Decouple I/O devices from Interconnect
Enable smarter I/O interfaces
Core0
Cache
Memory
Controller
I/O
Controller
Unified Memory and I/O Interconnect
Core1
Cache
Memory
Display
I/O
Controller
Disk
I/O
Controller
Keyboard
I/O
Controller
Network
Core0
Cache
Core1
Cache

## Slide 7: Round 3: I/O Controllers + Bridge
Separate high-performance processor, memory, display interconnect from lower-performance interconnect
Core0
Cache
Memory
Controller
I/O
Controller
High Performance
Interconnect
Core1
Cache
Memory
Display
I/O
Controller
Disk
I/O
Controller
Keyboard
I/O
Controller
Network
Lower Performance
Legacy Interconnect
Bridge

## Slide 8: Bus Parameters
Width = number of wires
Transfer size = data words per bus transaction
Synchronous (with a bus clock) or asynchronous (no bus clock / “self clocking”)

## Slide 9: Bus Types
Processor – Memory (“Front Side Bus”. Also QPI)
  Short, fast, & wide
  Mostly fixed topology, designed as a “chipset”
    CPU + Caches + Interconnect + Memory Controller
I/O and Peripheral busses (PCI, SCSI, USB, LPC, …)
  Longer, slower, & narrower
  Flexible topology, multiple/varied connections
  Interoperability standards for devices
  Connect to processor-memory bus through a bridge

## Slide 10: Round 3: I/O Controllers + Bridge
Separate high-performance processor, memory, display interconnect from lower-performance interconnect

## Slide 11: Example Interconnects
Name | Use | Devices per channel | Channel Width | Data Rate (B/sec)
Firewire 800 | External | 63 | 4 | 100M
USB 2.0 | External | 127 | 2 | 60M
USB 3.0 | External | 127 | 2 | 625M
Parallel ATA | Internal | 1 | 16 | 133M
Serial ATA (SATA) | Internal | 1 | 4 | 300M
PCI 66MHz | Internal | 1 | 32-64 | 533M
PCI Express v2.x | Internal | 1 | 2-64 | 16G/dir
Hypertransport v2.x | Internal | 1 | 2-64 | 25G/dir
QuickPath (QPI) | Internal | 1 | 40 | 12G/dir

## Slide 12: Interconnecting Components
Interconnects are (were?) busses
  parallel set of wires for data and control
  shared channel
    multiple senders/receivers
    everyone can see all bus transactions
  bus protocol: rules for using the bus wires
Alternative (and increasingly common):
  dedicated point-to-point channels
e.g. Intel
Xeon
e.g. Intel
Nehalem

## Slide 13: Round 4: I/O Controllers+Bridge+ NUMA
Remove bridge as bottleneck with Point-to-point interconnects
E.g. Non-Uniform Memory Access (NUMA)

## Slide 14: Takeaways
Diverse I/O devices require hierarchical interconnect which is more recently transitioning to point-to-point topologies.

## Slide 15: Next Goal
How does the processor interact with I/O devices?

## Slide 16: I/O Device Driver Software Interface
Set of methods to write/read data to/from device and control device
Example: Linux Character Devices
// Open a toy " echo " character device
int fd = open("/dev/echo", O_RDWR);
// Write to the device
char write_buf[] = "Hello World!";
write(fd, write_buf, sizeof(write_buf));
// Read from the device
char read_buf [32];
read(fd, read_buf, sizeof(read_buf));
// Close the device
close(fd);
// Verify the result
assert(strcmp(write_buf, read_buf)==0);

## Slide 17: I/O Device API
Typical I/O Device API
  a set of read-only or read/write registers
Command registers
  writing causes device to do something
Status registers
  reading indicates what device is doing, error codes, …
Data registers
  Write: transfer data to a device
  Read: transfer data from a device
Every device uses this API

## Slide 18: I/O Device API
Simple (old) example: AT Keyboard Device
8-bit Status:
8-bit Command: 0xAA = “self test” 0xAE = “enable kbd” 0xED = “set LEDs”
…
8-bit Data: scancode (when reading) LED state (when writing) or …
PE | TO | AUXB | LOCK | AL2 | SYSF | IBS | OBS
Input
Buffer
Status
Input
Buffer
Status

## Slide 19: Communication Interface
Q: How does program OS code talk to device?
A: special instructions to talk over special busses
Programmed I/O
  inb xa, 0x64
  outb xa, 0x60
  Specifies: device, data, direction
  Protection: only allowed in kernel mode
*x86: $a implicit; also inw, outw, inh, outh, …
Interact with cmd, status, and
data device registers directly
kbd status register
kbd data register
Kernel boundary crossing is expensive

## Slide 20: Communication Interface
Q: How does program OS code talk to device?
A: Map registers into virtual address space
Memory-mapped I/O
  Accesses to certain addresses redirected to I/O devices
  Data goes over the memory bus
  Protection: via bits in pagetable entries
  OS+MMU+devices configure mappings
Faster. Less boundary crossing

## Slide 21
Memory-Mapped I/O
Physical
Address
Space
Virtual
Address
Space
0xFFFF FFFF
0x00FF FFFF
0x0000 0000
0x0000 0000
Display
Disk
Keyboard
Network
I/O
Controller
I/O
Controller
I/O
Controller
I/O
Controller
Less-favored alternative = Programmed I/O:
Syscall instructions that communicate with I/O
Communicate via special device registers
agreed-upon locations for communication

## Slide 22: Device Drivers
Programmed I/O
char read_kbd()
{
do {
sleep();
status = inb(0x64);
} while(!(status & 1));
return inb(0x60);
}
Memory Mapped I/O
struct kbd {
char status, pad[3];
char data, pad[3];
};
kbd *k = mmap(...);
char read_kbd()
{
do {
sleep();
status = k->status;
} while(!(status & 1));
return k->data;
}
syscall
syscall

## Slide 23: I/O Data Transfer
How to talk to device?
  Programmed I/O or Memory-Mapped I/O
How to get events?
  Polling or Interrupts
How to transfer lots of data?
disk->cmd = READ_4K_SECTOR;
disk->data = 12;
while (!(disk->status & 1) { }
for (i = 0..4k)
buf[i] = disk->data;
Very,
Very,
Expensive

## Slide 24: Data Transfer
1. Programmed I/O: Device  CPU  RAM
  for (i = 1 .. n)
  CPU issues read request
  Device puts data on bus & CPU reads into registers
  CPU writes data to memory
2. Direct Memory Access (DMA): Device  RAM
  CPU sets up DMA request
  for (i = 1 ... n) Device puts data on bus & RAM accepts it
  Device interrupts CPU after done
CPU
RAM
DISK
CPU
RAM
DISK
Which one is the winner? Which one is the loser?

## Slide 25: DMA Example
DMA example: reading from audio (mic) input
  DMA engine on audio device… or I/O controller … or …
int dma_size = 4*PAGE_SIZE;
int *buf = alloc_dma(dma_size);
...
dev->mic_dma_baseaddr = (int)buf;
dev->mic_dma_count = dma_len;
dev->cmd = DEV_MIC_INPUT | DEV_INTERRUPT_ENABLE | DEV_DMA_ENABLE;

## Slide 26: DMA Issues (1): Addressing
Issue #1: DMA meets Virtual Memory
RAM: physical addresses
Programs: virtual addresses
CPU
RAM
DISK
MMU

## Slide 27: DMA Example
DMA example: reading from audio (mic) input
  DMA engine on audio device… or I/O controller … or …
int dma_size = 4*PAGE_SIZE;
void *buf = alloc_dma(dma_size);
...
dev->mic_dma_baseaddr = virt_to_phys(buf);
dev->mic_dma_count = dma_len;
dev->cmd = DEV_MIC_INPUT | DEV_INTERRUPT_ENABLE | DEV_DMA_ENABLE;

## Slide 28: DMA Issues (1): Addressing
Issue #1: DMA meets Virtual Memory
RAM: physical addresses
Programs: virtual addresses
CPU
RAM
DISK
MMU
uTLB

## Slide 29: DMA Issues (2): Virtual Mem
Issue #2: DMA meets Paged Virtual Memory
DMA destination page may get swapped out
CPU
RAM
DISK

## Slide 30: DMA Issues (4): Caches
Issue #4: DMA meets Caching
DMA-related data could be cached in L1/L2
  DMA to Mem: cache is now stale
  DMA from Mem: dev gets stale data
CPU
RAM
DISK
L2

## Slide 31: DMA Issues (4): Caches
Issue #4: DMA meets Caching
DMA-related data could be cached in L1/L2
  DMA to Mem: cache is now stale
  DMA from Mem: dev gets stale data
CPU
RAM
DISK
L2

## Slide 32: Programmed I/O vs Memory Mapped I/O
Programmed I/O
  Requires special instructions
  Can require dedicated hardware interface to devices
  Protection enforced via kernel mode access to instructions
  Virtualization can be difficult
Memory-Mapped I/O
  Re-uses standard load/store instructions
  Re-uses standard memory hardware interface
  Protection enforced with normal memory protection scheme
  Virtualization enabled with normal memory virtualization scheme

## Slide 33: Polling vs. Interrupts
How does program learn device is ready/done?
1. Polling: Periodically check I/O status register
  Common in small, cheap, or real-time embedded systems
  Predictable timing, inexpensive
  Wastes CPU cycles
2. Interrupts: Device sends interrupt to CPU
  Cause register identifies the interrupting device
  Interrupt handler examines device, decides what to do
  Only interrupt when device ready/done
  Forced to save CPU context (PC, SP, registers, etc.)
  Unpredictable, event arrival depends on other devices’ activity
Clicker Question: Which is better?
Polling (B) Interrupts (C) Both equally good/bad

## Slide 34: I/O Takeaways
Diverse I/O devices require hierarchical interconnect which is more recently transitioning to point-to-point topologies.
Memory-mapped I/O is an elegant technique to read/write device registers with standard load/stores.
Interrupt-based I/O avoids the wasted work in polling-based I/O and is usually more efficient.
Modern systems combine memory-mapped I/O,
interrupt-based I/O, and direct-memory access
to create sophisticated I/O device subsystems.