## Slide 1: Architectural Support for Operating Systems
Prof. Sirer
CS 4410
Cornell University

## Slide 2: Basic Computer Organization
CPU
Memory
?

## Slide 3: Keyboard
Let’s build a keyboard
Reading input
  Mechanical switches
  Single pole, single throw
  Double pole, single throw
Digital processing
  Encoders, decoders, muxes, latches, tristate buffers, logic gates, …
SPST
DPST

## Slide 4: Keyboard
When a key is pressed, a 7-bit key identifier is computed
+
3-bit encoder
(4 to 3)
4-bit encoder
(16 to 4)
not all 16 wires are shown

## Slide 5: Keyboard
A latch can store the keystroke indefinitely
+
3-bit encoder
(4 to 3)
4-bit encoder
(16 to 4)
not all 16 wires are shown
Latch

## Slide 6: Keyboard
The keyboard can then appear to the CPU as if it is a special memory address
+
3-bit encoder
(4 to 3)
4-bit encoder
(16 to 4)
not all 16 wires are shown
Latch
CPU

## Slide 7: Device Interfacing Techniques
Memory-mapped I/O
  Device communication goes over the memory bus
  Reads/Writes to special addresses are converted into I/O operations by dedicated device hardware
  Each device appears as if it is part of the memory address space
Programmed I/O
  CPU has dedicated, special instructions
  CPU has additional input/output wires (I/O bus)
  Instruction specifies device and operation
Memory-mapped I/O is the predominant device interfacing technique in use

## Slide 8: Polling vs. Interrupts
In our design, the CPU constantly needs to read the keyboard latch memory location to see if a key is pressed
  Called polling
  Inefficient
An alternative is to add extra circuitry so the keyboard can alert the CPU when there is a keypress
  Called interrupt driven I/O
Interrupt driven I/O enables the CPU and devices to perform tasks concurrently, increasing throughput
  Only needs a tiny bit of circuitry and a few extra wires to implement the “alert” operation

## Slide 9: Interrupt Driven I/O
CPU
Memory
An interrupt controller mediates between competing devices
  Raises an interrupt flag to get the CPU’s attention
  Identifies the interrupting device
Can disable (aka mask) interrupts if the CPU so desires
intr
dev id
Interrupt Controller

## Slide 10: Interrupt Driven I/O
CPU
Memory
An interrupt controller mediates between competing devices
  Raises an interrupt flag to get the CPU’s attention
  Identifies the interrupting device
Can disable (aka mask) interrupts if the CPU so desires
intr

## Slide 11: Interrupt Management
Interrupt controllers manage interrupts
  Maskable interrupts: can be turned off by the CPU for critical processing
  Nonmaskable interrupts: signifies serious errors (e.g. unrecoverable memory error, power out warning, etc)
Interrupts contain a descriptor of the interrupting device
  A priority selector circuit examines all interrupting devices, reports highest level to the CPU
Interrupt controller implements interrupt priorities
  Can optionally remap priority levels

## Slide 12: Interrupt-driven I/O summary
Normal interrupt-driven operation with memory-mapped I/O proceeds as follows
  CPU initiates a device operation (e.g. read from disk) by writing an operation descriptor to a device register
  CPU continues its regular computation
  The device asynchronously performs the operation
  When the operation is complete, interrupts the CPU
This would incur high-overhead for moving bulk-data
  One interrupt per byte!

## Slide 13: Direct Memory Access (DMA)
Transfer data directly between device and memory
  No CPU intervention required for moving bits
Device raises interrupts solely when the block transfer is complete
Critical for high-performance devices

## Slide 14: Recap
We now have a basic computer system to which devices can be connected
How do we execute applications on this system?
  Applications are not necessarily trusted!

## Slide 15: Privilege Levels
Some processor functionality cannot be made accessible to untrusted user applications
  e.g. HALT, change MMU settings, set clock, reset devices, manipulate device settings, …
Need to have a designated mediator between untrusted/untrusting applications
  The operating system (OS)
Need to delineate between untrusted applications and OS code
  Use a “privilege mode” bit in the processor
  0 = Untrusted = user, 1 = Trusted = OS

## Slide 16: Privilege Mode
Privilege mode bit indicates if the current program can perform privileged operations
  On system startup, privilege mode is set to 1, and the processor jumps to a well-known address
  The operating system (OS) boot code resides at this address
  The OS sets up the devices, initializes the MMU, loads applications, and resets the privilege bit before invoking the application
Applications must transfer control back to OS for privileged operations

## Slide 17: Sample System Calls
Print character to screen
  Needs to multiplex the shared screen resource between multiple applications
Send a packet on the network
  Needs to manipulate the internals of a device whose hardware interface is unsafe
Allocate a page
  Needs to update page tables & MMU

## Slide 18: System Calls
A system call is a controlled transfer of execution from unprivileged code to the OS
  A potential alternative is to make OS code read-only, and allow applications to just jump to the desired system call routine. Why is this a bad idea?
A SYSCALL instruction transfers control to a system call handler at a fixed address

## Slide 19: SYSCALL instruction
SYSCALL instruction does an atomic jump to a controlled location
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value (= return address)
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel syscall handler
Kernel system call handler carries out the desired system call
  Saves callee-save registers
  Examines the syscall number
  Checks arguments for sanity
  Performs operation
  Stores result in v0
  Restores callee-save registers
  Performs a “return from syscall” instruction, which restores the privilege mode, SP and PC

## Slide 20: Libraries and Wrappers
Compilers do not emit SYSCALL instructions
  They do not know the interface exposed by the OS
Instead, applications are compiled with standard libraries, which provide “syscall wrappers”
  printf() -> write(); malloc() -> sbrk(); recv(); open(); close(); …
Wrappers are:
  written in assembler,
  internally issue a SYSCALL instruction,
  pass arguments to kernel,
  pass result back to calling application

## Slide 21: Typical Process Layout
Libraries provide the glue between user processes and the OS
  libc linked in with all C programs
  Provides printf, malloc, and a whole slew of other routines necessary for programs
OBJECT1
OBJECT2
Stack
Heap
Data
Text
HELLO WORLD
GO BIG RED CS!
printf(char * fmt, …) {
create the string to be printed
SYSCALL 80
}
malloc() { … }
strcmp() { … }
main() {
printf (“HELLO WORLD”);
printf(“GO BIG RED CS”);
!
Program
Library
Activation Records

## Slide 22: Full System Layout
The OS is omnipresent and steps in where necessary to aid application execution
  Typically resides in high memory
When an application needs to perform a privileged operation, it needs to invoke the OS
OBJECT1
OBJECT2
Stack
Heap
Data
HELLO WORLD
GO BIG RED CS!
printf(char * fmt, …) {
main() { … }
Program
Library
Activation Records
USER OBJECT1
OBJECT2
OS Stack
OS Heap
OS Data
LINUX
syscall_entry_point() { … }
OS Text
Kernel Activation Records

## Slide 23: Exceptional Situations
System calls are control transfers to the OS, performed under the control of the user application
Sometimes, need to transfer control to the OS at a time when the user program least expects it
  Division by zero,
  Alert from the power supply that electricity is about to go out,
  Alert from the network device that a packet just arrived,
  Clock notifying the processor that the clock just ticked,
Some of these causes for interruption of execution have nothing to do with the user application
Need a (slightly) different mechanism, that allows resuming the user application

## Slide 24: Interrupts & Exceptions
On an interrupt or exception
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value
  Saves the old privilege mode
  Saves cause of the interrupt/exception
  Sets the new privilege mode to 1
  Sets the new PC to the kernel interrupt/exception handler
Kernel interrupt/exception handler handles the event
  Saves all registers
  Examines the cause
  Performs operation required
  Restores all registers
  Performs a “return from interrupt” instruction, which restores the privilege mode, SP and PC

## Slide 25: Syscall vs. Interrupt
The differences lie in how they are initiated, and how much state needs to be saved and restored
Syscall requires much less state saving
  Caller-save registers are already saved by the application
Interrupts typically require saving and restoring the full state of the processor
  Because the application got struck by a lightning bolt without anticipating the control transfer

## Slide 26: Terminology
Trap
  Any kind of a control transfer to the OS
Syscall
  Synchronous, program-initiated control transfer from user to the OS to obtain service from the OS
  e.g. SYSCALL
Exception
  Asynchronous, program-initiated control transfer from user to the OS in response to an exceptional event
  e.g. Divide by zero, segmentation fault
Interrupt
  Asynchronous, device-initiated control transfer from user to the OS
  e.g. Clock tick, network packet

## Slide 27: Memory Protection
Some memory addresses need protection
  The OS text, data, heap and stack need to be protected from untrusted applications
  Some devices should be out of reach of applications
Memory Management Unit (MMU) aids with memory management
  Provides a virtual to physical address translation
  Examines every load/store/jump and ensures that applications remain within bounds using protection (RWX) bits associated with every page of memory
Modern architectures use a Translation Lookaside Buffer (TLB) for keeping track of virtual to physical mappings
  Software is invoked on a miss

## Slide 28: TLB Operation
TLB examines every virtual address uttered by the CPU, and if there is a match, and the permissions are appropriate, replaces the virtual page number with the physical page number
CPU
Memory
TLB
Vaddr
Paddr
RWX

## Slide 29: Atomic Instructions
Hardware needs to provide special instructions to enable concurrent programs to operate correctly