## Slide 1: The Evolution and Architecture of Modern Computers
Professor Ken Birman
CS4414 Lecture 2

## Slide 2: Idea Map for today
Goal: Learn just a little about NUMA architectures.
We are not trying to be an architecture course. But we do need to be able to visualize what we are “asking the hardware to do”
Computers are multicore NUMA machines capable of many forms of parallelism. They are extremely complex and sophisticated.
Individual CPUs don’t make this NUMA dimension obvious. The whole idea is that if you don’t want to know, you can ignore the presence of parallelism
Compiled languages are translated to machine language. Understanding this mapping will allow us to make far more effective use of the machine.

## Slide 3: What’s Inside? Architecture = components of a computer + operating System
CPU
Registers (L1 cache)
L2 Cache
CPU
Registers (L1 cache)
L2 Cache
L3 Cache
Memory Bus
Core
Core
PCIe Bus
SSD storage
100G Ethernet
Memory Unit (DRAM)
A BIG PILE OF HARDWARE REQUIRING A LOT OF HIGHLY SKILLED CARE AND FEEDING!

## Slide 4: What’s Inside? Architecture = components of a computer + operating System
CPU
Registers (L1 cache)
L2 Cache
CPU
Registers (L1 cache)
L2 Cache
L3 Cache
Memory Bus
Core
Core
PCIe Bus
SSD storage
100G Ethernet
Memory Unit (DRAM)

## Slide 5: What’s Inside? Architecture = components of a computer + operating System
Job of the operating system (e.g. Linux) is to manage the hardware and offer easily used, efficient abstractions that hide details where feasible
Operating System
File System
Network
Bash shell
Process you launched by running some program

## Slide 6: Architectures are changing rapidly!
As an undergraduate (in the late 1970’s) I programmed a DEC PDP 11/70 computer:
A CPU (~1/2 MIPS), main memory (4MB)
A storage device (8MB rotational magnetic disk), tape drive
I/O devices (mostly a keyboard with a printer).
At that time this cost about $100,000

## Slide 7: Architectures are changing rapidly!
As an undergraduate (in the late 1970’s) I programmed a DEC PDP 11/70 computer:
A CPU (~1/2 MIPS), main memory (4MB)
A storage device (8MB rotational magnetic disk), tape drive
I/O devices (mostly a keyboard with a printer).
At that time this cost about $100,000
Bill Gates: “640K ought to be enough for anybody.”

## Slide 8: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C/C++, assembly, machine code

## Slide 9: Modern Computer: Dell R-740: $2,600
2 Intel Xenon chips with 28 “hyperthreaded” cores running at 1GIPS (clock rate is 3Ghz)
Up to 3 TB of memory, multiple levels of memory caches
All sorts of devices accessible directly or over the network
NVIDIA Tesla T4 GPU: adds $6,000, peaks at 269 TFLOPS

## Slide 10: Modern Computer: Dell R-740: $2,600
2 Intel Xenon chips with 28 “hyperthreaded” cores running at 1GIPS (clock rate is 3Ghz)
Up to 3 TB of memory, multiple levels of memory caches
All sorts of devices accessible directly or over the network
NVIDIA Tesla T4 GPU: adds $6,000, peaks at 269 TFLOPS
One CPU core actually runs two programs at the same time

## Slide 11: Intel Xenon NVIDIA TESLA
Each core is like a little computer, talking to the others over an on-chip network (the CMS)
The GPU has so many cores that a photo of the chip is pointless. Instead they draw graphics like these to help you visualize ways of using hundreds of cores to process a tensor (the “block” in the middle) in parallel!

## Slide 12: Intel Core 200 Series
Will be released in October 2024.
24 cores, split into 8 “performance” (P) cores that use a lot of power but can do many very demanding computations rapidly, and 16 “efficiency” (E) cores, that are slower but use less power.
Researchers will have fun inventing schedulers that can be smart about which core to run each task on!

## Slide 13: How did we get here?
In the early years of computing, we went from machines built from distinct electronic components (earliest generations) to ones built from integrated circuits with everything on one chip.
Quickly, people noticed that each new generation of computer had roughly double the capacity of the previous one and could run roughly twice as fast! Gordon Moore proposed this as a “law”.

## Slide 14: But by 2006 Moore’s Law seemed to be ending

## Slide 15: What ended Moore’s Law?
To run a chip at higher and higher speeds, we use a faster clock rate and keep more of the circuitry busy.
Computing is a form of “work” and work generates heat… as roughly the square of the clock rate.
Chips began to fail. Some would (literally) melt or catch fire!
If you overclock your desktop this can happen…

## Slide 16: But parallelism saved us!
A new generation of computers emerged in which we ran the clocks at a somewhat lower speed (usually around 2 GHz, which corresponds to about 1 billion instructions per second), but had many CPUs in each computer.
A computer needs to have nearby memory, but applications needed access to “all” the memory. This leads to what we call a “non-uniform memory access behavior”: NUMA.

## Slide 17: Moore’s Law with NUMA
Graph from prior slide

## Slide 18: … making modern machines complicated!
Prior to 2006, a good program
Used the best algorithm: computational complexity, elegance
Implemented it in a language like C++ that offers efficiency
Ran on one machine
But the past decade has been disruptive! Suddenly even a single computer might have the ability to do hundreds of parallel tasks!

## Slide 19: The Hardware shapes the Application Design process
We need to ask how a NUMA architecture impacts our designs.
If not all variables are equally fast to access, how can we “code” to achieve the fastest solution?
And how do we keep all of this hardware “optimally busy”?

## Slide 20: Definitions of terms we often use
Architecture: (also ISA: instruction set architecture) The parts of a processor design that one needs to understand for writing correct machine/assembly code
  Examples: instruction set specification, registers
  Machine Code: Byte-level programs a processor executes
  Assembly Code: Readable text representation of machine code

## Slide 21: Definitions of terms we often use
Microarchitecture: “drill down”.
Details or implementation of the architecture
  Examples: memory or cache sizes, clock speed (frequency)
Example ISAs:
  Intel: x86, IA32, Itanium, x86-64
  ARM: Used in almost all mobile phones
  RISC V: New open-source ISA

## Slide 22: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C/C++, assembly, machine code

## Slide 23: How a single thread computes
In CS4414 we think of each computation in terms of a “thread”
A thread owns a pointer into the program instructions. The CPU loads the instruction that the “PC” points to, fetches any operands from memory, does the action, saves the results back to memory.
Then the PC is incremented to point to the next instruction
Common way to depict a single thread

## Slide 24: Assembly/Machine Code View
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
Memory
    Byte addressable array
    Code and user data
    Stack to support procedures
Puzzle:
    On a NUMA machine, a CPU is near a fast memory but can access all memory.
    How does this impact software design?

## Slide 25: Assembly/Machine Code View
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
Memory
    Byte addressable array
    Code and user data
    Stack to support procedures
Puzzle:
    On a NUMA machine, a CPU is near a fast memory but can access all memory.
    How does this impact software design?
This memory is slower to access!
Same with this one…
…
…
…
Example: With 6 on-board DRAM modules and 12 NUMA CPUs, each pair of CPUs has one nearby DRAM module. Memory in that range of addresses will be very fast. The other 5 DRAM modules are further away. Data in those address ranges is visible and everything looks identical, but access is slower!

## Slide 26: Linux tries to hide memory delays
If it runs thread t on core k, Linux tries to allocate memory for t (stack, malloc…) in the DRAM close to that k.
Yet all memory operations work identically even if the thread is actually accessing some other DRAM. They are just slower.
Linux doesn’t even tell you which parts of your address space are mapped to which DRAM units.

## Slide 27: Machine Language
(We’ll cover what we can but probably won’t have time for all of this)

## Slide 28: The hardware understands “primitive” data types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes (new: 4-bit, 8-bit, 16-bit)
Code: Byte sequences encoding series of instructions
(SIMD vector data types of 8, 16, 32 or 64 bytes)
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory
  Example: Raw images are arrays in a format defined by the camera or video, such as RGB, jpeg, mpeg. The camera understands the format. The host computer the camera is attached to just sees bytes

## Slide 29: The hardware understands “primitive” data types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes (new: 4-bit, 8-bit, 16-bit)
Code: Byte sequences encoding series of instructions
(SIMD vector data types of 8, 16, 32 or 64 bytes)
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory
  Example: Raw images are arrays in a format defined by the camera or video, such as RGB, jpeg, mpeg. The camera understands the format. The host computer the camera is attached to just sees bytes

## Slide 30: x86-64 Integer Registers
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
  Not part of memory (or cache)

## Slide 31: Some History: IA32 Registers

## Slide 32: Assembly Characteristics: Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches
  Indirect branches

## Slide 33: Moving Data
Moving Data
  movq Source, Dest
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “addressing modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN
Warning: Intel docs use mov Dest, Source

## Slide 34: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C/C++ Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest

## Slide 35: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 36: Example of Simple Addressing Modes
whatAmI:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret
void
whatAmI(<type> a, <type> b)
{
????
}
%rdi
%rsi

## Slide 37: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 38: Understanding swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers
xp
Addr
yp

## Slide 39: Understanding swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 40: Understanding swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 41: Understanding swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 42: Understanding swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 43: Understanding swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 44: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 45: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 46: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 47: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 48: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C/C++, assembly, machine code

## Slide 49: Address Computation Instruction
leaq Src, Dst
  Src is address mode expression
  Set Dst to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t = x+2*x
salq $2, %rax # return t<<2
Converted to ASM by compiler:

## Slide 50: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    shlq Src,Dest Dest = Dest << Src Synonym: salq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order! Src,Dest (Warning: very old Intel docs use “op Dest,Src”)
No distinction between signed and unsigned int (why?)

## Slide 51: Some Arithmetic Operations
One Operand Instructions
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
    notq Dest Dest = ~Dest
See book for more instructions
  Depending how you count, there are 2,034 total x86 instructions
  (If you count all addr modes, op widths, flags, it’s actually 3,683)

## Slide 52: Arithmetic Expression Example
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    Curious: only used once…
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret
Notes: (rsi,rsi,2) = 3y; 3y << 4 == 3y * 16 = 48y

## Slide 53: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z, t4
%rax | t1, t2, rval
%rcx | t5

## Slide 54: Evolution of Intel Instruction Set
The Intel instruction set has changed over the decades since it was first introduced.
Intel is a believer in the “CISC” model: complex instructions that are highly optimized
Modern example: vector parallel instructions (also called SIMD: Single instruction, multiple data). Introduced to make the x86 more competitive with GPU accelerators
  Such as “Multiply these two vectors and put the result in this third vector”, or “sum up the elements in this vector, and put the result here.”
  The underlying hardware uses parallel processing to do the job faster.
  The C++ compiler can recognize many of these patterns and will emit vector parallel instructions (if the target computer supports them). You can also provide “hints” to the compiler, to do so.
There are many more examples; we will see a few later in the semester

## Slide 55: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C/C++, assembly, machine code

## Slide 56: Turning C/C++ into Object Code
text
text
binary
binary
Compiler (c++)
Assembler (c++ or as)
Linker (c++ or ld)
C/C++ program (p1.cpp p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.cpp p2.c
  Compile with command: c++ pp1.cpp p2.c -o p
    There are often additional arguments such as –O3, -pg, -g…
    Put resulting binary in file p

## Slide 57: Compiling Into Assembly
C/C++ Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Obtain with command
  C++ sum.c
Produces file sum.s
This uses the “indirect” addressing mode: dest holds a memory address and *dest is a long integer at that address. We are using that location as a variable here!

## Slide 58: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore

## Slide 59: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore
Things that look weird and are preceded by a ‘.’ are generally directives.
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret

## Slide 60: Assembly Characteristics: Data Types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
(SIMD vector data types of 8, 16, 32 or 64 bytes)
Code: Byte sequences encoding series of instructions
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 61: Assembly Characteristics: Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches

## Slide 62: Object Code
Code for sumstore
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    e.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 14 bytes
  Each instruction 1, 3, or 5 bytes
  Starts at address 0x0400595

## Slide 63: Machine Instruction Example
C Code
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Object Code
  3-byte instruction
  Stored at address 0x40059e
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 64: Disassembling Object Code
Disassembled
Disassembler
  objdump –d sum
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
0000000000400595 <sumstore>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 65: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore