## Slide 1: Images have structure at various scales

## Slide 2: Frequency
Frequency of a signal is how fast it changes
  Reflects scale of structure

## Slide 3: A combination of frequencies
0.1 X
0.3 X
0.5 X
+
+
=

## Slide 4: Fourier transform
Can we figure out the canonical single-frequency signals that make up a complex signal?
  Yes!
Can any signal be decomposed in this way?
  Yes!

## Slide 5: Fourier transform for periodic signals
Suppose x is periodic with period T
All components must be periodic with period T/k for some integer k
  Only frequencies are of the form k/T
Thus:
Given a signal x(t), Fourier transform gives us the coefficients ak (we will denote these as X[k])
”Pure” signal

## Slide 6: Fourier transform for aperiodic signals
What if signal is not periodic?
Can still decompose into sines and cosines!
But no restriction on frequency
Now need a continuous space of frequencies
Fourier transform gives us the function X(v)
”Pure” signal

## Slide 7: Fourier transform
Note: X can in principle be complex: we often look at the magnitude |X(v)|

## Slide 8
Time
Frequency
Why is there a peak at 0?

## Slide 9: Fourier transform

## Slide 10: Dual domains
Signal: time domain (or spatial domain)
Fourier Transform: Frequency domain
  Amplitudes are called spectrum
For any transformations we do in time domain, there are corresponding transformations we can do in the frequency domain
And vice-versa
Spatial Domain

## Slide 11: Dual domains
Convolution in time domain = Point-wise multiplication in frequency domain
Convolution in frequency domain = Point-wise multiplication in time domain

## Slide 12: Proof (if curious)

## Slide 13: Properties of Fourier transforms

## Slide 14: Back to 2D images
Images are 2D signals
Discrete, but consider as samples from continuous function
Signal: f(x,y)
Fourier transform F(vx, vy): contribution of a “pure” signal with frequency vx in x and vy in y

## Slide 15: Back to 2D images

## Slide 16: Signals and their Fourier transform
Spatial
Sine
Gaussian
Box
Frequency
Impulse
Gaussian
Sinc

## Slide 18: The Gaussian special case
Fourier transform of a Gaussian is a gaussian

## Slide 19: Sharp discontinuities require very high frequencies

## Slide 20: Duality
Since Fourier and inverse Fourier look so much alike:
  Fourier transform of sinc is box
  Fourier transform of impulse is sine

## Slide 21: Why talk about Fourier transforms?
Convolution is point-wise multiplication in frequency space
  Analyze which frequency components a particular filter lets through, e.g., low-pass, high-pass or band-pass filters
  Leads to fast algorithms for convolution with large filters: Fast FFT

## Slide 22: Why talk about Fourier transforms
Frequency space reveals structure at various scales
  Noise is high-frequency
  ”Average brightness” is low-frequency
Useful to understand how we resize/resample images
  Sampling causes information loss
  What is lost exactly?
  What can we recover?

## Slide 23: Fourier transforms from far away
Fourier transforms are basically a “change of basis”
Instead of representing image as “the value of each pixel”,
Represent image as “how much of each frequency component”
“Frequency components” are intuitive: slowly-changing or fast-changing images

## Slide 24
”The cat has some serious periodic components.”
https://xkcd.com/26/

## Slide 25: Resizing and resampling

## Slide 26: Let’s enhance!
Louis Daguerre, 1838

## Slide 27: Let’s enhance!
When is enhancement possible?
How can we model what happens when we upsample or downsample an image?
Resizing up or down very common operation
  Searching across scales
  applications have different memory/quality tradeoffs

## Slide 28: What is a (digital) image?
True image is a function from R2 to R
Digital image is a sample from it
1D example:
To enhance, we need to recover the original signal and sample again

## Slide 29: Undersampling
© Kavita Bala, Computer Science, Cornell University

## Slide 30: Undersampling
What if we “missed” things between the samples?
Simple example: undersampling a sine wave
  unsurprising result: information is lost
  surprising result: indistinguishable from lower frequency
  also was always indistinguishable from higher frequencies
  aliasing: signals “traveling in disguise” as other frequencies

## Slide 31: Aliasing
© Kavita Bala, Computer Science, Cornell University
When sampling is not adequate, impossible to distinguish between low and high frequency signal

## Slide 32: Aliasing in time

## Slide 33: Aliasing in time

## Slide 34
Cornell CS4620 Fall 2015 • Lecture 23
Point sampling
in action

## Slide 35: How many samples do we need?
1 sample per time period is too less:

## Slide 36: How many samples do we need?
2 samples per time-period is enough
Nyquist sampling theorem: Need to sample at least 2 times the frequency
General signals? Need to sample at least 2 times the maximum frequency

## Slide 37: Nyquist sampling: why?
Sampling = Keep values at , make everything else 0
Sampling = Make frequency domain periodic with period by making copies
Spatial domain
Frequency domain

## Slide 38: Nyquist sampling: why?

## Slide 39: Nyquist sampling: why?

## Slide 40: How to subsample correctly
Nyquist says must sample at at least twice maximum frequency
What if signal has high frequencies?
Eliminate them before sampling!
  Convert to frequency space
  Multiply with band-pass filter

## Slide 41: Eliminating High Frequencies
© Kavita Bala, Computer Science, Cornell University

## Slide 42: Process
Can we do this in spatial domain?
  Yes!
Multiplication in frequency domain = convolution in spatial domain
Box filter in frequency domain = sinc in spatial domain
Multiplication with box filter in frequency domain = convolution with sinc filter in spatial domain

## Slide 43: Reconstruction from samples
Sampling = Keep values at , make everything else 0
Sampling = Make frequency domain periodic with period by making copies
Spatial domain
Frequency domain

## Slide 44: Reconstruction from samples
Box filter in frequency space

## Slide 45: Reconstruction from samples
Multiplication in frequency domain = convolution in spatial domain
Box filter in frequency domain = sinc filter in spatial domain
Convolve sampled signal with sinc filter to reconstruct

## Slide 46: Reconstruction from samples
”Sampled signal” is non-zero at sample points and 0 everywhere else
  i.e., has holes
*

## Slide 47: Recap: subsampling and reconstruction
Subsampling
Convolve with sinc filter to eliminate high frequencies
Sample by picking only values at sample points
Reconstruction
Start with sampled signal (0 at non-sample points)
Convolve with sinc to reconstruct

## Slide 48: Sinc is annoying

## Slide 49: Sinc and Gaussian
Sinc is annoying: infinite spatial extent
Use Gaussian instead!
Spatial domain
Frequency domain
Sinc/box
Gaussian

## Slide 50: Subsampling images
Step 1: Convolve with Gaussian to eliminate high frequencies
Step 2: Drop unneeded pixels
Subsampling without removing high frequencies
Subsampling after removing high frequencies

## Slide 51: Upsampling images
Step 1: blow up to original size with 0’s in between

## Slide 52: Upsampling images
Step 2: Convolve with Gaussian

## Slide 53: Take-away
Subsampling causes aliasing
  High frequencies masquerading as low frequencies
Remove low frequencies by blurring!
  Ideal: sinc
  Common: Gaussian
When upsampling, reconstruct missing values by convolution
  Ideal: sinc
  Common: Gaussian

## Slide 54: So… can we enhance?
Nyquist theorem limits frequencies we can reconstruct from subsampled image
Can only reconstruct max sampling frequency/2
Sorry CSI!