## Slide 1: Pyramids

## Slide 2: Gaussian pre-filtering
Solution: filter the image, then subsample
blur
F0 H
*
subsample
blur
subsample
…
F1
F1 H
*
F2
F0

## Slide 3
blur
F0 H
*
subsample
blur
subsample
…
F1
F1 H
*
F2
F0
{
Gaussian pyramid

## Slide 4: Gaussian pyramids [Burt and Adelson, 1983]
In computer graphics, a mip map [Williams, 1983]
Gaussian Pyramids have all sorts of applications in computer vision
Source: S. Seitz

## Slide 5: Gaussian pyramids - Searching over scales

## Slide 6: Gaussian pyramids - Searching over scales

## Slide 7
The Gaussian Pyramid
High resolution
Low resolution
blur
blur
blur
sub-sample
sub-sample
sub-sample
blur
sub-sample

## Slide 8: Gaussian pyramid and stack
Source: Forsyth

## Slide 9: Memory Usage
What is the size of the pyramid?
Notes: 4/3

## Slide 10: Laplacian pyramid
Re-duce
Expand (upsample + blur)
=
Expand (upsample + blur)
-
Expand (upsample + blur)
Expand (upsample + blur)
-
-
=
=
=
-

## Slide 11: Laplacian pyramid
L3 = G3 - expand(G4) =
L2 = G2 - expand(G3) =
L1 = G1 - expand(G2) =
L0 = G0 - expand(G1) =
L4 = G4 =

## Slide 12: Reconstructing the image from a Laplacian pyramid
Expand (upsample + blur)
=
Expand (upsample + blur)
+
Expand (upsample + blur)
Expand (upsample + blur)
+
+
=
=
=
+

## Slide 13: Laplacian pyramid
Source: Forsyth

## Slide 14: Edge detection

## Slide 15: Why edges?
Resilience to lighting and color
  useful for recognition, matching patches across images

## Slide 16: Why edges?
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAA
Humans are sensitive to edges
Convert a 2D image into a set of curves
  Extracts salient features of the scene, more compact

## Slide 17: Why edges?
Cue to shape and geometry
  useful for recognition, understanding 3D structure
Credit: Jitendra Malik
Credit: Attneave

## Slide 18: Why edges?
Grouping pixels into objects (“perceptual organization”)

## Slide 19: This lecture
Edge detection in general
Edge detection for grouping

## Slide 20: Edges
Edges are curves in the image, across which the brightness changes “a lot”
Corners/Junctions
Notes: Reflctance edges
Shadow edges
Depth edges
Normal edges

## Slide 21: Aside

## Slide 22: Closeup of edges
Source: D. Hoiem

## Slide 23: Closeup of edges
Source: D. Hoiem

## Slide 24: Closeup of edges
Source: D. Hoiem

## Slide 25: Closeup of edges
Source: D. Hoiem

## Slide 26: Characterizing edges
An edge is a place of rapid change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative
Source: L. Lazebnik

## Slide 27: Intensity profile
Source: D. Hoiem

## Slide 28: Derivatives and convolution
Differentiation is linear
Differentiation is shift-invariant
  Derivative of shifted signal is shifted derivative
Hence, differentiation can be represented as convolution!

## Slide 29: Image derivatives
How can we differentiate a digital image F[x,y]?
  Option 1: reconstruct a continuous image, f, then compute the derivative
  Option 2: take discrete derivative (finite difference)
1 | -1 | 
How would you implement this as a linear filter?
 | -1 | 
 | 1 | 
:
:
Source: S. Seitz
Notes: give definition of partial derivative: lim h->0 [f(x+h,y) – f(x,y)]/h

## Slide 30: Image gradient
The gradient points in the direction of most rapid increase in intensity
The gradient of an image:
The edge strength is given by the gradient magnitude:
The gradient direction is given by:
  how does this relate to the direction of the edge?
Source: Steve Seitz
Notes: give definition of partial derivative: lim h->0 [f(x+h,y) – f(x,y)]/h
Gradient direction perpendicular to edge direction

## Slide 31: Image gradient
Source: L. Lazebnik
Notes: Top right: gradient magnitude
x, y

## Slide 32: With a little Gaussian noise
Gradient
Source: D. Hoiem

## Slide 33: Effects of noise
Where is the edge?
Source: S. Seitz
Noisy input image
Notes: How to fix?

## Slide 34: Effects of noise
Noise is high frequency
Differentiation accentuates noise

## Slide 35: Solution: smooth first
f
h
f * h
Source: S. Seitz
To find edges, look for peaks in

## Slide 36: Associative property of convolution
Differentiation is a convolution
Convolution is associative:
This saves us one operation:
f
Source: S. Seitz

## Slide 37: 2D edge detection filters
Gaussian
derivative of Gaussian (x)
Notes: How many 2nd derivative filters are there? There are four 2nd partial derivative filters.
In practice, it’s handy to define a single 2nd derivative filter—the Laplacian

## Slide 38: Derivative of Gaussian filter
x-direction
y-direction

## Slide 40: Two Dimensional Gaussian

## Slide 41: Oriented Gaussian First and Second Derivatives

## Slide 42: Grouping

## Slide 43: What is grouping?

## Slide 44: Why grouping?
Pixels property of sensor, not world
Reasoning at object level (might) make things easy:
  objects at consistent depth
  objects can be recognized
  objects move as one
"I stand at the window and see a house, trees, sky. Theoretically I might say there were 327 brightnesses and nuances of colour. Do I have "327"? No. I have sky, house, and trees."
Max Wertheimer

## Slide 45: Regions Boundaries

## Slide 46: Is grouping well-defined?
Depends on purpose
  Object parts
  Background segmentation
A
B
C

## Slide 47: Is grouping well-defined?
A
B
C
Image
BG
L-bird
R-bird
grass
bush
head
eye
beak
far
body
head
eye
beak
body
Perceptual organization forms a tree:
B
A
C
D. Martin, C. Fowlkes, D. Tal, J. Malik. "A Database of Human Segmented Natural Images and its Application to Evaluating Segmentation Algorithms and Measuring Ecological Statistics", ICCV, 2001

## Slide 48: How do we group things?
Gestalt principles
Principle of proximity
https://courses.lumenlearning.com/wsu-sandbox/chapter/gestalt-principles-of-perception/

## Slide 49: How do we group things?
Gestalt principles
Principle of similarity
https://courses.lumenlearning.com/wsu-sandbox/chapter/gestalt-principles-of-perception/

## Slide 50: How do we group things?
Gestalt principles
Principle of continuity and closure
https://courses.lumenlearning.com/wsu-sandbox/chapter/gestalt-principles-of-perception/

## Slide 51: How do we group things?
Gestalt principles
Principle of common fate

## Slide 52: Gestalt principles in the context of images
Principle of proximity: nearby pixels are part of the same object
Principle of similarity: similar pixels are part of the same object
  Look for differences in color, intensity, or texture across the boundary
Principle of closure and continuity: contours are likely to continue
High-level knowledge?

## Slide 53: Regions Boundaries

## Slide 54: Designing a good boundary detector
Differences in color, intensity, or texture across the boundary
Continuity and closure
High-level knowledge

## Slide 55: Criteria for a good boundary detector
Criteria for a good boundary detector:
  Good detection: Fire only on real edges, not anywhere else
  Good localization
    the edges detected must be as close as possible to the true edges
    the detector must return one point only for each true edge point
Source: L. Fei-Fei

## Slide 56: Canny edge detector
The classic edge detector
Baseline for all later work on grouping
Theoretical model: step-edges corrupted by additive Gaussian noise
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.
Source: L. Fei-Fei
22,000 citations!

## Slide 57: Example
original image

## Slide 58: Compute Gradients (DoG)
X-Derivative of Gaussian
Y-Derivative of Gaussian

## Slide 59: Gradient magnitude and orientation
Orientation is undefined at pixels with 0 gradient
Orientation
theta = numpy.arctan2(gy, gx)
Magnitude

## Slide 60: Non-maximum suppression for each orientation
At q, we have a maximum if the value is larger than those at both p and at r. Interpolate to get these values.
Source: D. Forsyth

## Slide 61: Before Non-max Suppression

## Slide 62
After Non-max Suppression

## Slide 63: Hysteresis thresholding
Threshold at low/high levels to get weak/strong edge pixels
Do connected components, starting from strong edge pixels

## Slide 64: Final Canny Edges

## Slide 65: Canny edge detector
Filter image with x, y derivatives of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression:
  Thin multi-pixel wide “ridges” down to single pixel width
Thresholding and linking (hysteresis):
  Define two thresholds: low and high
  Use the high threshold to start edge curves and the low threshold to continue them
Source: D. Lowe, L. Fei-Fei

## Slide 66: Does Canny always work?

## Slide 67: The challenges of edge detection
Texture
Low-contrast boundaries