## Slide 1: Lecture 2: Image filtering

## Slide 2: What is an image?
A grid (matrix) of intensity values
(common to use one byte per value: 0 = black, 255 = white)
=
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 20 | 0 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 75 | 75 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 75 | 95 | 95 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 96 | 127 | 145 | 175 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 175 | 175 | 175 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 47 | 255 | 255
255 | 255 | 127 | 145 | 145 | 175 | 127 | 127 | 95 | 47 | 255 | 255
255 | 255 | 74 | 127 | 127 | 127 | 95 | 95 | 95 | 47 | 255 | 255
255 | 255 | 255 | 74 | 74 | 74 | 74 | 74 | 74 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255

## Slide 3: Images as functions
An image contains discrete numbers of pixels
Pixel value
  grayscale/intensity
    [0,255]
  Color
    RGB [R, G, B], where [0,255] per channel
    Lab [L, a, b]: Lightness, a and b are color-opponent dimensions
    HSV [H, S, V]: Hue, saturation, value

## Slide 4: Images as functions
Can think of image as a function, f, from R2 to R or RM:
  Grayscale: f (x,y) gives intensity at position (x,y)
    f: [a,b] x [c,d] [0,255]
  Color: f (x,y) = [r(x,y), g(x,y), b(x,y)]

## Slide 5: What is an image?
  A digital image is a discrete (sampled, quantized) version of this function
x
y
f (x, y)

## Slide 6: Image transformations
  g (x,y) = f (x,y) + 20
  g (x,y) = f (-x,y)

## Slide 7
Super-resolution
Noise reduction

## Slide 8: Image denoising

## Slide 9: Why would images have noise?
Sensor noise
  Sensors count photons: noise in count
Dead pixels
Old photographs
…

## Slide 10: What is an image?
A grid (matrix) of intensity values: 1 color or 3 colors
(common to use one byte per value: 0 = black, 255 = white)
=
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 20 | 0 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 75 | 75 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 75 | 95 | 95 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 96 | 127 | 145 | 175 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 175 | 175 | 175 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 47 | 255 | 255
255 | 255 | 127 | 145 | 145 | 175 | 127 | 127 | 95 | 47 | 255 | 255
255 | 255 | 74 | 127 | 127 | 127 | 95 | 95 | 95 | 47 | 255 | 255
255 | 255 | 255 | 74 | 74 | 74 | 74 | 74 | 74 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255

## Slide 11: An assumption about noise
Let us assume noise at a pixel is
  independent of other pixels
  distributed according to a Gaussian distribution
    i.e., low noise values are more likely than high noise values
    “grainy images”

## Slide 12: Noise reduction
Nearby pixels are likely to belong to same object
  thus likely to have similar color
Replace each pixel by average of neighbors

## Slide 13: Mean filtering
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
(0 + 0 + 0 + 10 + 40 + 0 + 10 + 0 + 0)/9 = 6.66

## Slide 14: Mean filtering
(0 + 0 + 0 + 0 + 0 + 10 + 0 + 0 + 0 + 0 + 20 + 10 + 40 + 0 + 0 + 20 + 10 + 0 + 0 + 0 + 30 + 20 + 10 + 0 + 0)/25 = 6.8
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0

## Slide 15: Mean filtering
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
(0 + 0 + 0 + 0 + 0 + 0 + 0 + 0 + 10)/9 = 1.11
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 16: Mean filtering
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
(0 + 0 + 0 + 0 + 0 + 10 + 0 + 10 + 20)/9 = 4.44
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 17: Mean filtering
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 4 | 8 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
(0 + 0 + 0 + 0 + 10 + 10 + 10 + 20 + 20)/9 = 7.77

## Slide 18: Mean filtering
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 4 | 8 | 10 | 8 | 9 | 6 | 4 | 0
0 | 4 | 11 | 13 | 16 | 11 | 12 | 7 | 4 | 0
0 | 6 | 14 | 19 | 23 | 19 | 18 | 10 | 6 | 0
0 | 8 | 18 | 23 | 28 | 23 | 17 | 8 | 2 | 0
0 | 8 | 16 | 26 | 31 | 30 | 20 | 10 | 3 | 0
0 | 10 | 18 | 27 | 29 | 27 | 17 | 8 | 2 | 0
0 | 8 | 14 | 22 | 22 | 20 | 11 | 8 | 3 | 0
0 | 4 | 11 | 17 | 17 | 12 | 6 | 4 | 2 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 19: Noise reduction using mean filtering

## Slide 20: Filters
Filtering
  Form a new image whose pixels are a combination of the original pixels
Why?
  To get useful information from images
    E.g., extract edges or contours (to understand shape)
  To enhance the image
    E.g., to blur to remove noise
    E.g., to sharpen to “enhance image” a la CSI

## Slide 21: Mean filtering
Replace pixel by mean of neighborhood
5
1
4
1
7
1
5
3
10
Local image data
f
4.1
Modified image data
S[f]

## Slide 22: A more general version
5
1
4
1
7
1
5
3
10
Local image data
7
Kernel / filter

## Slide 23: A more general version
Local image data
Kernel size = 2k+1
0 | 10 | 5 | 7 | 0
5 | 11 | 6 | 8 | 3
9 | 22 | 4 | 5 | 1
2 | 9 | 14 | 6 | 7
3 | 10 | 15 | 12 | 9
 |  | 7 |  | 

## Slide 24: A more general version
w(i,j) = 1/(2k+1)2 for mean filter
If w(i,j) >=0 and sum to 1, weighted mean
But w(i,j) can be arbitrary real numbers!

## Slide 25: Properties: Linearity

## Slide 26: Properties: Linearity

## Slide 27: Properties: Linearity

## Slide 28: Properties: Linearity

## Slide 29: Properties: Shift invariance
f
f’

## Slide 30: Shift invariance

## Slide 31: Shift invariance
Shift, then convolve = convolve, then shift
Output of convolution does not depend on where the pixel is
f
f’

## Slide 32: Convolution and cross-correlation
Cross correlation
Convolution

## Slide 33: Cross-correlation
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
1*1 + 2*2 + 3*3 + 4*4 + 5*5 + 6*6 + 7*7 + 8*8 + 9*9
w
f

## Slide 34: Convolution
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
1*9 + 2*8 + 3*7 + 4*6 + 5*5 + 6*4 + 7*3 + 8*2 + 9*1
w
f

## Slide 35: Convolution
Adapted from F. Durand

## Slide 36: Filters: examples
1
1
1
1
1
1
1
1
1
Blur (with a mean filter) (g)
Source: D. Lowe
*
=
Original (f)
Kernel (k)

## Slide 37: Filters: examples
0
0
0
0
1
0
0
0
0
Original (f)
Identical image (g)
Source: D. Lowe
*
=
Kernel (k)

## Slide 38: Sharpening
Source: D. Lowe

## Slide 39: Sharpening
What does blurring take away?
–
=
Let’s add it back:
original
detail
+ α
=

## Slide 40: Sharpening

## Slide 41: Sharpening
What does blurring take away?
–
=
Let’s add it back:
original
detail
+ α
=

## Slide 42: Sharpening
1
1
1
1
1
1
1
1
1
0
0
0
0
1
0
0
0
0

## Slide 43: Sharpening filter
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter (accentuates edges)
Source: D. Lowe
=
*

## Slide 44: Another example
-1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
1 | 1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
1 | 1 | 1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
1 | 1 | 1 | 1 | -1 | -1 | -1 | -1 | -1 | -1 | -1
1 | 1 | 1 | 1 | 1 | -1 | -1 | -1 | -1 | -1 | -1
1 | 1 | 1 | 1 | 1 | 1 | -1 | -1 | -1 | -1 | -1
1 | 1 | 1 | 1 | 1 | 1 | 1 | -1 | -1 | -1 | -1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | -1 | -1 | -1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | -1 | -1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | -1

## Slide 45: Another example

## Slide 46: Convolution is everywhere
Horse

## Slide 47: Why is convolution important?
Shift invariance is a crucial property

## Slide 48: Why is convolution important?
We like linearity
  Linear functions behave predictably when input changes
  Lots of theory just easier with linear functions
All linear shift-invariant systems can be expressed as a convolution

## Slide 49: Non-linear filters: Thresholding

## Slide 50: Non-linear filters: Rectification
g(m,n) = max(f(m,n), 0)
Crucial component of modern convolutional networks

## Slide 51: Non-linear filters
Sometimes mean filtering does not work

## Slide 52: Non-linear filters
Sometimes mean filtering does not work

## Slide 53: Non-linear filters
Mean is sensitive to outliers
Median filter: Replace pixel by median of neighbors

## Slide 54: Non-linear filters

## Slide 55: Takeaway
Two general recipes:
  convolution
  cross-correlation
Properties
  Shift-invariant: a sensible thing to require
  Linearity: convenient
Can be used for smoothing, sharpening
Also main component of CNNs

## Slide 56: Next up
Back to linear filters
Signal processing view of filtering
Filtering for detecting edges etc

## Slide 57: Images as functions
An image contains discrete numbers of pixels
Pixel value
  grayscale/intensity
    [0,255]
  Color
    RGB [R, G, B], where [0,255] per channel

## Slide 58: Images as functions
Can think of image as a function, f, from R2 to R or RM:
  Grayscale: f (x,y) gives intensity at position (x,y)
    f: [a,b] x [c,d] [0,255]
  Color: f (x,y) = [r(x,y), g(x,y), b(x,y)]
Most adjacent pixels are correlated => function is continuous

## Slide 59: What is an image?
  A digital image is a discrete (sampled, quantized) version of this function
x
y
f (x, y)