## Slide 1: Resizing and resampling

## Slide 2: Aliasing
Images are made up of high frequency and low frequency components
High frequency components: pixel-to-pixel details
Low frequency components: high-level structure
What subsampling should do: remove pixel-to-pixel details, keep high-level structure
What naïve subsampling does: converts pixel-to-pixel details to new coarse structures  problem

## Slide 3: Aliasing

## Slide 4: Aliasing
Aliasing artifacts

## Slide 5: Image sub-sampling
1/4 (2x zoom)
1/16 (4x zoom)
Why does this look so crufty? Aliasing!
1/2
Source: S. Seitz

## Slide 6: How to avoid aliasing
To recover a sinusoid, need to sample at least twice per cycle
For a general image, need to sample at least twice the rate of the highest frequency component
Nyquist sampling theorem:
To subsample, remove high frequency components
To remove high frequency components, blur the image with a Gaussian

## Slide 7
Image
Fourier spectrum
Gaussian filters
Fourier transform
Zeros out high frequencies
Keeps low frequencies

## Slide 8: Gaussian pre-filtering
Solution: filter the image, then subsample
blur
F0 H
*
subsample
blur
subsample
…
F1
F1 H
*
F2
F0

## Slide 9
blur
F0 H
*
subsample
blur
subsample
…
F1
F1 H
*
F2
F0
{
Gaussian pyramid

## Slide 10: Gaussian pyramids [Burt and Adelson, 1983]
In computer graphics, a mip map [Williams, 1983]
Gaussian Pyramids have all sorts of applications in computer vision
Source: S. Seitz

## Slide 11: Gaussian pyramids - Searching over scales

## Slide 12: Gaussian pyramids - Searching over scales

## Slide 13
The Gaussian Pyramid
High resolution
Low resolution
blur
blur
blur
sub-sample
sub-sample
sub-sample
blur
sub-sample

## Slide 14: Gaussian pyramid and stack
Source: Forsyth

## Slide 15: Memory Usage
Each color is a separate pyramid
3 pyramids fit into 2W x 2H image
Notes: 4/3

## Slide 16: What about upsampling?
Simple solution: Fill rest of the pixels with zeros
Obviously wrong. How can we do better?

## Slide 17: Upsampling
Need to interpolate intermediate pixels. What is the best way to interpolate?
  Find the most likely high-res image
Recall: before subsampling, we removed high frequencies
Key idea: upsampled image should not have high frequencies either
Gaussian blur again!

## Slide 18: Upsampling
Step 1: upsample and fill with 0s
Step 2: Gaussian blur to interpolate
Step 3: Scale correction
  Gaussian blur is just weighted average
  But we just introduced a bunch of zeros ==> need to scale up the resulting image

## Slide 19: Upsampling: Step 1

## Slide 20: Upsampling: Step 2 + 3

## Slide 21: Laplacian pyramid
Re-duce
Expand (upsample + blur)
=
Expand (upsample + blur)
-
Expand (upsample + blur)
Expand (upsample + blur)
-
-
=
=
=
-

## Slide 22: Laplacian pyramid
L3 = G3 - expand(G4) =
L2 = G2 - expand(G3) =
L1 = G1 - expand(G2) =
L0 = G0 - expand(G1) =
L4 = G4 =

## Slide 23: Reconstructing the image from a Laplacian pyramid
Expand (upsample + blur)
=
Expand (upsample + blur)
+
Expand (upsample + blur)
Expand (upsample + blur)
+
+
=
=
=
+

## Slide 24: Laplacian pyramid
Source: Forsyth

## Slide 25: Interpolation in general
A more general question
Given some known pixels in the image (shown in blue) how can we get the value of other pixels (shown in red)
In our case, known pixels are in every other row/column

## Slide 26: Interpolation in general
Gaussian interpolation: set new pixels to be weighted combination of known pixels
Other forms of interpolation: other weights

## Slide 27: Interpolation in general
Nearest neighbor interpolation
  Find the nearest known pixel
  Copy its value

## Slide 28: Nearest-neighnbor interpolation

## Slide 29: Bilinear interpolation
Find the four nearest neighbors
Compute weighted average of the four

## Slide 30: Bilinear interpolation

## Slide 31: Geometric transformations
Geometric transformations involve changes to pixel coordinates instead of pixel values
For example, resizing
  Reducing size:
  Increasing size:
In general:
How can we do this?

## Slide 32: Geometric transformations
Simplest solution: copy over pixel values to the new location
Problem?
  Only integer coordinates in f
  So, not every pixel in g will be produced
  Holes!

## Slide 33: Geometric transformations
Better solution: find
For every pixel of output g, set:
Problem: may not be integers
Solution: interpolate!