## Slide 1: Using Gossip for Aggregation and Monitoring. Astrolabe.
Ken Birman
Cornell University. CS5410 Fall 2008.

## Slide 2: Gossip 201
Last time we saw that gossip spreads in log(system size) time
But is this actually “fast”?
% infected
0.0
1.0
Time 

## Slide 3: Gossip in distributed systems
Log(N) can be a very big number!
  With N=100,000, log(N) would be 12
  So with one gossip round per five seconds, information needs one minute to spread in a large system!
Some gossip protocols combine pure gossip with an accelerator
  For example, Bimodal Multicast and lpbcast are protocols that use UDP multicast to disseminate data and then gossip to repair if any loss occurs
  But the repair won’t occur until the gossip protocol runs

## Slide 4: A thought question
What’s the best way to
  Count the number of nodes in a system?
  Compute the average load, or find the most loaded nodes, or least loaded nodes?
Options to consider
  Pure gossip solution
  Construct an overlay tree (via “flooding”, like in our consistent snapshot algorithm), then count nodes in the tree, or pull the answer from the leaves to the root…

## Slide 5: … and the answer is
Gossip isn’t very good for some of these tasks!
  There are gossip solutions for counting nodes, but they give approximate answers and run slowly
  Tricky to compute something like an average because of “re-counting” effect, (best algorithm: Kempe et al)
On the other hand, gossip works well for finding the c most loaded or least loaded nodes (constant c)
Gossip solutions will usually run in time O(log N) and generally give probabilistic solutions

## Slide 6: Yet with flooding… easy!
Recall how flooding works
Basically: we construct a tree by pushing data towards the leaves and linking a node to its parent when that node first learns of the flood
Can do this with a fixed topology or in a gossip style by picking random next hops
1
3
3
3
2
2
Labels: distance of the node from the root

## Slide 7: This is a “spanning tree”
Once we have a spanning tree
  To count the nodes, just have leaves report 1 to their parents and inner nodes count the values from their children
  To compute an average, have the leaves report their value and the parent compute the sum, then divide by the count of nodes
  To find the least or most loaded node, inner nodes compute a min or max…
Tree should have roughly log(N) depth, but once we build it, we can reuse it for a while

## Slide 8: Not all logs are identical!
When we say that a gossip protocol needs time log(N) to run, we mean log(N) rounds
  And a gossip protocol usually sends one message every five seconds or so, hence with 100,000 nodes, 60 secs
But our spanning tree protocol is constructed using a flooding algorithm that runs in a hurry
  Log(N) depth, but each “hop” takes perhaps a millisecond.
  So with 100,000 nodes we have our tree in 12 ms and answers in 24ms!

## Slide 9: Insight?
Gossip has time complexity O(log N) but the “constant” can be rather big (5000 times larger in our example)
Spanning tree had same time complexity but a tiny constant in front
But network load for spanning tree was much higher
  In the last step, we may have reached roughly half the nodes in the system
  So 50,000 messages were sent all at the same time!

## Slide 10: Gossip vs “Urgent”?
With gossip, we have a slow but steady story
  We know the speed and the cost, and both are low
  A constant, low-key, background cost
  And gossip is also very robust
Urgent protocols (like our flooding protocol, or 2PC, or reliable virtually synchronous multicast)
  Are way faster
  But produce load spikes
  And may be fragile, prone to broadcast storms, etc

## Slide 11: Introducing hierarchy
One issue with gossip is that the messages fill up
  With constant sized messages…
  … and constant rate of communication
  … we’ll inevitably reach the limit!
Can we inroduce hierarchy into gossip systems?

## Slide 12
Astrolabe
Intended as help for applications adrift in a sea of information
Structure emerges from a randomized gossip protocol
This approach is robust and scalable even under stress that cripples traditional systems
Developed at RNS, Cornell
By Robbert van Renesse, with many others helping…
Today used extensively within Amazon.com

## Slide 13: Astrolabe is a flexible monitoring overlay
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2003 | .67 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1971 | 1.5 | 1 | 0 | 4.1
cardinal | 2004 | 4.5 | 1 | 0 | 6.0
swift.cs.cornell.edu
cardinal.cs.cornell.edu
Periodically, pull data from monitored systems
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2271 | 1.8 | 0 | 1 | 6.2
falcon | 1971 | 1.5 | 1 | 0 | 4.1
cardinal | 2004 | 4.5 | 1 | 0 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2003 | .67 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2231 | 1.7 | 1 | 1 | 6.0

## Slide 14: Astrolabe in a single domain
Each node owns a single tuple, like the management information base (MIB)
Nodes discover one-another through a simple broadcast scheme (“anyone out there?”) and gossip about membership
  Nodes also keep replicas of one-another’s rows
  Periodically (uniformly at random) merge your state with some else…

## Slide 15: State Merge: Core of Astrolabe epidemic
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2003 | .67 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1971 | 1.5 | 1 | 0 | 4.1
cardinal | 2004 | 4.5 | 1 | 0 | 6.0
swift.cs.cornell.edu
cardinal.cs.cornell.edu

## Slide 16: State Merge: Core of Astrolabe epidemic
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2003 | .67 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1971 | 1.5 | 1 | 0 | 4.1
cardinal | 2004 | 4.5 | 1 | 0 | 6.0
swift.cs.cornell.edu
cardinal.cs.cornell.edu
swift | 2011 | 2.0
cardinal | 2201 | 3.5

## Slide 17: State Merge: Core of Astrolabe epidemic
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1971 | 1.5 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 0 | 6.0
swift.cs.cornell.edu
cardinal.cs.cornell.edu

## Slide 18: Observations
Merge protocol has constant cost
  One message sent, received (on avg) per unit time.
  The data changes slowly, so no need to run it quickly – we usually run it every five seconds or so
  Information spreads in O(log N) time
But this assumes bounded region size
  In Astrolabe, we limit them to 50-100 rows

## Slide 19: Big systems…
A big system could have many regions
  Looks like a pile of spreadsheets
  A node only replicates data from its neighbors within its own region

## Slide 20: Scaling up… and up…
With a stack of domains, we don’t want every system to “see” every domain
  Cost would be huge
So instead, we’ll see a summary
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
cardinal.cs.cornell.edu
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0
Name | Time | Load | Weblogic? | SMTP? | Word Version
swift | 2011 | 2.0 | 0 | 1 | 6.2
falcon | 1976 | 2.7 | 1 | 0 | 4.1
cardinal | 2201 | 3.5 | 1 | 1 | 6.0

## Slide 21: Astrolabe builds a hierarchy using a P2P protocol that “assembles the puzzle” without any servers
Name | Load | Weblogic? | SMTP? | Word Version | …
swift | 2.0 | 0 | 1 | 6.2 | 
falcon | 1.5 | 1 | 0 | 4.1 | 
cardinal | 4.5 | 1 | 0 | 6.0 | 
Name | Load | Weblogic? | SMTP? | Word Version | …
gazelle | 1.7 | 0 | 0 | 4.5 | 
zebra | 3.2 | 0 | 1 | 6.2 | 
gnu | .5 | 1 | 0 | 6.2 | 
Name | Avg Load | WL contact | SMTP contact
SF | 2.6 | 123.45.61.3 | 123.45.61.17
NJ | 1.8 | 127.16.77.6 | 127.16.77.11
Paris | 3.1 | 14.66.71.8 | 14.66.71.12
Name | Load | Weblogic? | SMTP? | Word Version | …
swift | 2.0 | 0 | 1 | 6.2 | 
falcon | 1.5 | 1 | 0 | 4.1 | 
cardinal | 4.5 | 1 | 0 | 6.0 | 
Name | Load | Weblogic? | SMTP? | Word Version | …
gazelle | 1.7 | 0 | 0 | 4.5 | 
zebra | 3.2 | 0 | 1 | 6.2 | 
gnu | .5 | 1 | 0 | 6.2 | 
Name | Avg Load | WL contact | SMTP contact
SF | 2.6 | 123.45.61.3 | 123.45.61.17
NJ | 1.8 | 127.16.77.6 | 127.16.77.11
Paris | 3.1 | 14.66.71.8 | 14.66.71.12
San Francisco
New Jersey
SQL query “summarizes” data
Dynamically changing query output is visible system-wide
Name | Load | Weblogic? | SMTP? | Word Version | …
swift | 1.7 | 0 | 1 | 6.2 | 
falcon | 2.1 | 1 | 0 | 4.1 | 
cardinal | 3.9 | 1 | 0 | 6.0 | 
Name | Load | Weblogic? | SMTP? | Word Version | …
gazelle | 4.1 | 0 | 0 | 4.5 | 
zebra | 0.9 | 0 | 1 | 6.2 | 
gnu | 2.2 | 1 | 0 | 6.2 | 
Name | Avg Load | WL contact | SMTP contact
SF | 2.2 | 123.45.61.3 | 123.45.61.17
NJ | 1.6 | 127.16.77.6 | 127.16.77.11
Paris | 2.7 | 14.66.71.8 | 14.66.71.12

## Slide 22: Large scale: “fake” regions
These are
  Computed by queries that summarize a whole region as a single row
  Gossiped in a read-only manner within a leaf region
But who runs the gossip?
  Each region elects “k” members to run gossip at the next level up.
  Can play with selection criteria and “k”

## Slide 23: Hierarchy is virtual… data is replicated
Name | Load | Weblogic? | SMTP? | Word Version | …
swift | 2.0 | 0 | 1 | 6.2 | 
falcon | 1.5 | 1 | 0 | 4.1 | 
cardinal | 4.5 | 1 | 0 | 6.0 | 
Name | Load | Weblogic? | SMTP? | Word Version | …
gazelle | 1.7 | 0 | 0 | 4.5 | 
zebra | 3.2 | 0 | 1 | 6.2 | 
gnu | .5 | 1 | 0 | 6.2 | 
Name | Avg Load | WL contact | SMTP contact
SF | 2.6 | 123.45.61.3 | 123.45.61.17
NJ | 1.8 | 127.16.77.6 | 127.16.77.11
Paris | 3.1 | 14.66.71.8 | 14.66.71.12
San Francisco
New Jersey
Yellow leaf node “sees” its neighbors and the domains on the path to the root.
Falcon runs level 2 epidemic because it has lowest load
Gnu runs level 2 epidemic because it has lowest load

## Slide 24: Hierarchy is virtual… data is replicated
Name | Load | Weblogic? | SMTP? | Word Version | …
swift | 2.0 | 0 | 1 | 6.2 | 
falcon | 1.5 | 1 | 0 | 4.1 | 
cardinal | 4.5 | 1 | 0 | 6.0 | 
Name | Load | Weblogic? | SMTP? | Word Version | …
gazelle | 1.7 | 0 | 0 | 4.5 | 
zebra | 3.2 | 0 | 1 | 6.2 | 
gnu | .5 | 1 | 0 | 6.2 | 
Name | Avg Load | WL contact | SMTP contact
SF | 2.6 | 123.45.61.3 | 123.45.61.17
NJ | 1.8 | 127.16.77.6 | 127.16.77.11
Paris | 3.1 | 14.66.71.8 | 14.66.71.12
San Francisco
New Jersey
Green node sees different leaf domain but has a consistent view of the inner domain

## Slide 25: Worst case load?
A small number of nodes end up participating in O(logfanoutN) epidemics
  Here the fanout is something like 50
  In each epidemic, a message is sent and received roughly every 5 seconds
We limit message size so even during periods of turbulence, no message can become huge.

## Slide 26: Who uses Astrolabe?
Amazon uses Astrolabe throughout their big data centers!
  For them, Astrolabe helps them track overall state of their system to diagnose performance issues
  They can also use it to automate reaction to temporary overloads

## Slide 27: Example of overload handling
Some service S is getting slow…
  Astrolabe triggers a “system wide warning”
Everyone sees the picture
  “Oops, S is getting overloaded and slow!”
  So everyone tries to reduce their frequency of requests against service S
What about overload in Astrolabe itself?
  Could everyone do a fair share of inner aggregation?

## Slide 28: A fair (but dreadful) aggregation tree
A B C D E F G H I J K L M N O P
A
C
E
G
I
K
M
O
B
F
J
N
D
L

An event e occurs at H
P learns O(N) time units later!
G gossips with H and learns e

## Slide 29: What went wrong?
In this horrendous tree, each node has equal “work to do” but the information-space diameter is larger!
Astrolabe benefits from “instant” knowledge because the epidemic at each level is run by someone elected from the level below

## Slide 30: Insight: Two kinds of shape
We’ve focused on the aggregation tree
But in fact should also think about the information flow tree

## Slide 31: Information space perspective
Bad aggregation graph: diameter O(n)
Astrolabe version: diameterO(log(n))
H – G – E – F – B – A – C – D – L – K – I – J – N – M – O – P
A – B
C – D
E – F
G – H
I – J
K – L
M – N
O – P

## Slide 32: Summary
We looked at ways of using Gossip for aggregation
  Pure gossip isn’t ideal for this… and competes poorly with flooding and other urgent protocols
  But Astrolabe introduces hierarchy and is an interesting option that gets used in at least one real cloud platform
Power: make a system more robust, self-adaptive, with a technology that won’t make things worse
But performance can still be sluggish