## Slide 1: CS5412: The RealTime Cloud
Ken Birman
Lecture XXIV

## Slide 2: Can the Cloud Support Real-Time?
More and more “real time” applications are migrating into cloud environments
  Monitoring of traffic in various situations, control of the traffic lights and freeway lane limitations
  Tracking where people are and using that to support social networking applications that depend on location
  Smart buildings and the smart power grid
Can we create a real-time cloud?

## Slide 3: Core Real-Time Mechanism
We’ve discussed publish-subscribe
  Topic-based pub-sub systems (like the TIB system)
  Content-based pub-sub solutions (like Sienna)
Real-time systems often center on a similar concept that is called a real-time data distribution service
  DDS technology has become highly standardized
  It mixes a kind of storage solution with a kind of pub-sub interface but the guarantees focus on real-time

## Slide 4: What is the DDS?
The Data Distribution Service for Real-Time Systems (DDS) is an Object Management Group (OMG) standard that aims to enable scalable, real-time, dependable, high performance and interoperable data exchanges between publishers and subscribers.
DDS is designed to address the needs of applications like financial trading, air traffic control, smart grid management, and other big data applications.

## Slide 5: Air Traffic Example
DDS combines database and pub/sub functionality
Owner of flight plan updates it… there can only be one owner.
DDS makes the update persistent, records the ordering of the event, reports it to client systems
… Other clients see real-time read-only updates

## Slide 6: Quality of Service options
Early in the semester we discussed a wide variety of possible guarantees a group communication system could provide
Real-time systems often do this too but the more common term is quality of service in this case
  Describes the quality guarantees a subscriber can count upon when using the DDS
  Generally expressed in terms of throughput and latency

## Slide 7: CASD (-T atomic multicast)
Let’s start our discussion of DDS technology by looking at a form of multicast with QoS properties
  This particular example was drawn from the US Air Traffic Control effort of the period 1995-1998
  It was actually a failure, but there were many issues
  At the core was a DDS technology that combined the real-time protocol we will look at with a storage solution to make it durable, like making an Isis2 group durable by having it checkpoint to a log file (you use g.SetPersistent() or, with SafeSend, enable Paxos logging)

## Slide 8: Real-time multicast: Problem statement
The community that builds real-time systems favors proofs that the system is guaranteed to satisfy its timing bounds and objectives
The community that does things like data replication in the cloud tends to favor speed
  We want the system to be fast
  Guarantees are great unless they slow the system down

## Slide 9: Can a guarantee slow a system down?
Suppose we want to implement broadcast protocols that make direct use of temporal information
Examples:
  Broadcast that is delivered at same time by all correct processes (plus or minus the clock skew)
  Distributed shared memory that is updated within a known maximum delay
  Group of processes that can perform periodic actions

## Slide 10: A real-time broadcast
p0
p1
p2
p3
p4
p5
t
t+a
t+b
*
*
*
*
*
Message is sent at time t by p0. Later both p0 and p1 fail. But message is still delivered atomically, after a bounded delay, and within a bounded interval of time (at non-faulty processes)

## Slide 11: A real-time distributed shared memory
p0
p1
p2
p3
p4
p5
t
t+a
t+b
At time t p0 updates a variable in a distributed shared memory. All correct processes observe the new value after a bounded delay, and within a bounded interval of time.
set x=3
x=3

## Slide 12: Periodic process group: Marzullo
p0
p1
p2
p3
p4
p5
Periodically, all members of a group take some action. Idea is to accomplish this with minimal communication

## Slide 13: The CASD protocol suite
Also known as the “ -T” protocols
Developed by Cristian and others at IBM, was intended for use in the (ultimately, failed) FAA project
Goal is to implement a timed atomic broadcast tolerant of Byzantine failures

## Slide 14: Basic idea of the CASD protocols
Assumes use of clock synchronization
Sender timestamps message
Recipients forward the message using a flooding technique (each echos the message to others)
Wait until all correct processors have a copy, then deliver in unison (up to limits of the clock skew)

## Slide 15: CASD picture
p0
p1
p2
p3
p4
p5
t
t+a
t+b
*
*
*
*
*
p0, p1 fail. Messages are lost when echoed by p2, p3

## Slide 16: Idea of CASD
Assume known limits on number of processes that fail during protocol, number of messages lost
Using these and the temporal assumptions, deduce worst-case scenario
Now now that if we wait long enough, all (or no) correct process will have the message
Then schedule delivery using original time plus a delay computed from the worst-case assumptions

## Slide 17: The problems with CASD
In the usual case, nothing goes wrong, hence the delay can be very conservative
Even if things do go wrong, is it right to assume that if a message needs between 0 and ms to make one hope, it needs [0,n*  ] to make n hops?
How realistic is it to bound the number of failures expected during a run?

## Slide 18: CASD in a more typical run
p0
p1
p2
p3
p4
p5
t
t+a
t+b
*
*
*
*
*
*

## Slide 19: ... leading developers to employ more aggressive parameter settings
p0
p1
p2
p3
p4
p5
t
t+a
t+b
*
*
*
*
*
*

## Slide 20: CASD with over-aggressive paramter settings starts to “malfunction”
p0
p1
p2
p3
p4
p5
t
t+a
t+b
*
all processes look “incorrect” (red) from time to time
*
*
*

## Slide 21: CASD “mile high”
When run “slowly” protocol is like a real-time version of abcast
When run “quickly” protocol starts to give probabilistic behavior:
  If I am correct (and there is no way to know!) then I am guaranteed the properties of the protocol, but if not, I may deliver the wrong messages

## Slide 22: How to repair CASD in this case?
Gopal and Toueg developed an extension, but it slows the basic CASD protocol down, so it wouldn’t be useful in the case where we want speed and also real-time guarantees
Can argue that the best we can hope to do is to superimpose a process group mechanism over CASD (Verissimo and Almeida are looking at this).

## Slide 23: Why worry?
CASD can be used to implement a distributed shared memory (“delta-common storage”)
But when this is done, the memory consistency properties will be those of the CASD protocol itself
If CASD protocol delivers different sets of messages to different processes, memory will become inconsistent

## Slide 24: Why worry?
In fact, we have seen that CASD can do just this, if the parameters are set aggressively
Moreover, the problem is not detectable either by “technically faulty” processes or “correct” ones
Thus, DSM can become inconsistent and we lack any obvious way to get it back into a consistent state

## Slide 25: Using CASD in real environments
Once we build the CASD mechanism how would we use it?
  Could implement a shared memory
  Or could use it to implement a real-time state machine replication scheme for processes
US air traffic project adopted latter approach
  But stumbled on many complexities…

## Slide 26: Using CASD in real environments
Pipelined computation
Transformed computation

## Slide 27: Issues?
Could be quite slow if we use conservative parameter settings
But with aggressive settings, either process could be deemed “faulty” by the protocol
  If so, it might become inconsistent
    Protocol guarantees don’t apply
  No obvious mechanism to reconcile states within the pair
Method was used by IBM in a failed effort to build a new US Air Traffic Control system

## Slide 28: Can we combine CASD with consensus?
Consensus-based mechanisms (Isis2, Paxos) give strong guarantees, such as “there is one leader”
CASD overcomes failures to give real-time delivery if parameterized correctly (clearly, not if parameterized incorrectly!)
Why not use both, each in different roles?

## Slide 29: A comparison
Virtually synchronous Send is fault-tolerant and very robust, and very fast, but doesn’t guarantee realtime delivery of messages
CASD is fault-tolerant and very robust, but rather slow. But it does guarantee real-time delivery
CASD is “better” if our application requires absolute confidence that real-time deadlines will be achieved... but only if those deadlines are “slow”

## Slide 30: Weird insight
If a correctly functioning version of CASD would be way too slow for practical use, then a protocol like Send might be better even for the real-time uses!
The strange thing is that Send isn’t designed to provide guaranteed real-time behavior
But in practice it is incredibly fast, compared to CASD which can be incredibly slow…

## Slide 31: Which is better for real-time uses?
Virtually synchronous Send or CASD?
  CASD may need seconds before it can deliver, but comes with a very strong proof that it will do so correctly
  Send will deliver within milliseconds unless strange scheduling delays impact a node
    But actually delay limit is probably ~10 seconds
    Beyond this, if ISIS_DEFAULT_TIMEOUT is set to a small value like 5s, node will be declared to have crashed

## Slide 32: Back to the DDS concept
In a cloud setting, a DDS is typically
  A real-time protocol, such as CASD
  Combined with a database technology, generally transactional with strong durability
  Combined with a well defined notion of “objects”, for example perhaps in the IBM Air Traffic Control project something like “Flight Data Records”
  Combined with a rule: when the FDR is updated, we will also use the DDS to notify any “subscribers” to that object. So the object name is a topic in pub-sub terms.

## Slide 33: IBM Air Traffic Concept
Everyone uses the -Common storage abstraction and maintains a local “copy” of all FDRs relevant to the current air traffic control state
To update an FDR, there should be a notion of an owner who is the (single) controller allowed to change the FDR.
  Owner performs some action, this updates the durable storage subsystem
  Then when update is completely final, -T atomic multicast is used to update all the -Common storage records
  Then this updates applications on all the controller screens

## Slide 34: Safety needs?
Clearly there needs to be a well defined guarantee of a single controller for each FDR
  There must always be an assigned controller
  … but there can only be one per FDR
Also we need the DDS to be reliable; CASD could be used, for example
But we also need a certain level of speed and latency guarantees

## Slide 35: What makes it hard?
As we see with CASD, sometimes the analysis used to ensure reliability “fights” the QoS properties needed for safety in the application as a whole
Moreover, we didn’t even consider delays associated with recovering the DDS storage subsystem when a failure or restart disrupts it
  E.g. bringing a failed DDS storage element back online
  We need to be sure that every FDR goes through a single well-defined sequence of “states”

## Slide 36: If a system is too slow…
… it may not be useable even if the technology that was used to build it is superb!
With real DDS solutions in today’s real cloud settings this entire issue is very visible and a serious problem for developers
They constantly struggle between application requirements and what the cloud can do quickly

## Slide 37: Generalizing to the whole cloud
Massive scale
And most of the thing gives incredibly fast responses: sub 100ms is a typical goal
But sometimes we experience a long delay or a failure

## Slide 38: Traditional view of real-time control favored CASD view of assurances
In this strongly assured model, the assumption was that we need to prove our claims and guarantee that the system will meet goals
And like CASD this leads to slow systems
  And to CAP and similar concerns

## Slide 39: And this leads back to our question
So can the cloud do high assurance?
  Presumably not if we want CASD kinds of proofs
  But if we are willing to “overwhelm” delays with redundancy, why shouldn’t we be able to do well?
Suppose that we connect our user to two cloud nodes and they perform read-only tasks in parallel
  Client takes first answer, but either would be fine
  We get snappier response but no real “guarantee”

## Slide 40: A vision: “Good enough assurance”
Build applications to protect themselves against rare but extreme problems (e.g. a medical device might warn that it has lost connectivity)
  This is needed anyhow: hardware can fail…
  So: start with “fail safe” technology
Now make our cloud solution as reliable as we can without worrying about proofs
  We want speed and consistency but are ok with rare crashes that might be noticed by the user

## Slide 41: Will this do?
Probably not for some purposes… but some things just don’t belong under computer control
For most purposes, this sort of solution might balance the benefits of the cloud with the kinds of guarantees we know how to provide
Use redundancy to compensate for delays, insecurity, failures of individual nodes

## Slide 42: Summary: Should we trust the cloud?
We’ve identified a tension centering on priorities
  If your top priority is assurance properties you may be forced to sacrifice scalability and performance in ways that leave you with a useless solution
  If your top priorities center on scale and performance and then you layer in other characteristics it may be feasible to keep the cloud properties and get a good enough version of the assurance properties
These tradeoffs are central to cloud computing!
But like the other examples, cloud could win even if in some ways, it isn’t the “best” or “most perfect” solution

## Slide 43: But how can anyone trust the cloud?
The cloud seems so risky that it makes no sense at all to trust it in any way!
Yet we seem to trust it in many ways
This puts the fate of your company in the hands of third parties!

## Slide 44: The concept of “good enough”
We’ve seen that there really isn’t any foolproof way to build a computer, put a large, complex program on it, and then run it with confidence
We also know that with effort, many kinds of systems really start to work very well
When is a “pretty good” solution good enough?

## Slide 45: Life with technology is about tradeoffs
Clearly, we err if we use a technology in a dangerous or inappropriate way
  Liability laws need to be improved: they let software companies escape pretty much all responsibility
  Yet gross negligence is still a threat to those who build things that will play critical roles and yet fail to take adequate steps to achieve assurance