## Slide 1: Overview: Internet vs Data Center Networks
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
August 29, 2014

## Slide 2: Goals for Today
Overview
  What is the Internet?
    What is it and how did we get here?
  What is about Data Centers?
Network Structure
  Internet
  Data center

## Slide 3
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
What is the Internet?
Notes: 3

## Slide 4
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use
What is the Internet?

## Slide 5
Internet: “network of networks”
  Interconnected ISPs
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
mobile network
global ISP
regional ISP
home
network
institutional
network
What is the Internet?

## Slide 6
Infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network
What is the Internet?

## Slide 7
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles
How did we get here: Internet History

## Slide 8
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets
How did we get here: Internet History

## Slide 9: Goals for Today
Overview
  What is the Internet?
    What is it and how did we get here?
  What is about Data Centers?
Network Structure
  Internet
  Data center

## Slide 10
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
How did we get here: Internet History

## Slide 11
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps
How did we get here: Internet History

## Slide 12
2005-present
~750 million hosts
  Smartphones and tablets
Aggressive deployment of broadband access
Increasing ubiquity of high-speed wireless access
Emergence of online social networks:
  Facebook: soon one billion users
Service providers (Google, Microsoft) create their own networks
  Bypass Internet, providing “instantaneous” access to search, emai, etc.
E-commerce, universities, enterprises running their services in “cloud” (eg, Amazon EC2)
How did we get here: Internet History

## Slide 13: What is different about Data Centers?
Cost
  “It is the economics stupid”
    James Hamilton, VP & Distinguished engineer, Amazon Web Services
  In 2008, data center staff to servers was 1:1000
  Today, closer to 1:10,000
Scale
  Millions of servers, billions of users, trillions of objects
  Scale out instead of scale up
Efficient
  Massive scale in the same location eases design and lowers costs
Global scale data centers
  Data Centers strategically placed where power is cheap and close to consumers

## Slide 14: Where do the costs go?
Breakdown
  45% Servers - CPU, memory, storage subsystems
  25% Infrastructure - Power distribution and cooling
  15% Power draw - Electrical utility costs
  15% Network - Links, transit, equipment

## Slide 15: Where do the costs go?
Breakdown
  45% Servers - CPU, memory, storage subsystems
  25% Infrastructure - Power distribution and cooling
  15% Power draw - Electrical utility costs
  15% Network - Links, transit, equipment
How to reduced costs
  Servers and Infrastructure
    Let servers fail and infrastructure fail
    Software, Replication and network efficiency can help
  Power and Network
    High utilization (better on than off)
    Agility (ability to run applications anywhere in data center)

## Slide 16: Networking in Data Centers
…
…
…
…
…
…
…
…
…
ToR
Aggregate
Switch (AS)
Core Switch (CS)
Internet

## Slide 17: Networking in Data Centers
…
…
…
…
…
…
…
…
…
ToR
Aggregate
Switch (AS)
Core Switch (CS)
Internet

## Slide 18: Geo-distributed Data Centers

## Slide 19: Goals for Today
Overview
  What is the Internet?
    What is it and how did we get here?
  What is about Data Centers?
Structure
  Internet
  Data Centers

## Slide 20: Internet Structure
Network Protocols
Edge Network
Core Networks

## Slide 21
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt
Network Protocols

## Slide 22
a human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
Network Protocols

## Slide 23
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
Network Protocol “Layers”

## Slide 24
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Network Protocol “Layers”
Similar to Traveling protocol

## Slide 25
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
Network Protocol “Layers”
Similar to Traveling protocol

## Slide 26: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 27
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical
Internet Protocol Stack

## Slide 28
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical
ISO/OSI Reference Model
Not used with due to Internet Protocol Stack

## Slide 29: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 30: What About Data Centers?
Data Centers use the same network protocol stack
But, is this a good thing?

## Slide 31: What About Data Centers?
Data Centers use the same network protocol stack
But, is this a good thing?
  Pro
    Standard for all applications and services
  Con
    Efficiency
    Can prevent full utilization of data center resourcces

## Slide 32: Internet Structure
Network Protocols
Edge Network
Core Networks

## Slide 33
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network
Internet Structure

## Slide 34
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?
Internet Structure

## Slide 35
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
The network Core
Internet Structure

## Slide 36
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header
Two key network core functions
Internet Structure

## Slide 37
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks
Alternative Core: Circuit Switching
Internet Structure

## Slide 38
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Circuit Switching: FDM vs TDM
Internet Structure
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 39
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
* Check out the online interactive exercises for more examples
Packet switching versus circuit switching
Internet Structure

## Slide 40
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Internet Structure

## Slide 41
End systems connect to Internet via access ISPs (Internet Service Providers)
  Residential, company and university ISPs
Access ISPs in turn must be interconnected.
  So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure
Internet Structure: Network of Networks

## Slide 42
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Internet Structure: Network of Networks

## Slide 43
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
Internet Structure: Network of Networks

## Slide 44
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP
Internet Structure: Network of Networks

## Slide 45
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C
Internet Structure: Network of Networks

## Slide 46
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point
Internet Structure: Network of Networks

## Slide 47
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
regional net
Internet Structure: Network of Networks

## Slide 48
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Internet Structure: Network of Networks

## Slide 49
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Internet Structure: Network of Networks

## Slide 50
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence
Internet Structure: Network of Networks
E.g. AT&T

## Slide 51: Goals for Today
Overview
  What is the Internet?
    What is it and how did we get here?
  What is about Data Centers?
Network Structure
  Internet
  Data center

## Slide 52: Networking in Data Centers
…
…
…
…
…
…
…
…
…
ToR
Aggregate
Switch (AS)
Core Switch (CS)
Internet

## Slide 53: Networking in Data Centers
…
…
…
…
…
…
…
…
…
ToR
Aggregate
Switch (AS)
Core Switch (CS)
Internet

## Slide 54: Geo-distributed Data Centers

## Slide 55: Perspective
Large cloud service provides have deployed their own networks
  Private networks, perhaps as large as the Internet
  But, bypass the Internet core and connect directly with ISPs
  Near instantaneous access betwee consumers and data centers
Economies of scale dominate in cloud data centers
Notes: As discussed in Section 1.3.3, online service providers, such as Google and
Microsoft, have deployed their own extensive private networks, which not only
connect together their globally distributed data centers, but are used to bypass
the Internet as much as possible by peering directly with lower-tier ISPs. As a
result, Google provides search results and email access almost instantaneously,
as if their data centers were running within one’s own computer.
• Many Internet commerce companies are now running their applications in the
“cloud”—such as in Amazon’s EC2, in Google’s Application Engine, or in
Microsoft’s Azure. Many companies and universities have also migrated their Internet
applications (e.g., email and Web hosting) to the cloud. Cloud companies not
only provide applications scalable computing and storage environments, but also
provide the applications implicit access to their high-performance private networks.

## Slide 56: Before Next time
No required reading and review due
But, review chapter 2 from the book, Application Layer
Create a project group
  Start asking questions about possible projects
Check website for updated schedule