## Slide 1: Network Layer and Data Center Topologies
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
September 8, 2014
Slides used and adapted judiciously from Computer Networking, A Top-Down Approach

## Slide 2: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 3: Network Layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 4: Network Layer
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange
Two key functions

## Slide 5
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router
Network Layer
Interplay between routing and forwarding

## Slide 6: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 7: Network Layer
datagram network provides network-layer connectionless service
virtual-circuit network provides network-layer connection service
analogous to TCP/UDP connecton-oriented / connectionless transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: in network core
Connection, Connection-less services

## Slide 8: Network Layer
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host address)
every router on source-dest path maintains “state” for each passing connection
link, router resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path
Virtual Circuits (VC)

## Slide 9: Network Layer
a VC consists of:
  path from source to destination
  VC numbers, one number for each link along path
  entries in forwarding tables in routers along path
packet belonging to VC carries VC number (rather than dest address)
VC number can be changed on each link.
  new VC number comes from forwarding table
Virtual Circuits (VC) implementation

## Slide 10: Network Layer
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
forwarding table in
northwest router:
VC routers maintain connection state information!
Virtual Circuits (VC) forwarding table

## Slide 11: Network Layer
application
transport
network
data link
physical
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
1. initiate call
2. incoming call
3. accept call
4. call connected
5. data flow begins
6. receive data
application
transport
network
data link
physical
Virtual Circuits (VC) signaling protocol

## Slide 12: Network Layer
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams
Datagram Networks

## Slide 13: Network Layer
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)
Datagram Forwarding Table

## Slide 14: Network Layer
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?
Datagram Forwarding Table

## Slide 15: Network Layer
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3
Datagram Forwarding Table: Longest Prefix Matching

## Slide 16: Network Layer
Internet (datagram)
data exchange among computers
  “elastic” service, no strict timing req.
many link types
  different characteristics
  uniform service difficult
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
ATM (VC)
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network
Datagram versus Virtual Circuits (VC)

## Slide 17: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 18: The Internet Protocol Network Layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 19: The Internet Protocol Network Layer
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead
IP Datagram format

## Slide 20: The Internet Protocol Network Layer
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…
IP Fragmentation/Reassembly

## Slide 21: The Internet Protocol Network Layer
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
IP Fragmentation/Reassembly

## Slide 22: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 23: The Internet Protocol Network Layer
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
IP Addressing

## Slide 24: The Internet Protocol Network Layer
Q: how are interfaces actually connected?
A: we’ll learn about that in chapter 5, 6.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)
IP Addressing

## Slide 25: The Internet Protocol Network Layer
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
Subnets

## Slide 26: The Internet Protocol Network Layer
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
Subnets

## Slide 27: The Internet Protocol Network Layer
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
Subnets

## Slide 28: The Internet Protocol Network Layer
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
IP Addressing: CIDR (Classess InterDomain Routing)

## Slide 29: The Internet Protocol Network Layer
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
IP Addresses: How to get one?

## Slide 30: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing / subnets
    Routing Algorithms
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 31: The Internet Protocol Network Layer
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router
Interplay between routing and forwarding

## Slide 32: The Internet Protocol Network Layer
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections
Graph Abstractions

## Slide 33: The Internet Protocol Network Layer
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path
Graph Abstractions: Costs

## Slide 34: The Internet Protocol Network Layer
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
  periodic update
  in response to link cost changes
Routing Algorithm Classifications

## Slide 35: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing / subnets
    Routing Algorithms
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 36: The Internet Protocol Network Layer
scale: with 600 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice
Hierarchical Routing

## Slide 37: The Internet Protocol Network Layer
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
gateway router:
at “edge” of its own AS
has link to router in another AS
Hierarchical Routing

## Slide 38: The Internet Protocol Network Layer
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal dests
  inter-AS & intra-AS sets entries for external dests
Hierarchical Routing: Interconnected
Autonomous Systems (AS)

## Slide 39: The Internet Protocol Network Layer
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)
Hierarchical Routing: Intra-AS routing

## Slide 40: The Internet Protocol Network Layer
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASs.
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”
Hierarchical Routing: Inter-AS routing—BGP

## Slide 41: The Internet Protocol Network Layer
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: contains ASs through which prefix advertisement has passed: e.g., AS 67, AS 17
  NEXT-HOP: indicates specific internal-AS router to next-hop AS. (may be multiple links from current AS to next-hop-AS)
gateway router receiving route advertisement uses import policy to accept/decline
  e.g., never route through AS x
  policy-based routing
Hierarchical Routing: Inter-AS routing—BGP
Path Attributes and BGP Routes

## Slide 42: The Internet Protocol Network Layer
router may learn about more than 1 route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria
Hierarchical Routing: Inter-AS routing—BGP
BGP Route Selection

## Slide 43: The Internet Protocol Network Layer
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection
Hierarchical Routing: Inter-AS routing—BGP
BGP Messages

## Slide 44: The Internet Protocol Network Layer
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Hierarchical Routing: Inter-AS routing—BGP
BGP Routing Policy

## Slide 45: The Internet Protocol Network Layer
A advertises path AW to B
B advertises path BAW to X
Should B advertise path BAW to C?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Hierarchical Routing: Inter-AS routing—BGP
BGP Routing Policy

## Slide 46: The Internet Protocol Network Layer
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance
Hierarchical Routing: Intra vs Inter-AS routing

## Slide 47: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing / subnets
    Routing Algorithms
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 48: Data Center Topology: FatTree
A scalable, commodity data center network architecture, M. Al-Fares, A. Loukissas, and A. Vahdat. ACM SIGCOMM Computer Communication Review, Volume 38, Issue 4 (August 2008), pages 63-74.

## Slide 49: Data Center Topology: FatTree
Structure and Properties of a Data Center
Desired properties in a DC Architecture
Fat tree based solution
Overview

## Slide 50: Data Center Topology: FatTree
Topology:
  2 layers: 5K to 8K hosts
  3 layer: >25K hosts
  Switches:
    Leaves: have N GigE ports (48-288) + N 10 GigE uplinks to one or more layers of network elements
    Higher levels: N 10 GigE ports (32-128)
Multi-path Routing:
  Ex. ECMP
    without it, the largest cluster = 1,280 nodes
    Performs static load splitting among flows
    Lead to oversubscription for simple comm. patterns
    Routing table entries grows multiplicatively with number of paths, cost ++, lookup latency ++
Background

## Slide 51: Data Center Topology: FatTree
Internet
Servers
Layer-2 switch
Access
Data Center
Layer-2/3 switch
Aggregation
Layer-3 router
Core
Common Data Center Topology

## Slide 52: Data Center Topology: FatTree
Single point of failure
Over subscript of links higher up in the topology
  Trade off between cost and provisioning
Issues with Traditional Data Center Topology

## Slide 53: Data Center Topology: FatTree
Oversubscription:
  Ratio of the worst-case achievable aggregate bandwidth among the end hosts to the total bisection bandwidth of a particular communication topology
  Lower the total cost of the design
  Typical designs: factor of 2:5:1 (400 Mbps)to 8:1(125 Mbps)
Cost:
  Edge: $7,000 for each 48-port GigE switch
  Aggregation and core: $700,000 for 128-port 10GigE switches
  Cabling costs are not considered!
Issues with Traditional Data Center Topology

## Slide 54: Data Center Topology: FatTree
Backwards compatible with existing infrastructure
  No changes in application
  Support of layer 2 (Ethernet)
Cost effective
  Low power consumption & heat emission
  Cheap infrastructure
Allows host communication at line speed
Properties of Desired Solution

## Slide 55: Data Center Topology: FatTree
Leverages specialized hardware and communication protocols, such as InfiniBand, Myrinet.
  These solutions can scale to clusters of thousands of nodes with high bandwidth
  Expensive infrastructure, incompatible with TCP/IP applications
Leverages commodity Ethernet switches and routers to interconnect cluster machines
  Backwards compatible with existing infrastructures, low-cost
  Aggregate cluster bandwidth scales poorly with cluster size, and achieving the highest levels of bandwidth incurs non-linear cost increase with cluster size
Properties of Desired Solution: Tradeoffs

## Slide 56: Data Center Topology: FatTree
Adopt a special instance of a Clos topology
Similar trends in telephone switches led to designing a topology with high bandwidth by interconnecting smaller commodity switches.
Proposed Solution: FatTree (Clos Network)

## Slide 57: Data Center Topology: FatTree
Inter-connect racks (of servers) using a fat-tree topology
  K-ary fat tree: three-layer topology (edge, aggregation and core)
  each pod consists of (k/2)2 servers & 2 layers of k/2 k-port switches
  each edge switch connects to k/2 servers & k/2 aggr. switches
  each aggr. switch connects to k/2 edge & k/2 core switches
  (k/2)2 core switches: each connects to k pods
Fat-tree with K=4
FatTree Based Data Center Architecture

## Slide 58: Data Center Topology: FatTree
Why Fat-Tree?
  Fat tree has identical bandwidth at any bisections
  Each layer has the same aggregated bandwidth
Can be built using cheap devices with uniform capacity
  Each port supports same speed as end host
  All devices can transmit at line speed if packets are distributed uniform along available paths
Great scalability: k-port switch supports k3/4 servers
FatTree Based Data Center Architecture

## Slide 59: Data Center Topology: FatTree
Layer 3 will only use one of the existing equal cost paths
  Bottlenecks up and down the fat-tree
    Simple extension to IP forwarding
  Packet re-ordering occurs if layer 3 blindly takes advantage of path diversity ; further load may not necessarily be well-balanced
Wiring complexity in large networks
  Packing and placement technique
Problems with FatTree

## Slide 60: Data Center Topology: FatTree
Enforce a special (IP) addressing scheme in DC
  unused.PodNumber.switchnumber.Endhost
  Allows host attached to same switch to route only through switch
  Allows inter-pod traffic to stay within pod
FatTree Modified

## Slide 61: Data Center Topology: FatTree
Use two level look-ups to distribute traffic and maintain packet ordering
  First level is prefix lookup
    used to route down the topology to servers
  Second level is a suffix lookup
    used to route up towards core
    maintain packet ordering by using same ports for same server
    Diffuses and spreads out traffic
FatTree Modified

## Slide 62: Before Next time
Project Proposal
  due this Friday
  Project group meeting Tuesday, 4:15pm, in 122 Gates Hall
  Meet with groups, TA, and professor
Lab1
  Lab1 help session in MEng Lab, Wednesday, Sept 10, during lecture time
  Single threaded TCP proxy
  Due this Friday
No required reading and review due
But, review chapter 5 from the book, Data Link and Physical Layer
  We will also briefly discuss data center topologies
Check website for updated schedule

## Slide 63: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 64: DHCP (Dynamic Host Configuration Protocol)
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 65: DHCP (Dynamic Host Configuration Protocol)
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 66: DHCP (Dynamic Host Configuration Protocol)
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network
Client-Server Scenario

## Slide 67: DHCP (Dynamic Host Configuration Protocol)
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Client-Server Scenario

## Slide 68: DHCP (Dynamic Host Configuration Protocol)
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 69: DHCP (Dynamic Host Configuration Protocol)
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP Example

## Slide 70: DHCP (Dynamic Host Configuration Protocol)
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router
DHCP Example

## Slide 71: IP Addressing: Hierarchical Addressing
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 72: IP Addressing: Hierarchical Addressing
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:
Hierarchical Addressing: Route Aggregation

## Slide 73: IP Addressing: Hierarchical Addressing
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 74: IP Addressing: Hierarchical Addressing
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 75: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 76: NAT (Network Address Translation)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 77: NAT (Network Address Translation)
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 78: NAT (Network Address Translation)
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 79: NAT (Network Address Translation)
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 80: NAT (Network Address Translation)
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  address shortage should instead be solved by IPv6

## Slide 81: NAT (Network Address Translation)
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATed address: 138.76.29.7
solution1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (123.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?
NAT Traversal Problem

## Slide 82: NAT (Network Address Translation)
solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATed host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
NAT
router
IGD
NAT Traversal Problem

## Slide 83: NAT (Network Address Translation)
solution 3: relaying (used in Skype)
  NATed client establishes connection to relay
  external client connects to relay
  relay bridges packets between to connections
138.76.29.7
client
1. connection to
relay initiated
by NATed host
2. connection to
relay initiated
by client
3. relaying
established
NAT
router
10.0.0.1
NAT Traversal Problem

## Slide 84: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 85: ICMP (Internet control message protocol)
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 86: ICMP (Internet control message protocol)
source sends series of UDP segments to dest
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when nth set of datagrams arrives to nth router:
  router discards datagrams
  and sends source ICMP messages (type 11, code 0)
  ICMP messages includes name of router & IP address
when ICMP messages arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
ICMP and Traceroute

## Slide 87: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 88: IPv6
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 89: IPv6
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
IPv6 Datagram Format

## Slide 90: IPv6
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions
Changes from IPv4

## Slide 91: IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
Transition to IPv6 from IPv4

## Slide 92: IPv6
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
Transition to IPv6 from IPv4 via Tunneling

## Slide 93: IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4
Transition to IPv6 from IPv4 via Tunneling

## Slide 94: Goals for Today
Network Layer
  Abstraction / services
    Datagram vs Virtual Circuit (VC)
  Internet Protocol
    IP Datagram format
    IP Addressing
    Hierarchical Routing
Data Center Topologies
  FatTree
Backup Slides
  DHCP and NAT
  ICMP and Traceroute
  IPv6
  Hierarchical Routing: RIP, OSPF, BGP

## Slide 95: Hierarchical Routing
scale: with 600 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 96: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
gateway router:
at “edge” of its own AS
has link to router in another AS

## Slide 97: Hierarchical Routing
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal dests
  inter-AS & intra-AS sets entries for external dests
Interconnected Autonomous Systems (ASes)

## Slide 98: Hierarchical Routing
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
Inter-AS tasks

## Slide 99: Hierarchical Routing
suppose AS1 learns (via inter-AS protocol) that subnet x reachable via AS3 (gateway 1c), but not via AS2
  inter-AS protocol propagates reachability info to all internal routers
router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c
  installs forwarding table entry (x,I)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
…
Example: Setting forwarding table in router 1d

## Slide 100: Hierarchical Routing
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine which gateway it should forward packets towards for dest x
  this is also job of inter-AS routing protocol!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
……
…
?
Example: Choosing among multiple ASes

## Slide 101: Hierarchical Routing
learn from inter-AS
protocol that subnet
x is reachable via
multiple gateways
use routing info
from intra-AS
protocol to determine
costs of least-cost
paths to each
of the gateways
hot potato routing:
choose the gateway
that has the
smallest least cost
determine from
forwarding table the
interface I that leads
to least-cost gateway.
Enter (x,I) in
forwarding table
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine towards which gateway it should forward packets for dest x
  this is also job of inter-AS routing protocol!
hot potato routing: send packet towards closest of two routers.
Example: Choosing among multiple ASes

## Slide 102: Hierarchical Routing
also known as interior gateway protocols (IGP)
most common intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)
Intra-AS Routing

## Slide 103: Hierarchical Routing
included in BSD-UNIX distribution in 1982
distance vector algorithm
  distance metric: # hops (max = 15 hops), each link has cost 1
  DVs exchanged with neighbors every 30 sec in response message (aka advertisement)
  each advertisement: list of up to 25 destination subnets (in IP addressing sense)
D
C
B
A
u
v
w
x
y
z
subnet hops
u 1
v 2
w 2
x 3
y 3
z 2
from router A to destination subnets:
Intra-AS Routing: RIP (Routing Information Protocol)

## Slide 104: Hierarchical Routing
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
w
x
y
z
A
C
D
B
Intra-AS Routing: RIP (Routing Information Protocol)

## Slide 105: Hierarchical Routing
w
x
y
z
A
C
D
B
destination subnet next router # hops to dest
w A 2
y B 2
z B 7
x -- 1
…. …. ....
routing table in router D
A
5
dest next hops
w - 1
x - 1
z C 4
…. … ...
A-to-D advertisement
Intra-AS Routing: RIP (Routing Information Protocol)

## Slide 106: Hierarchical Routing
if no advertisement heard after 180 sec --> neighbor/link declared dead
  routes via neighbor invalidated
  new advertisements sent to neighbors
  neighbors in turn send out new advertisements (if tables changed)
  link failure info quickly (?) propagates to entire net
  poison reverse used to prevent ping-pong loops (infinite distance = 16 hops)
Intra-AS Routing: RIP—Link failure and recovery

## Slide 107: Hierarchical Routing
RIP routing tables managed by application-level process called route-d (daemon)
advertisements sent in UDP packets, periodically repeated
physical
link
network forwarding
(IP) table
transport
(UDP)
routed
physical
link
network
(IP)
transprt
(UDP)
routed
forwarding
table
Intra-AS Routing: RIP—Table processing

## Slide 108: Hierarchical Routing
“open”: publicly available
uses link state algorithm
  LS packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor
advertisements flooded to entire AS
  carried in OSPF messages directly over IP (rather than TCP or UDP
IS-IS routing protocol: nearly identical to OSPF
Intra-AS Routing: OSPF (Open Shortest Path First)

## Slide 109: Hierarchical Routing
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
for each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort ToS; high for real time ToS)
integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
hierarchical OSPF in large domains.
Intra-AS Routing: OSPF—Advanced features (not in RIP)

## Slide 110: Hierarchical Routing
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers
Intra-AS Routing: Hiearchical OSPF

## Slide 111: Hierarchical Routing
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’s.
Intra-AS Routing: Hierarchical OSPF

## Slide 112: Hierarchical Routing
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASs.
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”
Inter-AS Routing—BGP

## Slide 113: Hierarchical Routing
when AS3 advertises a prefix to AS1:
  AS3 promises it will forward datagrams towards that prefix
  AS3 can aggregate prefixes in its advertisement
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP session: two BGP routers (“peers”) exchange BGP messages:
  advertising paths to different destination network prefixes (“path vector” protocol)
  exchanged over semi-permanent TCP connections
BGP
message
Inter-AS Routing—BGP

## Slide 114: Hierarchical Routing
AS3
AS2
3b
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
  1c can then use iBGP do distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
when router learns of new prefix, it creates entry for prefix in its forwarding table.
eBGP session
iBGP session
Inter-AS Routing—BGP distributing path information

## Slide 115: Hierarchical Routing
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: contains ASs through which prefix advertisement has passed: e.g., AS 67, AS 17
  NEXT-HOP: indicates specific internal-AS router to next-hop AS. (may be multiple links from current AS to next-hop-AS)
gateway router receiving route advertisement uses import policy to accept/decline
  e.g., never route through AS x
  policy-based routing
Inter-AS Routing—BGP routes and Path attributes

## Slide 116: Hierarchical Routing
router may learn about more than 1 route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria
Inter-AS Routing—BGP Route Selection

## Slide 117: Hierarchical Routing
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection
Inter-AS Routing—BGP Messages

## Slide 118: Hierarchical Routing
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Inter-AS Routing—BGP Routing Policy

## Slide 119: Hierarchical Routing
A advertises path AW to B
B advertises path BAW to X
Should B advertise path BAW to C?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Inter-AS Routing—BGP Routing Policy

## Slide 120: Hierarchical Routing
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance
Intra- vs Inter-AS Routing