## Slide 1: Data Link and Physical Layers and 10 GbE Protocol
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
September 12, 2014
Slides used and adapted judiciously from Computer Networking, A Top-Down Approach

## Slide 2: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet Switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 3: Link layer
goals:
understand principles behind link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks: Ethernet, VLANs
instantiation, implementation of various link layer technologies

## Slide 4: Link Layer
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link
global ISP

## Slide 5: Link Layer
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide rdt over link
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 6: Link Layer
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?
Services

## Slide 7: Link Layer
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time
Services

## Slide 8: Link Layer
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical
Where is the link layer implemented?

## Slide 9: Link Layer
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame
Adapters communicating

## Slide 10: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 11: Switches and Local Area Networks
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “number” represents 4 bits)
MAC (medium access control) addresses and
ARP (address resolution protocol)

## Slide 12: Switches and Local Area Networks
each adapter on LAN has unique LAN address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)
LAN (MAC) addresses and ARP

## Slide 13: Switches and Local Area Networks
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached
LAN (MAC) addresses and ARP

## Slide 14: Switches and Local Area Networks
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
LAN (MAC) addresses and ARP: Address
Resolution Protocol

## Slide 15: Switches and Local Area Networks
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  dest MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator
ARP: Address Resolution Protocol; Same LAN

## Slide 16: Switches and Local Area Networks
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
ARP: Address Resolution Protocol; different LAN

## Slide 17: Switches and Local Area Networks
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
ARP: Address Resolution Protocol; different LAN

## Slide 18: Switches and Local Area Networks
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222
ARP: Address Resolution Protocol; different LAN

## Slide 19: Switches and Local Area Networks
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
ARP: Address Resolution Protocol; different LAN

## Slide 20: Switches and Local Area Networks
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
ARP: Address Resolution Protocol; different LAN

## Slide 21: Switches and Local Area Networks
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
ARP: Address Resolution Protocol; different LAN

## Slide 22: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 23: Link and Physical Layer: Ethernet
“dominant” wired LAN technology:
cheap $20 for NIC
first widely used LAN technology
simpler, cheaper than token LANs and ATM
kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch

## Slide 24: Link and Physical Layer: Ethernet
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
star: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star
Ethernet Physical Topologies

## Slide 25: Link and Physical Layer: Ethernet
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type
Ethernet frame structure/format

## Slide 26: Link and Physical Layer: Ethernet
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type
Ethernet frame structure/format

## Slide 27: Link and Physical Layer: Ethernet
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesnt send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD wth binary backoff
Ethernet service abstraction and implementation

## Slide 28: Link and Physical Layer: Ethernet
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10G bps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer
IEEE 802.3 Ethernet Standards: link & physical layers

## Slide 29: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 30: Ethernet Switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 31: Ethernet Switch
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Switch: Multiple Simultaneous Transmission

## Slide 32: Ethernet Switch
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
Switch Forwarding Table

## Slide 33: Ethernet Switch
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
Switch: Self-learning

## Slide 34: Ethernet Switch
When frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */
Ethernet Switch
Switch: Frame filtering/forwarding

## Slide 35: Ethernet Switch
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, locaton unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send
on just one link
Example: Self-learning, forwarding

## Slide 36: Ethernet Switch
switches can be connected together
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
Interconnecting Switches

## Slide 37: Ethernet Switch
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
Example: Multiple Switch, Self-learning

## Slide 38: Ethernet Switch
to external
network
router
IP subnet
mail server
web server
Institutional Network

## Slide 39: Ethernet Switch
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
Switches vs Routers

## Slide 40: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 41: Multiple Access Links, Protocols
two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 42: Multiple Access Links, Protocols
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns
MAC Protocols: Taxonomy

## Slide 43: Multiple Access Links, Protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!
MAC Protocols: Tradeoffs

## Slide 44: Multiple Access Links, Protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  bluetooth, FDDI, token ring
MAC Protocols

## Slide 45: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 46: 10GbE (10 gigabit Ethernet)
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Data
/S/
/D/
/D/
/D/
/D/
/T/
/E/
Data
L3 Hdr
Data
L3 Hdr
L2 Hdr
Data
L3 Hdr
L2 Hdr
Gap
Eth Hdr
CRC
Preamble
011010010110100101101001011010010110100101101001011010010110100101101
Encode
Scrambler
Gearbox
PMA
64 bit
2 bit syncheader
16 bit
10.3125 Gigabits
/S/
/D/
/D/
/D/
/D/
/T/
/E/
Idle characters (/I/)
Notes: I need you to pay attention for 30 seconds,
I will discuss the details of a network stack.
Most of this you know, some you do not know
Going from the Data link layer to the physical layer:
The physical layer encodes an Ethernet frame into a sequence of 64 bit block.
Then for each 64bit block it adds 2 bit syncheaders.
That is why this is called 64/66bit encoding.
maintain eqaul number of zeros and ones, which we call it DC balance.
Where is /I/ characters?

## Slide 47: 10GbE (10 gigabit Ethernet)
Block Payload
Sync
0 8 16 24 32 40 48 56 65
D0
01
D1
D2
D3
D4
D5
D6
D7
0x1e
10
C0
C1
C2
C3
C4
C5
C6
C7
0x33
10
C0
C1
C2
C3
D5
D6
D7
0x78
10
D1
D2
D3
D4
D5
D6
D7
0x87
10
C1
C2
C3
C4
C5
C6
C7
0x99
10
D0
C2
C3
C4
C5
C6
C7
0xaa
10
D0
D1
C3
C4
C5
C6
C7
0xb4
10
D0
D1
D2
C4
C5
C6
C7
0xcc
10
D0
D1
D2
D3
C5
C6
C7
0xd2
10
D0
D1
D2
D3
D4
C6
C7
0xe1
10
D0
D1
D2
D3
D4
D5
C7
0xff
10
D0
D1
D2
D3
D4
D5
D6
Block Type
Data Block
/E/
/S/
/T/
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
64/66b PCS
PMA
PMD
Ethernet Frame
Gap
/S/
/D/
/D/
/D/
/D/
/T/
/E/
/S/
Start of Frame block
/T/
End of Frame block
/E/
Idle block
/D/
Data block

## Slide 48: 10GbE (10 gigabit Ethernet)
Interpacket gap, spacing, arrival time, …
Important metric for network measurements
  Can be improved with access to the PHY
Packet
Generation
Packet Capture
Characterization
Estimating bandwidth
Detecting timing channel
Increasing Throughput
IPG
Packet i
Packet i+1
IPD
Application
Transport
Network
Data Link
Physical
SoNIC: Software network interface card
Hyper-fidelity network measurements
Notes: Definition of IPD
How it is being used for network research.
We argue here that we Can improve them with access to the physical layer of network protocol stack

## Slide 49: 10GbE (10 gigabit Ethernet)
Valuable information: Idle characters
  Can provide precise timing base for control
    Each bit is ~97 ps wide
IPG
Packet i
Packet i+1
IPD
Application
Transport
Network
Data Link
Physical
SoNIC: Software network interface card
Hyper-fidelity network measurements
Notes: How can access to the physical layer of a network protocol stack improve network research?
Because of special characeters that only reside in the physical layer, called idle characters
Idle characters fills any gaps between two packets in 10 Gigabit Ethernet
  In particular, 10GbE protocol always sends 10 Gigabits per second, as a result each bit is about 100 ps wide, I need 7~8 of those to make up a idle characters
  Therefore, if we count the number of /I/s or the bits between two packets, we can measure the interpacket gaps very precisely.
For example, <click>

## Slide 50: 10GbE (10 gigabit Ethernet)
Valuable information: Idle characters
  Can provide precise timing base for control
    Each bit is ~97 ps wide
Packet
Generation
Packet Capture
Detecting timing channel
Packet i
Packet i+1
12 /I/s = 100bits = 9.7ns
Application
Transport
Network
Data Link
Physical
IPG
One Idle character (/I/)
= 7~8 bits
SoNIC: Software network interface card
Hyper-fidelity network measurements
Notes: * 12 /I/s can be translated into 100 bits, and consequently 9.7 ns
Therefore, by accessing and controlling bits, we can achieve unheard level of precision and control, which subsequently can improve network research applications that I previously mentioned.
specifically, for example, with 10GBE standard, there has to be minimum 12 characters, 7~8 bits and each bit is 97 ps wide.
For example, 10GbE protoco always sends at 10 Gigabit, each bit is 97 ps wide, I need 7~8 of those to make up a idle characters
Idle character, /I/ equals 7~8 bits

## Slide 51: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 52: Perspective
principles behind data link layer services:
  link layer addressing
  sharing a broadcast channel: multiple access
  error detection, correction
instantiation and implementation of various link layer technologies
  Ethernet
  switched LANS

## Slide 53: Perspective
Journey down protocol stack complete
Basic understanding of networking practices and principles
lots of interesting topics in data center and high performance systems and networks

## Slide 54: Before Next time
Project Proposal
  due today, Friday
  Meet with groups, TA, and professor
Lab1
  Single threaded TCP proxy
  Due today, Friday
Required review and reading
  “A 50-Gb/s IP Router,” Craig Partridge , Senior Member , Philip P. Carvey , Isidro Castineyra , Tom Clarke , John Rokosz , Joshua Seeger , Michael Sollins , Steve Starch , Benjamin Tober , Gregory D. Troxel , David Waitzman , Scott Winterble. IEEE/ACM Transactions on Networking (ToN), Volume 6, Issue 3 (June 1998), pages 237-248.
  http://ieeexplore.ieee.org/xpl/articleDetails.jsp?arnumber=700888
  http://citeseerx.ist.psu.edu/viewdoc/download?doi=10.1.1.129.3926&rep=rep1&type=pdf
Check website for updated schedule

## Slide 55: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 56: Virtual Local Area Networks (VLAN)
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering

## Slide 57: Virtual Local Area Networks (VLAN)
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 58: Virtual Local Area Networks (VLAN)
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers
Port-based VLAN

## Slide 59: Virtual Local Area Networks (VLAN)
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1
VLANs spanning multiple switches

## Slide 60
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type
802.1Q VLAN frame format
Virtual Local Area Networks (VLAN)

## Slide 61: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 62: Multiple Access Links, Protocols
two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch, host
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 63: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 64: An ideal multiple access protocol
given: broadcast channel of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 65: Multiple Access Links, Protocols
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns
MAC Protocols: Taxonomy

## Slide 66: Multiple Access Links, Protocols
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame
Channel Partitioning MAC protocols: TDMA

## Slide 67: Multiple Access Links, Protocols
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands
time
FDM cable
Channel Partitioning MAC protocols: FDMA

## Slide 68: Multiple Access Links, Protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA
Random Access Protocols

## Slide 69: Multiple Access Links, Protocols
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with prob. p until success
Slotted ALOHA

## Slide 70: Multiple Access Links, Protocols
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
Slotted ALOHA

## Slide 71: Multiple Access Links, Protocols
suppose: N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
max efficiency: find p* that maximizes Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
at best: channel
used for useful
transmissions 37%
of time!
!
Slotted ALOHA: Efficiency

## Slide 72: Multiple Access Links, Protocols
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]
Pure (unslotted) ALOHA

## Slide 73: Multiple Access Links, Protocols
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0-1,t0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n
= 1/(2e) = .18
even worse than slotted Aloha!
Pure (unslotted) ALOHA

## Slide 74: Multiple Access Links, Protocols
CSMA: listen before transmit:
if channel sensed idle: transmit entire frame
if channel sensed busy, defer transmission
human analogy: don’t interrupt others!
CSMA: Carrier Sense Multiple Access

## Slide 75: Multiple Access Links, Protocols
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes
CSMA collisions

## Slide 76: Multiple Access Links, Protocols
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
human analogy: the polite conversationalist
CSMA/CD (collision detection)

## Slide 77: Multiple Access Links, Protocols
spatial layout of nodes
CSMA/CD (collision detection)

## Slide 78: Multiple Access Links, Protocols
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions
Ethernet CSMA/CD algorithm

## Slide 79: Multiple Access Links, Protocols
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!
CSMA/CD efficiency

## Slide 80: Multiple Access Links, Protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 81: Multiple Access Links, Protocols
polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data
“Taking turns” MAC protocols

## Slide 82: Multiple Access Links, Protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T
“Taking turns” MAC protocols

## Slide 83
cable headend
CMTS
ISP
cable modem
termination system
multiple 40Mbps downstream (broadcast) channels
  single CMTS transmits into channels
multiple 30 Mbps upstream channels
  multiple access: all users contend for certain upstream channel time slots (others assigned)
cable
modem
splitter
…
…
Internet frames,TV channels, control transmitted
downstream at different frequencies
upstream Internet frames, TV control, transmitted
upstream at different frequencies in time slots
Multiple Access Links, Protocols
“Taking turns” MAC protocols: Cable Access Networks

## Slide 84
DOCSIS: data over cable service interface spec
FDM over upstream, downstream frequency channels
TDM upstream: some slots assigned, some have contention
  downstream MAP frame: assigns upstream slots
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots
MAP frame for
Interval [t1, t2]
Residences with cable modems
Downstream channel i
Upstream channel j
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS
Multiple Access Links, Protocols
“Taking turns” MAC protocols: Cable Access Networks

## Slide 85
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  bluetooth, FDDI, token ring
Multiple Access Links, Protocols
MAC Protocols

## Slide 86: Goals for Today
Link Layer and Physical Layer
  Abstraction / services
  Switches and Local Area Networks
    Addressing, ARP (address resolution protocol)
    Ethernet
    Ethernet switch
  Multiple Access Protocols
Data Center Network
  10GbE (10 Gigabit Ethernet)
Backup Slides
  Virtual Local Area Networks (VLAN)
  Multiple Access Protocols
  Putting it all together: A day and a life of a web request

## Slide 87: Putting it all together: A day and a life of a web req
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 88: Putting it all together: A day and a life of a web req
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser
Scenerio

## Slide 89: Putting it all together: A day and a life of a web req
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
Connecting to the Internet

## Slide 90: Putting it all together: A day and a life of a web req
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply
Connecting to the Internet

## Slide 91: Putting it all together: A day and a life of a web req
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply
ARP (before DNS, before HTTP)

## Slide 92: Putting it all together: A day and a life of a web req
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demux’ed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
Using DNS

## Slide 93: Putting it all together: A day and a life of a web req
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)
TCP Connection to carry HTTP

## Slide 94: Putting it all together: A day and a life of a web req
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
HTTP Request/Reply