## Slide 1: Data Center Networks and Basic Switching Technologies
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
September 15, 2014
Slides used and adapted judiciously from Computer Networking, A Top-Down Approach

## Slide 2: Where are we in the semester?
Overview and Basics
Data Center Networks
  Basic switching technologies (today)
  Data Center Network Topologies
  Software Routers (eg. Click, Routebricks, NetMap, Netslice)
  Alternative Switching Technologies
  Data Center Transport
Data Center Software Networking
  Software Defined networking (overview, control plane, data plane, NetFGPA)
  Data Center Traffic and Measurements
  Virtualizing Networks
  Middleboxes
Advanced Topics

## Slide 3: Goals for Today
Basic Switching Technologies/Router Architecture Overview
  See Section 4.3 in book
A 50-Gb/s IP Router
  Craig Partridge , Senior Member , Philip P. Carvey , Isidro Castineyra , Tom Clarke , John Rokosz , Joshua Seeger , Michael Sollins , Steve Starch , Benjamin Tober , Gregory D. Troxel , David Waitzman , Scott Winterble. IEEE/ACM Transactions on Networking (ToN), Volume 6, Issue 3 (June 1998), pages 237-248.

## Slide 4: Router Architecture Overview
two key router functions:
run routing algorithms/protocol (e.g. RIP, OSPF, BGP)
forwarding datagrams from incoming to outgoing link
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware)
routing, management
control plane (software)
forwarding tables computed,
pushed to input ports

## Slide 5: Router Architecture Overview
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
given datagram dest., lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric
Input Port Functions

## Slide 6: Router Architecture Overview
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfered from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar
Switching Fabrics

## Slide 7: Router Architecture Overview
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus
Switching via Memory: First Generation Routers

## Slide 8: Router Architecture Overview
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus
Switching via a bus

## Slide 9: Router Architecture Overview
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar
Switching via interconnection network

## Slide 10: Router Architecture Overview
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
Output Ports

## Slide 11: Router Architecture Overview
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
Output Port Queuing

## Slide 12: Router Architecture Overview
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N
How much buffering?

## Slide 13: Router Architecture Overview
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Input Port Queuing

## Slide 14: Goals for Today
Basic Switching Technologies/Router Architecture Overview
  See Section 4.3 in book
A 50-Gb/s IP Router
  Craig Partridge , Senior Member , Philip P. Carvey , Isidro Castineyra , Tom Clarke , John Rokosz , Joshua Seeger , Michael Sollins , Steve Starch , Benjamin Tober , Gregory D. Troxel , David Waitzman , Scott Winterble. IEEE/ACM Transactions on Networking (ToN), Volume 6, Issue 3 (June 1998), pages 237-248.

## Slide 15: Multigigabit Router (MGR)
Architecture
Network interfaces (Line cards)
Forwarding Engine
Network Processor
Switching Fabric
  .

## Slide 16: Multigigabit Router (MGR)
Contributions
Network interfaces (Line cards)
  Forwarding Engine distinct from line cards
Forwarding Engine
  Complete set of forwarding tables, fast path
  QoS
Network Processor
  Updates Routing Table
  Separates and handles slow path
Switching Fabric
  Switched backplane

## Slide 17: Multigigabit Router (MGR)
Forwarding Engine
RISC Architecture
  64-bit, 415MHz, Alpha 21164
  Quad issue (two integer and two floating point every cycle)
Cache
  Dcache and icache 8kB each
  Secondary Cache (Scache; unified, 96kB)
    Entire routing table fits in cache
  Tertiary cache (Bcache; 16MB)
    32 Byte cacheline
Hardware
Software

## Slide 18: Goals for Today
Basic Switching Technologies/Router Architecture Overview
  See Section 4.3 in book
A 50-Gb/s IP Router
  Craig Partridge , Senior Member , Philip P. Carvey , Isidro Castineyra , Tom Clarke , John Rokosz , Joshua Seeger , Michael Sollins , Steve Starch , Benjamin Tober , Gregory D. Troxel , David Waitzman , Scott Winterble. IEEE/ACM Transactions on Networking (ToN), Volume 6, Issue 3 (June 1998), pages 237-248.

## Slide 19: Before Next time
Project Proposal
  due this Friday, Sept 19
  Meet with groups, TA, and professor
Lab2
  Multi threaded TCP proxy
  Due this Friday, Sept 19
Required review and reading
  “A Guided Tour Through Datacenter Networking,” D. Abts and B. Felderman. Communications of the ACM (CACM), Volume 55, Issue 6 (June 2012), pages 44-51.
  http://dl.acm.org/citation.cfm?id=2184335
  http://wwwnew.cs.princeton.edu/courses/archive/spring13/cos598C/google-network.pdf
Check piazza: http://piazza.com/cornell/fall2014/cs5413
Check website for updated schedule