## Slide 1: Data Center Network Topologies: VL2 (Virtual Layer 2)
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
September 26, 2014
Slides used and adapted judiciously from COS-561, Advanced Computer Networks
At Princeton University

## Slide 2: Where are we in the semester?
Overview and Basics
Data Center Networks
  Basic switching technologies
  Data Center Network Topologies (today and Monday)
  Software Routers (eg. Click, Routebricks, NetMap, Netslice)
  Alternative Switching Technologies
  Data Center Transport
Data Center Software Networking
  Software Defined networking (overview, control plane, data plane, NetFGPA)
  Data Center Traffic and Measurements
  Virtualizing Networks
  Middleboxes
Advanced Topics

## Slide 3: Goals for Today
VL2: a scalable and flexible data center network
  A. Greenberg, J. R. Hamilton, N. Jain, S. Kandula, C. Kim, P. Lahiri, D. A. Maltz, P. Patel, and S. Sengupta. ACM Computer Communication Review (CCR), August 2009, pages 51-62.

## Slide 4: Architecture of Data Center Networks (DCN)

## Slide 5: Conventional DCN Problems
Static network assignment
Fragmentation of resource
Poor server to server connectivity
Traffics affects each other
Poor reliability and utilization
CR
CR
AR
AR
AR
AR
S
S
S
S
A
A
A
…
S
S
A
A
A
…
. . .
S
S
S
S
A
A
A
…
S
S
A
A
A
…
I want more
I have spare ones,
but…
1:5
1:80
1:240

## Slide 6: Objectives:
Uniform high capacity:
  Maximum rate of server to server traffic flow should be limited only by capacity on network cards
  Assigning servers to service should be independent of network topology
Performance isolation:
  Traffic of one service should not be affected by traffic of other services
Layer-2 semantics:
  Easily assign any server to any service
  Configure server with whatever IP address the service expects
  VM keeps the same IP address even after migration

## Slide 7: Measurements and Implications of DCN
Data-Center traffic analysis:
  Traffic volume between servers to entering/leaving data center is 4:1
  Demand for bandwidth between servers growing faster
  Network is the bottleneck of computation
Flow distribution analysis:
  Majority of flows are small, biggest flow size is 100MB
  The distribution of internal flows is simpler and more uniform
  50% times of 10 concurrent flows, 5% greater than 80 concurrent flows

## Slide 8: Measurements and Implications of DCN
Traffic matrix analysis:
  Poor summarizing of traffic patterns
  Instability of traffic patterns
Failure characteristics:
  Pattern of networking equipment failures: 95% < 1min, 98% < 1hr, 99.6% < 1 day, 0.09% > 10 days
  No obvious way to eliminate all failures from the top of the hierarchy

## Slide 9: Virtual Layer 2 Switch (VL2)
Design principle:
  Randomizing to cope with volatility:
    Using Valiant Load Balancing (VLB) to do destination independent traffic spreading across multiple intermediate nodes
  Building on proven networking technology:
    Using IP routing and forwarding technologies available in commodity switches
  Separating names from locators:
    Using directory system to maintain the mapping between names and locations
  Embracing end systems:
    A VL2 agent at each server

## Slide 10: Virtual Layer 2 Switch (VL2)
The Illusion of a Huge L2 Switch
1. L2 semantics
2. Uniform high capacity
3. Performance isolation
A
A
A
…
A
A
A
…
. . .
A
A
A
…
A
A
A
…
CR
CR
AR
AR
AR
AR
S
S
S
S
S
S
S
S
S
S
S
S
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
A
. . .

## Slide 11: VL2 Goals and Solutions
Solution
Approach
Objective
2. Uniform high capacity between servers
Enforce hose model using existing mechanisms only
Employ flat addressing
1. Layer-2 semantics
3. Performance Isolation
Guarantee bandwidth for hose-model traffic
Flow-based random traffic indirection (Valiant LB)
Name-location separation & resolution service
TCP
“Hose”: each node has ingress/egress bandwidth constraints

## Slide 12: Name/Location Separation
VL2
payload
ToR3
. . .
. . .
y
x
Servers use flat names
Switches run link-state routing and maintain only switch-level topology
Cope with host churns with very little overhead
y
z
payload
ToR4
z
ToR2
ToR4
ToR1
ToR3
y, z
payload
ToR3
z
. . .
Directory Service
…
x  ToR2
y  ToR3
z  ToR4
…
Lookup &
Response
…
x  ToR2
y  ToR3
z  ToR3
…
Allows to use low-cost switches
Protects network and hosts from host-state churn
Obviates host and switch reconfiguration
Notes: Lazy update of stale cache entries when packet erroneously reaches the old ToR (who forwards to the directory server, who updates with unicast)

## Slide 13: Clos Network Topology
VL2
. . .
. . .
TOR
20 Servers
Int
. . .
. . . . . .
Aggr
K aggr switches with D ports
20*(DK/4) Servers
. . .
. . . . . . . .
Offer huge aggr capacity & multi paths at modest cost
D (# of 10G ports) | Max DC size (# of Servers)
48 | 11,520
96 | 46,080
144 | 103,680
Notes: D/2 ports facing up, and D/2 ports facing down…

## Slide 14: Valiant Load Balancing: Indirection
x
y
payload
T3
y
z
payload
T5
z
IANY
IANY
IANY
IANY
Cope with arbitrary TMs with very little overhead
Links used for up paths
Links used for down paths
T1
T2
T3
T4
T5
T6
[ ECMP + IP Anycast ]
Harness huge bisection bandwidth
Obviate esoteric traffic engineering or optimization
Ensure robustness to failures
Work with switch mechanisms available today
1. Must spread traffic
2. Must ensure dst independence
Equal Cost Multi Path Forwarding

## Slide 15: VL2 Directory System
RSM
DS
RSM
DS
RSM
DS
Agent
. . .
Agent
. . .
. . .
Directory Servers
RSM Servers
2. Reply
2. Reply
1. Lookup
“Lookup”
5. Ack
2. Set
4. Ack
(6. Disseminate)
3. Replicate
1. Update
“Update”

## Slide 16: Evaluation
Uniform high capacity:
  All-to-all data shuffle stress test:
    75 servers, deliver 500MB
    Maximal achievable goodput is 62.3
    VL2 network efficiency as 58.8/62.3 = 94%

## Slide 17: Evaluation
Fairness:
  75 nodes
  Real data center workload
  Plot Jain’s fairness index for traffics to intermediate switches
Time (s)
0 100 200 300 400 500
1.00
0.98
0.96
0.94
Fairness Index
Aggr1 Aggr2 Aggr3

## Slide 18: Evaluation
Performance isolation:
  Two types of services:
    Service one: 18 servers do single TCP transfer all the time
    Service two: 19 servers starts a 8GB transfer over TCP every 2 seconds
    Service two: 19 servers burst short TCP connections

## Slide 19: Evaluation
Convergence after link failures
  75 servers
  All-to-all data shuffle
  Disconnect links between intermediate and aggregation switches

## Slide 20: Perspective
Studied the traffic pattern in a production data center and find the traffic patterns
Design, build and deploy every component of VL2 in an 80 server testbed
Apply VLB to randomly spreading traffics over multiple flows
Using flat address to split IP addresses and server names

## Slide 21: Critique
The extra servers are needed to support the VL2 directory system,:
  Brings more cost on devices
  Hard to be implemented for data centers with tens of thousands of servers.
All links and switches are working all the times, not power efficient
No evaluation of real time performance.

## Slide 22: VL2 vs. SEATTLE
Similar “virtual layer 2” abstraction
  Flat end-point addresses
  Indirection through intermediate node
Enterprise networks (Seattle)
  Hard to change hosts  directory on the switches
  Sparse traffic patterns  effectiveness of caching
  Predictable traffic patterns  no emphasis on TE
Data center networks (VL2)
  Easy to change hosts  move functionality to hosts
  Dense traffic matrix  reduce dependency on caching
  Unpredictable traffic patterns  ECMP and VLB for TE

## Slide 23: Other Data Center Architectures
VL2: A Scalable and Flexible Data Center Network
  consolidate layer-2/layer-3 into a “virtual layer 2”
  separating “naming” and “addressing”, also deal with dynamic load-balancing issues
A Scalable, Commodity Data Center Network Architecture
  a new Fat-tree “inter-connection” structure (topology) to increases “bi-section” bandwidth
    needs “new” addressing, forwarding/routing
Other Approaches:
PortLand: A Scalable Fault-Tolerant Layer 2 Data Center Network Fabric
BCube: A High-Performance, Server-centric Network Architecture for Modular Data Centers

## Slide 24: Ongoing Research

## Slide 25: Research Questions
What topology to use in data centers?
  Reducing wiring complexity
  Achieving high bisection bandwidth
  Exploiting capabilities of optics and wireless
Routing architecture?
  Flat layer-2 network vs. hybrid switch/router
  Flat vs. hierarchical addressing
How to perform traffic engineering?
  Over-engineering vs. adapting to load
  Server selection, VM placement, or optimizing routing
Virtualization of NICs, servers, switches, …

## Slide 26: Research Questions
Rethinking TCP congestion control?
  Low propagation delay and high bandwidth
  “Incast” problem leading to bursty packet loss
Division of labor for TE, access control, …
  VM, hypervisor, ToR, and core switches/routers
Reducing energy consumption
  Better load balancing vs. selective shutting down
Wide-area traffic engineering
  Selecting the least-loaded or closest data center
Security
  Preventing information leakage and attacks

## Slide 27: Before Next time
Project Progress
  Need to setup environment as soon as possible
  And meet with groups, TA, and professor
Lab0b – Getting Started with Fractus
  Use Fractus instead of Red Cloud
    Red Cloud instances will be terminated and state lost
  Due Monday, Sept 29
Required review and reading for Friday, September 26
  “The Click Modular Router”, E. Kohler, R. Morris, B. Chen, and M. F. Kaashoek. ACM Symposium on Operating Systems Principles (SOSP), December 1999, pages 217-231.
  http://dl.acm.org/citation.cfm?id=319166
  http://www.pdos.lcs.mit.edu/papers/click:sosp99/paper.pdf
Check piazza: http://piazza.com/cornell/fall2014/cs5413
Check website for updated schedule