## Slide 1: Software Routers: RouteBricks
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
October 3, 2014
Slides used and adapted judiciously from COS-561, Advanced Computer Networks
At Princeton University

## Slide 2: Where are we in the semester?
Overview and Basics
Data Center Networks
  Basic switching technologies
  Data Center Network Topologies (today and Monday)
  Software Routers (eg. Click, Routebricks, NetMap, Netslice)
  Alternative Switching Technologies
  Data Center Transport
Data Center Software Networking
  Software Defined networking (overview, control plane, data plane, NetFGPA)
  Data Center Traffic and Measurements
  Virtualizing Networks
  Middleboxes
Advanced Topics

## Slide 3: Goals for Today
RouteBricks: Exploiting Parallelism To Scale Software Routers
  M. Dobrescu, N. Egi, K. Argyraki, B.G. Chun, and K. Fall. ACM Symposium on Operating Systems Principles (SOSP), October 2009, pages 15-28

## Slide 4: Click Motivation
Flexibility
  Add new features
  Enable experimentation
Openness
  Allow users/researchers to build and extend
  (In contrast to most commercial routers)
Modularity
  Simplify the composition of existing features
  Simplify the addition of new features
Speed/efficiency
  Operation (optionally) in the operating system
  Without the user needing to grapple with OS internals

## Slide 5: Router as a Graph of Elements
Large number of small elements
  Each performing a simple packet function
  E.g., IP look-up, TTL decrement, buffering
Connected together in a graph
  Elements inputs/outputs snapped together
  Beyond elements in series to a graph
  E.g., packet duplication or classification
Packet flow as main organizational primitive
  Consistent with data-plane operations on a router
  (Larger elements needed for, say, control planes)

## Slide 6: Click Elements: Push vs. Pull
Packet hand-off between elements
  Directly inspired by properties of routers
  Annotations on packets to carry temporary state
Push processing
  Initiated by the source end
  E.g., when an unsolicited packet arrives (e.g., from a device)
Pull processing
  Initiated by the destination end
  E.g., to control timing of packet processing (e.g., based on a timer or packet scheduler)

## Slide 7: Click Language
Declarations
  Create elements
Connections
  Connect elements
Compound elements
  Combine multiple smaller elements, and treat as single, new element to use as a primitive class
Language extensions through element classes
  Configuration strings for individual elements
  Rather than syntactic extensions to the language
src :: FromDevice(eth0);
ctr :: Counter;
sink :: Discard;
src -> ctr;
ctr -> sink;

## Slide 8: Modular software forwarding plane: Click modular router
User-level
routing daemons
Control plane
Forwarding plane
Elements
  Small building blocks, performing simple operations
  Instances of C++ classes
Packets traverse a directed graph of elements
FromDevice(eth0)->CheckIPHeader(14)
->IPPrint->Discard;
Kohler, E., Morris, R., Chen, B., Jannotti, J., Kaashoek, M. F., The click modular router, ACM Trans. Comput. Syst. 18, 3 (Aug. 2000)
Andrea Bianco, Robert Birke, Davide Bolognesi, Jorge M. Finochietto, Giulio Galante, Marco Mellia, Click vs. Linux: Two Efficient Open-Source IP Network Stacks for Software Routers, HPSR 2005
Linux kernel
Click

## Slide 9
26-10-2014
PATS Research Group
9
Elements

## Slide 10
26-10-2014
PATS Research Group
10
Push connection
  Source pushes packets downstream
  Triggered by event, such as packet arrival
  Denoted by filled square or triangle
Agnostic connection
  Becomes push or pull depending on peer
  Denoted by double outline
Pull connection
  Destination pulls packets from upstream
  Packet transmission or scheduling
  Denoted by empty square or triangle
Push and Pull
Notes: 10

## Slide 11: Push and pull violations
26-10-2014
PATS Research Group
11

## Slide 12: Handlers and Control Socket
Access points for user interaction
  Appear like files in a file system
  Can have both read and write handlers
Examples
  Installing/removing forwarding-table entries
  Reporting measurement statistics
  Changing a maximum queue length
Control socket
  Allows other programs to call read/write handlers
  Command sent as single line of text to the server
  http://read.cs.ucla.edu/click/elements/controlsocket?s=llrpc

## Slide 13: Example: EtherSwitch Element
Ethernet switch
  Expects and produces Ethernet frames
  Each input/output pair of ports is a LAN
  Learning and forwarding switch among these LANs
Element properties
  Ports: any # of inputs, and same # of outputs
  Processing: push
Element handlers
  Table (read-only): returns port association table
  Timeout (read/write): returns/sets TIMEOUT
http://read.cs.ucla.edu/click/elements/etherswitch

## Slide 14: Implicit vs explicit queues
Implicit queue
Used by STREAM, Scout, etc.
Hard to control
Explicit queue
Led to push and pull, Click’s main idea
Contributes to high performance

## Slide 15: An Observation…
Click is widely used
  And the paper on Click is widely cited
Click elements are created by others
  Enabling an ecosystem of innovation
Take-away lesson
  Creating useful systems that others can use and extend has big impact in the research community
  And brings tremendous professional value
  Compensating amply for the time and energy 

## Slide 16: Improving software router performance: exploiting parallelism
Can you build a Tbps router out of PCs running Click?
  Not quite, but you can get close
RouteBricks: high-end software router
  Parallelism across servers and cores
  High-end servers: NUMA, multi-queue NICs
  RB4 prototype
    4 servers in full mesh acting as 4-port (10Gbps/port) router
    4  8.75 = 35Gbps
  Linearly scalable by adding servers (in theory)
Dobrescu, M., Egi, N., Argyraki, K., Chun, B., Fall, K., Iannaccone, G., Knies, A., Manesh, M., and Ratnasamy, S. RouteBricks: exploiting parallelism to scale software routers, SOSP 2009
Bolla, R. and Bruschi, R., PC-based software routers: high performance and application service support, PRESTO 2008

## Slide 17: Improving software router performance: specialized hardware
Jad Naous, Glen Gibb, Sara Bolouki, Nick McKeown, NetFPGA: Reusable Router Architecture for Experimental Research, PRESTO 2008
Spalink, T., Karlin, S., Peterson, L., and Gottlieb, Y., Building a robust software-based router using network processors, SOSP 2001
J. Turner, P. Crowley, J. Dehart, A. Freestone, B. Heller, F. Kuhms, S. Kumar, J. Lockwood, J. Lu, M.Wilson, C. Wiseman, D. Zar, Supercharging PlanetLab – A High Performance, Multi-Application, Overlay Network Platform, SIGCOMM 2007
Tilman Wolf, Challenges and applications for network-processor-based programmable routers, IEEE Sarnoff Symposium, Princeton, NJ, Mar. 2006
NetFPGA
Network processor

## Slide 18: Before Next time
Project Progress
  Need to setup environment as soon as possible
  And meet with groups, TA, and professor
Lab0b – Getting Started with Fractus
  Use Fractus instead of Red Cloud
    Red Cloud instances will be terminated and state lost
  Due Monday, Sept 29
Required review and reading for Friday, October 3
  RouteBrics
Check piazza: http://piazza.com/cornell/fall2014/cs5413
Check website for updated schedule