## Slide 1: Alternative Switching Technologies: Optical Circuit Switches
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
October 22, 2014
Slides from the “On the Feasibility of Completely Wireless Datacenters” at the ACM/IEEE
Symposium on Architectures for Networking and Communications Systems (ANCS),
October 2012.

## Slide 2: Where are we in the semester?
Overview and Basics
Data Center Networks
  Basic switching technologies
  Data Center Network Topologies (today and Monday)
  Software Routers (eg. Click, Routebricks, NetMap, Netslice)
  Alternative Switching Technologies
  Data Center Transport
Data Center Software Networking
  Software Defined networking (overview, control plane, data plane, NetFGPA)
  Data Center Traffic and Measurements
  Virtualizing Networks
  Middleboxes
Advanced Topics

## Slide 3: Goals for Today
On the Feasibility of Completely Wireless Datacenters
  J. Y. Shin, E. G. Sirer, H. Weatherspoon, and D. Kirovski, IEEE/ACM Transactions on Networking (ToN), Volume 21, Issue 5 (October 2013), pages 1666-1680.

## Slide 4: Current solutions for increasing data center network bandwidth
1. Hard to construct
2. Hard to expand
FatTree
BCube
Notes: Data intensive application operating on large volumes of data have motivated a lot of research work on data center networking. The basic problem is traditional tree-structure Ethernet are heavily over-subscribed when a large amount of data are shuffled across different server racks. Recent solutions propose to construct full bisection bandwidth network using commodity packet switches. Full bisection bandwidth network means each server can talk to another server at full NIC rate. Full bisection bandwidth is a nice property, but as you can see , these full bisection bandwidth network is quite complicated. They requires a lot of wires and we have to follow restricted rules to construct such networks. When the network is constructed, it is hard to expand because they requires major rewiring to expand.

## Slide 5: An alternative: hybrid packet/circuit switched data center network
Goal of this work:
  Feasibility: software design that enables efficient use of optical circuits
  Applicability: application performance over a hybrid network
Notes: In this work, we explore an alternate design that using optical circuit switching technology to construct a simple network
yet still achieve good performance. In particular, we propose a hybrid data center network which augment the existing
Electrical network with circuit switched optical paths. Optical paths can be provisioned dynamically to provide high bandwidth
For applications. The goal of our work is trying to answer the fundamental feasibility and applicability question of hybrid
data center network. We study the software design that can enable optical circuits in data center networks, and understand how application would perform over such a network.

## Slide 6: Optical circuit switching v.s. Electrical packet switching
 | Electrical packet switching | Optical circuit switching
Switching technology | Store and forward | Circuit switching
Switching capacity |  | 
Switching time |  | 
16x40Gbps at high end
e.g. Cisco CRS-1
320x100Gbps on market, e.g. Calient FiberConnect
Packet granularity
Less than 10ms
e.g. MEMS optical switch
Notes: Shorten for time 2:05, too long !!!
To understand our solution, let’s first take a look at the fundamental difference between electrical packet switching and optical circuit switching technologies. As you know, packet switches are based on the store-and-forward architecture.
Optical switches are circuit switched. There exist different technologies to realize optical circuit switching. For example, MEMS optical switches use MEMS mirror array to set up optical path by reflecting light beams between input and output ports.
These optical switches can switch at whatever rate modulated at input and output ports. Which can achieve very high switching capacity. For example, there already exist optical MEMS switches that can switch 320 optical links with 100Gbps rate.
On the contrast, today’s high end packet switched cisco routers can only switch 16 ports with 40gbps rate.
But the problem is that, the switching time of optical circuits are relatively long. Of course, packet switches can switch at packet granularity. But it takes a few ms to reconfigure optical paths. So, optical switches cannot provide full bisection bandwidth for all-to-all communication at packet granularity.

## Slide 7: Technology: Optical Circuit Switch
Lenses
Fixed
Mirror
Mirrors on Motors
Glass Fiber
Bundle
Input 1
Output 2
Output 1
Rotate Mirror
Full crossbar switch
Does not decode packets
Needs external scheduler
Notes: This animation shows the workings of an optical circuit switch.
Glass fiber brings a light beam from an input port to a lens, which focus the light as it exits the fiber.
The light beam then travels through the air and reflects off of a mirror, then another mirror, then a third mirror, and finally gets focused through a second lens, then travels over fiber to an output port.
Some mirrors are attached to motors, so if we want to choose a different output port, then we can rotate a mirror to select a different port.

## Slide 8: Wavelength Division Multiplexing
Electrical Packet Switch
1
2
3
4
5
6
7
8
WDM MUX
WDM DEMUX
Optical Circuit Switch
Superlink
10G
WDM Optical
Transceivers
No Transceivers
Required
80G
Notes: 1. Each 10 Gb/s transceiver in a LAG uses a non-overlapping wavelength (IEEE 802.1AX-2008 Link Aggregation Group).
2. This LAG, called a superlink, can fit onto a single fiber pair.
3. Superlinks are transparent to the packet switches, which deal only with LAGs.

## Slide 9: Optical circuit switching is promising despite slow switching time
Full bisection bandwidth at packet granularity
may not be necessary
[WREN09]: “…we find that traffic at the five edge switches exhibit an ON/OFF pattern… ”
[IMC09][HotNets09]: “Only a few ToRs are hot and most their traffic goes to a few other ToRs. …”
Notes: But why do we still believe that optical circuit still worth considering in data centers?
The reason is because many measurement studies have observed evidence of traffic concentration in data centers. For example, in IMC09, microsoft researcher measured the traffic of their production data centers and observe that ….,
In another paper, WREN09 , researcher observe ON/OFF traffic pattern on data center switches. All this suggestion that, applications
are not sending to all destinations at full speed anyway. Full bisection….. may not be necessary. So there is a potential that we can ….

## Slide 10: Hybrid packet/circuit switched network architecture
Optical circuit-switched network for high capacity transfer
Electrical packet-switched network for low latency delivery
Optical paths are provisioned rack-to-rack
  A simple and cost-effective choice
  Aggregate traffic on per-rack basis to better utilize optical circuits
Notes: So, our idea is, we augment the traffic tree-structure Ethernet with a simple, rack-to-rack optical circuit-switched network. The electrical packet-switched network is always available there for low latency delivery and high speed optical circuits are provisioned dynamic for high capacity transfer based on traffic demands.
Optical circuits are provisioned rack-to-rack so that we only need to one optical transcer and one optical fiber for one rack, to keep the network simple and reduce the cost. Given one optical circuits can send more than 40gbps, we can aggregate traffic on per-rack basis to ….

## Slide 11: Design requirements
Control plane:
  Traffic demand estimation
  Optical circuit configuration
Data plane:
  Dynamic traffic de-multiplexing
  Optimizing circuit utilization (optional)
Traffic demands
Notes: How can we manage optical circuits over such a hybrid network? We identify a set of design requirements that are needed.
On the control plane, we need to collect dynamic traffic demand and config …
When optical paths are provisioned, there exist two paths among different server racks. So on the data plane, we need to de-multiplex traffic to different network dynamically based on the current configuration. When optical paths are provisioned, applications may not be able to send fast enough to leverage optical paths. So the improve system performance, we also need to optimize circuit utilization. But this requirement is optional, the system can still work with out this.

## Slide 12: c-Through (a specific design)
No modification to applications and switches
Leverage end-hosts for traffic management
Centralized control for circuit configuration
Notes: There is many design choice to accomplish these design requirements. We have a detailed discussion in the paper about the design choices and their trade-offs. Please refer to the paper for the discussion. Here I will go directly to a specific system, called c-Through, we have built to manage optical circuits in a hybrid network. The design strategy for c-Through system is:
C-Through use a centralized controller for …, c-Through does not need any modification on …, it leverage end-hosts in the traffic management.

## Slide 13: c-Through - traffic demand estimation and traffic batching
Per-rack traffic demand vector
2. Packets are buffered per-flow
to avoid HOL blocking.
1. Transparent to applications.
Applications
Accomplish two requirements:
  Traffic demand estimation
  Pre-batch data to improve optical circuit utilization
Socket buffers
Notes: c-Through estimate traffic demands by simply enlarge output buffer limits of sockets. When an application is trying to send a large amount of data and network bandwidth is not enough, the data will be queued up in socket output buffers. But look at the occupancy of socket output buffer, we can infer which flow has high traffic demands. Then we can aggregate the socket buffer occupancy based on the destination rack to get a per-rack traffic demand vector. For example, in this vector, darker color means high traffic demands for a particular destination rack.
This technique is transparent to …, packets are buffered … But with this simple technique, we can accomplish two-requirements: (1) traffic demand estimation (2) Socket buffers can be used to pre-batch data when optical path is not available. When optical path is provisioned, we can release the data quickly to optical path to improve circuit utilization.

## Slide 14: c-Through - optical circuit configuration
Use Edmonds’ algorithm to compute optimal configuration
Many ways to reduce the control traffic overhead
Traffic demand
configuration
Controller
configuration
Notes: >2min too long !!!
C-Through use a centralize controller to collect traffic demands and configure optical circuits. The controller collect per-rack traffic demand vector from all the servers and aggregate them into a cross-rack traffic matrix. Then it compute a optimal configuration that can maximize the traffic volume that can be offload to optical network using a polynomial Edmonds’ alg. Everytime when the optical circuits are reconfigured, it will notified servers to tear down the path and configure it and then notify them about the new configuration. In a large data center, there could a significant overhead for the control traffic. But many ways can be used to reduce the overhead of control traffic.
For example, for traffic demand collection, servers only need to send to the controller when the demands change dramatically, traffic demand vectors can be aggregated within rack first, then send to the control. The configuration notification can be done using multicast.

## Slide 15: c-Through - traffic de-multiplexing
VLAN #1
Traffic
de-multiplexer
VLAN #1
VLAN #2
circuit configuration
traffic
VLAN #2
VLAN-based network isolation:
  No need to modify switches
  Avoid the instability caused by circuit reconfiguration
Traffic control on hosts:
  Controller informs hosts about the circuit configuration
  End-hosts tag packets accordingly
Notes: When optical path are configured, c-Through uses two techniques to realize traffic de-multiplexing.
First, we configure VLAN on all the ToR switches to isolate the electrical network and optical network into different VLANs.
As we mentioned before, it is a dynamic network. When optical circuits are reconfigured, the network topology is changing. If optical network and electrical network is organized into a unified network, this topology changes can cause instability in the control protocols in electrical network, such as spanning tree..
We isolate network to avoid the potential network instability caused by circuit reconfiguration.
C-Through leverage end-hosts to perform traffic de-multiplexing. Each server is configured with two virtual interface with VLAN1 and VLAN2 that mapping to electrical network and optical network. Everytime optical path is configured, controller will inform hosts about the current configuration. So a traffic de-multiplexer will tag packets accordingly to send them into appropriate network.

## Slide 16: Testbed setup
Ethernet switch
Emulated optical circuit switch
4Gbps links
100Mbps links
16 servers with 1Gbps NICs
Emulate a hybrid network on 48-port Ethernet switch
Optical circuit emulation
  Optical paths are available only when hosts are notified
  During reconfiguration, no host can use optical paths
  10 ms reconfiguration delay
Notes: > 2min, too long!!!!
We implement c-Through prototype and set up a small testbed to evaluate the performance. We have 16 servers in our testbed
Servers are connected with two networks .
(1) A electrical network with 100Mbps cross rack bandwidth, always available. (40:1) over-subscribed.
(2) A emulated optical circuit switched network with a 4Gbps links for each rack. We emulate optical circuit switching behavior over Ethernet switches. Optical paths are available only when notified. When optical path is provisioned, it can let all servers send at full rate. Controller reconfigure the optical path based on traffic demands. When decide to reconfigure, no hosts can use optical paths.
We emulate 10ms reconfiguration delay.

## Slide 17: Evaluation
Basic system performance:
  Can TCP exploit dynamic bandwidth quickly?
  Does traffic control on servers bring significant overhead?
  Does buffering unfairly increase delay of small flows?
Application performance:
  Bulk transfer (VM migration)?
  Loosely synchronized all-to-all communication (MapReduce)?
  Tightly synchronized all-to-all communication (MPI-FFT) ?
Yes
No
No
Yes
Yes
Yes
Notes: Shorten the slides
We perform evaluation on our testbed to answer a set of questions about system and application performance.

## Slide 18: TCP can exploit dynamic bandwidth quickly
Throughput ramps up
within 10 ms
Throughput stabilizes
within 100ms
Notes: We set up a TCP connection between src-dst pair and measure the TCP throughput when optical path is reconfigured every one second.
TCP protocol works reasonable well to exploit the dynamic bandwidth. We believe the reason is because RTT is small.

## Slide 19: MapReduce Overview
mapper
mapper
mapper
reducer
reducer
reducer
load
local write
data shuffling
output
file
write
output
file
output
file
Split 0
Split 1
Split 2
Input file
Concentrated traffic
in 64MB blocks
Concentrated traffic
in 64MB blocks
Independent transfers:
amenable to batching
Notes: > 2min , too long !!!!!
MapReduce application performance. To understand it, let’s first take a look at the structure of mapreduce application.
Two stages, several phases.

## Slide 20: MapReduce sort 10GB random data
Chart: 
| 128 KB | 50 MB | 100 MB | 300 MB | 500 MB
Completion Time | 793.2 | 251.2 | 164.7 | 153.8 | 156.9 | 155.8 | 135
c-Through varying socket buffer size limit (reconfiguration interval: 1 sec)
Electrical network
Full bisection bandwidth
c-Through
Completion time (s)
153s
135s
Notes: MapReduce is a parallel computing infrastructure used in many production data centers.
Three points: (1) significant speedup (2) Large buffer does not help too much for MapReduce application. Because application is not sending so aggressively.
In the first set of experiment, we reconfigure optical path every 1 second, and vary the socket buffer limits. If we use a very small buffer limit, … When we increase buffer limit to 50MB, close to optimal performance. Larger? No help , because 64MB block size.

## Slide 21: MapReduce sort 10GB random data
c-Through varying reconfiguration interval (socket buffer size limit: 100MB)
Chart: 
| 0.3 Sec | 0.5 Sec | 1.0 Sec | 3.0 Sec | 5.0 Sec
Completion Time | 793.2 | 153.2 | 145.4 | 155.1 | 168.8 | 189.4 | 135
Electrical network
Full bisection bandwidth
c-Through
168s
135s
Notes: In the second set, we fix the socket buffer limit to 100MB, and vary the reconfiguration interval. Still….
Even with 3 second reconfiguration, still close to optimal performance.

## Slide 22: Yahoo Gridmix benchmark
3 runs of 100 mixed jobs such as web query, web scan and sorting
200GB of uncompressed data, 50 GB of compressed data
Notes: What about more realistic mix jobs running simultaneously? Run Yahoo Gridmix.
100 mixed jobs with ……, 3 runs on different networks.
Still near optimal.

## Slide 23: Summary
Hybrid packet/circuit switched data center network
  c-Through demonstrates its feasibility
  Good performance even for applications with all to all traffic
Future directions to explore:
  The scaling property of hybrid data center networks
  Making applications circuit aware
  Power efficient data centers with optical circuits
Picture from Internet websites.
Notes: (1) Summarize the results.
(2) One of the first efforts exploring this design space, mention ucsd work ,
We believe that the hybrid architecture bring a new design with fundamentally different way of thinking. Which could
Leverage the best of both worlds: optics for bandwidth, electrical for low latency
(3) Future directions.

## Slide 24
 | Link Technology | Modifications Required | Working Prototype
Helios (SIGCOMM ‘10) | Optics w/ WDM 10G-180G (CWDM) 10G-400G (DWDM) | Switch Software | Glimmerglass, Fulcrum
c-Through (SIGCOMM ’10) | Optics (10G) | Host OS | Emulation
Flyways (SIGCOMM ‘11, HotNets ‘09) | Wireless (1G, 10m) | Unspecified | 
IBM System-S (GLOBECOM ‘09) | Optics (10G) | Host Application; Specific to Stream Processing | Calient, Nortel
HPC (SC ‘05) | Optics (10G) | Host NIC Hardware | 
Related Work

## Slide 25: Before Next time
Project Interim report
  Due Monday, October 27.
  And meet with groups, TA, and professor
Lab3 – Packet filter/sniffer
  Due tomorrow, Tuesday, October 21.
Lab1/2 redux due Friday, October 24
Fractus Upgrade: SAVE ALL YOUR DATA
  Fractus will be upgraded from October 28th to 30th
  Can use Red Cloud during upgrade period, then switch back to Fractus
Required review and reading for Wednesday, October 22
  “On the Feasibility of Completely Wireless Datacenters,” J. Y. Shin, E. G. Sirer, H. Weatherspoon, and D. Kirovski, IEEE/ACM Transactions on Networking (ToN), Volume 21, Issue 5 (October 2013), pages 1666-1680.
Check piazza: http://piazza.com/cornell/fall2014/cs5413
Check website for updated schedule