## Slide 1: Data Center Traffic and Measurements: SoNIC
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
November 12, 2014
Slides from USENIX symposium on Networked Systems Design and Implementation
(NSDI) 2013 presentation of “SoNIC: Precise Realtime Software Access and Control
of Wired Networks,”

## Slide 2: Where are we in the semester?
Overview and Basics
Data Center Networks
  Basic switching technologies
  Data Center Network Topologies (today and Monday)
  Software Routers (eg. Click, Routebricks, NetMap, Netslice)
  Alternative Switching Technologies
  Data Center Transport
Data Center Software Networking
  Software Defined networking (overview, control plane, data plane, NetFGPA)
  Data Center Traffic and Measurements
  Virtualizing Networks
  Middleboxes
Advanced Topics

## Slide 3: Goals for Today
Analysis and Network Traffic Characteristics of Data Centers in the wild
  T. Benson, A. Akella, and D. A. Maltz. In Proceedings of the 10th ACM SIGCOMM conference on Internet measurement (IMC), pp. 267-280. ACM, 2010.

## Slide 4: Interpacket Delay and Network Research
Interpacket gap, spacing, arrival time, …
Important metric for network research
  Can be improved with access to the PHY
Packet
Generation
Packet Capture
Characterization
Estimating bandwidth
Detecting timing channel
Increasing Throughput
IPG
Packet i
Packet i+1
IPD
Application
Transport
Network
Data Link
Physical
Notes: Definition of IPD
How it is being used for network research.
We argue here that we Can improve them with access to the physical layer of network protocol stack

## Slide 5: Network Research enlightened via the PHY
Valuable information: Idle characters
  Can provide precise timing base for control
    Each bit is ~97 ps wide
IPG
Packet i
Packet i+1
IPD
Application
Transport
Network
Data Link
Physical
Notes: How can access to the physical layer of a network protocol stack improve network research?
Because of special characeters that only reside in the physical layer, called idle characters
Idle characters fills any gaps between two packets in 10 Gigabit Ethernet
  In particular, 10GbE protocol always sends 10 Gigabits per second, as a result each bit is about 100 ps wide, I need 7~8 of those to make up a idle characters
  Therefore, if we count the number of /I/s or the bits between two packets, we can measure the interpacket gaps very precisely.
For example, <click>

## Slide 6: Network Research enlightened via the PHY
Valuable information: Idle characters
  Can provide precise timing base for control
    Each bit is ~97 ps wide
Packet
Generation
Packet Capture
Detecting timing channel
Packet i
Packet i+1
12 /I/s = 100bits = 9.7ns
Application
Transport
Network
Data Link
Physical
IPG
One Idle character (/I/)
= 7~8 bits
Notes: * 12 /I/s can be translated into 100 bits, and consequently 9.7 ns
Therefore, by accessing and controlling bits, we can achieve unheard level of precision and control, which subsequently can improve network research applications that I previously mentioned.
specifically, for example, with 10GBE standard, there has to be minimum 12 characters, 7~8 bits and each bit is 97 ps wide.
For example, 10GbE protoco always sends at 10 Gigabit, each bit is 97 ps wide, I need 7~8 of those to make up a idle characters
Idle character, /I/ equals 7~8 bits

## Slide 7
Principle #1: Precision
Precise network measurements is enabled via access to the physical layer (and the idle characters and bits within interpacket gap)
Notes: Our number one principle is precision.
Precision of network measurements can be significantly improved at sub-nanosecond resolution via access to the physical layer.

## Slide 8: How to control the idle characters (bits)?
Access to the entire stream is required
Issue1: The PHY is simply a black box
  No interface from NIC or OS
  Valuable information is invisible (discarded)
Issue2: Limited access to hardware
  We are network systems researchers
  a.k.a. we like software
Application
Transport
Network
Data Link
Physical
IPG
Packet i
Packet i+1
Packet i+2
Packet i
Packet i+1
Packet i+2
Packet i
Packet i+1
Packet i+2
Packet i
Packet i+1
Packet i+2
Packet i
Packet i+1
Notes: Then, are there any ways to access and control them?
* Unfortunately, (click), physical layer has been a black box to network researchers for a very long time
It is possible to access them with specialized hardware, such as costomized ASIC chips. However, we would do so in software for flexibility

## Slide 9
Principle #2: Software
Network Systems researchers need software access to the physical layer
Notes: So, the second principle is software.
We want to be able to control bits in the physical layer, as network systems researchers, we would want to do in software.

## Slide 10: Precision + Software = Physics equipment???
BiFocals [IMC’10 Freedman, Marian, Lee, Birman, Weatherspoon, Xu]
  Enabled novel network research
  Precision + Software =
  Laser + Oscilloscope + Offline analysis
  Allowed precise control in software
Limitations
  Offline (not realtime)
  Limited Buffering
  Expensive
Notes: In fact, we have done this. In our previous work called BiFocals, we were able to access and control idle characters in software to achieve unprecedented level of precision.
We used ….. To generate analog optical signals and … to capture optical signals to analyze them.
However, there are certain limitations.
- It is not a realtime tool
- can only capture 2.5 microseconds worth of data because of small buffer
- it is hals million dollars, and not portable

## Slide 11
Principle #3: Realtime
Network systems researchers need access and control of the physical layer (interpacket gap) continuously in realtime
Notes: Our last principle is realtime.
We would want achieve the same level of precision and control as in BiFocals, in realtime.

## Slide 12: Challenge
Goal: Control every bit in software in realtime
  Enable novel network research
Challenge
  Requires unprecedented software access to the PHY
Application
Transport
Network
Data Link
Physical
IPG
Packet i
Packet i+1
IPD
Notes: As a result, our ultimate goal is to control every single bit in software and in realtime, thus we can improve network research applications that rely on interpacket delays or gaps.
And therefore, the challenge here is how can we access the physical layer in software.

## Slide 13: Outline
Introduction
SoNIC: Software-defined Network Interface Card
  Background: 10GbE Network Stack
  Design
Network Research Applications
Conclusion
Notes: So, I am going to introduce SoNIC, software defined network interface card, and applications that sonic enables in this talk.

## Slide 14: SoNIC: Software-defined Network Interface Card
Implements the PHY in software
  Enabling control and access to every bit in realtime
  With commodity components
  Thus, enabling novel network research
How?
  Backgrounds: 10 GbE Network stack
  Design and implementation
    Hardware & Software
    Optimizations
Application
Transport
Network
Data Link
Physical
IPG
Packet i
Packet i+1
IPD
Notes: Main idea of SoNIC is to implement the physical layer in software.
So that we can access the entire network protocol stack similar to software defined radio for a wireless network.
Before I discuss the design and implementation of sonic, I will briefly discuss the 10GbE network stack to help you understand how sonic is designed first.
----- Meeting Notes (4/1/13 15:17) -----
don't forget to click,
Mention something about SDR here.

## Slide 15: 10GbE Network Stack
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Data
/S/
/D/
/D/
/D/
/D/
/T/
/E/
Data
L3 Hdr
Data
L3 Hdr
L2 Hdr
Data
L3 Hdr
L2 Hdr
Gap
Eth Hdr
CRC
Preamble
011010010110100101101001011010010110100101101001011010010110100101101
Encode
Scrambler
Gearbox
PMA
64 bit
2 bit syncheader
16 bit
10.3125 Gigabits
/S/
/D/
/D/
/D/
/D/
/T/
/E/
Idle characters (/I/)
Notes: I need you to pay attention for 30 seconds,
I will discuss the details of a network stack.
Most of this you know, some you do not know
Going from the Data link layer to the physical layer:
The physical layer encodes an Ethernet frame into a sequence of 64 bit block.
Then for each 64bit block it adds 2 bit syncheaders.
That is why this is called 64/66bit encoding.
maintain eqaul number of zeros and ones, which we call it DC balance.
Where is /I/ characters?

## Slide 16: 10GbE Network Stack
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Data
/S/
/D/
/D/
/D/
/D/
/T/
/E/
Data
L3 Hdr
Data
L3 Hdr
L2 Hdr
Data
L3 Hdr
L2 Hdr
Gap
Eth Hdr
CRC
Preamble
011010010110100101101001011010010110100101101001011010010110100101101
Encode
Scrambler
Gearbox
PMA
Commodity NIC
SW
HW
Packet i
Packet i+1
Packet i
Packet i+1

## Slide 17: 10GbE Network Stack
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Data
/S/
/D/
/D/
/D/
/D/
/T/
/E/
Data
L3 Hdr
Data
L3 Hdr
L2 Hdr
Data
L3 Hdr
L2 Hdr
Gap
Eth Hdr
CRC
Preamble
011010010110100101101001011010010110100101101001011010010110100101101
Encode
Scrambler
Gearbox
PMA
SoNIC
NetFPGA
Packet i
Packet i+1
SW
HW
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Encode
Scrambler
Gearbox
PMA
SW
HW
Notes: we are actually doing physical layer in software.

## Slide 18: SoNIC Design
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Data
/S/
/D/
/D/
/D/
/D/
/T/
/E/
Data
L3 Hdr
Data
L3 Hdr
L2 Hdr
Data
L3 Hdr
L2 Hdr
Gap
Eth Hdr
CRC
Preamble
011010010110100101101001011010010110100101101001011010010110100101101
Encode
Scrambler
Gearbox
PMA
SoNIC
SW
HW
Notes: Our approach was to separate what is sent in software and how it is in hardware
As I said in background, all these sublayes down in the physical layer do not manipulate bits, while all the layes above and including scrambler touches every bit.

## Slide 19: SoNIC Design and Architecture
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Data
/S/
/D/
/D/
/D/
/D/
/T/
/E/
Data
L3 Hdr
Data
L3 Hdr
L2 Hdr
Data
L3 Hdr
L2 Hdr
Gap
Eth Hdr
CRC
Preamble
011010010110100101101001011010010110100101101001011010010110100101101
Encode
Scrambler
Gearbox
PMA
SoNIC
SW
HW
TX MAC
TX PCS
Kernel
APP
RX MAC
RX PCS
Userspace
APP
Hardware
Gearbox
Transceiver
Blocksync
Transceiver
SFP+
Notes: This is overall design and architecture of SoNIC
Say I will discuss design, optimization, and interfae

## Slide 20: SoNIC Design: Hardware
SFP+
SFP+
FPGA
PCIeGen2
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
To deliver every bit from/to software
  High-speed transceivers
  PCIe Gen2 (=32Gbps)
Optimized DMA engine
SW
HW
PMD
PMA
Gearbox
Blocksync
Notes: we have a development board for hardware component
(Let’s not be too technical.)
The red here is where fiber is plugged and where optical signal is converted to digital signal and vice versa.
The purple here is than chops up a bitstream into smaller sized data and delivers them to the host machine.
We developed and optimized DMA engine to deliver two bitstreams from two physical port via a PCIe Generation 2 interface which can support up to 32 Gbps.

## Slide 21: SoNIC Design: Software
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Dedicated Kernel Threads
  TX / RX PCS, TX / RX MAC threads
  APP thread: Interface to userspace
TX MAC
TX PCS
Port 0
RX MAC
RX PCS
APP
RX MAC
RX PCS
TX MAC
TX PCS
Port 1
APP
Packet i
Packet i+1
SW
HW
Encode
Scrambler
Decode
Descrambler
Data Link
Notes: what are pictures (talk them through)
… in purple,
… in red

## Slide 22: SoNIC Design: Synchronization
TX MAC
TX PCS
Port 0
RX MAC
RX PCS
APP
RX MAC
RX PCS
TX MAC
TX PCS
Port 1
APP
SFP+
SFP+
FPGA
PCIeGen2
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Low-latency FIFOs
Pointer-polling
No Interrupts
SW
HW
Notes: It is very important to tightly synchronize cores and hardware and software to continuously process bits, because otherwise, broken link and lost packets.’
We do two things for this

## Slide 23: SoNIC Design: Optimizations
Physical
64/66b PCS
PMA
PMD
Encode
Scrambler
Gearbox
Decode
Descrambler
Blocksync
Data Link
Network
Transport
Application
Scrambler
CRC computation
DMA engine
Naïve Implementation | Optimized Implementation
s  state d  data for i = 0 63 do in  (d >> i) & 1 out  (in (s >> 38) (s >> 57))&1 s  (s << 1) ¦ out r  r ¦ (out << i) state  s end for | s  state d  data r  (s >> 6) (s >> 25) d r  r (r << 39) (r << 58) state  r
0.436 Gbps | 21 Gbps
Scrambler
Descrambler
Data Link
Notes: This is not enough, we still had to optimize our functional blocks to achieve realtime capability
For example, to generate one output bit to the medium, scrambler requires 59 preceding. This fine-grained dependency became the bottle of the PCS when we developed SoNIC.
So we optimized it to reduce a for loop which iterates 64 times to produce a 64bit value, as well as we significantly reduced the number of shift and xor operations to achieve high performance.
There are other optimizations we performed. They are discussed in the paper and I will not discuss them because of time limits.

## Slide 24: SoNIC Design: Interface and Control
Hardware control: ioctl syscall
I/O : character device interface
Sample C code for packet generation and capture
1: #include "sonic.h"
2:
3: struct sonic_pkt_gen_info info = {
4: .mode = 0,
5: .pkt_num = 1000000000UL,
6: .pkt_len = 1518,
7: .mac_src = "00:11:22:33:44:55",
8: .mac_dst = "aa:bb:cc:dd:ee:ff",
9: .ip_src = "192.168.0.1",
10: .ip_dst = "192.168.0.2",
11: .port_src = 5000,
12: .port_dst = 5000,
13: .idle = 12,
14: };
15:
16: /* OPEN DEVICE*/
17: fd1 = open(SONIC_CONTROL_PATH, O_RDWR);
18: fd2 = open(SONIC_PORT1_PATH, O_RDONLY);
19: /* CONFIG SONIC CARD FOR PACKET GEN*/
20: ioctl(fd1, SONIC_IOC_RESET)
21: ioctl(fd1, SONIC_IOC_SET_MODE, PKT_GEN_CAP)
22: ioctl(fd1, SONIC_IOC_PORT0_INFO_SET, &info)
23
24: /* START EXPERIMENT*/
25: ioctl(fd1, SONIC_IOC_START)
26: // wait till experiment finishes
27: ioctl(fd1, SONIC_IOC_STOP)
28:
29: /* CAPTURE PACKET */
30: while ((ret = read(fd2, buf, 65536)) > 0) {
31: // process data
32: }
33:
34: close(fd1);
35: close(fd2);
Notes: interface is a regular C
e.g., source C code for packet generation / caption
What is the significance of “12”?

## Slide 25: Outline
Introduction
SoNIC: Software-defined Network Interface Card
Network Research Applications
  Packet Generation
  Packet Capture
  Covert timing channel
Conclusion

## Slide 26: Network Research Applications
Interpacket delays and gaps
IPG
Packet i
Packet i+1
IPD
Application
Transport
Network
Data Link
Physical
Packet
Generation
Packet Capture
Detecting timing channel

## Slide 27: Packet Generation and Capture
Basic functions for network research
  Generation: SoNIC allows control of IPGs in # of /I/s
  Capture: SoNIC captures what was sent with IPGs in bits
1518B
1518B
1518B
1518B
1518B
TX MAC
TX PCS
RX MAC
RX PCS
APP
TX MAC
TX PCS
RX MAC
RX PCS
APP
9Gbps, IPD =13992 bits (1357ns)

## Slide 28: Packet Generation
1518B
1518B
1518B
1518B
1518B
TX MAC
TX PCS
RX MAC
RX PCS
APP
TX MAC
TX PCS
RX MAC
RX PCS
APP
Interpacket delays (ns)
CDF
9Gbps, IPD =13992 bits (1357ns)
CDF of generated IPDs
SoNIC allows precise control of IPGs
SoNIC
Zero variance!!!
Specialized NIC
Higher variance
Notes: ***** Don’t forget to tell what axis are
We validated what was generated with techniques similar to BiFocals using high-precision oscilloscope , and specialized NIC.
The key is that we generated and variance of interpacket delays was zero.
In other words, in this case, interpacket delays was always 13992 bits

## Slide 29: Packet Capture
CDF of captured IPDs
SoNIC captures what is sent
1518B
1518B
1518B
1518B
1518B
TX MAC
TX PCS
RX MAC
RX PCS
APP
TX MAC
TX PCS
RX MAC
RX PCS
APP
Interpacket delays (ns)
9Gbps, IPD =13992 bits (1357ns)
CDF

## Slide 30: Covert Timing Channel
Embedding signals into interpacket gaps.
  Large gap: ‘1’
  Small gap: ‘0’
Covert timing channel by modulating IPGs at 100ns
Packet i
Packet i+1
Packet i
Packet i+1
TX MAC
TX PCS
RX MAC
RX PCS
APP
TX MAC
TX PCS
RX MAC
RX PCS
APP
  Overt channel at 3 Gbps
  Covert channel at 250 kbps
  Over 4-hops with < 1% BER
Notes: Takeaways:
Covert timing channel by modulating IPG
with overt channel 3 Gbps
with covert channel .25Mbps

## Slide 31: Covert Timing Channel
TX MAC
TX PCS
RX MAC
RX PCS
APP
‘1’: 3562 + 128 /I/s
‘0’: 3562 – 128 /I/s
‘1’: 3562 + a /I/s
‘0’: 3562 – a /I/s
‘0’
‘1’
Interpacket delays (ns)
Modulating IPGS at 100ns scale (=128 /I/s)
3562 /I/s
3562 - 128 /I/s
3562 + 128 /I/s
TX MAC
TX PCS
RX MAC
RX PCS
APP
CDF
BER = 0.37%
Notes: BER = 0.0037
Data rate = 0.2 Mbps
128 /I/ = 102.4 ns

## Slide 32: Contributions
Network Research
  Unprecedented access to the PHY with commodity hardware
  A platform for cross-network-layer research
  Can improve network research applications
Engineering
  Precise control of interpacket gaps (delays)
  Design and implementation of the PHY in software
  Novel scalable hardware design
  Optimizations / Parallelism
Status
  Measurements in large scale: DCN, GENI, 40 GbE
Notes: In two succinct sentences…
We developed sonic to achieve unprecedented access to the physical layer with commodity hardware so that cross-network-layer research becomes possible.
We carefully designed and did a lot of optimizations to achieve precise realtime software access to the physical layer.
we are current integrating sonic board into data center network, and geni testbeds for large scale measurements,
And trying to scale up sonic board to support 40GbE.

## Slide 33: Conclusion
Precise Realtime Software Access to the PHY
Commodity components
  An FPGA development board, Intel architecture
Network applications
  Network measurements
  Network characterization
  Network steganography
Webpage: http://sonic.cs.cornell.edu
  SoNIC is available Open Source.

## Slide 34: Before Next time
Project Interim report
  Due Monday, November 24.
  And meet with groups, TA, and professor
Fractus Upgrade: Should be back online
Required review and reading for Friday, November 14
  Timing is Everything: Accurate, Minimum Overhead, Available Bandwidth Estimation in High-speed Wired Networks, H. Wang, K. Lee, E. Li, C. L. Lim, A. Tang, and H. Weatherspoon. ACM SIGCOMM Internet Measurement Conference (IMC), November 2014.
  http://conferences2.sigcomm.org/imc/2014/papers/p407.pdf
Check piazza: http://piazza.com/cornell/fall2014/cs5413
Check website for updated schedule