## Slide 1: Data Center Traffic and Measurements: Available Bandwidth Estimation
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
November 14, 2014
Slides from ACM SIGCOMM conference on Internet measurement (IMC), 2014,
presentation of “MinProbe: Accurate, Minimum Overhead, Available Bandwidth
Estimation in High Speed Wired Networks”

## Slide 2: Where are we in the semester?
Overview and Basics
Data Center Networks
  Basic switching technologies
  Data Center Network Topologies (today and Monday)
  Software Routers (eg. Click, Routebricks, NetMap, Netslice)
  Alternative Switching Technologies
  Data Center Transport
Data Center Software Networking
  Software Defined networking (overview, control plane, data plane, NetFGPA)
  Data Center Traffic and Measurements
  Virtualizing Networks
  Middleboxes
Advanced Topics

## Slide 3: Goals for Today
MinProbe: Accurate, Minimum Overhead, Available Bandwidth Estimation in High Speed Wired Networks
  Ki Suh Lee, Erluo Li, ChiunLin Lim, Kevin Tang and Hakim Weatherspoon. In Proceedings of the 14th ACM SIGCOMM conference on Internet measurement (IMC), November 2014.

## Slide 4: Available Bandwidth Estimation
Basic building block
  Network Protocol
  Networked Systems
  Distributed Systems
Which of the two paths has more available bandwidth?
End-to-end: How to measure without access to anything in the network?
How do I measure with minimum overhead?
Notes: 1’20”

## Slide 5: Available Bandwidth Estimation
Passive Measurement
  Polling counters: Port Stats or Flow Stats
Active Measurement
  Probe Packets: Packet Pair or Packet Train
Probe Packets:
Notes: We are going to use active probe because we assume autonomous system.

## Slide 6: Active Measurement
Narrow link: least capacity
Tight link: least available bandwidth
Narrow link
Network Capacity
Cross Traffic
Available Bandwidth
Tight link
Notes: Quick example
Narrow link is 2 Gbps
Tight link is

## Slide 7: Active Measurement
Estimate available bandwidth by saturating the tight link
Estimate Available Bandwidth?
Saturate/Congest Tight Link
Packet Queuing Delays Increase
7
Narrow link
Network Capacity
Cross Traffic
Available Bandwidth
Measuring (Increased) Queuing Delay
Tight link

## Slide 8: Active Measurement
Estimate available bandwidth by saturating the tight link
Rate
Probe Train #
Narrow link
Network Capacity
Cross Traffic
LA1 == LB1, no congestion
LA1
LB1
1Gbps
1Gbps
LA8 < LB8, congestion!
LA8
LB8
8Gbps
6Gbps
LA4 == LB4, no congestion
LA4
LB4
4Gbps
4Gbps
Available Bandwidth
Tight link
Notes: Can also put the actual figure up.
----- Meeting Notes (11/6/14 13:26) -----
Circle the knee,
4 figures.

## Slide 9
By measuring the increase in packet train length*, we can compute the queuing delay experienced, hence estimate the available bandwidth.
* Increase in packet train length == increase in sum of inter-packet gap
Notes: Increase

## Slide 10: Limitations of Available Bandwidth Estimation
Intrusive/Expensive
  100s of probe packets per packet train
Inaccurate
  Especially in high speed network
Does not work well for bursty traffic

## Slide 11: Goals of Available Bandwidth Estimation
Cheap
  Use as little probe packets as possible
Accurate
  How close is the estimation to the actual value
Works for all traffic patterns
Notes: Challenges comes after problem.
Cheap, accurate.

## Slide 12: MinProbe: Bandwidth Estimation in PHY
Cheap
  Use as little probe packets as possible
  100s of probe packets per train 20 packets per train
  Using application traffic as probe
Accurate
  How close is the estimation to the actual value
  Error < 0.4Gbps, with a resolution of 0.1Gbps
Works for all traffic patterns
  Works with bursty cross traffic
Notes: Understand available bandwidth estimation,
Challenges
-overhead
-accurate
-works for all patterns
Change challenge to goal

## Slide 13: Outline
Introduction
Challenges
Design: MinProbe
Evaluation
Conclusion
Notes: ----- Meeting Notes (10/20/14 16:35) -----
Goal slide:
Two slides.
Cheap
-- 20 packets, application packets
Accurate
-- 0.5Gbps error
Work high bw
-- 10Gbps
----- Meeting Notes (10/30/14 15:49) -----
5 to 6 minues.

## Slide 14: Challenges
LA8
LB8
Cannot Control at 100ps
Cannot Measure at 100ps
Notes: ?
Summary: two basic issues.
At the sender end, in order to generate accurate probe rate, need fine control of packet timing at 100ps.
What can commodity machine do? forwarding.
Incoming rate is accurately controlled with increase rate.
Linux kernel forwarding lost control on timing.
Similarly, intel dpdk does better at lower data rate, but still have no control over high data rate.
Takeaway, with commodity machine, obtaining the level of control to generate accurate probe rate is not possible.
Similarly, the problem of measuring packet timing at the receiver end is also difficult.
----- Meeting Notes (11/6/14 13:57) -----
10Gbps every bit is 100ps.
In userspace we generated packet with instantenous rate from 0.1 Gbps, each pair of packet
Experiment is simple, we have one forwarding element.
The batching
slow down and clear.
Two lines to emphasize

## Slide 15: Challenges
State-of-art (software) tools do not work at high speed because they cannot control and capture inter-packet spacing with required precision.
LA8
LB8
Cannot Control at 100ps
Cannot Measure at 100ps
Notes: ?
Summary: two basic issues.
At the sender end, in order to generate accurate probe rate, need fine control of packet timing at 100ps.
What can commodity machine do? forwarding.
Incoming rate is accurately controlled with increase rate.
Linux kernel forwarding lost control on timing.
Similarly, intel dpdk does better at lower data rate, but still have no control over high data rate.
Takeaway, with commodity machine, obtaining the level of control to generate accurate probe rate is not possible.
Similarly, the problem of measuring packet timing at the receiver end is also difficult.
----- Meeting Notes (11/6/14 13:57) -----
10Gbps every bit is 100ps.
In userspace we generated packet with instantenous rate from 0.1 Gbps, each pair of packet
Experiment is simple, we have one forwarding element.
The batching
slow down and clear.
Two lines to emphasize

## Slide 16: Outline
Introduction
Challenges
Design: MinProbe
Evaluation
Conclusion
Notes: ----- Meeting Notes (10/20/14 16:35) -----
Goal slide:
Two slides.
Cheap
-- 20 packets, application packets
Accurate
-- 0.5Gbps error
Work high bw
-- 10Gbps
----- Meeting Notes (10/30/14 15:49) -----
5 to 6 minues.
----- Meeting Notes (11/6/14 13:57) -----
Missing transition
A slide with red font

## Slide 17
MinProbe can accurately control and measure inter-packet gaps, thus can accurately control and measure probe train lengths, enabling accurate available bandwidth estimation.
Notes: ----- Meeting Notes (10/20/14 16:35) -----
Goal slide:
Two slides.
Cheap
-- 20 packets, application packets
Accurate
-- 0.5Gbps error
Work high bw
-- 10Gbps
----- Meeting Notes (10/30/14 15:49) -----
5 to 6 minues.
----- Meeting Notes (11/6/14 13:57) -----
Missing transition
A slide with red font

## Slide 18: MinProbe: Better Accuracy
Application
Transport
Network
Data Link
Physical
Packet i
Packet i+1
Packet i+2
Notes: ----- Meeting Notes (10/17/14 17:10) -----
Modulating packet at PHY layer
----- Meeting Notes (10/20/14 16:35) -----
always sending bits
fill with idle.
key is access / control idle in phy layer
given this, we can precisely generate packet train, and measure packet train.
----- Meeting Notes (10/21/14 21:24) -----
Need to mention that it is sufficient to measure with packet gap

## Slide 19: MinProbe: Better Accuracy
Idle Characters (/I/)
  Each bit ~100 picoseconds
  7~8 bit special character in the physical layer
  700~800 picoseconds to transmit
  Only in PHY
Packet i
Packet i+1
Packet i+2
Application
Transport
Network
Data Link
Physical
Notes: ----- Meeting Notes (10/17/14 17:10) -----
Modulating packet at PHY layer
----- Meeting Notes (10/20/14 16:35) -----
always sending bits
fill with idle.
key is access / control idle in phy layer
given this, we can precisely generate packet train, and measure packet train.
----- Meeting Notes (10/21/14 21:24) -----
Need to mention that it is sufficient to measure with packet gap

## Slide 20: MinProbe: Better Accuracy
Probe Generation
1.0Gbps
Rate
Probe #
4.0Gbps
8.0Gbps
By modulating Inter-packet gap at PHY layer,
we can generate accurate probe rate.
1500 B
1500 B
1500 B
382 /I/s
382 /I/s
8Gbps
1500 B
1500 B
1500 B
2290 /I/s
2290 /I/s
4Gbps
1500 B
1500 B
1500 B
11374 /I/s
11374 /I/s
1Gbps
Notes: Emphasize exact amount. That is what makes us accurate.

## Slide 21: MinProbe: Better Accuracy
Probe Generation
1.0Gbps
Rate
Probe #
4.0Gbps
8.0Gbps
Notes: Emphasize exact amount. That is what makes us accurate.

## Slide 22: MinProbe: Better Accuracy
With shared N and (Rmin, Rstep, Rmax)
Emulate existing bandwidth estimation algorithm
  Pathload, Pathchirp, SLoPS …
1.0Gbps
Rate
Probe #
4.0Gbps
8.0Gbps
…
…
Notes: If sender and receiver both share certain information. Number of packet in a train.

## Slide 23: MinProbe: Low Overhead
Reduce the # of probe packets required
# of probe packet per probe train | Error (%)
5 | +15%
20 | -1%
40 | -2%
60 | -3%
80 | -3%
100 (Pathload) | -4%
Notes: Minprobe also reduces the number of probe packet we need in a packet train. The intuition is that because we have a more accurate instrumentation to the network, you need less probe to obtain a similar level of accuracy.

## Slide 24: MinProbe: Very Low Overhead
SoNIC (NSDI 2013)
Incoming Traffic
Modulated
Probe Traffic
MinProbe Middlebox
IPG Tx/Rx
Forwarding Path
Mbox Daemon
Estimator
Flow Table
Mbox Ctrl
Userspace
Kernel space
IPG Tx/Rx
Estimator
Notes: To further lower the overhead, we designed minprobe to be a middlebox.
Based on the sonic platform in NSDI 2013
It is very similar to a software switch, the datapath is in kernel and hardware.
The key component in the datapath is the module to modify the interpacket gap and measure the received interpacket gap.
The estimator communicates with the kernel datapath through a daemon and executes the estimation algorithm.

## Slide 25: MinProbe: Bandwidth Estimation in PHY
Incoming traffic
Packet Size 792 Bytes
200 /I/s @ 8Gbps
Modulated traffic
Modulated traffic
Un-modulated traffic
200 /I/s @ 8Gbps
Notes: Let me give you an example on how do we module the interpacket gap.
Here we have two flows that go through the middelbox and we are trying to modulate one of the flow.
The graph shows the interpacket gap distribution of both flows.
We modulated the red flow to generate a probe train of 8Gbps by modulating each interpacket gap to 200 idle characters, for a packet size of 792 bytes.
----- Meeting Notes (11/6/14 14:04) -----
Probability distribution
x-axis
two flow

## Slide 26: Outline
Introduction
Challenges
Design: MinProbe
Evaluation
Conclusion

## Slide 27: Questions:
Can MinProbe accurately estimate avail-bw at 10Gbps?
Can existing estimation algorithms work with MinProbe?
How do the following parameters affect accuracy?
  Packet train length
  probe packet size distribution
  cross packet size distribution
  cross packet burstiness
Does MinProbe work in the wild, Internet?
Does MinProbe work in rate limiting environments?
Can MinProbe accurately estimate avail-bw at 10Gbps?
Can existing estimation algorithms work with MinProbe?
How do the following parameters affect accuracy?
  Packet train length
  probe packet size distribution
  cross packet size distribution
  cross packet burstiness
Does MinProbe work in the wild, Internet?
Does MinProbe work in rate limiting environments?

## Slide 28: Experiment Setup
Controlled Environment
National Lambda Rail
NYC
Cornell(NYC)
Boston
Chicago
Cleveland

## Slide 29: MinProbe: Can we measure at 10Gbps?
Cross Traffic
tight link
Probe Traffic
MinProbe
MinProbe
10Gbps
Probe Traffic
Cross Traffic, paced at 1.0, 3.0, 6.0, 8.0Gbps

## Slide 30: MinProbe: Can we measure at 10Gbps?
Cross Traffic
10Gbps
tight link
MinProbe
MinProbe
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Cross Traffic, paced at 1.0, 3.0, 6.0, 8.0Gbps
Probe Traffic

## Slide 31: MinProbe: Can we measure at 10Gbps?
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 2Gbps
Cross Traffic 8Gbps
0.1Gbps
8.1Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 32: MinProbe: Can we measure at 10Gbps?
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 2Gbps
Cross Traffic 8Gbps
0.2Gbps
8.2Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 33: MinProbe: Can we measure at 10Gbps?
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 2Gbps
Cross Traffic 8Gbps
0.3Gbps
8.3Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 34: MinProbe: Can we measure at 10Gbps?
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 2Gbps
Cross Traffic 8Gbps
1.0Gbps
9.0Gbps
1.9Gbps
9.9Gbps
2.0Gbps
Queued
10.0Gbps
3.0Gbps
Queued
10.0Gbps
4.0Gbps
Queued
10.0Gbps
5.0Gbps
Queued
10.0Gbps
6.0Gbps
Queued
10.0Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 35: MinProbe: Can we measure at 10Gbps?
10Gbps
Available Bandwidth = 4Gbps
Cross Traffic 6Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 36: MinProbe: Can we measure at 10Gbps?
10Gbps
Available Bandwidth = 7Gbps
Cross Traffic 3Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 37: MinProbe: Can we measure at 10Gbps?
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 9Gbps
Cross Traffic 1Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 38: MinProbe: Can we measure at 10Gbps?
10Gbps
Notes: ----- Meeting Notes (1/24/14 10:03) -----
Robustness: Forward error correction
----- Meeting Notes (10/20/14 16:35) -----
Map
Show one at a time.
----- Meeting Notes (11/6/14 14:13) -----
Make this bigger.

## Slide 39: MinProbe: National Lambda Rail
10Gbps
NYC
Cornell(NYC)
Cornell(Ithaca)
Boston
Chicago
Cleveland
Notes: ----- Meeting Notes (1/24/14 10:03) -----
Robustness: Forward error correction
----- Meeting Notes (10/20/14 16:35) -----
Map
Show one at a time.

## Slide 40: Questions:
Can MinProbe accurately estimate avail-bw at 10Gbps?
Can existing estimation algorithms work with MinProbe?
How do the following parameters affect accuracy?
  Packet train length
  probe packet size distribution
  cross packet size distribution
  cross packet burstiness
Does MinProbe work in the wild, Internet?
Does MinProbe work in rate limiting environments?

## Slide 41: MinProbe: In rate limiting environment?
Rate Limiters may be an issue?
  Provisioned 1Gbps virtual network
  If the probe train is less than 1200 packets, no packet loss
No
Notes: ----- Meeting Notes (1/24/14 10:03) -----
Robustness: Forward error correction
----- Meeting Notes (10/20/14 16:35) -----
Map
Show one at a time.

## Slide 42: Outline
Introduction
Challenges
Design: MinProbe
Evaluation
Conclusion
Notes: ----- Meeting Notes (10/20/14 16:35) -----
Goal slide:
Two slides.
Cheap
-- 20 packets, application packets
Accurate
-- 0.5Gbps error
Work high bw
-- 10Gbps
----- Meeting Notes (10/30/14 15:49) -----
5 to 6 minues.

## Slide 43: Conclusion
Modulation of probe packets in PHY
Accurate control & measure of packet timing
Enabled available bandwidth estimation in 10Gbps
Accurate, Minimum Overhead, Available Bandwidth Estimation in High Speed Wired Networks

## Slide 44: Before Next time
Project Interim report
  Due Monday, November 24.
  And meet with groups, TA, and professor
Fractus Upgrade: Should be back online
Required review and reading for Monday, November 17
  The Xen-Blanket: Virtualize Once, Run Everywhere, D. Williams, H. Jamjoom, and H. Weatherspoon. ACM European Conference on Computer Systems (EuroSys), April 2012, pages 113-126.
  http://dl.acm.org/citation.cfm?id=2168849
  http://fireless.cs.cornell.edu/publications/xen-blanket.pdf
Check piazza: http://piazza.com/cornell/fall2014/cs5413
Check website for updated schedule