## Slide 1: Data Center Virtualization: VirtualWire
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
November 21, 2014
Slides from USENIX Workshop on Hot Topics in Cloud Computing (HotCloud) 2014
presentation and Dan Williams dissertation

## Slide 2: Where are we in the semester?
Overview and Basics
Data Center Networks
  Basic switching technologies
  Data Center Network Topologies (today and Monday)
  Software Routers (eg. Click, Routebricks, NetMap, Netslice)
  Alternative Switching Technologies
  Data Center Transport
Data Center Software Networking
  Software Defined networking (overview, control plane, data plane, NetFGPA)
  Data Center Traffic and Measurements
  Virtualizing Networks
  Middleboxes
Advanced Topics

## Slide 3: Goals for Today
VirtualWires for Live Migrating Virtual Networks across Clouds
  D. Williams, H. Jamjoom, Z. Jiang, and H. Weatherspoon. IBM Tech. Rep. RC25378, April 2013.

## Slide 4: Control of cloud networks
Enterprise Workloads
VM
VM
VM
VM
VM
Supercloud
VM
Cloud Interoperability
(The Xen-Blanket)
User Control of Cloud Networks
(VirtualWire)
Efficient Cloud Resource Utilization
(Overdriver)
Cloud interoperability
User control of cloud networks
Third-Party Clouds

## Slide 5: current clouds lack control over network
Cloud networks are provider-centric
  Control logic that encodes flow policies is implemented by provider
  Provider decides if low-level network features (e.g., VLANs, IP addresses, etc.) are supported
VM
Use APIs to specify addressing, access control, flow policies, etc
VM
Management Tools
Virtual Network
CLOUD USER
CLOUD PROVIDER
support rich network features
Control Logic (virtual switches, routers, etc)
What virtual network abstraction should a cloud provider expose?

## Slide 6: virtualwire
Key Insight: move control logic to user
Virtualized equivalents of network components
  Open vswitch, Cisco Nexus 1000V, NetSim, Click router, etc.
Provider just needs to enable connectivity
  Connect/disconnect
VirtualWire connectors
  Point-to-point layer-2 tunnels
Control Logic (virtual switches, routers, etc)
VM
Configure using native interfaces
VM
Management Tools
Virtual Network
Use APIs to specify peerings
support location independent tunnels
CLOUD USER
CLOUD PROVIDER

## Slide 7: Outline
Motivation
VirtualWire
  Design
  Implementation
Evaluation
Conclusion

## Slide 8: VirtualWire connectors / wires
Point-to-point layer-2 network tunnels
  VXLAN wire format for packet encapsulation
Endpoints migrated with virtual network components
Implemented in the kernel for efficiency

## Slide 9: VirtualWire connectors / wires
Connections between endpoints
  E.g. tunnel, VPN, local bridge
Each hypervisor contains endpoint controller
  Advertises endpoints
  Looks up endpoints
  Sets wire type
  Integrates with VM migration
Simple interface
  connect/disconnect

## Slide 10: VirtualWire connectors / wires
Types of wires
  Native (bridge)
  Encapsulating (in kernel module)
  Tunneling (Open-VPN based)
/proc interface for configuring wires
Integrated with live migration

## Slide 11: Connector Implementation
Connectors are layer-2-in-layer-3 tunnels
  44 byte UDP header includes 32-bit connector ID
Original Ethernet Payload
Inner Destination MAC Address
Source Port
Dest Port
UDP Length
UDP Checksum
VirtualWire Connector ID
Version
Outer Ethernet Header
IHL
TOS
Total Length
Identification
Fragment Offset
Flags
Time to Live
Protocol
Header Checksum
Outer Source Address
Outer Destination Address
Inner Destination MAC Address
Inner Source MAC Address
Inner Source MAC Address
Optional Ethertype = C-Tag [802.1Q]
Inner.VLAN Tag Information
Outer IP
Outer UDP
Inner Ethernet
...

## Slide 12: virtualwire and the xen-blanket
Xen-Blanket (non-nested)
Xen/Dom 0
Network Component
Endpoint Manager
Hardware
Third-party cloud (RackSpace, EC2, etc.)
Hardware
Blanket layer provides hypervisor level features through nested virtualization on third-party clouds
User owned
VirtualWire
Xen-Blanket (nested)
Xen/Dom 0
Network Component
Endpoint Manager
VirtualWire
Enables cross-provider live migration

## Slide 13: Implementation
Server
Dom U
Front
Dom 0
Back
Endpoint
Bridge
Network Component (Switch)
Dom U
Front
Dom 0
Back
Endpoint
Bridge
Back
Endpoint
Bridge
Front
Outgoing Interface
Server
Dom U
Front
Dom 0
Back
Endpoint
Bridge
Outgoing Interface
Outgoing Interface

## Slide 14: Implementation
Xen-Blanket 2
Xen-Blanket 1
Server
Dom U
Front eth0
Dom 0
Back vif1.0
Endpoint vwe1.0
Bridge br1.0
Network Component vSwitch
Dom U
Dom 0
Front eth0
Dom 0
Back vif1.0
xenbr0
Back vif2.0
Outgoing Interface eth0
Bridge br1.0
Bridge br1.1
Front eth0
Front eth1
Back vif1.0
Endpoint vwe1.0
Back vif1.1
Endpoint vwe1.1
Xen-Blanket 3
Server
Dom U
Front eth0
Dom 0
Back vif1.0
Endpoint vwe1.0
Bridge br1.0
Front eth0
Front eth0
Dom 0
Back vif1.0
xenbr0
Outgoing Interface eth0
Physical machine 1
Physical machine 2
User owned
third-party cloud

## Slide 15: Optimizations
Xen-Blanket 3
Xen-Blanket 2
Dom 0
Xen-Blanket 1
Server
Dom U
Front
Dom 0
Back
Endpoint
Bridge
Endpoint
vSwitch
Endpoint
Outgoing Interface
Server
Dom U
Front
Dom 0
Back
Endpoint
Bridge
Outgoing Interface
Outgoing Interface

## Slide 16: Optimizations
Xen-Blanket 2
Xen-Blanket 1
Dom 0
Server
Dom U
Front
Back
vSwitch
Dom U
Front
Back
Endpoint Bridge
Back
Endpoint
Bridge
Front
Server
Dom U
Front
Dom 0
Back
Endpoint
Bridge
Outgoing Interface
Outgoing Interface

## Slide 17: Optimizations
Xen-Blanket 1
Dom 0
Server
Dom U
Front
Back
Back
Loop
Endpoint Bridge
Server
Dom U
Front
Back
Back
Loop
Endpoint Bridge
vSwitch

## Slide 18: Outline
Motivation
VirtualWire
  Design
  Implementation
Evaluation
Conclusion

## Slide 19: cross provider live migration
Xen-Blanket
Gateway Server DNS, DHCP, NFS
Dom U
VM.img
Dom U
Dom 0
SSH
Xen-Blanket
VM
Dom U
Dom 0
SSH
FW
Our Cloud
EC2
both domain 0s can access the NFS share through the virtual network.
all orange interfaces are on the same layer 2 virtual segment (attached to the same bridge) that spans both clouds, connected through an SSH tunnel.
VM

## Slide 20
Amazon EC2 and local resources
  EC2 (4XL): 33 ECUs, 23 GB memory, 10 Gbps Ethernet
  Local: 12 cores @ 2.93 GHz, 24 GB memory, 1Gbps Ethernet
Xen-blanket for nested virtualization
  Dom 0: 8 vCPUs, 4 GB memory
  PV guests: 4 vCPUs, 8 GB memory
Local NFS server for VM disk images
netperf to measure throughput latency
  1400 byte packets

## Slide 21: cross-provider live migration
Migrated 2 VMs and a virtual switch between Cornell and EC2
No network reconfiguration
Downtime as low as 1.4 seconds

## Slide 22: Outline
Motivation
VirtualWire
  Design
  Implementation
Evaluation
Conclusion

## Slide 23: performance issues
Virtual network components can be bottlenecks
  physical interface limitations
Several approaches
  Co-location
  Distributed components
  Evolve virtual network

## Slide 24: Before Next time
Project Interim report
  Due Monday, November 24.
  And meet with groups, TA, and professor
Fractus Upgrade: Should be back online
Required review and reading for Monday, November 24
  Making Middleboxes Someone Else’s Problem: Network Processing as a Cloud Service, Making middleboxes someone else's problem: network processing as a cloud service, J. Sherry, S. Hasan, C. Scott, A. Krishnamurthy, S. Ratnasamy, and V. Sekar. ACM SIGCOMM Computer Communication Review (CCR) Volume 42, Issue 4 (August 2012), pages 13-24.
  http://dl.acm.org/citation.cfm?id=2377680
  http://conferences.sigcomm.org/sigcomm/2012/paper/sigcomm/p13.pdf
Check piazza: http://piazza.com/cornell/fall2014/cs5413
Check website for updated schedule

## Slide 25: Decoupling gives Flexibility
Cloud’s flexibility comes from decoupling device functionality from physical devices
  Aka virtualization
Can place VM anywhere
  Consolidation
  Instantiation
  Migration
  Placement Optimizations

## Slide 26: Are all Devices Decoupled
Today: Split driver model
  Guests don’t need device specific driver
  System portion interfaces with physical devices
Dependencies on hardware
  Presence of device (e.g. GPU, FPGA)
  Device-related configuration (e.g. VLAN)
Xen
Hardware
Dom 0
Dom U: Guest
Physical Device Driver
Ring 1
Ring 3
Ring 0
Kernel User
Backend Driver
Frontend Driver

## Slide 27: Devices Limit Flexibility
Today: Split driver model
  Dependencies break if VM moves
No easy place to plug into hardware driver
  System portion connected in ad-hoc way
  .
Xen
Hardware
Dom 0
Dom U: Guest VM
Physical Device Driver
Ring 1
Ring 3
Ring 0
Kernel User
Backend Driver
Frontend Driver

## Slide 28: Split driver again!
Clean separation between hardware driver and backend driver
Standard interface between endpoints
Connected with wires
  .
Xen
Hardware
Dom 0
Dom U: Guest VM
Physical Device Driver
Ring 1
Ring 3
Ring 0
Kernel User
Backend Driver
Frontend Driver