## Slide 1: Data Center Networks and Fast and Programmable Switching Technologies
Hakim Weatherspoon
Assistant Professor, Dept of Computer Science
CS 5413: High Performance Systems and Networking
March 3, 2017
Slides used and adapted judiciously from Computer Networking, A Top-Down Approach

## Slide 2: PISA: Protocol Independent Switch Architecture
P4: Specifying packet processing logic
Basic constructs: Header, Parser, Action, Table
/* Header definition */
header_type ethernet_t {
fields {
dstAddr : 48;
srcAddr : 48;
etherType : 16; } }
/* Parser */
parser parse_ethernet {
extract(ethernet);
return select(latest.etherType) {
0x800 : parse_ipv4;
0x806 : parse_arp;
default : ingress; } }
action _drop()
{
drop();
}
action next_hop(arg1, arg2, …) {
// instructions
}
table forwarding_tbl {
read { ipv4.dstAddr : lpm; }
actions { next_hop; _drop; }}
Notes: P4 is a dataplane programming language for packet processing. The best way to think about P4 is it is like the instruction set for packet processing pipeline, as a result,
P4 provides a set of basic constructs to describe a packet processing pipeline, for example, you can define headers, parser, action and table in a packet pipeline.
In this example, we define a ethernet header as a struct with three fields, dst, src and etherType; then we define a parser to extract information from the header
and make a decision on the next parsing step.
We designed an assembler for FPGA.
Next, tables can be defined with two clauses. First the key that the table will match on. Second, the action to be performed on a packet if match is true.
For example, we can define an action of drop, to drop a packet. An action can also take arguments, which is from an entry in the table.

## Slide 3: PISA: Protocol Independent Switch Architecture
P4: Specifying packet processing logic
Basic constructs: Header, Parser, Action, Table
/* Header definition */
header_type udp_t {
fields {
srcPort : 16;
dstPort : 16;
length : 16;
checksum : 16; } }
/* Parser */
header udp_t udp;
parser parse_udp {
extract(udp);
return ingress; } }
action _drop()
{
drop();
}
action count_c1(arg1, arg2, …) {
// instructions
}
table table_count {
read { udp.dstPort : exact; }
actions { count_c1; _drop; }}
control ingress {
if { valid(eth)) {
if { valid(ip4)) {
if { valid(udp)) {
apply (table_count); }}}}
Notes: P4 is a dataplane programming language for packet processing. The best way to think about P4 is it is like the instruction set for packet processing pipeline, as a result,
P4 provides a set of basic constructs to describe a packet processing pipeline, for example, you can define headers, parser, action and table in a packet pipeline.
In this example, we define a ethernet header as a struct with three fields, dst, src and etherType; then we define a parser to extract information from the header
and make a decision on the next parsing step.
We designed an assembler for FPGA.
Next, tables can be defined with two clauses. First the key that the table will match on. Second, the action to be performed on a packet if match is true.
For example, we can define an action of drop, to drop a packet. An action can also take arguments, which is from an entry in the table.

## Slide 4: PISA: Protocol Independent Switch Architecture
PISA Protocol Independent Switch Architecture

## Slide 5: Before Next time
Project Proposal
  due thoday Friday, March 3
  Meet with groups, TA, and professor
HW2
  Chat Server
  Due this next Friday, March 10
Check website for updated schedule