## Slide 1: Data Center Networks and Switching and Queueing
Hakim Weatherspoon
Associate Professor, Dept of Computer Science
CS 5413: High Performance Computing and Networking
March 6, 2017

## Slide 2: Network Queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
What happens when a burst of packets arrive at a
switch destined to the same output port?

## Slide 3: Network Queueing
Ideally, each flow sends at its “fair share”, 1/n the network path capacity
TCP uses packet drops to signal congestion and flows adjust rates, AIMD
How do we proactively estimate available bandwidth?
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
TCP congestion control and avoidance attempts to
share bandwidth and prevent buffering (queueing)

## Slide 4: Available Bandwidth Estimation
Basic building block
  Network Protocol
  Networked Systems
  Distributed Systems
Which of the two paths has more available bandwidth?
End-to-end: How to measure without access to anything in the network?
How do I measure with minimum overhead?
Notes: 1’20”

## Slide 5: Available Bandwidth Estimation
Passive Measurement
  Polling counters: Port Stats or Flow Stats
Active Measurement
  Probe Packets: Packet Pair or Packet Train
Probe Packets:
Notes: We are going to use active probe because we assume autonomous system.

## Slide 6: Active Measurement
Narrow link: least capacity
Tight link: least available bandwidth
Narrow link
Network Capacity
Cross Traffic
Available Bandwidth
Tight link
Notes: Quick example
Narrow link is 2 Gbps
Tight link is

## Slide 7: Active Measurement
Estimate available bandwidth by saturating the tight link
Estimate Available Bandwidth?
Saturate/Congest Tight Link
Packet Queuing Delays Increase
7
Narrow link
Network Capacity
Cross Traffic
Available Bandwidth
Measuring (Increased) Queuing Delay
Tight link

## Slide 8: Active Measurement
Estimate available bandwidth by saturating the tight link
Rate
Probe Train #
Narrow link
Network Capacity
Cross Traffic
LA1 == LB1, no congestion
LA1
LB1
1Gbps
1Gbps
LA8 < LB8, congestion!
LA8
LB8
8Gbps
6Gbps
LA4 == LB4, no congestion
LA4
LB4
4Gbps
4Gbps
Available Bandwidth
Tight link
Notes: Can also put the actual figure up.
----- Meeting Notes (11/6/14 13:26) -----
Circle the knee,
4 figures.

## Slide 9
By measuring the increase in packet train length*, we can compute the queuing delay experienced, hence estimate the available bandwidth.
* Increase in packet train length == increase in sum of inter-packet gap
Notes: Increase

## Slide 10: Challenge
State-of-art (software) tools do not work at high speed because they cannot control and capture inter-packet spacing with required precision.
LA8
LB8
Cannot Control at 100ps
Cannot Measure at 100ps
Notes: ?
Summary: two basic issues.
At the sender end, in order to generate accurate probe rate, need fine control of packet timing at 100ps.
What can commodity machine do? forwarding.
Incoming rate is accurately controlled with increase rate.
Linux kernel forwarding lost control on timing.
Similarly, intel dpdk does better at lower data rate, but still have no control over high data rate.
Takeaway, with commodity machine, obtaining the level of control to generate accurate probe rate is not possible.
Similarly, the problem of measuring packet timing at the receiver end is also difficult.
----- Meeting Notes (11/6/14 13:57) -----
10Gbps every bit is 100ps.
In userspace we generated packet with instantenous rate from 0.1 Gbps, each pair of packet
Experiment is simple, we have one forwarding element.
The batching
slow down and clear.
Two lines to emphasize

## Slide 11: Accurate available bandwidth estimation [IMC 2014]
Application
Transport
Network
Data Link
Physical
Packet i
Packet i+1
Packet i+2
Notes: ----- Meeting Notes (10/17/14 17:10) -----
Modulating packet at PHY layer
----- Meeting Notes (10/20/14 16:35) -----
always sending bits
fill with idle.
key is access / control idle in phy layer
given this, we can precisely generate packet train, and measure packet train.
----- Meeting Notes (10/21/14 21:24) -----
Need to mention that it is sufficient to measure with packet gap

## Slide 12: Accurate available bandwidth estimation [IMC 2014]
Idle Characters (/I/)
  Each bit ~100 picoseconds
  7~8 bit special character in the physical layer
  700~800 picoseconds to transmit
  Only in PHY
Packet i
Packet i+1
Packet i+2
Application
Transport
Network
Data Link
Physical
Notes: ----- Meeting Notes (10/17/14 17:10) -----
Modulating packet at PHY layer
----- Meeting Notes (10/20/14 16:35) -----
always sending bits
fill with idle.
key is access / control idle in phy layer
given this, we can precisely generate packet train, and measure packet train.
----- Meeting Notes (10/21/14 21:24) -----
Need to mention that it is sufficient to measure with packet gap

## Slide 13: Accurate available bandwidth estimation [IMC 2014]
Probe Generation
1.0Gbps
Rate
Probe #
4.0Gbps
8.0Gbps
By modulating Inter-packet gap at PHY layer,
we can generate accurate probe rate.
1500 B
1500 B
1500 B
382 /I/s
382 /I/s
8Gbps
1500 B
1500 B
1500 B
2290 /I/s
2290 /I/s
4Gbps
1500 B
1500 B
1500 B
11374 /I/s
11374 /I/s
1Gbps
Notes: Emphasize exact amount. That is what makes us accurate.

## Slide 14: Questions:
Can MinProbe accurately estimate avail-bw at 10Gbps?
Can existing estimation algorithms work with MinProbe?
How do the following parameters affect accuracy?
  Packet train length
  probe packet size distribution
  cross packet size distribution
  cross packet burstiness
Does MinProbe work in the wild, Internet?
Does MinProbe work in rate limiting environments?
Can MinProbe accurately estimate avail-bw at 10Gbps?
Can existing estimation algorithms work with MinProbe?
How do the following parameters affect accuracy?
  Packet train length
  probe packet size distribution
  cross packet size distribution
  cross packet burstiness
Does MinProbe work in the wild, Internet?
Does MinProbe work in rate limiting environments?

## Slide 15: Experiment Setup
Controlled Environment
National Lambda Rail
NYC
Cornell(NYC)
Boston
Chicago
Cleveland

## Slide 16: Accurate available bandwidth estimation [IMC 2014]
Cross Traffic
tight link
Probe Traffic
MinProbe
MinProbe
10Gbps
Probe Traffic
Cross Traffic, paced at 1.0, 3.0, 6.0, 8.0Gbps

## Slide 17: Accurate available bandwidth estimation [IMC 2014]
Cross Traffic
10Gbps
tight link
MinProbe
MinProbe
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Cross Traffic, paced at 1.0, 3.0, 6.0, 8.0Gbps
Probe Traffic

## Slide 18: Accurate available bandwidth estimation [IMC 2014]
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 2Gbps
Cross Traffic 8Gbps
0.1Gbps
8.1Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 19: Accurate available bandwidth estimation [IMC 2014]
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 2Gbps
Cross Traffic 8Gbps
0.2Gbps
8.2Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 20: Accurate available bandwidth estimation [IMC 2014]
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 2Gbps
Cross Traffic 8Gbps
0.3Gbps
8.3Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 21: Accurate available bandwidth estimation [IMC 2014]
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 2Gbps
Cross Traffic 8Gbps
1.0Gbps
9.0Gbps
1.9Gbps
9.9Gbps
2.0Gbps
Queued
10.0Gbps
3.0Gbps
Queued
10.0Gbps
4.0Gbps
Queued
10.0Gbps
5.0Gbps
Queued
10.0Gbps
6.0Gbps
Queued
10.0Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 22: Accurate available bandwidth estimation [IMC 2014]
10Gbps
Available Bandwidth = 4Gbps
Cross Traffic 6Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 23: Accurate available bandwidth estimation [IMC 2014]
10Gbps
Available Bandwidth = 7Gbps
Cross Traffic 3Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 24: Accurate available bandwidth estimation [IMC 2014]
10Gbps
0.1Gbps
Rate
…
9.6 Gbps
0.2Gbps
…
Available Bandwidth = 9Gbps
Cross Traffic 1Gbps
Notes: ----- Meeting Notes (11/6/14 14:13) -----
Show blue
Show orange,
Show little green
Show all green.

## Slide 25: Accurate available bandwidth estimation [IMC 2014]
10Gbps
Notes: ----- Meeting Notes (1/24/14 10:03) -----
Robustness: Forward error correction
----- Meeting Notes (10/20/14 16:35) -----
Map
Show one at a time.
----- Meeting Notes (11/6/14 14:13) -----
Make this bigger.

## Slide 26: Accurate available bandwidth estimation [IMC 2014]
10Gbps
NYC
Cornell(NYC)
Cornell(Ithaca)
Boston
Chicago
Cleveland
Notes: ----- Meeting Notes (1/24/14 10:03) -----
Robustness: Forward error correction
----- Meeting Notes (10/20/14 16:35) -----
Map
Show one at a time.

## Slide 27: Questions:
Can MinProbe accurately estimate avail-bw at 10Gbps?
Can existing estimation algorithms work with MinProbe?
How do the following parameters affect accuracy?
  Packet train length
  probe packet size distribution
  cross packet size distribution
  cross packet burstiness
Does MinProbe work in the wild, Internet?
Does MinProbe work in rate limiting environments?

## Slide 28: Perspective
Modulation of probe packets in PHY
Accurate control & measure of packet timing
Enabled available bandwidth estimation in 10Gbps
Accurate, Minimum Overhead, Available Bandwidth Estimation in High Speed Wired Networks

## Slide 29: Before Next time
Project
  Continue to make progress.
  Intermediate project report due Mar 22. BOOM proposal due Mar 29.
HW2
  Chat Server
  Due this Friday, March 10
Background for next time (not required reading)
  Queues Don’t Matter When You Can JUMP Them!, Matthew P. Grosvenor, Malte Schwarzkopf, Ionel Gog, Robert N. M. Watson, Andrew W. Moore, Steven Hand, and Jon Crowcroft. Appears in the Proceedings of the USENIX symposium on Networked Systems Design and Implementation (NSDI), pp 1--14, May 2015.
Check website for updated schedule