## Slide 1: Data Center Networks and Switching and Queueing and Covert Timing Channels
Hakim Weatherspoon
Associate Professor, Dept of Computer Science
CS 5413: High Performance Computing and Networking
March 10, 2017

## Slide 2: Network Queueing
Ideally, each flow sends at its “fair share”, 1/n the network path capacity
TCP uses packet drops to signal congestion and flows adjust rates, AIMD
How do we proactively estimate available bandwidth?
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
TCP congestion control and avoidance attempts to
share bandwidth and prevent buffering (queueing)

## Slide 3: Network Queueing
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
Available bandwidth estimation:
What instantaneous probe rate causes buffering?

## Slide 4: Active Measurement
Narrow link: least capacity
Tight link: least available bandwidth
Narrow link
Network Capacity
Cross Traffic
Available Bandwidth
Tight link
Notes: Quick example
Narrow link is 2 Gbps
Tight link is

## Slide 5: Covert timing channel
Can we create a covert channel by modulating packet timings?
How effective would it be? E.g. bit error rate?
Narrow link
Network Capacity
Cross Traffic
Available Bandwidth
Tight link
Notes: Quick example
Narrow link is 2 Gbps
Tight link is

## Slide 6: Network Covert Channels
Hiding information
  Through communication not intended for data transfer
Notes: Covert channel is defined as a channel that are not indented for information transfer by Lampson
In the same way we have entities that may want to communicate in a hidden fashion in a network
in tthe same we will investigate covert channels in computer science especially in computer networks

## Slide 7: Network Covert Channels
Hiding information
  Through communication not intended for data transfer
  Using legitimate packets (Overt channel)
    Storage Channels: Packet headers
    Timing Channels: Arrival times of packets
Notes: In the same way we have entities that may want to communicate in a hidden fashion in a network
in tthe same we will investigate covert channels in computer science especially in computer networks

## Slide 8: Network Covert Channels
Hiding information
  Through communication not intended for data transfer
  Using legitimate packets (Overt channel)
    Storage Channels: Packet headers
    Timing Channels: Arrival times of packets

## Slide 9: Goals of Covert Channels
Bandwidth
  How much information can be delivered in a second
Robustness
  How much information can be delivered without loss / error
Undetectability
  How well communication is hidden
Notes: historically, prior state-of-art covert channels "exremely" slow and implemented lay3~4 using IP/TCP of protocol stack

## Slide 10: Goals of Covert Channels
Bandwidth
  How much information can be delivered in a second
  10~100s bits per second
Robustness
  How much information can be delivered without loss / error
  Cabuk’04, Shah’06
Undetectability
  How well communication is hidden
  Liu’09, Liu’10
Application
Transport
Network
Data Link
Physical
Notes: Cabuk’04: IP Covert Timing Channels: Design and Detection
Shah’06: Keyboards and covert channels
Liu’09: Hide and Seek in Time: Robust Covert Timing Channels
Liu’10: Robust and Undetectable Steganographic Timing Channels for i.i.d. Traffic

## Slide 11
Current network covert channels
are implemented in L3~4 (TCP/IP) layers
and are extremely slow.
Notes: Too Long
----- Meeting Notes (3/31/14 11:18) -----
Chupja is network covert channel which is thousands times faster than prior covert channels.
----- Meeting Notes (3/31/14 11:21) -----
takeway: l3-4 (TCP/IP) layers of netork protocol stack

## Slide 12: Chupja: PHY Covert Channel
Bandwidth
  How much information can be delivered in a second
  10~100s bits per second
Robustness
  How much information can be delivered without loss / error
  Bit Error Rate < 10%
Undetectability
  How well communication is hidden
  Invisible to detection software
Application
Transport
Network
Data Link
Physical
Physical
-> 10s~100s Kilo bits per second
Notes: ----- Meeting Notes (1/24/14 10:03) -----
Robustness: Forward error correction
----- Meeting Notes (3/28/14 15:22) -----
in the same way, we want to explore bounds
we want to do this in a network.
this was never done before.
"Let's pause for a second"

## Slide 13
Chupja is a network covert channel
which is faster than prior art.
It is implemented in L1 (PHY),
robust and virtually invisible to software.
Notes: Too Long

## Slide 14: Outline
Introduction
Design
Evaluation
Conclusion
Notes: ----- Meeting Notes (1/22/14 16:13) -----
Design outline
Discussion;

## Slide 15: Outline
Introduction
Design
  Threat Model
  10 Gigabit Ethernet
Evaluation
Conclusion

## Slide 16: Threat Model
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Sender
Receiver
Passive Adversary
Commodity Server
Commodity NIC
Notes: Implies no access to PHY

## Slide 17: 10 Gigabit Ethernet
Idle Characters (/I/)
  Each bit is ~100 picosecond wide
  7~8 bit special character in the physical layer
  700~800 picoseconds to transmit
  Only in PHY
Packet i
Packet i+1
Packet i+2
Application
Transport
Network
Data Link
Physical
Notes: We can implement covert timing channel by modulating IPGS at sub-microsecond scale

## Slide 18: Terminology
Interpacket delays (D) and gaps (G)
Homogeneous packet stream
  Same packet size,
  Same IPD (IPG),
  Same destination
IPG
Packet i
Packet i+1
IPD
Packet i
Packet i+1
Packet i+2
Notes: Why am I using homogeneous.

## Slide 19: Chupja: Design
Homogeneous stream
Sender
Receiver
Packet i
Packet i+1
Packet i+2
G - Ɛ
G + Ɛ
D - Ɛ
D + Ɛ
‘0’
‘1’
Packet i
Packet i+2
Gi
Gi+1
Di
Di+1
‘0’
‘1’
Packet i+1
Packet i
Packet i+2
G
G
D
D
IPG
IPG
Packet i+1
Notes: Assume G is shared
Why homogeneous?

## Slide 20: Chupja: Design
With shared G
  Encoding ‘1’: Gi = G + ε
  Encoding ‘0’: Gi = G - ε
Packet i
Packet i+1
Packet i+2
G - Ɛ
G + Ɛ
D - Ɛ
D + Ɛ
‘0’
‘1’
Notes: we add and remove idles symbols, meaning that we are operating at hundreds of pico microseconds
We are interested in optimal modulation of \epsilon. If \epsilon is large, it will be robust against network noise.

## Slide 21: Implementation
SoNIC [NSDI ’13]
  Software-defined Network Interface Card
  Allows control and access every bit of PHY
    In realtime, and in software
50 lines of C code addition
Application
Transport
Network
Data Link
Physical
Notes: That I presented last year

## Slide 22: Outline
Introduction
Design
Evaluation
  Bandwidth
  Robustness
  Undetectability
Conclusion

## Slide 23: Evaluation
What is the bandwidth of Chupja?
How robust is Chupja?
  Why is Chupja robust?
How undetectable is Chupja?

## Slide 24
What is the bandwidth of Chupja?
Notes: ----- Meeting Notes (1/24/14 11:25) -----
theoretical bound

## Slide 25: Evaluation: Bandwidth
Covert bandwidth equals to packet rate of overt channel
Chart: Overt Channel Throughput (Gbps)
| 0.01 | 0.1 | 0.5 | 1 | 3 | 6 | 9
64B | 17361 | 173611 | 868055 | 1736111 | 5208333 | 10416666 | 15625000
512B | 2403 | 24038 | 120192 | 240384 | 720046 | 1433486 | 2140410
1024B | 1211 | 12112 | 60562 | 121124 | 363372 | 726744 | 1085069
1518B | 819 | 8191 | 40956 | 81913 | 245676 | 491352 | 737028
1518B 1Gbps
81kbps
Notes: I need be clear about this graph.

## Slide 26
How robust is Chupja?
Notes: What is optimal modulation of /I/s that achieves BER < 10%?
----- Meeting Notes (1/24/14 10:25) -----
In association with modulating interpacket gaps (/I/s)

## Slide 27: Evaluation Setup
Boston
Cornell (Ithaca)
Cornell (NYC)
NLR (NYC)
Chicaco
Cleveland
Sender
Receiver
SW1
SW1
SW2
SW2
SW3
SW4
Sender
Receiver
Small Network
  Six commercial switches
  Average RTT: 0.154 ms
National Lambda Rail
  Nine routing hops
  Average RTT: 67.6ms
  1~2 Gbps External Traffic
Notes: NLR similar to GENI or Internet2

## Slide 28: Evaluation: Robustness
Overt Channel at 1 Gbps (D = 12211ns, G=13738 /I/s)
Covert Channel at 81 kbps
?
Sender
Receiver
Chart: Ɛ (/I/s)
| 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Small No Ext. | 0.43067 | 0.35931 | 0.22221 | 0.076841 | 0.02043 | 0.019484 | 0 | 0 | 0
Small Ext 3.6G | 0.47997 | 0.46057 | 0.42383 | 0.3782 | 0.31517 | 0.24555 | 0.13162 | 0.028731 | 0.003204
NLR | 0.49293 | 0.49049 | 0.46706 | 0.45593 | 0.36679 | 0.39184 | 0.28123 | 0.089341 | 0.01296
REF | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
7.7%
2.8%
8.9%

## Slide 29: Evaluation: Robustness
?
Overt Channel at 1 Gbps (D = 12211ns, G=13738 /I/s)
Covert Channel at 81 kbps
Modulating IPGS at 1.6us scale (=2048 /I/s)
Sender
Receiver
Chart: Ɛ (/I/s)
| 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
Small No Ext. | 0.43067 | 0.35931 | 0.22221 | 0.076841 | 0.02043 | 0.019484 | 0 | 0 | 0
Small Ext 3.6G | 0.47997 | 0.46057 | 0.42383 | 0.3782 | 0.31517 | 0.24555 | 0.13162 | 0.028731 | 0.003204
NLR | 0.49293 | 0.49049 | 0.46706 | 0.45593 | 0.36679 | 0.39184 | 0.28123 | 0.089341 | 0.01296
REF | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
7.7%
2.8%
8.9%
Notes: Not in this slide, but covert channels works better with big packets and slow data rates.

## Slide 30
Why is Chupja robust?

## Slide 31: Evaluation: Why?
Switches do not add significant perturbations to IPDs
Switches treat ‘1’s and ‘0’s as uncorrelated
  Over multiple hops when there is no external traffic.
  With external traffic
Notes: What i90? Reiterate I90 to make it clear

## Slide 32: Evaluation: Why?
Switches do not add significant perturbations to IPDs
Switches treat ‘1’s and ‘0’s as uncorrelated
  Over multiple hops when there is no external traffic.
  With external traffic
Sender
Homogeneous
1518B at 1 Gbps
Receiver
Sender
Chupja (Ɛ = 256/I/s)
1518B at 1 Gbps
Receiver
Notes: What i90? Reiterate I90 to make it clear

## Slide 33: Evaluation: Why?
Switches do not add significant perturbations to IPDs
Switches treat encoded ‘0’ and ‘1’ as uncorrelated
  Over multiple hops when there is no external traffic.
Chart: Interpacket Delayy (ns)
1 hop
3 hop
6 hop
9 hop
12 hop
15 hop
15 hop
D - Ɛ
90% in
D - Ɛ ± 250ns
Chart: Interpacket Delay (ns)
 | 1000000
1 hop
3 hop
6 hop
9 hop
12 hop
90% in
D ± 250ns
Homogeneous stream
Chupja stream ( Ɛ=256/I/s )
90% in
D ± 100ns
90% in
D – Ɛ ± 100ns
D + Ɛ
Notes: Takeaways:
Covert timing channel by modulating IPG
with overt channel 3 Gbps
with covert channel .25Mbps
E = 256 /I/s

## Slide 34: Evaluation: Why?
Boston
Cornell (Ithaca)
Cornell (NYC)
NLR (NYC)
Chicaco
Cleveland
Most of IPDs are within some range from original IPD
  Even when there is external traffic.
Encoded ‘Zero’
Encoded ‘One’
Sender
Receiver
Ɛ (/I/s) (ns) | 256 (=204.8ns) | 512 (=409.6) | 1024 (=819.2) | 2048 (=1638.4) | 4096 (=3276.8)
BER | 0.367 | 0.391 | 0.281 | 0.089 | 0.013
Notes: 10% can be recovered by redundancy or forward error correction
----- Meeting Notes (11/24/13 17:54) -----
x, y-axis

## Slide 35: Evaluation: Why?
Switches do not add significant perturbations to IPDs
Switches treat ‘1’s and ‘0’s as uncorrelated
  Over multiple hops when there is no external traffic.
  With external traffic
?
Sender
Receiver
1518B at 1 Gbps
With sufficiently large Ɛ,
the interpacket spacing holds throughout
the network, and BER is less than 10%
Notes: What i90? Reiterate I90 to make it clear

## Slide 36
How undetectable is Chupja?
Notes: What is optimal modulation of /I/s that achieves BER < 10%?

## Slide 37: Evaluation: Detection Setup
Commodity server with 10G NIC
  Kernel timestamping
NLR
Sender
Kernel timestamping
Receiver
NLR
Sender
SoNIC timestamping
Receiver

## Slide 38: Evaluation: Detection
Chart: Interpacket Delay (ns)
REF | 1000000
Chart: Interpacket Delay (ns)
REF | 1000000
Adversary cannot detect patterns of Chupja
Kernel Timestamping
SoNIC Timestamping
Ɛ = 1024
Ɛ = 4096
Ɛ = 1024
Ɛ = 4096

## Slide 39: Evaluation: Summary
What is the bandwidth of Chupja?
  10s~100s Kilo bits per second
How robust is Chupja?
  BER < 10% over NLR
  Why is Chupja robust?
    Sufficiently large Ɛ holds throughout the network
How undetectable is Chupja?
  Invisible to software

## Slide 40: Before Next time
Project
  Continue to make progress.
  Intermediate project report due Mar 22. BOOM proposal due Mar 29.
HW2
  Chat Server
  Due this Sunday, March 12
Monday, bring your laptop
Check website for updated schedule

## Slide 41: Where are we in the semester?
Overview and Basics
  Overview
  Basic Switch and Queuing (today)
  Low-latency and congestion avoidance (DCTCP)
Data Center Networks
  Data Center Network Topologies
  Software defined networking
    Software control plane (SDN)
    Programmable data plane (hardware [P4] and software [Netmap])
  Rack-scale computers and networks
  Disaggregated datacenters
  Alternative Switching Technologies
  Data Center Transport
  Virtualizing Networks
  Middleboxes
Advanced topics