## Slide 1: Data Center Networks and Software-defined Networking
Hakim Weatherspoon
Associate Professor, Dept of Computer Science
CS 5413: High Performance Computing and Networking
March 20, 2017
Slides taken liberally from Jennifer Rexford’s Computer Networks, COS 461 http://www.cs.princeton.edu/courses/archive/spr12/cos461/docs/lec24-sdn.ppt

## Slide 2: Agenda for semester
HW2 grading
  Sign up interactive demo session
  This Wednesday and Thursday
Project
  Continue to make progress.
  Intermediate project report due Mar 24. BOOM proposal due Mar 31.
  Spring break, week of April 2nd
  Intermediate project report 2 due April 12th.
  BOOM, Wednesday, April 19
  End of Semester, Wednesday, May 10
Check website for updated schedule

## Slide 3: Where are we in the semester?
Overview and Basics
  Overview
  Basic Switch and Queuing (today)
  Low-latency and congestion avoidance (DCTCP)
Data Center Networks
  Data Center Network Topologies
  Software defined networking
    Software control plane (SDN)
    Programmable data plane (hardware [P4] and software [Netmap])
  Rack-scale computers and networks
  Disaggregated datacenters
  Alternative Switching Technologies
  Data Center Transport
  Virtualizing Networks
  Middleboxes
Advanced topics

## Slide 4: Results from Survey
Interested Topics:
  SDN and programmable data planes
  Disaggregated datacenters and rack-scale computers
  Alternative switch technologies
  Datacenter topologies
  Datacenter transports
  Advanced topics
Interest in student presentations
  Not really

## Slide 5: Results from Survey
Load
  A bit High
Interesting: lectures, Lab’s, homeworks, projects
  4 out of 5 on average.
How to make the class a 5 out of 5
  Easier or no homework!
  In class labs
  Guidance and assistance on project
  Linux kernel modules!
  Labs about the cloud.

## Slide 6: The Internet: A Remarkable Story
Tremendous success
  From research experiment to global infrastructure
Brilliance of under-specifying
  Network: best-effort packet delivery
  Hosts: arbitrary applications
Enables innovation in applications
  Web, P2P, VoIP, social networks, virtual worlds
But, change is easy only at the edge… 

## Slide 7: Inside the ‘Net: A Different Story…
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Over specified
  Slow protocol standardization
Few people can innovate
  Equipment vendors write the code
  Long delays to introduce new features
Impacts performance, security, reliability, cost…

## Slide 8: Networks are Hard to Manage
Operating a network is expensive
  More than half the cost of a network
  Yet, operator error causes most outages
Buggy software in the equipment
  Routers with 20+ million lines of code
  Cascading failures, vulnerabilities, etc.
The network is “in the way”
  Especially a problem in data centers
  … and home networks

## Slide 9: Creating Foundation for Networking
A domain, not (yet?) a discipline
  Alphabet soup of protocols
  Header formats, bit twiddling
  Preoccupation with artifacts
From practice, to principles
  Intellectual foundation for networking
  Identify the key abstractions
  … and support them efficiently
To build networks worthy of society’s trust

## Slide 10: Rethinking the “Division of Labor”

## Slide 11: Traditional Computer Networks
Data plane:
Packet streaming
  Forward, filter, buffer, mark,
  rate-limit, and measure packets
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 12: Traditional Computer Networks
  Track topology changes, compute routes, install forwarding rules
Control plane:
Distributed algorithms
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 13: Traditional Computer Networks
  Collect measurements and configure the equipment
Management plane:
Human time scale
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 14: Death to the Control Plane!
Simpler management
  No need to “invert” control-plane operations
Faster pace of innovation
  Less dependence on vendors and standards
Easier interoperability
  Compatibility only in “wire” protocols
Simpler, cheaper equipment
  Minimal software

## Slide 15: Software Defined Networking (SDN)
API to the data plane
(e.g., OpenFlow)
Logically-centralized control
Switches
Smart,
slow
Dumb,
fast

## Slide 16: OpenFlow Networks

## Slide 17: Data-Plane: Simple Packet Handling
Simple packet-handling rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 18: Unifies Different Kinds of Boxes
Router
  Match: longest destination IP prefix
  Action: forward out a link
Switch
  Match: destination MAC address
  Action: forward or flood
Firewall
  Match: IP addresses and TCP/UDP port numbers
  Action: permit or deny
NAT
  Match: IP address and port
  Action: rewrite address and port

## Slide 19: Controller: Programmability
Network OS
Controller Application
Events from switches
Topology changes,
Traffic statistics,
Arriving packets
Commands to switches
(Un)install rules,
Query statistics,
Send packets

## Slide 20: Example OpenFlow Applications
Dynamic access control
Seamless mobility/migration
Server load balancing
Network virtualization
Using multiple wireless access points
Energy-efficient networking
Adaptive traffic monitoring
Denial-of-Service attack detection
See http://www.openflow.org/videos/

## Slide 21: E.g.: Dynamic Access Control
Inspect first packet of a connection
Consult the access control policy
Install rules to block or route traffic

## Slide 22: E.g.: Seamless Mobility/Migration
See host send traffic at new location
Modify rules to reroute the traffic

## Slide 23: E.g.: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*
src=1*

## Slide 24: E.g.: Network Virtualization
Partition the space of packet headers
Controller #1
Controller #2
Controller #3

## Slide 25: OpenFlow in the Wild
Open Networking Foundation
  Google, Facebook, Microsoft, Yahoo, Verizon, Deutsche Telekom, and many other companies
Commercial OpenFlow switches
  HP, NEC, Quanta, Dell, IBM, Juniper, …
Network operating systems
  NOX, Beacon, Floodlight, Nettle, ONIX, POX, Frenetic
Network deployments
  Eight campuses, and two research backbone networks
  Commercial deployments (e.g., Google backbone)

## Slide 26: A Helpful Analogy
From Nick McKeown’s talk “Making SDN Work” at the Open Networking Summit, April 2012

## Slide 27: Mainframes
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface

## Slide 28: Routers/Switches
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface

## Slide 29: Challenges

## Slide 30: Heterogeneous Switches
Number of packet-handling rules
Range of matches and actions
Multi-stage pipeline of packet processing
Offload some control-plane functionality (?)
access
control
MAC
look-up
IP
look-up

## Slide 31: Controller Delay and Overhead
Controller is much slower the the switch
Processing packets leads to delay and overhead
Need to keep most packets in the “fast path”
packets

## Slide 32: Distributed Controller
Network OS
Controller Application
Network OS
Controller Application
For scalability and reliability
Partition and replicate state

## Slide 33: Testing and Debugging
OpenFlow makes programming possible
  Network-wide view at controller
  Direct control over data plane
Plenty of room for bugs
  Still a complex, distributed system
Need for testing techniques
  Controller applications
  Controller and switches
  Rules installed in the switches

## Slide 34: Programming Abstractions
Controller APIs are low-level
  Thin veneer on the underlying hardware
Need better languages
  Composition of modules
  Managing concurrency
  Querying network state
  Network-wide abstractions
Ongoing at Princeton
  http://www.frenetic-lang.org/
Controller
Switches

## Slide 35: Perspective
Rethinking networking
  Open interfaces to the data plane
  Separation of control and data
  Leveraging techniques from distributed systems
Significant momentum
  In both research and industry