## Slide 1: Lecture 9: Cameras
CS5670: Computer Vision
Noah Snavely
Source: S. Lazebnik

## Slide 3: Reading
Szeliski 2.1.3-2.1.6

## Slide 4: Announcements
Project 2 due Friday by 11:59pm
  If you haven’t created your team on CMS, please do so ASAP
Take-home midterm
  To be handed out next Thursday, due the following Tuesday by the beginning of class
Planning on in-class final, last lecture of class

## Slide 5: Third Place

## Slide 6: Zhen Liu

## Slide 7: Second Place

## Slide 8: Gabriel Ruttner

## Slide 9: First Place

## Slide 10: Jaldeep Acharya

## Slide 11: Last time

## Slide 12: Can we use homographies to create a 360 panorama?
In order to figure this out, we need to learn what a camera is

## Slide 13: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?

## Slide 14: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
  How does this transform the image?
Notes: It gets inverted

## Slide 15: Camera Obscura
Basic principle known to Mozi (470-390 BC), Aristotle (384-322 BC)
Drawing aid for artists: described by Leonardo da Vinci (1452-1519)
Gemma Frisius, 1558
Source: A. Efros

## Slide 16: Camera Obscura

## Slide 17: Home-made pinhole camera
http://www.debevec.org/Pinhole/
Why so
blurry?
Slide by A. Efros

## Slide 18: Pinhole photography
Justin Quinnell, The Clifton Suspension Bridge. December 17th 2007 - June 21st 2008 6-month exposure

## Slide 19: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects...

## Slide 20: Shrinking the aperture

## Slide 21: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 22: Lytro Lightfield Camera

## Slide 23: Lenses
A lens focuses parallel rays onto a single focal point
  focal point at a distance f beyond the plane of the lens (the focal length)
    f is a function of the shape and index of refraction of the lens
  Aperture restricts the range of rays
    aperture may be on either side of the lens
  Lenses are typically spherical (easier to produce)
focal point
F

## Slide 24: The eye
The human eye is a camera
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Notes: Note that the retina is curved

## Slide 25
http://www.telegraph.co.uk/news/earth/earthpicturegalleries/7598120/Animal-eyes-quiz-Can-you-work-out-which-creatures-these-are-from-their-eyes.html?image=25

## Slide 26
http://www.telegraph.co.uk/news/earth/earthpicturegalleries/7598120/Animal-eyes-quiz-Can-you-work-out-which-creatures-these-are-from-their-eyes.html?image=25

## Slide 27: Eyes in nature: eyespots to pinhole camera
http://upload.wikimedia.org/wikipedia/commons/6/6d/Mantis_shrimp.jpg

## Slide 28: Eyes in nature: eyespots to pinhole camera

## Slide 29: Eyes in nature
Source: Animal Eyes, Land & Nilsson
(polychaete fan worm)

## Slide 30: Projection

## Slide 31: Projection

## Slide 32: Müller-Lyer Illusion
http://www.michaelbach.de/ot/sze_muelue/index.html

## Slide 33: Modeling projection
The coordinate system
  We will use the pinhole model as an approximation
  Put the optical center (Center Of Projection) at the origin
  Put the image plane (Projection Plane) in front of the COP
    Why?
  The camera looks down the negative z axis
    we need this if we want right-handed-coordinates
Notes: This way the image is right-side-up

## Slide 34: Modeling projection
Projection equations
  Compute intersection with PP of ray from (x,y,z) to COP
  Derived using similar triangles (on board)
  We get the projection by throwing out the last coordinate:

## Slide 35: Modeling projection
Is this a linear transformation?
Homogeneous coordinates to the rescue!
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
  no—division by z is nonlinear

## Slide 36: Perspective Projection
Projection is a matrix multiply using homogeneous coordinates:
divide by third coordinate
This is known as perspective projection
  The matrix is the projection matrix
(Can also represent as a 4x4 matrix – OpenGL does something like this)

## Slide 37: Perspective Projection
How does scaling the projection matrix change the transformation?

## Slide 38: Orthographic projection
Special case of perspective projection
  Distance from the COP to the PP is infinite
  Good approximation for telephoto optics
  Also called “parallel projection”: (x, y, z) → (x, y)
  What’s the projection matrix?
Image
World

## Slide 39: Orthographic projection

## Slide 40: Perspective projection

## Slide 41: Variants of orthographic projection
Scaled orthographic
  Also called “weak perspective”
Affine projection
  Also called “paraperspective”

## Slide 42: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image
What have we lost?
  Angles
  Distances (lengths)
Slide by A. Efros

## Slide 43: Projection properties
Many-to-one: any points along same ray map to same point in image
Points → points
Lines → lines (collinearity is preserved)
  But line through focal point projects to a point
Planes → planes (or half-planes)
  But plane through focal point projects to line

## Slide 44: Projection properties
Parallel lines converge at a vanishing point
  Each direction in space has its own vanishing point
  But parallels parallel to the image plane remain parallel

## Slide 45: Questions?

## Slide 46: Camera parameters
How can we model the geometry of a camera?
“The World”
Camera
x
y
z
v
w
u
o
COP
Two important coordinate systems:
1. World coordinate system
2. Camera coordinate system

## Slide 47: Camera parameters
To project a point (x,y,z) in world coordinates into a camera
First transform (x,y,z) into camera coordinates
Need to know
  Camera position (in world coordinates)
  Camera orientation (in world coordinates)
The project into the image plane
  Need to know camera intrinsics

## Slide 48: Camera parameters
Projection equation
  The projection matrix models the cumulative effect of all parameters
  Useful to decompose into a series of operations
projection
intrinsics
rotation
translation
identity matrix
A camera is described by several parameters
  Translation T of the optical center from the origin of world coords
  Rotation R of the image plane
  focal length f, principle point (x’c, y’c), pixel size (sx, sy)
  blue parameters are called “extrinsics,” red are “intrinsics”
  The definitions of these parameters are not completely standardized
    especially intrinsics—varies from one book to another

## Slide 49: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c

## Slide 50: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
How do we represent translation as a matrix multiplication?

## Slide 51: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R
3x3 rotation matrix

## Slide 52: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R

## Slide 53: Perspective projection
(intrinsics)
in general,
: aspect ratio (1 unless pixels are not square)
: skew (0 unless pixels are shaped like rhombi/parallelograms)
: principal point ((0,0) unless optical axis doesn’t intersect projection plane at origin)
(upper triangular matrix)
(converts from 3D rays in camera coordinate system to pixel coordinates)

## Slide 54: Focal length
Can think of as “zoom”
Also related to field of view
24mm
50mm
200mm
800mm

## Slide 55: Projection matrix
(t in book’s notation)
translation
rotation
projection
intrinsics

## Slide 56: Projection matrix
(t in book’s notation)
or

## Slide 57: Projection matrix
0
=
(in homogeneous image coordinates)

## Slide 58: Questions?