## Slide 1: Lecture 10: Cameras
CS5670: Computer Vision
Noah Snavely
Source: S. Lazebnik

## Slide 2: Announcements
Project 2 is out, due next Thursday, March 8
  Report due Friday, March 9
  Project to be done in pairs
    Please form groups on CMS!
Take-home midterm
  To be distributed in class next Thursday, March 8
  Due at the beginning of class the following Tuesday (March 13)
Planning on in-class final, last lecture of class

## Slide 3: Can we use homographies to create a 360 panorama?
In order to figure this out, we need to learn what a camera is

## Slide 4: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?

## Slide 5: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
  How does this transform the image?
Notes: It gets inverted

## Slide 6: Camera Obscura
Basic principle known to Mozi (470-390 BC), Aristotle (384-322 BC)
Drawing aid for artists: described by Leonardo da Vinci (1452-1519)
Gemma Frisius, 1558
Source: A. Efros

## Slide 7: Camera Obscura

## Slide 8: Home-made pinhole camera
http://www.debevec.org/Pinhole/
Why so
blurry?
Slide by A. Efros

## Slide 9: Pinhole photography
Justin Quinnell, The Clifton Suspension Bridge. December 17th 2007 - June 21st 2008 6-month exposure

## Slide 10: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects...

## Slide 11: Shrinking the aperture

## Slide 12: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 14: Lytro Lightfield Camera
Captures “all the rays”

## Slide 15: Lenses
A lens focuses parallel rays onto a single focal point
  focal point at a distance f beyond the plane of the lens (the focal length)
    f is a function of the shape and index of refraction of the lens
  Aperture restricts the range of rays
    aperture may be on either side of the lens
  Lenses are typically spherical (easier to produce)
focal point
F

## Slide 16: The eye
The human eye is a camera
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Notes: Note that the retina is curved

## Slide 17
http://www.telegraph.co.uk/news/earth/earthpicturegalleries/7598120/Animal-eyes-quiz-Can-you-work-out-which-creatures-these-are-from-their-eyes.html?image=25

## Slide 18
http://www.telegraph.co.uk/news/earth/earthpicturegalleries/7598120/Animal-eyes-quiz-Can-you-work-out-which-creatures-these-are-from-their-eyes.html?image=25

## Slide 19: Eyes in nature: eyespots to pinhole camera
http://upload.wikimedia.org/wikipedia/commons/6/6d/Mantis_shrimp.jpg

## Slide 20: Eyes in nature: eyespots to pinhole camera

## Slide 21: Eyes in nature
Source: Animal Eyes, Land & Nilsson
(polychaete fan worm)

## Slide 22: Projection

## Slide 23: Projection

## Slide 24: Müller-Lyer Illusion
http://www.michaelbach.de/ot/sze_muelue/index.html

## Slide 25: Modeling projection
The coordinate system
  We will use the pinhole model as an approximation
  Put the optical center (Center Of Projection) at the origin
  Put the image plane (Projection Plane) in front of the COP
    Why?
  The camera looks down the negative z axis
    we like this if we want right-handed-coordinates
Notes: This way the image is right-side-up

## Slide 26: Modeling projection
Projection equations
  Compute intersection with PP of ray from (x,y,z) to COP
  Derived using similar triangles (on board)
  We get the projection by throwing out the last coordinate:

## Slide 27: Modeling projection
Is this a linear transformation?
Homogeneous coordinates to the rescue—again!
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
  no—division by z is nonlinear

## Slide 28: Perspective Projection
Projection is a matrix multiply using homogeneous coordinates:
divide by third coordinate
This is known as perspective projection
  The matrix is the projection matrix
(Can also represent as a 4x4 matrix – OpenGL does something like this)

## Slide 29: Perspective Projection
How does scaling the projection matrix change the transformation?

## Slide 30: Orthographic projection
Special case of perspective projection
  Distance from the COP to the PP is infinite
  Good approximation for telephoto optics
  Also called “parallel projection”: (x, y, z) → (x, y)
  What’s the projection matrix?
Image
World

## Slide 31: Orthographic projection

## Slide 32: Perspective projection

## Slide 33: Variants of orthographic projection
Scaled orthographic
  Also called “weak perspective”
Affine projection
  Also called “paraperspective”

## Slide 34: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image
What have we lost?
  Angles
  Distances (lengths)
Slide by A. Efros

## Slide 35: Projection properties
Many-to-one: any points along same ray map to same point in image
Points → points
Lines → lines (collinearity is preserved)
  But line through focal point projects to a point
Planes → planes (or half-planes)
  But plane through focal point projects to line

## Slide 36: Projection properties
Parallel lines converge at a vanishing point
  Each direction in space has its own vanishing point
  But parallels parallel to the image plane remain parallel

## Slide 37: Questions?

## Slide 38: Camera parameters
How can we model the geometry of a camera?
“The World”
Camera
x
y
z
v
w
u
o
COP
Two important coordinate systems:
1. World coordinate system
2. Camera coordinate system
(x, y, z)
How do we project a given point (x, y, z) in world coordinates?

## Slide 39: Camera parameters
To project a point (x,y,z) in world coordinates into a camera
First transform (x,y,z) into camera coordinates
Need to know
  Camera position (in world coordinates)
  Camera orientation (in world coordinates)
Then project into the image plane to get a pixel coordinate
  Need to know camera intrinsics

## Slide 40: Camera parameters
Projection equation
  The projection matrix models the cumulative effect of all parameters
  Useful to decompose into a series of operations
projection
intrinsics
rotation
translation
identity matrix
A camera is described by several parameters
  Translation T of the optical center from the origin of world coords
  Rotation R of the image plane
  focal length f, principle point (x’c, y’c), pixel size (sx, sy)
  blue parameters are called “extrinsics,” red are “intrinsics”
  The definitions of these parameters are not completely standardized
    especially intrinsics—varies from one book to another

## Slide 41: Projection matrix
0
=
(in homogeneous image coordinates)

## Slide 42: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c

## Slide 43: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
How do we represent translation as a matrix multiplication?

## Slide 44: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R
3x3 rotation matrix

## Slide 45: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R
(with extra row/column of [0 0 0 1])

## Slide 46: Perspective projection
(intrinsics)
in general,
: aspect ratio (1 unless pixels are not square)
: skew (0 unless pixels are shaped like rhombi/parallelograms)
: principal point ((0,0) unless optical axis doesn’t intersect projection plane at origin)
(upper triangular matrix)
(converts from 3D rays in camera coordinate system to pixel coordinates)

## Slide 47: Focal length
Can think of as “zoom”
Also related to field of view
24mm
50mm
200mm
800mm

## Slide 48: Field of view
http://www.dslrsolutions.net/3298/using-your-hands-as-focal-length-calculator/

## Slide 53
Notes: http://www.stsite.com/camera/telephoto-wideangle.php
Wide angle deepens
Telephoto magnifies and pulls it in

## Slide 54
http://petapixel.com/2013/01/11/how-focal-length-affects-your-subjects-apparent-weight-as-seen-with-a-cat/

## Slide 55: Projection matrix
translation
rotation
projection
intrinsics
This part converts 3D points in world coordinates to 3D rays in the camera’s coordinate system. There are 6 parameters represented (3 for position/translation, 3 for rotation).
The K matrix converts 3D rays in the camera’s coordinate system to 2D image points in image (pixel) coordinates.

## Slide 56: Projection matrix
(t in book’s notation)
translation
rotation
projection
intrinsics

## Slide 57: Projection matrix
(t in book’s notation)
or

## Slide 58: Projection matrix
0
=
(in homogeneous image coordinates)

## Slide 59: Questions?

## Slide 60: Perspective distortion
Problem for architectural photography: converging verticals
Source: F. Durand

## Slide 61: Perspective distortion
Problem for architectural photography: converging verticals
Solution: view camera (lens shifted w.r.t. film)
Source: F. Durand
Tilting the camera upwards results in converging verticals
Keeping the camera level, with an ordinary lens, captures only the bottom portion of the building
Shifting the lens upwards results in a picture of the entire subject
http://en.wikipedia.org/wiki/Perspective_correction_lens

## Slide 62: Perspective distortion
Problem for architectural photography: converging verticals
Result:
Source: F. Durand

## Slide 63: Perspective distortion
What does a sphere project to?
Image source: F. Durand

## Slide 64: Perspective distortion
The exterior columns appear bigger
The distortion is not due to lens flaws
Problem pointed out by Da Vinci
Slide by F. Durand

## Slide 65: Perspective distortion: People

## Slide 66: Distortion
Radial distortion of the image
  Caused by imperfect lenses
  Deviations are most noticeable for rays that pass through the edge of the lens
No distortion
Pin cushion
Barrel

## Slide 68: Correcting radial distortion
from Helmut Dersch

## Slide 69: Distortion

## Slide 70: Modeling distortion
To model lens distortion
  Use above projection operation instead of standard projection matrix multiplication
Apply radial distortion
Apply focal length translate image center
Project to “normalized” image coordinates

## Slide 71: Other types of projection
Lots of intriguing variants…
(I’ll just mention a few fun ones)

## Slide 72: 360 degree field of view…
Basic approach
  Take a photo of a parabolic mirror with an orthographic lens (Nayar)
  Or buy one a lens from a variety of omnicam manufacturers…
    See http://www.cis.upenn.edu/~kostas/omni.html

## Slide 73: Tilt-shift
Titlt-shift images from Olivo Barbieri and Photoshop imitations
http://www.northlight-images.co.uk/article_pages/tilt_and_shift_ts-e.html

## Slide 74: Rotating sensor (or object)
Rollout Photographs © Justin Kerr
http://research.famsi.org/kerrmaya.html
Also known as “cyclographs”, “peripheral images”