## Slide 1: Single-View Modeling
CS5670: Computer Vision
Noah Snavely

## Slide 2: Congratulations to Noah!
It’s Baby Charlie!

## Slide 3: Some Notes
I (Abe) will take on most of the instructor duties moving forward
  I will defer to Noah’s precedent on course structure and policy whenever possible
Bear with us on the transition
  First time teaching a course, but frequently give talks (hopefully this will translate well…)
  If I can’t answer a question in class, I will try to answer it at the beginning of next class or send out a correction.
  I may occasionally describe things differently from Noah---don’t hesitate to ask for clarifications

## Slide 4: Single-View Modeling
Readings
  Mundy, J.L. and Zisserman, A., Geometric Invariance in Computer Vision, Appendix: Projective Geometry for Machine Vision, MIT Press, Cambridge, MA, 1992, (read 23.1 - 23.5, 23.10)
    available online: http://www.cs.cmu.edu/~ph/869/papers/zisser-mundy.pdf
Ames Room

## Slide 5: Announcements
Midterm Due Today
Assignment 3 (DEMO)

## Slide 6: Roadmap ahead
The next few lectures will finish up geometry
  Next up is recognition / learning
We already know about camera geometry & panoramas
Coming up
  Single-view modeling (today)
  Two-view geometry
  Multi-view geometry

## Slide 7: Ames Room
https://www.youtube.com/watch?v=bZGWRJyo0YU

## Slide 8
Notes: https://www.youtube.com/watch?v=hCV2Ba5wrcs

## Slide 9: Ames Room: What does this illustrate?
Computer vision is under-constrained
One image has multiple explanations
  We are good at picking the most likely one
“Are children small, or just far away?”
-Magical Mysteries
by Thrilla Killa Klownz
SNL Digital Short

## Slide 10: Projective geometry—what’s it good for?
Uses of projective geometry
  Drawing
  Measurements
  Mathematics for projection
  Undistorting images
  Camera pose estimation
  Object recognition
Paolo Uccello

## Slide 11: Applications of projective geometry
Vermeer’s Music Lesson
Reconstructions by Criminisi et al.

## Slide 12: Making measurements in images
https://www.warbyparker.com/pd/instructions

## Slide 13: Measurements on planes
1
2
3
4
1
2
3
4
Approach: unwarp then measure
Notes: homography!

## Slide 14: Homogeneous coordinates and lines
(X,Y,W) same as (SX,SY,SW)
Line in projective plane
  ax + by + c = 0
  aX + bY + cW = 0
  uTp = pTu =0
    u = [a,b,c] T and p = [X,Y,W] T
    (x,y) Euclidean = (X/W,Y/W)
    W = 0? Ideal points, points at infinity (X,Y,0)

## Slide 15: Homogeneous Coordinates & Projection (Review?)
y-axis
z-axis
z=1
(Image plane)
p= (x, y, z)
z
(Image Coordinates)
p’= (?,?,1)
1
p’= (?,?,1)
p’= (x/z, y/z, 1)
Homogenization =
Apply Similar Triangles Rule

## Slide 16: Point and line duality
l
  A line l is a homogeneous 3-vector
  It is  to every point (ray) p on the line: l.p=0
p1
p2
  What is the intersection of two lines l1 and l2 ?
    p is  to l1 and l2  p = l1  l2
  Points and lines are dual in projective space
l1
l2
p
  What is the line l spanned by rays p1 and p2 ?
    l is  to p1 and p2  l = p1  p2
    l can be interpreted as a plane normal

## Slide 17: Ideal points and lines
Ideal point (“point at infinity”)
  p  (x, y, 0) – parallel to image plane
  It has infinite image coordinates
(sx,sy,0)
-y
x
-z
image plane
Ideal line
  l  (a, b, 0) – parallel to image plane
(a,b,0)
-y
x
-z
image plane
  Corresponds to a line in the image (finite coordinates)
    goes through image origin (principal point)

## Slide 18: 3D projective geometry
These concepts generalize naturally to 3D
  Homogeneous coordinates
    Projective 3D points have four coords: P = (X,Y,Z,W)
  Duality
    A plane N is also represented by a 4-vector
    Points and planes are dual in 3D: N·P=0
    Three points define a plane, three planes define a point
When z-axis is no longer the optical axis of our imaging system (eye or camera), we need to add a new homogeneous coordinate

## Slide 19: 3D to 2D: perspective projection
Projection:
Notes: Preserved: lines, incidence
Not preserved: lengths, angles, parallelism

## Slide 21: Vanishing points (1D)
Vanishing point
  projection of a point at infinity
  can often (but not always) project to a finite point in the image
image plane
camera
center
ground plane
vanishing point
camera
center
image plane
ground plane

## Slide 22: Vanishing points (2D)
image plane
camera
center
line on ground plane
vanishing point

## Slide 23: Vanishing points
Properties
  Any two parallel lines (in 3D) have the same vanishing point v
  The ray from C through v is parallel to the lines
  An image may have more than one vanishing point
    in fact, every image point is a potential vanishing point
image plane
camera
center
C
line on ground plane
vanishing point V
line on ground plane
Notes: How to determine which lines in the scene vanish at a given pixel?

## Slide 24: One-point perspective

## Slide 25: Two-point perspective
vx
vy

## Slide 26: Three-point perspective

## Slide 27: Questions?

## Slide 28: Vanishing lines
Multiple Vanishing Points
  Any set of parallel lines on the plane define a vanishing point
  The union of all of these vanishing points is the horizon line
    also called vanishing line
  Note that different planes (can) define different vanishing lines
v1
v2

## Slide 29: Vanishing lines
Multiple Vanishing Points
  Any set of parallel lines on the plane define a vanishing point
  The union of all of these vanishing points is the horizon line
    also called vanishing line
  Note that different planes (can) define different vanishing lines

## Slide 30: Computing vanishing points
V
P0
D

## Slide 31: Computing vanishing points
Properties
  P is a point at infinity, v is its projection
  Depends only on line direction
  Parallel lines P0 + tD, P1 + tD intersect at P
V
P0
D
Takeaway:
Every directions maps to a vanishing point. Every vanishing point maps to a direction

## Slide 32: Computing vanishing lines
Properties
  l is intersection of horizontal plane through C with image plane
  Compute l from two sets of parallel lines on ground plane
  All points at same height as C project to l
    points higher than C project above l
  Provides way of comparing height of objects in the scene
ground plane
l
C
v1
v2
l

## Slide 33: Riddle me this…
Notes: Is this parachuter higher or lower than the person taking this picture?
Lower—he is below the horizon

## Slide 34: Fun with vanishing points

## Slide 35: Lots of fun with vanishing points

## Slide 36: Perspective cues

## Slide 37: Perspective cues

## Slide 38: Perspective cues

## Slide 39: Comparing heights
Vanishing
Point

## Slide 40: Measuring height
1
2
3
4
5
5.4
2.8
3.3
Camera height
How high is the camera?

## Slide 41: Computing vanishing points (from lines)
q1
Intersect p1q1 with p2q2
v
p1
p2
q2
Least squares version
  Better to use more than two lines and compute the “closest” point of intersection
  See notes by Bob Collins for one good way of doing this:
    http://www-2.cs.cmu.edu/~ph/869/www/notes/vanishing.txt

## Slide 42: Measuring height without a ruler
H
R

## Slide 43: Measuring height without a ruler
C
ground plane
Compute Z from image measurements
  Need more than vanishing points to do this
Z

## Slide 44: The cross ratio
A Projective Invariant
  Something that does not change under projective transformations (including perspective projection)
P1
P2
P3
P4
The cross-ratio of 4 collinear points
Can permute the point ordering
  4! = 24 different orders (but only 6 distinct values)
This is the fundamental invariant of projective geometry

## Slide 45: Measuring height
vZ
r
t
b
image cross ratio
B (bottom of object)
T (top of object)
R (reference point)
ground plane
H
C
scene cross ratio

scene points represented as
image points as
R

## Slide 46: Finding the vertical (z) vanishing point
Find intersection of projections of vertical lines

## Slide 47: Measuring height
R
H
vz
r
b
t
image cross ratio
H
v
vx
vy
vanishing line (horizon)
b0
t0

## Slide 48
vz
r
b
vx
vy
vanishing line (horizon)
t0
What if the point on the ground plane b0 is not known?
  Here the person is standing on the box, height of box is known
  Use one side of the box to help find b0 as shown above
b0
t1
b1
Measuring height
v
m0

## Slide 49: 3D modeling from a photograph
St. Jerome in his Study, H. Steenwick

## Slide 50: 3D modeling from a photograph

## Slide 51: 3D modeling from a photograph
Flagellation, Piero della Francesca

## Slide 52: 3D modeling from a photograph
video by Antonio Criminisi

## Slide 53: 3D modeling from a photograph

## Slide 54: Related problem: camera calibration
Goal: estimate the camera parameters
  Version 1: solve for 3x4 projection matrix
  Version 2: solve for camera parameters separately
    intrinsics (focal length, principal point, pixel size)
    extrinsics (rotation angles, translation)
    radial distortion

## Slide 55: Vanishing points and projection matrix
= vx (X vanishing point)
Z
3
Y
2
,
similarly,
v
π
v
π
=
=
Not So Fast! We only know v’s up to a scale factor
  Can fully specify by providing 3 additional reference points with known coordinates

## Slide 56: Calibration using a reference object
Place a known object in the scene
  identify correspondence between image and scene
  compute mapping from scene to image
Issues
  must know geometry very accurately
  must know 3D->2D correspondence

## Slide 57: Chromaglyphs
Courtesy of Bruce Culbertson, HP Labs
http://www.hpl.hp.com/personal/Bruce_Culbertson/ibr98/chromagl.htm

## Slide 58: AR codes
ArUco

## Slide 59: Estimating the projection matrix
Place a known object in the scene
  identify correspondence between image and scene
  compute mapping from scene to image

## Slide 60: Direct linear calibration

## Slide 61: Direct linear calibration
Can solve for mij by linear least squares
  use eigenvector trick that we used for homographies

## Slide 62: Direct linear calibration
Advantage:
  Very simple to formulate and solve
Disadvantages:
  Doesn’t tell you the camera parameters
  Doesn’t model radial distortion
  Hard to impose constraints (e.g., known f)
  Doesn’t minimize the right error function
For these reasons, nonlinear methods are preferred
  Define error function E between projected 3D points and image positions
    E is nonlinear function of intrinsics, extrinsics, radial distortion
  Minimize E using nonlinear optimization techniques

## Slide 63: Alternative: multi-plane calibration
Images courtesy Jean-Yves Bouguet
Advantage
  Only requires a plane
  Don’t have to know positions/orientations
  Good code available online! (including in OpenCV)
    Matlab version by Jean-Yves Bouget: http://www.vision.caltech.edu/bouguetj/calib_doc/index.html
    Zhengyou Zhang’s web site: http://research.microsoft.com/~zhang/Calib/

## Slide 64: Some Related Techniques
Image-Based Modeling and Photo Editing
  Mok et al., SIGGRAPH 2001
  http://graphics.csail.mit.edu/graphics/ibedit/
Single View Modeling of Free-Form Scenes
  Zhang et al., CVPR 2001
  http://grail.cs.washington.edu/projects/svm/index.htm
Tour Into The Picture
  Anjyo et al., SIGGRAPH 1997
  http://www.mizuno.org/gl/tip/

## Slide 65: Single-image depth prediction
Image
Depth map
Deep learning

## Slide 66: Using Classic Vision to Understand Modern Learning
Vision is under-constrained
  Many explanations for the same image
  Some prior assumptions always necessary
Deep learning is a tool for developing data-driven priors
Understanding the geometry of image formation guides this process
  Designing learnable representations
  Designing deep architectures
  Curating data

## Slide 67: Questions?