## Slide 1: Cameras
CS5670: Computer Vision
Source: S. Lazebnik

## Slide 2: Announcements
Take-home midterm will be handed out at the end of class
  Due Tuesday, March 7, by 1pm (beginning of class)
Project 2 Report due tonight by 8pm
Project 3: Panorama Stitching
  To be released next Tuesday, March 7
  Tentative due date: Friday, March 17

## Slide 3: Can we use homographies to create a 360 panorama?
In order to figure this out, we need to learn what a camera is

## Slide 4: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
  No. This is a bad camera.

## Slide 5: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
  How does this transform the image?
Notes: It gets inverted

## Slide 6: Camera Obscura
Basic principle known to Mozi (470-390 BC), Aristotle (384-322 BC)
Drawing aid for artists: described by Leonardo da Vinci (1452-1519)
Gemma Frisius, 1558
Source: A. Efros

## Slide 7: Camera Obscura

## Slide 8: Home-made pinhole camera
http://www.debevec.org/Pinhole/
Why so blurry?
Slide by A. Efros

## Slide 9: Pinhole photography
Justin Quinnell, The Clifton Suspension Bridge. December 17th 2007 - June 21st 2008 6-month exposure

## Slide 10
https://petapixel.com/2019/07/17/this-is-the-worlds-first-solargraphy-timelapse/

## Slide 11: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects...

## Slide 12: Shrinking the aperture

## Slide 13: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion”

## Slide 14: The eye
The human eye is a camera
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Notes: Note that the retina is curved

## Slide 15
http://www.telegraph.co.uk/news/earth/earthpicturegalleries/7598120/Animal-eyes-quiz-Can-you-work-out-which-creatures-these-are-from-their-eyes.html?image=25

## Slide 16
http://www.telegraph.co.uk/news/earth/earthpicturegalleries/7598120/Animal-eyes-quiz-Can-you-work-out-which-creatures-these-are-from-their-eyes.html?image=25

## Slide 17: Eyes in nature: eyespots to pinhole camera
http://upload.wikimedia.org/wikipedia/commons/6/6d/Mantis_shrimp.jpg

## Slide 18: Projection

## Slide 19: Projection

## Slide 20: Müller-Lyer Illusion
https://en.wikipedia.org/wiki/Müller-Lyer_illusion

## Slide 21: Geometric Model: A Pinhole Camera
Figure credit: Peter Hedman

## Slide 22: Modeling projection
The coordinate system
  We use the pinhole model as an approximation
  Put the optical center (aka Center of Projection, or COP) at the origin
  Put the Image Plane (aka Projection Plane) in front of the COP (Why)?
  The camera looks down the positive z-axis, and the y-axis points down
    we like this if we want right-handed-coordinates
    other versions are possible (e.g., OpenGL)
z
x
y
(x, y, z)
(x’, y’, f)
f
Center of Projection (COP)
Image Plane
Notes: This way the image is right-side-up

## Slide 23: Modeling projection
z
x
y
(x, y, z)
(x’, y’, f)
f
Center of Projection (COP)
Image Plane
Projection equations
  Compute intersection with PP of ray from (x,y,z) to COP
  Derived using similar triangles
  We get the projection by throwing out the last coordinate:
Notes: This way the image is right-side-up

## Slide 24: Modeling projection
Is this a linear transformation?
Homogeneous coordinates to the rescue—again!
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
  no—division by z is nonlinear

## Slide 25: Perspective Projection
Projection is a matrix multiply using homogeneous coordinates:
This is known as perspective projection
  The matrix is the projection matrix
  (Can also represent as a 4x4 matrix – OpenGL does something like this)
divide by third coordinate
Notes: $$
\begin{bmatrix}
1 & 0 & 0 & 0 \\
0 & 1 & 0 & 0 \\
0 & 0 & 1/f & 0
\end{bmatrix}
\begin{bmatrix}
x \\
y \\
z \\
1
\end{bmatrix}
=
\begin{bmatrix}
x \\
y \\
z / f
\end{bmatrix}
$$

## Slide 26: Perspective Projection
How does scaling the projection matrix change the transformation?
Scale by f:
Scaling a projection matrix produces an equivalent projection matrix!

## Slide 27: Orthographic projection
Special case of perspective projection
  Distance from the COP to the PP is infinite
  Good approximation for telephoto optics
  Also called “parallel projection”: (x, y, z) → (x, y)
  What’s the projection matrix?
Image
World

## Slide 28: Orthographic projection

## Slide 29: Perspective projection

## Slide 30: Variants of orthographic projection
Scaled orthographic
  Also called “weak perspective”
Affine projection
  Also called “paraperspective”

## Slide 31: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image
What have we lost?
  Angles
  Distances (lengths)
Slide by A. Efros

## Slide 32: Projection properties
Many-to-one: any points along same ray map to same point in image
Points → points
Lines → lines (collinearity is preserved)
  But line through focal point projects to a point
Planes → planes (or half-planes)
  But plane through focal point projects to line

## Slide 33: Projection properties
Parallel lines converge at a vanishing point
  Each direction in space has its own vanishing point
  But parallel lines parallel to the image plane remain parallel

## Slide 34: Questions?

## Slide 35: Camera parameters
How can we model the geometry of a camera?
“The World”
Camera
x
y
z
v
w
u
o
COP
Three important coordinate systems:
World coordinates
Camera coordinates
Image coordinates
(x, y, z)
How do we project a given world point (x, y, z) to an image point?

## Slide 36: Coordinate frames
World coordinates
Camera coordinates
Image coordinates
Figure credit: Peter Hedman

## Slide 37: Camera parameters
To project a point (x, y, z) in world coordinates into a camera
First transform (x, y, z) into camera coordinates
Need to know
  Camera position (in world coordinates)
  Camera orientation (in world coordinates)
Then project into the image plane to get image (pixel) coordinates
  Need to know camera intrinsics

## Slide 38: Camera parameters
Projection equation
  The projection matrix models the cumulative effect of all parameters
  Useful to decompose into a series of operations
projection
intrinsics
rotation
translation
identity matrix
A camera is described by several parameters
  Translation T of the optical center from the origin of world coords
  Rotation R of the image plane
  focal length f, principal point (cx, cy), pixel aspect size α
  blue parameters are called “extrinsics,” red are “intrinsics”
  The definitions of these parameters are not completely standardized
    especially intrinsics—varies from one book to another

## Slide 39: Projection matrix
0
=
(in homogeneous image coordinates)

## Slide 40: Extrinsics
How do we get the camera to “canonical form”?
  Canonical form: Center of projection at the origin, x-axis points right, y-axis points down, z-axis points forwards
Step 1: Translate by -c
0

## Slide 41: Extrinsics
0
Step 1: Translate by -c
How do we represent translation as a matrix multiplication?
How do we get the camera to “canonical form”?
  Canonical form: Center of projection at the origin, x-axis points right, y-axis points down, z-axis points forwards

## Slide 42: Extrinsics
Step 1: Translate by -c
Step 2: Rotate by R
3x3 rotation matrix
0
How do we get the camera to “canonical form”?
  Canonical form: Center of projection at the origin, x-axis points right, y-axis points down, z-axis points forwards

## Slide 43: Extrinsics
0
Step 1: Translate by -c
Step 2: Rotate by R
(with extra row/column of [0 0 0 1])
How do we get the camera to “canonical form”?
  Canonical form: Center of projection at the origin, x-axis points right, y-axis points down, z-axis points forwards

## Slide 44: Perspective projection
(intrinsics)
in general,
: aspect ratio (1 unless pixels are not square)
: skew (0 unless pixels are shaped like rhombi/parallelograms)
: principal point ((w/2,h/2) unless optical axis doesn’t intersect projection plane at image center)
(upper triangular matrix)
(converts from 3D rays in camera coordinate system to pixel coordinates)

## Slide 45: Typical intrinsics matrix
2D affine transform corresponding to a scale by f (focal length) and a translation by (cx, cy) (principal point)
Maps 3D rays to 2D pixels

## Slide 46: Focal length
Can think of as “zoom”
Also related to field of view
24mm
50mm
200mm
800mm

## Slide 47: Field of view

## Slide 52
Notes: http://www.stsite.com/camera/telephoto-wideangle.php
Wide angle deepens
Telephoto magnifies and pulls it in

## Slide 53
http://petapixel.com/2013/01/11/how-focal-length-affects-your-subjects-apparent-weight-as-seen-with-a-cat/

## Slide 54: Projection matrix
translation
rotation
projection
intrinsics
This part converts 3D points in world coordinates to 3D rays in the camera’s coordinate system. There are 6 parameters represented (3 for position/translation, 3 for rotation).
The K matrix converts 3D rays in the camera’s coordinate system to 2D image points in image (pixel) coordinates.

## Slide 55: Projection matrix
(t in book’s notation)
translation
rotation
projection
intrinsics

## Slide 56: Projection matrix
0
=
(in homogeneous image coordinates)

## Slide 57: Questions?

## Slide 58: Perspective distortion
Problem for architectural photography: converging verticals
Source: F. Durand

## Slide 59: Perspective distortion
Problem for architectural photography: converging verticals
Solution: view camera (lens shifted w.r.t. film)
Source: F. Durand
Tilting the camera upwards results in converging verticals
Keeping the camera level, with an ordinary lens, captures only the bottom portion of the building
Shifting the lens upwards results in a picture of the entire subject
http://en.wikipedia.org/wiki/Perspective_correction_lens

## Slide 60: Perspective distortion
Problem for architectural photography: converging verticals
Result:
Source: F. Durand

## Slide 61: Perspective distortion
What does a sphere project to?
Image source: F. Durand

## Slide 62: Perspective distortion
The exterior columns appear bigger
The distortion is not due to lens flaws
Problem pointed out by Da Vinci
Slide by F. Durand

## Slide 63
https://aaronhertzmann.com/2022/02/28/how-does-perspective-work.html

## Slide 64: Perspective distortion: People

## Slide 65: Distortion-Free Wide-Angle Portraits on Camera Phones
YiChang Shih, Wei-Sheng Lai, and Chia-Kai Liang, Distortion-Free Wide-Angle Portraits on Camera Phones, SIGGRAPH 2019
https://people.csail.mit.edu/yichangshih/wide_angle_portrait/

## Slide 66: Distortion
Radial distortion of the image
  Caused by imperfect lenses
  Deviations are most noticeable for rays that pass through the edge of the lens
No distortion
Pin cushion
Barrel

## Slide 68: Radial distortion
[Image credit: J. Bouguet http://www.vision.caltech.edu/bouguetj/calib_doc/htmls/example.html]
Arrows show motion of projected points relative to an ideal (distortion-free lens)

## Slide 69: Correcting radial distortion
from Helmut Dersch

## Slide 70: Distortion

## Slide 71: Modeling distortion
To model lens distortion
  Use above projection operation instead of standard projection matrix multiplication
Apply radial distortion
Apply focal length translate image center
Project to “normalized” image coordinates

## Slide 72: Other types of projection
Lots of intriguing variants…
(I’ll just mention a few fun ones)

## Slide 73: 360 degree field of view…
Basic approach
  Take a photo of a parabolic mirror with an orthographic lens (Nayar)
  Or buy one a lens from a variety of omnicam manufacturers…
    See http://www.cis.upenn.edu/~kostas/omni.html

## Slide 74: Tilt-shift
Tilt-shift images from Olivo Barbieri and Photoshop imitations
http://www.northlight-images.co.uk/article_pages/tilt_and_shift_ts-e.html

## Slide 75: Rotating sensor (or object)
Rollout Photographs © Justin Kerr
http://research.famsi.org/kerrmaya.html
Also known as “cyclographs”, “peripheral images”

## Slide 76: Questions?