## Slide 1: Software-Defined Networking: OpenFlow and Frenetic
Mohamed Ismail

## Slide 2: Background

## Slide 3: Problem: Programming Networks is Hard

## Slide 4: Network Stack Pros
Key to the success of the Internet
Layers and layers of abstraction
Independent innovation at each layer
  Communication media
  Ethernet standards
  Transport layer protocols
Follows end-to-end argument
(Source: Shenker, 2011)

## Slide 5: Network Stack Cons
Network switches and routers built and optimized for internet traffic
Network components and internet protocols set in stone
  Difficulty to switch from IPv4 to IPv6
Difficult to perform research on Internet
(Source: Shenker, 2011)
Problem:
Network infrastructure has “ossified”

## Slide 6: Functions of a switch/router
Receive a packet and send to appropriate destination
Prevent a packet from reaching a certain destination
Packet
In
Packet
Out
Switch/Router

## Slide 7: Programming a switch/router
Use a limited API to program the switch/router flow table
Must program each network device separately
Programming dependent on topology
Does not scale
Packet
In
Packet
Out
Switch/Router
Flow Table
Problem: No generalized API for programming scalable networks

## Slide 8: Data Plane vs. Control Plane
Data Plane
Receive a packet
Forward packet based on flow table
Network stack abstractions are data plane abstractions
Control Plane
Update flow table to specify where packets should go
Update flow table to specify where packets should not go
No abstractions for updating the control plane

## Slide 9: Programming networks is hard because…
Network stack is an abstraction for the data plane
Network infrastructure has “ossified” due to the success of the internet
Switch and router internals vary by manufacturer and there is no standard API for the control plane
Without any abstractions for control plane, research and innovation in network programming is near impossible
  Must compute configuration of each device
  Can only work with given network-level protocol (i.e. IP)

## Slide 10: OpenFlow

## Slide 11: Authors
Nick McKeown
  ‘95 PhD UC Berkeley
  Co-founded Nicira Networks, ONF
  Faculty at Stanford
Tom Anderson
  ‘91 PhD Univ. of Wash.
  UC Berkeley ‘91-’97
  Faculty at Univ. of Wash.
Hari Balakrishnan
  ‘98 PhD UC Berkeley
  Faculty at MIT
Guru Parulkar
  ‘87 PhD Univ. of Deliware
  Many network-related startups
  Executive director of Clean Slate Internet Design Program
Larry Peterson
  ‘85 PhD Purdue University
  GENI project chair
  Faculty at Princeton
Jennifer Rexford
  ‘96 PhD Univ. of Mich.
  AT&T Labs ‘96-’05
  Broader Gateway Protocol
  Faculty at Princeton
Scott Shenker
  ‘83 PhD Univ. of Chig.
  XEROX Parc
  Co-founder of Nicira Networks, ONF
  Faculty at Berkeley
Jonathan Turner
  Faculty at Washington University in St. Louis

## Slide 12: Goals
Run experiments on campus networks
  Reluctance to using experimental equipment on college network
  Isolation: Control over network without disruptions to normal traffic
  What functionality is needed for experiments?
Software-based approach
  Low performance
  Low port density
Low cost
  Take advantage of existing infrastructure
  Closed platforms from vendors

## Slide 13: Goals and Challenges
Run experiments on campus networks
  Reluctance by admins to using experimental equipment on college network
  Isolation: Control over network without disruptions to normal traffic
  What functionality is needed for experiments?
Software-based approach
  Software-based solutions have low performance
  Software-based solutions support low port density
Low cost
  Take advantage of existing infrastructure
  Closed platforms from vendors

## Slide 14: Take Aways
OpenFlow allows network devices to decouple the data plane from the control plane
Data plane processing done by network device
Data plane abstraction is the network stack
Control plane processing done by controller
New control stack for OpenFlow devices provides standardized API and abstractions necessary to innovate in field of network management

## Slide 15: Design
Separate data plane from control plane
Data plane
  High performance forwarding
Control plane
  Flow table is programmable
  Accessed through controller using OpenFlow Protocol
Packet
In
Packet
Out
Switch/Router
Flow Table
OpenFlow

## Slide 16: OpenFlow API
Forward packets to given port (or ports)
Forward packets to controller
  Usage: Can analyze and process packets
Drop the packet
  Usage: Protect against attacks by removing suspicious packets

## Slide 17: Flow Table Entry
Packet header to define flow
Action to be performed
Statistics
(Source: ONF, 2012)

## Slide 18: Isolation
Two Options:
Add another action to the OpenFlow API
  Forward packets through normal pipeline
OR
Define separate VLANs
  No overlap over production and experimental traffic

## Slide 19: Discussion
What is easy to accomplish with the OpenFlow solution?
What is still hard to do with OpenFlow?

## Slide 20: Controllers
Must communicate using OpenFlow protocol
Individual controllers for multiple switches or single controller for all switches
Use with Network OS
  NOX
Should provide some permissions to prevent mixing of traffic or unauthorized flow table changes
Implementation details left unspecified

## Slide 21: Control Stack
OpenFlow is only a means to achieve the decoupling needed for Software-Defined Networking
Network OS provides common control functionality that can be used by multiple applications
(Sources: Casado, 2011; Shenker, 2011)

## Slide 22: Discussion
What functionality should the Network OS have?
What layers or abstractions are missing from the control stack?

## Slide 23: Google B4
Provides connectivity among Google datacenters
Use SDN and OpenFlow
Centralized traffic engineering application
  Resource contention
  Multipath forwarding/tunneling to leverage network capacity according to application priority
  Dynamically relocate bandwidth
Many links run at near 100% utilization for extended periods of time
(Source: Jain, 2013)

## Slide 24: Open Network Foundation
Promote adoption of Sotware-Defined Networking through open standards such as OpenFlow
Partners:

## Slide 25: Open Network Foundation
Promote adoption of Sotware-Defined Networking through open standards such as OpenFlow
Partners:

## Slide 26: Open Network Foundation
Promote adoption of Sotware-Defined Networking through open standards such as OpenFlow
Partners:

## Slide 27: Open Network Foundation
Promote adoption of Sotware-Defined Networking through open standards such as OpenFlow
Partners:

## Slide 28: Open Network Foundation
Promote adoption of Sotware-Defined Networking through open standards such as OpenFlow
Partners:

## Slide 29: Take Aways
OpenFlow allows network devices to decouple the data plane from the control plane
Data plane processing done by network device
Data plane abstraction is the network stack
Control plane processing done by controller
New control stack for OpenFlow devices provides standardized API and abstractions necessary to innovate in field of network management

## Slide 30: Frenetic

## Slide 31: Authors
Nate Foster
  ‘09 PhD Upenn
  Faculty at Cornell
Rob Harrison
  ‘11 Masters Princeton
  Westpoint
Matthew L. Meola
  ?
Michael J. Freedman
  PhD NYU
  CoralCDN
  Faculty at Princeton
Jennifer Rexford
  ‘96 PhD Univ. of Mich.
  AT&T Labs ‘96-’05
  Broader Gateway Protocol
  Faculty at Princeton
David Walker
  ‘01 PhD Cornell (Morrisett)
  Faculty at Princeton

## Slide 32: Problems
OpenFlow is a “machine language”
  Directly reflects underlying hardware
  High level policy may require multiple low-level rules
Network programs are not isolated from each other
  No equivalent of virtual memory space
  Composition of programs is a manual process and error prone
Controller does not see all traffic, so some information may be hidden
  Delay in programming switches and routers
  Must take care of additional corner cases
Hard to effectively program OpenFlow tables using NOX

## Slide 33: Take Aways
OpenFlow is the “machine language” of network programming
  Difficult to program correctly and efficiently
  Not enough layers of abstraction for programmers
Frenetic addresses issues with composibility, low-level interaction, and providing a unified view through the Frenetic run-time system and Frenetic programming language

## Slide 34: Approach
Add a layer of abstraction
  Run-time system converts between high-level program to correct low-level network rules
Frenetic programming language based on functional reactive programming (FRP)
  “See every packet” abstraction
  Composition
  Rich pattern algebra
(Source: Foster, 2010)

## Slide 35: Example w/o Frenetic
def repeater(switch):
  p1 = {IN_PORT:1}
  p2 = {IN_PORT:2}
  a1 = [output(2)]
  a2 = [output(1)]
  install(switch, p1, a1, DEFAULT)
  install(switch, p2, a2, DEFAULT)
def monitor(switch):
  p = {IN_PORT:2,TP_SRC:80}
  install(switch, p, [], DEFAULT)
  query_stats(switch, p)
def repeater_monitor(switch):
  p1 = {IN_PORT:1}
  p2 = {IN_PORT:2}
  p2web = {IN_PORT:2,TP_SRC:80}
  a1 = [output(2)]
  a2 = [output(1)]
  install(switch, p1, a1, DEFAULT)
  install(switch, p2, a2, DEFAULT)
  install(switch, p2web, a2, HIGH)
  query_stats(switch, p2web)

## Slide 36: Example w/ Frenetic
def monitor_sf():
  return(Filter(inport_p(2) & srcport_p(80)) |o|
  GroupByTime(30) |o|
  SumSizes())
rules = [Rule(inport_p(1), [output(2)]),
Rule(inport_p(2), [output(1)])]
def repeater_monitor():
  register_static(rules)
  stats = Apply(Packets(), monitor_sf())
  print_stream(stats)

## Slide 37: Discussion
Are there any issues with OpenFlow that Frenetic could not address?
How does Frenetic reinforce the idea that innovation in this field will come through abstractions and layering?
Does Frenetic or OpenFlow help address the issue of “ossification” of the internet?

## Slide 38: Take Aways
OpenFlow is the “machine language” of network programming
  Difficult to program correctly and efficiently
  Not enough layers of abstraction for programmers
Frenetic addresses issues with composibility, low-level interaction, and providing a unified view through the Frenetic run-time system and Frenetic programming language

## Slide 39: References
OpenFlow: Enabling innovation in campus networks. Nick McKeown et al. (2008-04). ACM Communications Review.
Frenetic: A High-Level Langauge for OpenFlow Networks. Nate Foster, Rob Harrison, Matthew L. Meola, Michael J. Freedman, Jennifer Rexford, and David Walker. In ACM Workshop on Programmable Routers for Extensible Services of Tomorrow (PRESTO), Philadelphia, PA, November 2010.
Open Network Foundation. http://opennetworking.org
Origins and Evolution of OpenFlow/SDN. Martin Casado. In Open Networking Summit, Stanford, CA, October 2011.
The Future of Networking, and the Past of Protocols. Scott Shenker. In Open Networking Summit, Stanford, CA, October 2011.
B4: Experience with a Globally-Deployed Software Deﬁned WAN. Sushant Jain, Alok Kumar, Subhasree Mandal, Joon Ong, Leon Poutievski, Arjun Singh, Subbaiah Venkata, Jim Wanderer, Junlan Zhou, Min Zhu, Jonathan Zolla, Urs Hölzle, Stephen Stuart and Amin Vahdat. In SIGCOMM 2013.