## Slide 1: Modern systems: security
Hakim Weatherspoon
CS6410
Slides borrowed liberally from past presentations from Sai Krishna Deepak Maram

## Slide 2: Move to a Cloud-based model
User apps
Software
Hypervisor
OS
User apps
Software
Hypervisor
OS
PaaS Cloud Provider manages the stack
Notes: A traditional PaaS model. Applies to Saas, IaaS as well.

## Slide 3: Move to a Cloud-based model
User apps
Software
Hypervisor
OS
Privileged code
Software
Hypervisor
OS
Malicious cloud provider?

## Slide 4: Can you trust the cloud?
Huge Trusted Computing Base (TCB)
Cloud Provider’s software
Management stack
Sysadmins
Notes: User needs to trust the cloud provider’s software, cloud sysad, even other cloud users co-located => large trusted computing base (TCB)

## Slide 5: What do we want?
Notes: Simply put, we want the raw resources of the cloud provider. Without trusting all the middlemen

## Slide 6: Shielded Execution using SGX
Privileged code
Software
Hypervisor
OS
Cloud Provider manages the stack
SGX
Enclave
Confidentiality
  The execution state is unobservable to the rest of the system.
Integrity
  If the program completes, its output is the same as a correct execution on a reference platform
Notes: At a high level, the abstraction we are looking for is that of “Shielded execution” - Irrespective of the environment, SGX provides a hardware-based guarantee of isolation.
the props we want are...

## Slide 7: Is shielded execution sufficient?
Notes: To complete this piece of puzzle i.e., trusted hardware, we need one final piece.
“An isolation mechanism must permit interaction with untrusted software or hardware, to communicate results or access system services, and it is at these points that a na¨ıve isolated program is vulnerable”

## Slide 8: Remote Attestation
Goal: Allow cryptographic verification that specific software has been loaded within an enclave
  While an enclave is initialized, its contents is cryptographically hashed by the CPU forming the enclave’s measurement
Generated using a key burnt on the SGX chip
  Root of trust: Intel
  Intel attestation service (IAS) for verification
Intel
Private key
Public key
IAS
SGX Chip
Enclave Initialization
Measurement hash
Private key
Notes: Allows for providing the end-to-end guarantee , Intel controls it

## Slide 9: How does SGX achieve this?
Notes: Let’s look a bit into the SGX internals

## Slide 10: Memory protection
EPC (Enclave Page Cache)
  A separate region in physical memory
  All enclave pages reside here
  Hardware tracks meta info corresponding to each page
  Virtualized

## Slide 11: Memory protection
EPC (Enclave Page Cache): A separate region in physical memory
  Encrypted and integrity-protected before writing to the main memory
Same page table as the underlying OS
  Access checks are performed to ensure any other application (not even other enclaves) can access an enclave’s data

## Slide 12: Execution lifecycle (high-level)
Loading stage: Performed by untrusted code
  Enclave is initialized by copying code/data into EPC Pages
  At the end of which, contents are hashed to compute enclave’s measurement hash
Enclave mode:
  Special instructions to create an enclave, add pages to enclave and exit an enclave
  Similar to switching from user to kernel mode
  Secure mechanisms to handle interrupts (or) page faults to protect from OS exception handlers

## Slide 13: Before SGX?
Notes: Architectures before SGX: Dedicated crypto hardware (not general-purpose), trusted hypervisors, TPM

## Slide 14: Trusted Platform Module (TPM)
Attestation-based
Can be used with commodity systems
Weak security
  Much bigger TCB than SGX: Measurement hash covers all the OS modules and device drivers
  Very hard to keep an up-to-date list of the hashes
  Many more attacks....

## Slide 15: How to port legacy applications into SGX?
Notes: Related question: How different is it to develop new applications in SGX?
Ask for any thoughts here?

## Slide 16: Developing applications in SGX
Untrusting OS: Makes it harder
Any function call (or) syscall made outside the enclave are not guaranteed to return
Even if data returns, enclave cannot trust the data returned

## Slide 17: Haven
Haven design goals:
  Mutual distrust b/w guest and host
  Run legacy apps inside SGX without any modifications
Application interacts only with LibOS
  Assumes libOS is carefully implemented
Shield module interacts with the untrusted host OS
Notes: Exokernel connection: All OS apps at the user level.

## Slide 18: How Haven handles Iago attacks
Iago attacks: “Malicious kernel attempts to subvert an isolated application by exploiting its assumption of correct OS behavior, for example when using the results of system calls”
LibOS: Implement entire OS as part of the Trusted Computing Base. Limits the interaction of enclave app with the actual OS, thus reducing the attack surface.

## Slide 19: Haven

## Slide 20: LibOS and Exokernels
Both bring OS level functionalities to the user space, but for what reasons?
Efficiency in Exokernel
  “Move OS functionality to the user space to grant more flexibility”
Security in Haven’s LibOS
  “Move OS functionality into the enclave to reduce attack space”
Notes: libOS and exokernel

## Slide 21: Haven Performance
35% - 65% slowdown
Depends on the exact use case
Notes: The usual security vs efficiency tradeoff

## Slide 22: Haven influencing SGX

## Slide 23: Haven influencing SGX design
Dynamic memory allocation
  SGX does not allow addition of enclave pages after the creation of enclave
Exception Handling
  SGX does not allow handling of all exceptions
Some other limitations
Fixed in v2.0
Notes: Mismatch b/w what Haven wants and SGX provides

## Slide 24: SGX: What’s New?
Latest v2.4
  Trusted randomness, other crypto operations
  File abstractions inside an enclave
Baidu’s Rust SGX SDK
  Dockerized
  Runs a simulated version on machines without SGX chip as well

## Slide 25: Is SGX Secure?
Sophisticated side channel attacks
  Foreshadow – Usenix Security 2018
  Speculative execution
  Komodo: Using verification to disentangle secure-enclave hardware from software – SOSP 2017
Notes: “Nothing is secure”

## Slide 26: Trusted hardware makes the attacker’s job costly

## Slide 27: Discussion
Haven
  Exokernel connection to Haven
  Impact of Haven and why it’s not more widely used?
SGX
  Does trusted hardware solve the problem of security in the cloud?
  Can SGX still be useful in face of side channel attacks?

## Slide 28: Next Time
Project: next step is the Survey Paper due next Friday
Read and write a review:
  The Google file system, Sanjay Ghemawat, Howard Gobioff, Shun-Tak Leung. 19th ACM symposium on Operating systems principles (SOSP), October 2003, 29--43.
  Spanner: Google's Globally Distributed Database, James C. Corbett, Jeffrey Dean, Michael Epstein, Andrew Fikes, Christopher Frost, J. J. Furman, Sanjay Ghemawat, Andrey Gubarev, Christopher Heiser, Peter Hochschild, Wilson Hsieh, Sebastian Kanthak, Eugene Kogan, Hongyi Li, Alexander Lloyd, Sergey Melnik, David Mwaura, David Nagle, Sean Quinlan, Rajesh Rao, Lindsay Rolig, Yasushi Saito, Michal Szymaniak, Christopher Taylor, Ruth Wang, and Dale Woodford. In Proceedings of the 10th USENIX conference on Operating Systems Design and Implementation (OSDI'12), October 2012, 251--264.

## Slide 29: Thank you!
References:
Haven, Slides
Intel SGX explained

## Slide 30: Thank You!